## Slide 1: Multicast and Anycast
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/

## Slide 2: Outline today
IP Anycast
  N destinations, 1 should receive the message
  Providing a service from multiple network locations
  Using routing protocols for automated failover
Multicast protocols
  N destinations, N should receive the message
  Examples
    IP Multicast
    SRM (Scalable Reliable Multicast)
    PGM (Pragmatic General Multicast)

## Slide 3
http://en.wikipedia.org/wiki/Multicast

## Slide 4: Limitations of DNS-based failover
Failover/load balancing via multiple A records
  ;; ANSWER SECTION:
  www.cnn.com. 300 IN A 157.166.255.19
  www.cnn.com. 300 IN A 157.166.224.25
  www.cnn.com. 300 IN A 157.166.226.26
  www.cnn.com. 300 IN A 157.166.255.18
If server fails, service unavailable for TTL
  Very low TTL: Extra load on DNS
  Anyway, browsers cache DNS mappings 
What if root NS fails? All DNS queries take > 3s?

## Slide 5: Motivation for IP anycast
Failure problem: client has resolved IP address
  What if IP address can represent many servers?
Load-balancing/failover via IP addr, rather than DNS
IP anycast is simple reuse of existing protocols
  Multiple instances of a service share same IP address
  Each instance announces IP address / prefix in BGP / IGP
  Routing infrastructure directs packets to nearest instance of the service
    Can use same selection criteria as installing routes in the FIB
  No special capabilities in servers, clients, or network

## Slide 6: IP anycast in action
Client
Router 1
Server Instance A
Server Instance B
Router 3
Router 2
Router 4
10.0.0.1
10.0.0.1
192.168.0.1
192.168.0.2
Announce 10.0.0.1/32
Announce 10.0.0.1/32

## Slide 7: IP anycast in action
Router 1
Client
Server Instance A
Server Instance B
Router 3
Router 2
Router 4
10.0.0.1
10.0.0.1
192.168.0.1
192.168.0.2
Routing Table from Router 1:
Destination Mask Next-Hop Distance
192.168.0.0 /29 127.0.0.1 0
10.0.0.1 /32 192.168.0.1 1
10.0.0.1 /32 192.168.0.2 2

## Slide 8: IP anycast in action
Client
Router 1
Server Instance A
Server Instance B
Router 3
Router 2
Router 4
10.0.0.1
10.0.0.1
192.168.0.1
192.168.0.2
DNS lookup for http://www.server.com/
produces a single answer:
www.server.com. IN A 10.0.0.1

## Slide 9: IP anycast in action
Router 1
Client
Server Instance A
Server Instance B
Router 3
Router 2
Router 4
10.0.0.1
10.0.0.1
192.168.0.1
192.168.0.2
Routing Table from Router 1:
Destination Mask Next-Hop Distance
192.168.0.0 /29 127.0.0.1 0
10.0.0.1 /32 192.168.0.1 1
10.0.0.1 /32 192.168.0.2 2

## Slide 10: IP anycast in action
Router 1
Client
Server Instance A
Server Instance B
Router 3
Router 2
Router 4
10.0.0.1
10.0.0.1
192.168.0.1
192.168.0.2
Routing Table from Router 1:
Destination Mask Next-Hop Distance
192.168.0.0 /29 127.0.0.1 0
10.0.0.1 /32 192.168.0.1 1
10.0.0.1 /32 192.168.0.2 2
Client

## Slide 11: IP anycast in action
Router 1
Client
Server Instance A
Server Instance B
Router 3
Router 2
10.0.0.1
10.0.0.1
192.168.0.1
192.168.0.2
Routing Table from Router 1:
Destination Mask Next-Hop Distance
192.168.0.0 /29 127.0.0.1 0
10.0.0.1 /32 192.168.0.1 1
10.0.0.1 /32 192.168.0.2 2
Router 4
Client

## Slide 12: IP anycast in action
Router 1
Client
Server
Router 3
Router 2
Router 4
10.0.0.1
192.168.0.1
192.168.0.2
Routing Table from Router 1:
Destination Mask Next-Hop Distance
192.168.0.0 /29 127.0.0.1 0
10.0.0.1 /32 192.168.0.1 1
10.0.0.1 /32 192.168.0.2 2
From client/router perspective, topology could as well be:

## Slide 13: Downsides of IP anycast
Many Tier-1 ISPs ingress filter prefixes > /24
  Publish a /24 to get a “single” anycasted address: Poor utilization
Scales poorly with the # anycast groups
  Each group needs entry in global routing table
Not trivial to deploy
  Obtain an IP prefix and AS number; speak BGP

## Slide 14: Downsides of IP anycast
Subject to the limitations of IP routing
  No notion of load or other application-layer metrics
  Convergence time can be slow (as BGP or IGP converge)
Failover doesn’t really work with TCP
  TCP is stateful: if switch destination replicas, other server instances will just respond with RSTs
  May react to network changes, even if server online
Root nameservers (UDP) anycasted, little else

## Slide 15: Multicast

## Slide 16: Multicast
Many receivers
  Receiving the same content
Applications
  Video conferencing
  Online gaming
  IP television (IPTV)
  Financial data feeds

## Slide 17: Iterated Unicast
Unicast message to each recipient
Advantages
  Simple to implement
  No modifications to network
Disadvantages
  High overhead on sender
  Redundant packets on links
  Sender must maintain list of receivers

## Slide 18: IP Multicast
Embed receiver-driven tree in network layer
  Sender sends a single packet to the group
  Receivers “join” and “leave” the tree
Advantages
  Low overhead on the sender
  Avoids redundant network traffic
Disadvantages
  Control-plane protocols for multicast groups
  Overhead of duplicating packets in the routers

## Slide 19: Multicasting messages
Simple application multicast: Iterated unicast
  Client simply unicasts message to every recipient
  Pros: simple to implement, no network modifications
  Cons: O(n) work on sender, network
Advanced overlay multicast (“peer-to-peer”)
  Build receiver-driven tree
  Pros: Scalable, no network modifications
  Cons: O(log n) work on sender, network; complex to implement
IP multicast
  Embed receiver-driven tree in network layer
  Pros: O(1) work on client, O(# receivers) on network
  Cons: requires network modifications; scalability concerns?

## Slide 20: Multicast Tree
A
B
G
D
E
c
F

## Slide 21: IP multicast in action
Router 1
Client
Server Instance A
Server Instance B
Router 3
Router 2
Router 4
239.1.1.1
239.1.1.1
192.168.0.1
192.168.0.2
Routing Table from Router 1:
Destination Mask Next-Hop Distance
192.168.0.0 /29 127.0.0.1 0
239.1.1.1 /32 192.168.0.1 1
239.1.1.1 /32 192.168.0.2 2

## Slide 22: Single vs. Multiple Senders
Source-based tree
  Separate tree for each sender
  Tree is optimized for that sender
  But, requires multiple trees for multiple senders
Shared tree
  One common tree
  Spanning tree that reaches all participants
  Single tree may be inefficient
  But, avoids having many different trees

## Slide 23: Multicast Addresses
Multicast “group” defined by IP address
  Multicast addresses look like unicast addresses
  224.0.0.0 to 239.255.255.255
Using multicast IP addresses
  Sender sends to the IP address
  Receivers join the group based on IP address
  Network sends packets along the tree

## Slide 24: Example Multicast Protocol
Receiver sends a “join” messages to the sender
  And grafts to the tree at the nearest point
A
B
G
D
E
c
F

## Slide 25: IGMP v1
Two types of IGMP msgs (both have IP TTL of 1)
  Host membership query: Routers query local networks to discover which groups have members
  Host membership report: Hosts report each group (e.g., multicast addr) to which belong, by broadcast on net interface from which query was received
Routers maintain group membership
  Host senders an IGMP “report” to join a group
  Multicast routers periodically issue host membership query to determine liveness of group members
  Note: No explicit “leave” message from clients
Notes: Why no explicit leave? Unwanted packets can just be dropped at client!

## Slide 26: IGMP: Improvements
IGMP v2 added:
  If multiple routers, one with lowest IP elected querier
  Explicit leave messages for faster pruning
  Group-specific query messages
IGMP v3 added:
  Source filtering: Join specifies multicast “only from” or “all but from” specific source addresses
Notes: Why no explicit leave? Unwanted packets can just be dropped at client!

## Slide 27: IGMP: Parameters and Design
Parameters
  Maximum report delay: 10 sec
  Membership query internal default: 125 sec
  Time-out interval: 270 sec = 2 * (query interval + max delay)
Router tracks each attached network, not each peer
Should clients respond immediately to queries?
  Random delay (from 0..D) to minimize responses to queries
  Only one response from single broadcast domain needed
What if local networks are layer-2 switched?
  L2 switches typically broadcast multicast traffic out all ports
  Or, IGMP snooping (sneak peek into layer-3 contents), Cisco’s proprietary protocols, or static forwarding tables
Notes: 1. Router not tracking each peer, only each network: because these local networks at broadcast media (e.g., unswitched ethernet).
2. Random delay (from 0…D) in order to minimize responses to queries: Only one response from broadcast domain needed.
3. L2 switches typically broadcast multicast traffic out all ports. Alternatively, IGMP snooping (sneak peek into the layer 3 content of a multicast packet), Cisco’s proprietary, or static forwarding tables…

## Slide 28: IP Multicast is Best Effort
Sender sends packet to IP multicast address
  Loss may affect multiple receivers
A
B
G
D
E
c
F

## Slide 29: Challenges for Reliable Multicast
Send an ACK, much like TCP?
  ACK-implosion if all destinations ACK at once
  Source does not know # of destinations
How to retransmit?
  To all? One bad link effects entire group
  Only where losses? Loss near sender makes retransmission as inefficient as replicated unicast
Negative acknowledgments more common

## Slide 30: Scalable Reliable Multicast
Data packets sent via IP multicast
  Data includes sequence numbers
Upon packet failure
  If failures relatively rare, use Negative ACKs (NAKs) instead: “Did not receive expected packet”
  Sender issues heartbeats if no real traffic. Receiver knows when to expect (and thus NAK)

## Slide 31: Handling Failure in SRM
Receiver multicasts a NAK
  Or send NAK to sender, who multicasts confirmation
Scale through NAK suppression
  If received a NAK or NCF, don’t NAK yourself
  Add random delays before NAK’ing
Repair through packet retransmission
  From initial sender
  From designated local repairer

## Slide 32: Pragmatic General Multicast (RFC 3208)
Similar approach as SRM: IP multicast + NAKs
  … but more techniques for scalability
Hierarchy of PGM-aware network elements
  NAK suppression: Similar to SRM
  NAK elimination: Send at most one NAK upstream
    Or completely handle with local repair!
  Constrained forwarding: Repair data can be suppressed downstream if no NAK seen on that port
  Forward-error correction: Reduce need to NAK
Works when only sender is multicast-able

## Slide 33: Outline today
IP Anycast
  N destinations, 1 should receive the message
  Providing a service from multiple network locations
  Using routing protocols for automated failover
Multicast protocols
  N destinations, N should receive the message
  Examples
    IP Multicast and IGMP
    SRM (Scalable Reliable Multicast)
    PGM (Pragmatic General Multicast)