## Slide 1: Discovery and DNS
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/
http://mosaic.cnfolio.com/B101CW2011Article581

## Slide 2: Relationship Between Layers
logical link
name

## Slide 3: Routing: Mapping Link to Path
name
address
logical link
physical
path

## Slide 4: Discovery: Mapping Name to Address
logical link
name
address

## Slide 5: Discovery

## Slide 6: Directories
A key-value store
  Key: name; value: address(es)
  Answer queries: given name, return address(es)
Caching the response
  Reuse the response, for a period of time
  Better performance and lower overhead
Allow entries to change
  Updating the address(es) associated with a name
  Invalidating or expiring cached responses

## Slide 7: Directory Design: Three Extremes
Flood the query (e.g., ARP)
  The named node responds with its address
  But, high overhead in large networks
Push data to all clients (/etc/hosts)
  All nodes store a full copy of the directory
  But, high overhead for many names and updates
Central directory server
  All data and queries handled by one machine
  But, poor performance, scalability, and reliability

## Slide 8: Directory Design: Distributed Solutions
Hierarchical directory (e.g., DNS)
  Follow the hierarchy in the name space
  Distribute the directory, distribute the queries
  Enable decentralized updates to the directory
Distributed Hash Table (e.g. P2P applications)
  Directory as a hash table with flat names
  Each directory node handles range of hash outputs
  Use hash to direct query to the directory node

## Slide 9: Domain Name System (DNS)
Computer science concepts underlying DNS
  Indirection: names in place of addresses
  Hierarchy: in names, addresses, and servers
  Caching: of mappings from names to/from addresses

## Slide 10: Strawman Solution #1: Local File
Original name to address mapping
  Flat namespace
  /etc/hosts
  SRI kept main copy
  Downloaded regularly
Count of hosts was increasing: moving from a machine per domain to machine per user
  Many more downloads
  Many more updates

## Slide 11: Strawman Solution #2: Central Server
Central server
  One place where all mappings are stored
  All queries go to the central server
Many practical problems
  Single point of failure
  High traffic volume
  Distant centralized database
  Single point of update
  Does not scale
Need a distributed, hierarchical collection of servers

## Slide 12: Domain Name System (DNS)
Properties of DNS
  Hierarchical name space divided into zones
  Distributed over a collection of DNS servers
Hierarchy of DNS servers
  Root servers
  Top-level domain (TLD) servers
  Authoritative DNS servers
Performing the translations
  Local DNS servers and client resolvers
12

## Slide 13: Distributed Hierarchical Database
com
edu
org
ac
uk
zw
arpa
unnamed root
bar
west
east
foo
my
ac
cam
usr
in-
addr
12
34
56
generic domains
country domains
my.east.bar.edu
usr.cam.ac.uk
12.34.56.0/24

## Slide 14: DNS Root Servers
13 root servers (see http://www.root-servers.org/)
Labeled A through M. Most are IP Anycasted.
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software C. Palo Alto, CA (and 17 other locations)
I Autonomica, Stockholm (plus 3 other locations)
K RIPE London (+ Amsterdam, Frankfurt)
m WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign, ( 11 locations)

## Slide 15: TLD and Authoritative DNS Servers
Global Top-level domain (gTLD) servers
  Generic domains (e.g., .com, .org, .edu)
  Country domains (e.g., .uk, .fr, .ca, .jp)
  Managed professionally (e.g., Verisign for .com .net)
Authoritative DNS servers
  Provide public records for hosts at an organization
  For the organization’s servers (e.g., Web and mail)
  Can be maintained locally or by a service provider
15

## Slide 16: Reliability
DNS servers are replicated
  Name service available if at least one replica is up
  Queries can be load balanced between replicas
$ dig NS nytimes.com +norecurse
;; QUESTION SECTION:
;nytimes.com. IN NS
;; AUTHORITY SECTION:
nytimes.com. 349 IN NS ns2.p24.dynect.net.
nytimes.com. 349 IN NS ns3.p24.dynect.net.
nytimes.com. 349 IN NS dns2.p06.nsone.net.
nytimes.com. 349 IN NS ns4.p24.dynect.net.
nytimes.com. 349 IN NS ns1.p24.dynect.net.
nytimes.com. 349 IN NS dns3.p06.nsone.net.
nytimes.com. 349 IN NS dns4.p06.nsone.net.
nytimes.com. 349 IN NS dns1.p06.nsone.net.

## Slide 17: Reliability
DNS servers are replicated
  Name service available if at least one replica is up
  Queries can be load balanced between replicas
UDP used for queries
  Need reliability: must implement this on top of UDP
Try alternate servers on timeout
  Exponential backoff when retrying same server
Same identifier for all queries
  Don’t care which server responds

## Slide 18: DNS Queries and Caching

## Slide 19: Using DNS
Local DNS server (“default name server”)
  Usually near the end hosts who use it
  Local hosts configured with local server (e.g., /etc/resolv.conf) or learn the server via DHCP
Client application
  Extract server name (e.g., from the URL)
  Do gethostbyname() or getaddrinfo() to get address
Server application
  Extract client IP address from socket
  Optional gethostbyaddr() to translate into name
19

## Slide 20: DNS Protocol
DNS protocol : query and reply msg,
both with same msg format
Message header
Identification: 16 bit # for query, reply to query uses same #
Flags:
  Query or reply
  Recursion desired
  Recursion available
  Reply is authoritative

## Slide 21: DNS Resource Records
RR format: (name, value, type, ttl)
Type=A
  Name: hostname
  Value: IP address
Type=CNAME
  Name: alias for some “canonical” (the real) name:
  www.ibm.com is really
  srveast.backup2.ibm.com
  Value: canonical name
Type=MX
  Value: name of mailserver associated with name
Type=NS
  Name: domain
  Value: hostname of name server for domain

## Slide 22: Break for Demo

## Slide 23: DNS Queries
requesting host
a.cs.princeton.edu
www.umass.edu
root DNS server for .
local DNS server
dns.princeton.edu
3
authoritative DNS server
for umass.edu
dns.umass.edu
TLD DNS server for .edu
Host a.cs.princeton.edu wants IP address for www.umass.edu
Note Recursive vs. Iterative Queries
23
local DNS server
dns.cs.princeton.edu
1
2
4
5
6
7
8
9
10

## Slide 24: DNS Caching
root DNS server for .
3
authoritative DNS server
for umass.edu
dns.umass.edu
TLD DNS server for .edu
24
1
2
4
5
6
7
8
9
10
DNS query latency
  E.g., 1 sec latency before starting a download
Caching to reduce overhead and delay
  Small # of top-level servers, that change rarely
  Popular sites visited often
Where to cache?
  Local DNS server
  Browser
requesting host
a.cs.princeton.edu
www.umass.edu

## Slide 25
$ dig nytimes.com +norecurse @a.root-servers.net
;; QUESTION SECTION:
;nytimes.com. IN A
;; AUTHORITY SECTION:
com. 172800 IN NS a.gtld-servers.net.
com. 172800 IN NS b.gtld-servers.net.
com. 172800 IN NS c.gtld-servers.net.
com. 172800 IN NS d.gtld-servers.net.
com. 172800 IN NS e.gtld-servers.net.
com. 172800 IN NS f.gtld-servers.net.
com. 172800 IN NS g.gtld-servers.net.
com. 172800 IN NS h.gtld-servers.net.
com. 172800 IN NS i.gtld-servers.net.
com. 172800 IN NS j.gtld-servers.net.
com. 172800 IN NS k.gtld-servers.net.
com. 172800 IN NS l.gtld-servers.net.
com. 172800 IN NS m.gtld-servers.net.
;; ADDITIONAL SECTION:
a.gtld-servers.net. 172800 IN A 192.5.6.30
b.gtld-servers.net. 172800 IN A 192.33.14.30
c.gtld-servers.net. 172800 IN A 192.26.92.30
d.gtld-servers.net. 172800 IN A 192.31.80.30
e.gtld-servers.net. 172800 IN A 192.12.94.30
f.gtld-servers.net. 172800 IN A 192.35.51.30

## Slide 26
$ dig nytimes.com +norecurse @b.gtld-servers.net
;; QUESTION SECTION:
;nytimes.com. IN A
;; AUTHORITY SECTION:
nytimes.com. 172800 IN NS ns3.p24.dynect.net.
nytimes.com. 172800 IN NS ns1.p24.dynect.net.
nytimes.com. 172800 IN NS ns2.p24.dynect.net.
nytimes.com. 172800 IN NS ns4.p24.dynect.net.
nytimes.com. 172800 IN NS dns1.p06.nsone.net.
nytimes.com. 172800 IN NS dns2.p06.nsone.net.
nytimes.com. 172800 IN NS dns3.p06.nsone.net.
nytimes.com. 172800 IN NS dns4.p06.nsone.net.
;; Query time: 11 msec
;; SERVER: 192.33.14.30#53(192.33.14.30)
;; WHEN: Sat Mar 28 10:56:03 2020
;; MSG SIZE rcvd: 201

## Slide 27
$ dig nytimes.com +norecurse @ns3.p24.dynect.net
;; QUESTION SECTION:
;nytimes.com. IN A
;; ANSWER SECTION:
nytimes.com. 500 IN A 151.101.193.164
nytimes.com. 500 IN A 151.101.129.164
nytimes.com. 500 IN A 151.101.65.164
nytimes.com. 500 IN A 151.101.1.164
;; AUTHORITY SECTION:
nytimes.com. 300 IN NS ns2.p24.dynect.net.
nytimes.com. 300 IN NS ns4.p24.dynect.net.
nytimes.com. 300 IN NS ns3.p24.dynect.net.
nytimes.com. 300 IN NS ns1.p24.dynect.net.
nytimes.com. 300 IN NS dns3.p06.nsone.net.
nytimes.com. 300 IN NS dns2.p06.nsone.net.
nytimes.com. 300 IN NS dns4.p06.nsone.net.
nytimes.com. 300 IN NS dns1.p06.nsone.net.
;; Query time: 14 msec
;; SERVER: 208.78.71.24#53(208.78.71.24)
;; WHEN: Sat Mar 28 11:23:19 2020
;; MSG SIZE rcvd: 265

## Slide 28
$ dig ANY nytimes.com +norecurse @ns3.p24.dynect.net
;; Truncated, retrying in TCP mode.
;; QUESTION SECTION:
;nytimes.com. IN ANY
;; ANSWER SECTION:
nytimes.com. 300 IN SOA dns1.p06.nsone.net. hostmaster.nytimes.com. 2019121930 300 150 1209600 300
nytimes.com. 300 IN NS dns3.p06.nsone.net.
nytimes.com. 300 IN NS dns1.p06.nsone.net.
nytimes.com. 300 IN NS dns4.p06.nsone.net.
nytimes.com. 300 IN NS ns3.p24.dynect.net.
nytimes.com. 300 IN NS ns4.p24.dynect.net.
nytimes.com. 300 IN NS ns2.p24.dynect.net.
nytimes.com. 300 IN NS ns1.p24.dynect.net.
nytimes.com. 300 IN NS dns2.p06.nsone.net.
nytimes.com. 500 IN A 151.101.129.164
nytimes.com. 500 IN A 151.101.193.164
nytimes.com. 500 IN A 151.101.1.164
nytimes.com. 500 IN A 151.101.65.164
nytimes.com. 300 IN MX 10 ASPMX2.GOOGLEMAIL.COM.
nytimes.com. 300 IN MX 10 ASPMX3.GOOGLEMAIL.COM.
nytimes.com. 300 IN MX 1 ASPMX.L.GOOGLE.com.
nytimes.com. 300 IN MX 5 ALT2.ASPMX.L.GOOGLE.com.
nytimes.com. 300 IN MX 5 ALT1.ASPMX.L.GOOGLE.com.

## Slide 29
nytimes.com. 500 IN TXT "google-site-verification=aReMr8hkX3gxeHLKKk4tJ1s970U7QdEqUMIhMmLUfjQ"
nytimes.com. 500 IN TXT "dropbox-domain-verification=4ld3jahx0psi"
nytimes.com. 500 IN TXT "google-site-verification=ZTCMdpSKM7HwqTvGUf_00Ef008JhOnbzGgCSUGYfsro"
nytimes.com. 500 IN TXT "docusign=bd506110-db79-430e-b159-cc1d74fe1176"
nytimes.com. 500 IN TXT "google-site-verification=NIqXa_F8IaqdPJhTtexgR0NYbzVLD_-X-uRUvyf4GyQ"
nytimes.com. 500 IN TXT "MS=ms22827202"
nytimes.com. 500 IN TXT "adobe-idp-site-verification=5ce4d99c-af0a-4b76-9217-bd49d3336df0"
nytimes.com. 500 IN TXT "google-site-verification=4qJm5sAZa1_29BTwFjqW09t7_7D4Vee3LBFQqg8xYbs"
nytimes.com. 500 IN TXT "google-site-verification=ZsySMeZ_SRbJZFu-53ptepytP7h5pxHO0qAg8Z2bKug"
nytimes.com. 500 IN TXT "MS=A1BFCA84E21B7011CA98DF9DC251CDDF90E0174B"
nytimes.com. 500 IN TXT "google-site-verification=4TE2ggBoy6PktLjtZ03t32A2oEZ0VD0PY6MnTj8IL_g"
nytimes.com. 500 IN TXT "v=spf1 mx ptr ip4:170.149.160.0/19 ip4:170.149.240.0/19 ip4:209.11.220.51/32 include:alerts.wallst.com include:authsmtp.com include:sendgrid.net include:_spf.google.com include:inyt.com include:_spf.e.sparkpost.com include:mail.zendesk.com ~all"
nytimes.com. 500 IN TXT "google-site-verification=ic0Ur9LVhZ1hIjTj8LhMOhqx2Z52oS3hU_W2EqBY6UM"
nytimes.com. 500 IN TXT "google-site-verification=jZcmQFxPEP38yqYpmRvo0v_9hQFAdBZPUEBwTNUPUF8"
nytimes.com. 500 IN TXT "253961548-4297453"
nytimes.com. 500 IN TYPE257 \# 22 000569737375656C657473656E63727970742E6F7267
nytimes.com. 500 IN TYPE257 \# 19 00056973737565636F6D6F646F63612E636F6D
nytimes.com. 500 IN TYPE257 \# 19 0005697373756561777374727573742E636F6D
nytimes.com. 500 IN TYPE257 \# 22 00056973737565616D617A6F6E74727573742E636F6D
nytimes.com. 500 IN TYPE257 \# 15 00056973737565706B692E676F6F67
nytimes.com. 500 IN TYPE257 \# 19 0005697373756564696769636572742E636F6D
nytimes.com. 500 IN TYPE257 \# 17 00056973737565616D617A6F6E2E636F6D
nytimes.com. 500 IN TYPE257 \# 19 0005697373756573796D616E7465632E636F6D
nytimes.com. 500 IN TYPE257 \# 20 00056973737565616D617A6F6E6177732E636F6D

## Slide 30: DNS Cache Consistency
Goal: Ensuring cached data is up to date
DNS design considerations
  Cached data is “read only”
  Explicit invalidation would be expensive
    Server would need to keep track of all resolvers caching
Avoiding stale information
  Responses include a “time to live” (TTL) field
  Delete the cached entry after TTL expires
Perform negative caching (for dead links, misspellings)
  So failures quick and don’t overload gTLD servers

## Slide 31: Setting the Time To Live (TTL)
TTL trade-offs
  Small TTL: fast response to change
  Large TTL: higher cache hit rate
Following the hierarchy
  Top of the hierarchy: days or weeks
  Bottom of the hierarchy: seconds to hours
Tension in practice
  CDNs set low TTLs for load balancing and failover
  Browsers cache for 15-60 seconds

## Slide 32: Questions
Tension:
  DNS operators want high TTL for low load on DNS servers,
  Domains want low TTL for faster failover b/w IP addrs
  (Y) True (M) False
By returning IP addresses in “round robin” fashion, DNS operators can ensure equal load better servers
(Y) True (M) False
Most applications obey TTLs on DNS records
(Y) True (M) False

## Slide 33: Questions
Tension:
  DNS operators want high TTL for low load on DNS servers,
  Domains want low TTL for faster failover b/w IP addrs
  (Y) True (M) False
By returning IP addresses in “round robin” fashion, DNS operators can ensure equal load better servers
(Y) True (M) False
Most applications obey TTLs on DNS records
(Y) True (M) False

## Slide 34: Inserting Resource Records into DNS
Example: just created startup “FooBar”
Register foobar.com at namecheap.com
  Provide registrar with names and IP addresses of authoritative name server (primary and secondary)
  Registrar inserts two RRs into the com TLD server:
    (foobar.com, dns1.foobar.com, NS)
    (dns1.foobar.com, 212.212.212.1, A)
Put in authoritative server dns1.foobar.com
  Type A record for www.foobar.com
  Type MX record for foobar.com

## Slide 35: DNS attacks (1)
DNS cache poisoning
  Client: Ask for www.evil.com
  Attacker responds with additional section for (www.cnn.com, 1.2.3.4, A)
  Client/resolver: Thanks! I won’t bother check what I asked for.

## Slide 36: DNS attacks (2)
DNS hijacking
  Attacker sends forged DNS reply to client for www.cnn.com, even when they don’t receive the request
  How to prevent?
    Client remembers the 16-bit DNS ID
    Client only accepts reply if reply ID matches query ID
  16 bits: 65K possible IDs
    What rate for attacker to enumerate all in 1 sec? 64B/packet
    64*65536*8 / 1024 / 1024 = 32 Mbps
  Prevention: Also randomize the DNS source port
    e.g., Windows DNS alloc’s 2500 DNS ports, leads to ~164M possible IDs
    Would require 80 Gbps
    Kaminsky attack: this source port…wasn’t random after all