## Slide 1: Naming Security
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/

## Slide 2: Network Security
Application layer
  E-mail: PGP, using a web-of-trust
  Web: HTTP-S, using a certificate hierarchy
Transport layer
  Transport Layer Security/ Secure Socket Layer
Network layer
  IP Sec
Network infrastructure
  DNS-Sec and BGP-Sec

## Slide 3: Continuation of Lec 18

## Slide 4: Transport Layer Security (TLS)
Based on the earlier Secure Socket Layer (SSL) originally developed by Netscape

## Slide 5: TLS Handshake Protocol
Send new random value, list of supported ciphers
Send pre-secret, encrypted under PK
Create shared secret key from pre-secret and random
Switch to new symmetric-key cipher using shared key
Send new random value, digital certificate with PK
Create shared secret key from pre-secret and random
Switch to new symmetric-key cipher using shared key

## Slide 6: TLS Record Protocol
Messages from application layer are:
  Fragmented or coalesced into blocks
  Optionally compressed
  Integrity-protected using an HMAC
  Encrypted using symmetric-key cipher
  Passed to the transport layer (usually TCP)
Sequence #s on record-protocol messages
  Prevents replays and reorderings of messages

## Slide 7: Comments on HTTPS
HTTPS authenticates server, not content
  If CDN (Akamai) serves content over HTTPS, customer must trust Akamai not to change content
Symmetric-key crypto after public-key ops
  Handshake protocol using public key crypto
  Symmetric-key crypto much faster (100-1000x)
HTTPS on top of TCP, so reliable byte stream
  Can leverage fact that transmission is reliable to ensure: each data segment received exactly once
  Adversary can’t successfully drop or replay packets

## Slide 8: IP Security

## Slide 9: IP Security
There are range of app-specific security mechanisms
  eg. TLS/HTTPS, S/MIME, PGP, Kerberos, …
But security concerns that cut across protocol layers
Implement by the network for all applications?
  Enter IPSec!

## Slide 10: IPSec
General IP Security framework
Allows one to provide
  Access control, integrity, authentication, originality, and confidentiality
Applicable to different settings
  Narrow streams: Specific TCP connections
  Wide streams: All packets between two gateways

## Slide 11: IPSec Uses

## Slide 12: Benefits of IPSec
If in a firewall/router:
  Strong security to all traffic crossing perimeter
  Resistant to bypass
Below transport layer
  Transparent to applications
  Can be transparent to end users
Can provide security for individual users

## Slide 13: IP Security Architecture
Specification quite complex
  Mandatory in IPv6, optional in IPv4
Two security header extensions:
  Authentication Header (AH)
    Connectionless integrity, origin authentication
      MAC over most header fields and packet body
    Anti-replay protection
  Encapsulating Security Payload (ESP)
    These properties, plus confidentiality
Notes: Not as robust: Can detect duplicates, but not lost or re-ordered…
• RFC 2401: An overview of a security architecture
• RFC 2402: Description of a packet authentication extension to IPv4 and IPv6
• RFC 2406: Description of a packet encryption extension to IPv4 and IPv6
• RFC 2408: Specification of key management capabilities

## Slide 14: Encapsulating Security Payload (ESP)
Transport mode: Data encrypted, but not header
  After all, network headers needed for routing!
  Can still do traffic analysis, but is efficient
  Good for host-to-host traffic
Tunnel mode (“IP-in-IP”)
  Encrypts entire IP packet
  Add new header for next hop
  Good for VPNs, gateway-to-gateway security

## Slide 15: Replay Protection is Hard
Goal: Eavesdropper can’t capture encrypted packet and duplicate later
  Easy with TLS/HTTP on TCP: Reliable byte stream
  But IP Sec at packet layer; transport may not be reliable
IP Sec solution: Sliding window on sequence #’s
  All IPSec packets have a 64-bit monotonic sequence number
  Receiver keeps track of which seqno’s seen before
    [lastest – windowsize + 1 , latest] ; windowsize typically 64 packets
  Accept packet if
    seqno > latest (and update latest)
    Within window but has not been seen before
  If reliable, could just remember last, and accept iff last + 1

## Slide 16: DNS Security

## Slide 17: Hierarchical Naming in DNS
com
edu
org
ac
uk
zw
arpa
unnamed root
bar
west
east
foo
my
ac
cam
usr
in-
addr
12
34
56
generic domains
country domains
my.east.bar.edu
usr.cam.ac.uk
12.34.56.0/24

## Slide 18: DNS Root Servers
13 root servers (see http://www.root-servers.org/)
Labeled A through M
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software C. Palo Alto, CA (and 17 other locations)
I Autonomica, Stockholm (plus 3 other locations)
K RIPE London (+ Amsterdam, Frankfurt)
m WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign, ( 11 locations)

## Slide 19: DoS attacks on DNS Availability
Feb. 6, 2007
  Botnet attack on the 13 Internet DNS root servers
  Lasted 2.5 hours
  None crashed, but two performed badly:
    g-root (DoD), l-root (ICANN)
    Most other root servers use anycast

## Slide 20: Defense: Replication and Caching
source: wikipedia

## Slide 21: Denial-of-Service Attacks on Hosts
580,000 open resolvers on Internet (Kaminsky-Shiffman’06)
DNS Server
DoS Source
DoS Target
DNS Query SrcIP: DoS Target
(60 bytes)
DNS Response
(3000 bytes)
40 amplification

## Slide 22: Preventing Amplification Attacks
attacker
ip spoofed packets
replies
victim
open
amplifier
prevent
ip spoofing
disable
open amplifiers

## Slide 23: DNS Integrity and the TLD Operators
If domain name doesn’t exist, DNS should return NXDOMAIN (non-existant domain) msg
Verisign instead creates wildcard records for all .com and .net names not yet registered
  September 15 – October 4, 2003
Redirection for these domain names to Verisign web portal: “to help you search”
  And serve you ads…and get “sponsored” search
  Verisign and online advertising companies make $$

## Slide 24: DNS Integrity: Cache Poisoning
Was answer from an authoritative server?
  Or from somebody else?
DNS cache poisoning
  Client asks for www.evil.com
  Nameserver authoritative for www.evil.com returns additional section for (www.cnn.com, 1.2.3.4, A)
  Thanks! I won’t bother check what I asked for

## Slide 25: DNS Integrity: DNS Hijacking
To prevent cache poisoning, client remembers:
  The domain name in the request
  A 16-bit request ID (used to demux UDP response)
DNS hijacking
  16 bits: 65K possible IDs
  What rate to enumerate all in 1 sec? 64B/packet
  64*65536*8 / 1024 / 1024 = 32 Mbps
Prevention: also randomize DNS source port
  Kaminsky attack: this source port… wasn’t random
http://unixwiz.net/techtips/iguide-kaminsky-dns-vuln.html

## Slide 26: Let’s strongly believe the answer! Enter DNSSEC
DNSSEC protects against data spoofing and corruption
DNSSEC also provides mechanisms to authenticate servers and requests
DNSSEC provides mechanisms to establish authenticity and integrity

## Slide 27: PK-DNSSEC (Public Key)
The DNS servers sign the hash of resource record set with its private (signature) keys
  Public keys can be used to verify the SIGs
Leverages hierarchy:
  Authenticity of name server’s public keys is established by a signature over the keys by the parent’s private key
  In ideal case, only roots’ public keys need to be distributed out-of-band

## Slide 28: Verifying the Tree
stub
resolver
Question: www.cnn.com ?
www.cnn.com A ?
resolver
. (root)
www.cnn.com A ?
ask .com server
SIG (ip addr and PK of .com server)
.com
www.cnn.com A ?
ask cnn.com server
SIG (ip addr and PK of cnn.com server)
cnn.com
www.cnn.com A ?
SIG (xxx.xxx.xxx.xxx)
xxx.xxx.xxx.xxx
add to cache
src.cs.princeton.edu
dns.cs.princeton.edu
transaction
signatures

## Slide 29: Conclusions
Security at many layers
  Application, transport, and network layers
  Customized to the properties and requirements
Exchanging keys
  Public key certificates
  Certificate authorities vs. Web of trust
Next time
  Interdomain routing security
Learn more: take COS 432 next year!