## Slide 1: Course Overview
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/
Light at the
end of the tunnel

## Slide 2: Key Concepts in Networking

## Slide 3: Some Key Concepts
Course was organized around protocols
  But a small set of concepts recur in many protocols
General CS concepts
  Hierarchy, indirection, caching, randomization
Networking-specific concepts
  Soft state, layering, (de)multiplexing
  End-to-end argument

## Slide 4: Hierarchy
Scalability of large systems
  Cannot store all information everywhere
  Cannot centrally coordinate everything
Hierarchy to manage scale
  Divide system into smaller pieces
Hierarchy to divide control
  Decentralized management
Examples in the Internet
  IP addresses, routing protocols, DNS, peer-to-peer

## Slide 5: Hierarchy: IP Address Blocks
Number related hosts from a common subnet
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 6: Hierarchy: IP Address Blocks
Separation of control
  Prefix: assigned to an institution
  Addresses: assigned by institution to its nodes
Who assigns prefixes?
  Internet Corporation for Assigned Names & Numbers
  Regional Internet Registries (RIRs)
  Internet Service Providers (ISPs)
  Stub networks
  Regions within an enterprise

## Slide 7: Hierarchy: Routing Protocols
AS-level topology
  Nodes are Autonomous Systems (ASes)
  Edges are links and business relationships
  Hides the detail within each AS’s network
1
2
3
4
5
6
7
Client
Web server

## Slide 8: Hierarchy: Routing Protocols
Interdomain routing ignores details in an AS
  Routers flood information to learn the topology
  Routers determine “next hop” to other routers…
  By computing shortest paths based on link weights
3
2
2
1
1
3
1
4
5
3

## Slide 9: Hierarchy: Domain Name System
13 root servers (see http://www.root-servers.org/)
Labeled A through M
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software C. Palo Alto, CA (and 17 other locations)
I Autonomica, Stockholm (plus 3 other locations)
K RIPE London (also Amsterdam, Frankfurt)
m WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign, ( 11 locations)

## Slide 10: Hierarchy: Domain Name System
com
edu
org
ac
uk
zw
arpa
unnamed root
bar
west
east
foo
my
ac
cam
usr
in-
addr
12
34
56
generic domains
country domains
my.east.bar.edu
usr.cam.ac.uk
12.34.56.0/24

## Slide 11: Hierarchy: Super Peers in P2P (KaZaA)
Each peer is either group leader or assigned to group leader
  TCP connection between peer and its group leader
  TCP connections between some pairs of group leaders
Group leader tracks the content in all its children

## Slide 12: Indirection
Referencing by name
  Rather than the value itself
  E.g., manipulating a variable through a pointer
Benefits of indirection
  Human convenience
  Reducing overhead when things change
Examples of indirection in the Internet
  Names vs. addresses
  Mobile IP

## Slide 13: Indirection: Names vs. Addresses
Host name to IP address
  Mnemonic names to location-dependent addresses
  E.g., from www.cnn.com to 64.236.16.20
  Using the Domain Name System (DNS)
From IP address to MAC address
  From hierarchical global address to interface card
  E.g., from 64.236.16.20 to 00-15-C5-49-04-A9
  Using the Address Resolution Protocol (ARP)

## Slide 14: Indirection: Load Balancers & Switches
Not fixed binding of IPs or MAC address to physical machine
  NAT allows multiple machines to share single public IP address
  Load balancers: Machines share IP address, LB maps to physical machine by network flow
  VM can migrate across L2 network through gratuitous ARP

## Slide 15: Indirection: Mobile IP
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent

## Slide 16: Caching
Duplicating data stored elsewhere
  To reduce latency for accessing the data
  To reduce resources consumed
Caching is often quite effective
  Speed difference between cache and primary copy
  Locality of reference, and small set of popular data
Examples from the Internet
  DNS caching, Web caching

## Slide 17: Caching: DNS Caching
Application
DNS resolver
Local DNS
server
1
10
DNS cache
DNS query
DNS response
2
9
Root server
Top-level
domain server
Second-level
domain server
3
4
5
6
7
8

## Slide 18: Caching: Web Caching
Caching location
  Proxy cache
  Browser cache
Better performance
  Lower RTT
  Existing connection
  Less network load
client
Proxy
server
client
HTTP request
HTTP request
HTTP response
HTTP response
HTTP request
HTTP response
origin
server
origin
server

## Slide 19: Randomization
Distributed adaptive algorithms
  Multiple distributed parties
  Adapting independently
Risk of synchronization
  Many parties reacting at the same time
  Leading to bad aggregate behavior
Randomization can desynchronize
  Ethernet back-off, Random Early Detection
Rather than imposing centralized control

## Slide 20: Randomization: Ethernet Back-off
Random access: exponential back-off
  After collision, wait random time before retrying
  After mth, choose K randomly from {0, …, 2m-1}
  Wait for K*512 bit times before trying again

## Slide 21: Randomization: Dropping Packets Early
Congestion on a link
  Eventually the queue becomes full
  And new packets must be dropped
Drop-tail queuing leads to bursty loss
  Many packets encounter a full queue
  Many TCP senders reduce their sending rates

## Slide 22: Randomization: Dropping Packets Early
Better to give early feedback
  Get a few connections to slow down
  … before it is too late
Random Early Detection (RED)
  Randomly drop packets when queue (near) full
  Drop rate increases as function of queue length
Average Queue Length
Probability

## Slide 23: Soft State
State: stored in nodes by network protocols
  Installed by receiver of a set-up message
  Updated when conditions change
Hard state: valid unless told otherwise
  Removed by receiver of tear-down message
  Requires error handling to deal with sender failure
Soft state: invalid if not told to refresh
  Periodically refreshed, removed by timeout
Soft state reduces complexity
  DNS caching, DHCP leases

## Slide 24: Soft State: DNS Caching
Cache consistency is a hard problem
  Ensuring the cached copy is not out of date
Strawman: explicit revocation or updates
  Keep track of everyone who has cached information
  If name-to-host mapping changes, update caches
Soft state solution
  DNS responses include a “time to live” (TTL) field
  Cached entry is deleted after TTL expires

## Slide 25: Soft State: DHCP Leases
DHCP “offer message” from the server
  Configuration parameters (proposed IP address, mask, gateway router, DNS server, ...)
  Lease time (the time information remains valid)
Why is a lease time necessary?
  Client can release address (DHCP RELEASE)
    E.g., “ipconfig /release” or clean shutdown of computer
  But, the host might not release the address
    E.g., the host crashes or buggy client software
  You don’t want address to be allocated forever

## Slide 26: Layering: A Modular Approach
Sub-divide the problem
  Each layer relies on services from layer below
  Each layer exports services to layer above
Interface between layers defines interaction
  Hides implementation details
  Layers can change without disturbing other layers
Link hardware
Host-to-host connectivity
Application-to-application channels
Application

## Slide 27: Layering: Standing on Shoulders
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame
SONET frame

## Slide 28: Layering: Internet Protocol Suite
UDP
TCP
Data Link
Physical
Applications
The Hourglass Model
Waist
The waist facilitates interoperability
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…

## Slide 29: Layering: Encapsulation of Data
Different devices switch different things
  Physical layer: electrical signals (repeaters and hubs)
  Link layer: frames (bridges and switches)
  Network layer: packets (routers)
Application gateway
Transport gateway
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data

## Slide 30: Demultiplexing
Separating multiple streams out of one
  Recognizing the separate streams
  Treating the separate streams accordingly
Examples in the Internet
Frame header
Packet header
TCP header
User
data
type
protocol
port #

## Slide 31: (De)multiplexing: With a NAT
NAT
inside
outside
10.0.0.1
10.0.0.2
138.76.29.7

## Slide 32: Power at the End Host
End-to-End Principle
Whenever possible, communications protocol operations should be defined to occur at the end-points of a communications system.
Programmability
With programmable end hosts, new network services can be added at any time, by anyone.

## Slide 33: Why No Math in This Course?
Hypothesis #1: theory not relevant to Internet
  Body of math created for telephone networks
  Many of these models don’t work in data networks
Hypothesis #2: too many kinds of theory
  Queuing: statistical multiplexing works
  Control: TCP congestion control works
  Optimization: TCP maximizes aggregate utility
  Game: reasoning about competing ASes

## Slide 34: What Will Happen to the Internet

## Slide 35: No Strict Notions of Identity
Leads to
  Spam
  Spoofing
  Denial-of-service
  Route hijacking

## Slide 36: Protocols Designed Based on Trust
That you don’t spoof your addresses
  MAC spoofing, IP address spoofing, spam, …
That port numbers correspond to applications
  Rather than being arbitrary, meaningless numbers
That you adhere to the protocol
  Ethernet exponential back-off after a collision
  TCP additive increase, multiplicative decrease
That protocol specifications are public
  So others can build interoperable implementations

## Slide 37: Nobody in Charge
Traffic traverses many Autonomous Systems
  Who’s fault is it when things go wrong?
  How do you upgrade functionality?
Implicit trust in the end host
  What if some hosts violate congestion control?
Anyone can add any application
  Whether or not it is legal, moral, good, etc.
Spans many countries
  So no one government can be in charge

## Slide 38: Challenging New Requirements
Disseminating data
Mobile, multi-homed hosts
Sometimes-connected hosts
Large number of hosts
Real-time applications

## Slide 39: The Internet of the Future
Can we fix what ails the Internet
  Security, performance, reliability
  Upgradability, managability
  <Your favorite gripe here>
Without throwing out baby with bathwater
  Ease of adding new hosts
  Ease of adding new services
  Ease of adding new link technologies
An open technical and policy question…

## Slide 40: Thank You!