## Slide 1: Link Layer II: MACA and MACAW
COS 463: Wireless Networks
Lecture 5
Kyle Jamieson
[Parts adapted from J. Kurose, K. Ross, D. Holmar]

## Slide 2: Medium access: Timeline
Packet radio Wireless LAN Wired LAN
ALOHAnet 1960s
Amateur packet radio Ethernet 1970s

## Slide 3: Medium access: Timeline
Packet radio Wireless LAN Wired LAN
ALOHAnet 1960s
Amateur packet radio Ethernet 1970s
1980s
MACA 1990s
MACAW
IEEE 802.11 2000s
2010s

## Slide 4: Today: Wi-Fi Above the PHY
MACA
  Carrier sense in the wireless medium
  Hidden and exposed terminal problems
MACAW
802.11 MAC layer

## Slide 5: Fundamentals: Spectrum and Capacity
A particular radio transmits over some range of frequencies; its bandwidth, in the physical sense
When we’ve many senders near one another, how do we allocate spectrum among senders? Goals:
  Support for arbitrary communication patterns
  Simplicity of hardware
  Robustness to interference
Shannon’s Theorem: there’s a fundamental limit to channel capacity over a given spectrum range

## Slide 6: Multi-channel
Suppose we have 100 MHz of spectrum to use for a wireless LAN
Strawman: Subdivide into 50 channels of 2 MHz each: FDMA, narrow-band transmission
  Radio hardware simple, channels don’t mutually interfere, but
  Multi-path fading (mutual cancellation of out-of-phase reflections)
  Base station can allocate channels to users. How do you support arbitrary communication patterns?

## Slide 7: Idea: Use a single, shared channel
Spread transmission across whole 100 MHz of spectrum
  Remove constraints assoc. w/one channel per user
  Robust to multi-path fading
    Some frequencies likely to arrive intact
  Supports peer-to-peer communication
Collisions: Receiver must hear ≤1 strong transmission at a time
So adopt carrier sense and deference from Ethernet
  Listen before sending, defer to ongoing

## Slide 8: Assumptions and goals
Assumptions
  Uniform, circular radio propagation
    Fixed transmit power, all same ranges
  Equal interference and transmit ranges
Goals
  Fairness in sharing of medium
  Efficiency (total bandwidth achieved)
  Reliability of data transfer at MAC layer
Radios modeled as “conditionally connected” wires based on circular radio ranges

## Slide 9: Concurrency versus Taking Turns
Far-apart links should send concurrently:
Nearby links should take turns:

## Slide 10: When Does CS Work Well?
Two transmission pairs are far away from each other
  Neither sender carrier-senses the other
A
B
C
D
    B transmits to A, while D transmits to C.

## Slide 11: When Does CS Work Well?
Both transmitters can carrier sense each other
  Carrier sense uses thresholded correlation value to determine if medium occupied
A
B
C
D
    B transmits to A, D transmits to C, taking turns.
But what about cases in between these extremes?

## Slide 12: Hidden Terminal Problem
C can’t hear A, so will transmit while A transmits
  Result: Collision at B
Carrier Sense insufficient to detect all transmissions on wireless networks!
Key insight: Collisions are spatially located at the receiver
A
B
C

## Slide 13: Exposed Terminal Problem
If C transmits, does it cause a collision at A?
  Yet C cannot transmit while B transmits to A!
Same insight: Collisions spatially located at receiver
One possibility: directional antennas rather than omnidirectional. Why does this help? Why is it hard?
A
B
C

## Slide 14: MACA: Multiple Access with Collision Avoidance
Carrier sense became adopted in packet radio
But distances (cell size) remained large
Hidden and Exposed terminals abounded
Simple solution: use receiver’s medium state to determine transmitter behavior

## Slide 15: RTS/CTS
Exchange of two short messages: Request to Send (RTS) and Clear to Send (CTS)
Algorithm
  A sends an RTS (tells B to prepare)
  B replies an CTS (echoes message length)
  A sends its Data
A
B
C
1. “RTS, k bits”
2. “CTS, k bits”
defers
3. “Data”

## Slide 16: Deference to CTS
Hear CTS  Defer for length of expected data transmission time
  Solves hidden terminal problem
A
B
C
1. “RTS, k bits”
2. “CTS, k bits”
defers
3. “Data”

## Slide 17: Deference to RTS
Hear RTS  Defer one CTS-time (why?)
MACA: No carrier sense before sending!
  Karn concluded useless because of hidden terminals
So exposed terminals can transmit concurrently:
A
B
C
1. “RTS, k bits”
2. “CTS, k bits”
3. “Data”
D
(No deference after Step 2)

## Slide 18: Collision!
A’s RTS collides with C’s RTS, both are lost at B
  B will not reply with a CTS
Might collisions involving data packets occur?
  Not according to our (unrealistic) assumptions
  But Karn acknowledges interference range > communication range
A
B
C
RTS
RTS
Collision

## Slide 19: BEB in MACA
When collisions arise, MACA senders randomly backoff like Ethernet senders then retry the RTS
How long do collisions take to detect in the Experimental Ethernet?
What size should we make MACA backoff slots?

## Slide 20: BEB in MACA
Current backoff constant: CW
MACA sender:
  CW0 = 2 and CWM = 64
  Upon successful RTS/CTS, CW  CW0
  Upon failed RTS/CTS, CW  min[2CW, CWM]
Before retransmission, wait a uniform random number of RTS lengths (30 bytes) in [0, CW]
  30 bytes = 240 μs

## Slide 21: Today: Wi-Fi Above the PHY
MACA
MACAW
802.11 MAC layer

## Slide 22: MACAW: Context
Published in SIGCOMM 1994, work ’93/’94
Wi-Fi standards proceeded in parallel (IEEE standard ‘97)
  802.11 draws on MACAW, which draws on MACA
Assumptions and goals: Same as MACA
Setting: Wireless LAN
  Packet radio cell size: circa 100 mi. (528 μs)
  Wireless LAN cell size: circa 100 ft. (100 ns)

## Slide 23: Fairness in BEB/MACA
MACA’s BEB can lead to unfairness: backed-off sender has decreasing chance to acquire medium (“the poor get poorer”)
Simple example: A, C each sending at a rate that can alone saturate the network
C more likely to win the backoff and set minimum CW=2
A more likely to defer (maintain CW)
A
CW=32
B
C
CW=4

## Slide 24: BEB in MACAW: Copy
MACAW proposal: senders write their CW into packets
  Upon hearing a packet, copy and adopt its CW
Result: Dissemination of congestion level of “winning” transmitter to its competitors
Is this a good idea?
RTS failure rate at one node propagates far and wide
  Ambient noise? Regions with different loads?

## Slide 25: BEB in MACAW
Integrates with MACAW’s ACK mechanism
Multiplicative increase, linear decrease (MILD)
MACAW sender:
  CW0 = 2 and CWM = 64
  Upon failed RTS/CTS
    CW  min[1.5CW, CWM]
  Upon successful RTS/CTS but failed ACK, no change
  Upon successful RTS/CTS/DATA/ACK
    CW  CW−1

## Slide 26: Reliability: ACK
MACAW introduces an ACK after DATA packets; not in MACA
Sender resends if RTS/CTS succeeds but no ACK returns
Sender resends RTS. Two cases:
DATA was lost
  Receiver sends CTS, sender DATA
Receiver already has the DATA (reverse-link ACK loss)
  Receiver sends ACK

## Slide 27: ACK: Considerations
Avoid TCP window reductions when interference
Useful when there’s ambient noise (microwave ovens…)
Why are sequence numbers in DATA packets now important (not mentioned directly in paper!)
Are ACKs useful for multicast packets? Consequences for, e.g., ARP?

## Slide 28: MACAW and Exposed Terminals
C can proceed only if it can hear a CTS from D
  But B’s DATA will likely clobber
So B sends a Data Sending (DS) packet after CTS
  So C knows that B received a CTS
    C defers until after ACK
A
B
C
1. “RTS, k bits”
2. “CTS, k bits”
D
3. “DS”
Defer
4. “Data”
5. “ACK”
Conservative: Doesn’t leverage exposed terminal opportunities for concurrency

## Slide 29: Need for Synchronization
Suppose D has a smaller CW, ongoing transmission
B can not reply to A’s RTS
A doesn’t know when the contention periods are
  So, A’s backoff will increase: unfair
MACAW’s approach: let B contend “on behalf of” A
A
B
C
D

## Slide 30: MACAW: RRTS
But B knows when the gaps for contention are
B sends a Request for RTS (RRTS) packet to A when DATA completes (hears an ACK from C)
C defers transmissions for two slot periods (why?)
A sends a RTS immediately without backoff
A
B
C
D
RRTS
RTS
CTS
DATA

## Slide 31: A Problem not Solved by RRTS
What happens in this scenario?
  Assume C is successful, ongoing transmission
  When A sends RTS to B, B just can’t hear it
  So this problem is not solved by RRTS
A
B
C
D

## Slide 32: Today: Wi-Fi Above the PHY
MACA
MACAW
802.11 MAC layer
  Contention and backoff
  Frame aggregation
  Selective retransmission and Acknowledgement

## Slide 33: 802.11’s MAC
Adopts MACAW’s MAC from a high level:
  Same RTS/CTS/DATA/ACK
    RTS/CTS optional
  Different contention window control
Adopts CS and Deference from Ethernet:
  But not collision detection
    Transmit signal power ≫ receive signal power
Adds design elements for high data rates, TCP above

## Slide 34: Deference times for Prioritization
Fixed-time deference + CS = prioritization (DIFS > SIFS)
So, overhead of fixed time duration per Wi-Fi Frame:
  RTS/CTS (if present), DIFS, CW, preamble, SIFS, ACK
Overhead
Overhead
Distributed Coordination Function (DCF) Interframe Space (DIFS)
CW
Data
Short Interframe Space (SIFS)
ACK
Sender:
Receiver:
802.11 ac: SIFS = 16 μs, DIFS = 34 μs

## Slide 35: Backoff: Pausing and Resuming
data
wait
B1 = 5
B2 = 15
data
wait
B1 and B2 are backoff intervals
at nodes 1 and 2
CW = 31
B2 = 10
802.11 backoff slot time = Physical CS time + propagation time + time to switch radio from receive to transmit
No MACAW: No “copy,” no MILD, no DS, no RRTS
B1 = 25
B2 = 20
Node 1:
Node 2:
802.11 ac:
slot time = 9 μs
pause @ 5

## Slide 36: 802.11’s Pause
Adaptively sets CW with BEB
  Start with CW = 31, double if no CTS or ACK received
  Reset to 31 on successful transmission
Not fair in the short term
  Under contention, losers will use larger CW than winners (winners reset)
  Winners may be able to transmit several packets while unlucky nodes are still counting down
Could adopt MACAW’s copy & MILD, but has drawbacks

## Slide 37: Today: Wi-Fi Above the PHY
MACA
MACAW
802.11 MAC layer
  Contention and backoff
  Frame aggregation
  Selective retransmission and Acknowledgement

## Slide 38: Motivation: MAC Scaling Incommensurate with PHY Bitrate
1%
8%
29%
45%
73%
Preamble
(% overhead)
Payload (1,500 byte packet)
6 Mbps
(20 MHz, 1 x 1)
54 Mbps
(20 MHz, 1 x 1)
130 Mbps
(20 MHz, 2 x 2)
270 Mbps
(40MHz, 2 x 2)
540 Mbps
(40 MHz, 4 x 4)
Problem: Drop in efficiency with increasing data rate from fixed overheads in the preamble and inter-frame spaces

## Slide 39: Aggregation Amortizes Fixed Overheads
DIFS
CW
Data
SIFS
ACK
DIFS
CW
Data
SIFS
ACK
DIFS
CW
Data
SIFS
ACK
…...
DIFS
CW
Data
Data
Data
SIFS
BA
DIFS
CW
Data
Data
Data
SIFS
BA
Without aggregation:
With aggregation: Multiple frames/channel acquisition
  Block ack (BA) tells sender which arrived

## Slide 40: 802.11: Selective Retransmission
802.11 adopts TCP’s selective retransmission, but:
  Primary consideration is performance at the link layer
  Protocol is only semi-reliable: may drop packets
Receiver-side reorder buffer for in-order delivery
Receiver-side scoreboard for feedback to sender
Sender transmits Block ACK request (BAR) frames:
  If needed, sender can solicit a Block ACK response (BA response) from receiver
  Sender may direct receiver to drop (i.e., fail to deliver to the network layer) frames it deems old

## Slide 41: Reorder Buffer Operation
Like TCP, 802.11’s reorder buffer guarantees in-order delivery to the layer above
But at most once instead of exactly-once semantics
Deliver
6
5
4
3
2
1
BA
hole
Reorder buffer
6
5
2
1
3
8
7
4
6
5
4
7
8
sender
receiver

## Slide 42: Flushing the Reorder Buffer
On receiving a BAR containing starting sequence number SSN:
  Deliver all frames with sequence number < SSN
Deliver
6
5
4
3
2
1
BA
hole
Reorder buffer
6
5
2
1
3
8
7
4
6
5
7
8
BA
BAR: SSN=8
6
5
7
8
sender
receiver
4 stale!

## Slide 43: The Scoreboard
Each bit in BA frame scoreboard bitmap corresponds to receipt of frames in [WinStart, WinEnd) interval
Data and BAR frames move the scoreboard
0
212−1
WinStart
WinStart + 211
WinEnd
scoreboard
  (All arithmetic modulo 212)
Receiver’s view of the sequence number space:

## Slide 44: Scoreboard Dynamics
Receive frame (seq. # SN) from new sender:
  Set WinEnd  SN
Receive frame WinEnd < SN ≤ WinStart + 211:
  Shift scoreboard to accommodate SN
102
Receiver
Sequence number space
1
102
104
105
103
1
105
1
1
103
Scoreboard
WinStart
  (All arithmetic modulo 212)

## Slide 45: Scoreboard Dynamics
Receive frame, WinStart < SN ≤ WinEnd: Set SN’s bit
Receive BAR (seq. # SN): Shift scoreboard right (WinStart  SN)
Receive frame, WinStart + 211 < SN < WinStart: no-op
100
Receiver
Sequence number space
1
1
105
1
1
103
100
BAR: SN=100
BA
1
1
105
1
1
103
100
WinStart
  (All arithmetic modulo 212)

## Slide 46: Wi-Fi Above the PHY: Concluding Thoughts
Hard to understate the influence of ALOHAnet, Ethernet, MACA, and MACAW on Wi-Fi
  CS, deference, RTS/CTS, BEB...
Wi-Fi’s scoreboarding & selective retransmission serve as an example of the corollary to the E2E Principle
  Implement just enough of a function at the lower layer to get a performance advantage

## Slide 47
Thursday Topic:
Bit Rate Adaptation
Mesh Networks: Roofnet
Friday Precept:
Introduction to Lab 2:
HackRF MAC Protocols