## Slide 1: Transport Layer
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: IP Protocol Stack: Key Abstractions
Transport layer is where we “pay the piper”
  Provide applications with good abstractions
  Without support or feedback from the network
<number>
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application
Notes: <number>

## Slide 3: Transport Protocols
Logical communication between processes
  Sender divides a message into segments
  Receiver reassembles segments into message
Transport services
  (De)multiplexing packets
  Detecting corrupted data
  Optionally: reliable delivery, flow control, …
<number>

## Slide 4: Two Basic Transport Features
<number>
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption
Notes: <number>

## Slide 5: User Datagram Protocol (UDP)
<number>
Datagram messaging service
  Demultiplexing: port numbers
  Detecting corruption: checksum
Lightweight communication between processes
  Send and receive messages
  Avoid overhead of ordered, reliable delivery
SRC port
DST port
checksum
length
DATA
Notes: <number>

## Slide 6: Advantages of UDP
Fine-grain control
  UDP sends as soon as the application writes
No connection set-up delay
  UDP sends without establishing a connection
No connection state
  No buffers, parameters, sequence #s, etc.
Small header overhead
  UDP header is only eight-bytes long
<number>
Notes: <number>

## Slide 7: Popular Applications That Use UDP
Multimedia streaming
  Retransmitting packets is not always worthwhile
  E.g., phone calls, video conferencing, gaming, IPTV
Simple query-response protocols
  Overhead of connection establishment is overkill
  E.g., Domain Name System (DNS), DHCP, etc.
<number>
“Address for www.cnn.com?”
“12.3.4.15”
Notes: <number>

## Slide 8: Transmission Control Protocol (TCP)
Stream-of-bytes service
  Sends and receives a stream of bytes
Reliable, in-order delivery
  Corruption: checksums
  Detect loss/reordering: sequence numbers
  Reliable delivery: acknowledgments and retransmissions
Connection oriented
  Explicit set-up and tear-down of TCP connection
Flow control
  Prevent overflow of the receiver’s buffer space
Congestion control
  Adapt to network congestion for the greater good
<number>
Notes: <number>

## Slide 9: Breaking a Stream of Bytes into TCP Segments
<number>
Notes: <number>

## Slide 10: TCP “Stream of Bytes” Service
<number>
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 80
Notes: <number>

## Slide 11: …Emulated Using TCP “Segments”
<number>
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out, or
“Pushed” by application.
Notes: <number>

## Slide 12: TCP Segment
<number>
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes on an Ethernet link
TCP packet
  IP packet with a TCP header and data inside
  TCP header is typically 20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)
Notes: <number>

## Slide 13: Sequence Number
<number>
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number = 1st byte
Byte 81
Notes: <number>

## Slide 14: Initial Sequence Number (ISN)
Sequence number for the very first byte
  E.g., Why not a de facto ISN of 0?
Practical issue: reuse of port numbers
  Port numbers must (eventually) get used again
  … and an old packet may still be in flight
  … and associated with the new connection
So, TCP must change the ISN over time
  Set from a 32-bit clock that ticks every 4 microsec
  … which wraps around once every 4.55 hours!
<number>
Notes: <number>

## Slide 15: Reliable Delivery on a Lossy Channel With Bit Errors
<number>
Notes: <number>

## Slide 16: Challenges of Reliable Data Transfer
Over a perfectly reliable channel
  Easy: sender sends, and receiver receives
Over a channel with bit errors
  Receiver detects errors and requests retransmission
Over a lossy channel with bit errors
  Some data are missing, and others corrupted
  Receiver cannot always detect loss
Over a channel that may reorder packets
  Receiver cannot distinguish loss from out-of-order
<number>
Notes: <number>

## Slide 17: An Analogy
Alice and Bob are talking
  What if Alice couldn’t understand Bob?
  Bob asks Alice to repeat what she said
What if Bob hasn’t heard Alice for a while?
  Is Alice just being quiet? Has she lost reception?
  How long should Bob just keep on talking?
  Maybe Alice should periodically say “uh huh”
  … or Bob should ask “Can you hear me now?” 
<number>
Notes: <number>

## Slide 18: Take-Aways from the Example
Acknowledgments from receiver
  Positive: “okay” or “uh huh” or “ACK”
  Negative: “please repeat that” or “NACK”
Retransmission by the sender
  After not receiving an “ACK”
  After receiving a “NACK”
Timeout by the sender (“stop and wait”)
  Don’t wait forever without some acknowledgment
<number>
Notes: <number>

## Slide 19: TCP Support for Reliable Delivery
<number>
Detect bit errors: checksum
  Used to detect corrupted data at the receiver
  …leading the receiver to drop the packet
Detect missing data: sequence number
  Used to detect a gap in the stream of bytes
  ... and for putting the data back in order
Recover from lost data: retransmission
  Sender retransmits lost or corrupted data
  Two main ways to detect lost packets
Notes: <number>

## Slide 20: TCP Acknowledgments
<number>
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number = 1st byte
ACK sequence number = next expected byte
Notes: <number>

## Slide 21: Automatic Repeat reQuest (ARQ)
ACK and timeouts
  Receiver sends ACK when it receives packet
  Sender waits for ACK and times out
Simplest ARQ protocol
  Stop and wait
  Send a packet, stop and wait until ACK arrives
<number>
Time
Packet
ACK
Timeout
Sender
Receiver

## Slide 22: Flow Control: TCP Sliding Window
<number>
Notes: <number>

## Slide 23: Motivation for Sliding Window
<number>
Stop-and-wait is inefficient
  Only one TCP segment is “in flight” at a time
  Especially bad for high “delay-bandwidth product”
delay
bandwidth
Notes: <number>

## Slide 24: Numerical Example
1.5 Mbps link with 45 msec round-trip time (RTT)
  Delay-bandwidth product is 67.5 Kbits (or 8 KBytes)
Sender can send at most one packet per RTT
  Assuming a segment size of 1 KB (8 Kbits)
  8 Kbits/segment at 45 msec/segment  182 Kbps
  That’s just one-eighth of the 1.5 Mbps link capacity
<number>
Notes: <number>

## Slide 25: Sliding Window
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
<number>
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received
Notes: <number>

## Slide 26: Receiver Buffering
Receive window size
  Amount that can be sent without acknowledgment
  Receiver must be able to store this amount of data
Receiver tells the sender the window
  Tells the sender the amount of free space left
<number>
Window Size
Outstanding
Un-ack’d data
Data OK
to send
Data not OK
to send yet
Data ACK’d
Notes: <number>

## Slide 27: Optimizing Retransmissions
<number>

## Slide 28: Reasons for Retransmission
<number>
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS
Notes: <number>
Application may get duplicates in the case of early timeouts

## Slide 29: How Long Should Sender Wait?
<number>
Sender sets a timeout to wait for an ACK
  Too short: wasted retransmissions
  Too long: excessive delays when packet lost
TCP sets timeout as a function of the RTT
  Expect ACK to arrive after an “round-trip time”
  … plus a fudge factor to account for queuing
But, how does the sender know the RTT?
  Running average of delay to receive an ACK
Notes: <number>

## Slide 30: Example RTT Estimation
<number>
Notes: <number>

## Slide 31: Still, Timeouts are Inefficient
<number>
Notes: <number>

## Slide 32: Fast Retransmission
When packet n is lost…
  … packets n+1, n+2, and so on may get through
Exploit the ACKs of these packets
  ACK says receiver is still awaiting nth packet
  Duplicate ACKs suggest later packets arrived
  Sender uses “duplicate ACKs” as a hint
Fast retransmission
  Retransmit after “triple duplicate ACK”
<number>
Notes: <number>

## Slide 33: Effectiveness of Fast Retransmit
When does Fast Retransmit work best?
  High likelihood of many packets in flight
  Long data transfers, large window size, …
Implications for Web traffic
  Most Web transfers are short (e.g., 10 packets)
    So, often there aren’t many packets in flight
  Making fast retransmit is less likely to “kick in”
    Forcing users to click “reload” more often… 
<number>
Notes: <number>

## Slide 34: Starting and Ending a Connection: TCP Handshakes
<number>
Notes: <number>

## Slide 35: Establishing a TCP Connection
Three-way handshake to establish connection
  Host A sends a SYN (open) to the host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
<number>
SYN
SYN ACK
ACK
Data
A
B
Data
Each host tells its ISN to the other host.
Notes: <number>

## Slide 36: TCP Header
<number>
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
FIN
RST
PSH
URG
ACK
Notes: <number>

## Slide 37: Step 1: A’s Initial SYN Packet
<number>
A’s port
B’s port
A’s Initial Sequence Number
Acknowledgment
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it wants to open a connection…
Notes: <number>

## Slide 38: Step 2: B’s SYN-ACK Packet
<number>
B’s port
A’s port
B’s Initial Sequence Number
A’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
B tells A it accepts, and is ready to hear the next byte…
… upon receiving this packet, A can start sending data
Notes: <number>

## Slide 39: Step 3: A’s ACK of the SYN-ACK
<number>
A’s port
B’s port
B’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it is okay to start sending
Sequence number
… upon receiving this packet, B can start sending data
Notes: <number>

## Slide 40: What if the SYN Packet Gets Lost?
<number>
Suppose the SYN packet gets lost
  Packet is lost inside the network, or
  Server rejects the packet (e.g., listen queue is full)
Eventually, no SYN-ACK arrives
  Sender sets a timer and wait for the SYN-ACK
  … and retransmits the SYN if needed
How should the TCP sender set the timer?
  Sender has no idea how far away the receiver is
  Some TCPs use a default of 3 or 6 seconds
Notes: <number>

## Slide 41: SYN Loss and Web Downloads
<number>
User clicks on a hypertext link
  Browser creates a socket and does a “connect”
  The “connect” triggers the OS to transmit a SYN
If the SYN is lost…
  The 3-6 seconds of delay is very long
  The impatient user may click “reload”
User triggers an “abort” of the “connect”
  Browser “connects” on a new socket
  Essentially, forces a fast send of a new SYN!
Notes: <number>

## Slide 42: Tearing Down the Connection
<number>
Closing (each end of) the connection
  Finish (FIN) to close and receive remaining bytes
  And other host sends a FIN ACK to acknowledge
  Reset (RST) to close and not receive remaining bytes
SYN
SYN ACK
ACK
Data
FIN
ACK
ACK
time
A
B
FIN
ACK
Notes: <number>

## Slide 43: Sending/Receiving the FIN Packet
Sending a FIN: close()
  Process is done sending data via the socket
  Process invokes “close()” to close the socket
  Once TCP has sent all the outstanding bytes…
  … then TCP sends a FIN
Receiving a FIN: EOF
  Process is reading data from the socket
  Eventually, the attempt to read returns an EOF
<number>
Notes: <number>

## Slide 44: Conclusions
Transport protocols
  Multiplexing and demultiplexing
  Checksum-based error detection
  Sequence numbers
  Retransmission
  Window-based flow control
Precept on Friday
  Application-layer protocols: HTTP
  HTTP proxy assignment
<number>
Notes: <number>