## Slide 1: Congestion
Michael Freedman
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Last Week: Discovery and Routing
<number>
link
session
path
name
address
Provides end-to-end connectivity, but not necessarily good performance
Notes: Last week, we talked about how one end-point of a session reaches another, through (i) discovery (mapping a name in one layer to an address in the layer below) and (ii) routing (computing a path from one end-point to another in the lower layer). But, this does not ensure that the performance is good.
<number>

## Slide 3: Today: Congestion Control
<number>
?
?
link
session
path
name
address
What can the end-points do to collectively to make good use of shared underlying resources?
Notes: This week, we’ll talk about how to share resources. Today we’ll talk about what the end-points can do in a distributed fashion, from the edge of the network. On Wednesday, we’ll talk about what the lower-level elements can do.
<number>

## Slide 4: Distributed Resource Sharing
<number>

## Slide 5: Congestion
Best-effort network does not “block” calls
  So, they can easily become overloaded
  Congestion == “Load higher than capacity”
Examples of congestion
  Link layer: Ethernet frame collisions
  Network layer: full IP packet buffers
Excess packets are simply dropped
  And the sender can simply retransmit
queue

## Slide 6: Congestion Collapse
Easily leads to congestion collapse
  Senders retransmit the lost packets
  Leading to even greater load
  … and even more packet loss
<number>
Load
Goodput
“congestion
collapse”
Increase in load that results in a decrease in useful work done.

## Slide 7: Detect and Respond to Congestion
What does the end host see?
What can the end host change?
<number>
?
Notes: <number>

## Slide 8: Detecting Congestion
Link layer
  Carrier sense multiple access
  Seeing your own frame collide with others
Network layer
  Observing end-to-end performance
  Packet delay or loss over the path
<number>

## Slide 9: Responding to Congestion
Upon detecting congestion
  Decrease the sending rate
But, what if conditions change?
  If more bandwidth becomes available,
  … unfortunate to keep sending at a low rate
Upon not detecting congestion
  Increase sending rate, a little at a time
  See if packets get through
<number>
Notes: <number>

## Slide 10: Ethernet Back-off Mechanism
Carrier sense:
  Wait for link to be idle
  If idle, start sending
  If not, wait until idle
Collision detection: listen while transmitting
  If collision: abort transmission, and send jam signal
Exponential back-off: wait before retransmitting
  Wait random time, exponentially larger per retry
<number>

## Slide 11: TCP Congestion Control
Additive increase, multiplicative decrease
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
<number>
t
Window
halved
Loss

## Slide 12: Why Exponential?
Respond aggressively to bad news
  Congestion is (very) bad for everyone
  Need to react aggressively
Examples:
  Ethernet: double retransmission timer
  TCP: divide sending rate in half
Nice theoretical properties
  Makes efficient use of network resources
<number>

## Slide 13: TCP Congestion Control
<number>

## Slide 14: Congestion in a Drop-Tail FIFO Queue
Access to the bandwidth: first-in first-out queue
  Packets transmitted in the order they arrive
<number>
✗
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet
Notes: <number>

## Slide 15: How it Looks to the End Host
Delay: Packet experiences high delay
Loss: Packet gets dropped along path
How does TCP sender learn this?
  Delay: Round-trip time estimate
  Loss: Timeout and/or duplicate acknowledgments
<number>
✗
Notes: <number>

## Slide 16: TCP Congestion Window
Each TCP sender maintains a congestion window
  Max number of bytes to have in transit (not yet ACK’d)
Adapting the congestion window
  Decrease upon losing a packet: backing off
  Increase upon success: optimistically exploring
  Always struggling to find right transfer rate
Tradeoff
  Pro: avoids needing explicit network feedback
  Con: continually under- and over-shoots “right” rate
<number>
Notes: <number>

## Slide 17: Additive Increase, Multiplicative Decrease
How much to adapt?
  Additive increase: On success of last window of data, increase window by 1 Max Segment Size (MSS)
  Multiplicative decrease: On loss of packet, divide congestion window in half
Much quicker to slow than speed up!
  Over-sized windows (causing loss) are much worse than under-sized windows (causing lower thruput)
  AIMD: A necessary condition for stability of TCP
<number>
Notes: <number>

## Slide 18: Leads to the TCP “Sawtooth”
<number>
t
Window
halved
Loss
Notes: <number>

## Slide 19: Receiver Window vs. Congestion Window
Flow control
  Keep a fast sender from overwhelming a slow receiver
Congestion control
  Keep a set of senders from overloading the network
Different concepts, but similar mechanisms
  TCP flow control: receiver window
  TCP congestion control: congestion window
  Sender TCP window =
  min { congestion window, receiver window }
<number>
Notes: <number>

## Slide 20: Starting a New Flow
<number>

## Slide 21: How Should a New Flow Start?
<number>
t
Window
halved
Loss
But, could take a long time to get started!
Start slow (a small CWND) to avoid overloading network
Notes: <number>

## Slide 22: “Slow Start” Phase
Start with a small congestion window
  Initially, CWND is 1 MSS
  So, initial sending rate is MSS / RTT
Could be pretty wasteful
  Might be much less than actual bandwidth
  Linear increase takes a long time to accelerate
Slow-start phase (really “fast start”)
  Sender starts at a slow rate (hence the name)
  … but increases rate exponentially until the first loss
<number>
Notes: <number>

## Slide 23: Slow Start in Action
<number>
Double CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
A
1
2
4
8
Notes: <number>

## Slide 24: Slow Start and the TCP Sawtooth
TCP originally had no congestion control
  Source would start by sending entire receiver window
  Led to congestion collapse!
  “Slow start” is, comparatively, slower
<number>
t
Window
halved
Loss
Exponential “slow start”
Notes: <number>

## Slide 25: Two Kinds of Loss in TCP
Timeout
  Packet n is lost and detected via a timeout
  Blasting entire CWND would cause another burst
  Better to start over with a low CWND
Triple duplicate ACK
  Packet n is lost, but packets n+1, n+2, etc. arrive
  Then, sender quickly resends packet n
  Do a multiplicative decrease and keep going
<number>
Notes: <number>

## Slide 26: Repeating Slow Start After Timeout
<number>
t
Window
Slow-start restart: Go back to CWND of 1, but take advantage of knowing the previous value of CWND.
Slow start until reaching half of previous cwnd.
timeout
Notes: <number>

## Slide 27: Repeating Slow Start After Idle Period
Suppose a TCP connection goes idle for a while
Eventually, the network conditions change
  Maybe many more flows are traversing the link
Dangerous to start transmitting at the old rate
  Previously-idle TCP sender might blast network
  … causing excessive congestion and packet loss
So, some TCP implementations repeat slow start
  Slow-start restart after an idle period
<number>
Notes: <number>

## Slide 28: Fairness
<number>

## Slide 29: TCP Achieves a Notion of Fairness
Effective utilization is not only goal
  We also want to be fair to various flows
Simple definition: equal bandwidth shares
  N flows that each get 1/N of the bandwidth?
But, what if flows traverse different paths?
  Result: bandwidth shared in proportion to RTT
<number>
Notes: <number>

## Slide 30: What About Cheating?
Some folks are more fair than others
  Running multiple TCP connections in parallel (BitTorrent)
  Modifying the TCP implementation in the OS
    Some cloud services start TCP at > 1 MSS
  Use the User Datagram Protocol
What is the impact
  Good guys slow down to make room for you
  You get an unfair share of the bandwidth
<number>
Notes: <number>

## Slide 31: Preventing Cheating
Possible solutions?
  Routers detect cheating and drop excess packets?
  Per user/customer failness?
  Peer pressure?
<number>
Notes: <number>

## Slide 32: Conclusions
Congestion is inevitable
  Internet does not reserve resources in advance
  TCP actively tries to push the envelope
Congestion can be handled
  Additive increase, multiplicative decrease
  Slow start and slow-start restart
Fundamental tensions
  Feedback from the network?
  Enforcement of “TCP friendly” behavior?
<number>
Notes: <number>