## Slide 1: Queue Management
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Monday: Congestion Control
<number>
?
?
link
session
path
name
address
What can the end-points do to collectively to make good use of shared underlying resources?
Notes: This week, we’ll talk about how to share resources. Today we’ll talk about what the end-points can do in a distributed fashion, from the edge of the network. On Wednesday, we’ll talk about what the lower-level elements can do.
<number>

## Slide 3: Today: Queue Management
<number>
link
session
path
name
address
What can the individual links do to make good use of shared underlying resources?
?
Notes: This week, we’ll talk about how to share resources. Today we’ll talk about what the end-points can do in a distributed fashion, from the edge of the network. On Wednesday, we’ll talk about what the lower-level elements can do.
<number>

## Slide 4: Packet Queues
<number>

## Slide 5: Router
<number>
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane
Notes: <number>

## Slide 6: Line Cards (Interface Cards, Adaptors)
Packet handling
  Packet forwarding
  Buffer management
  Link scheduling
  Packet filtering
  Rate limiting
  Packet marking
  Measurement
<number>
to/from link
to/from switch
lookup
Receive
Transmit
Notes: <number>

## Slide 7: Packet Switching and Forwarding
<number>
R1
Link 1
Link 2
Link 3
Link 4
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Link 4, ingress
Link 4, egress
Choose
Egress
Choose
Egress
Choose
Egress
Choose
Egress
“4”
“4”
Notes: <number>

## Slide 8: Queue Management Issues
Scheduling discipline
  Which packet to send?
  Some notion of fairness? Priority?
Drop policy
  When should you discard a packet?
  Which packet to discard?
Goal: balance throughput and delay
  Huge buffers minimize drops, but add to queuing delay (thus higher RTT, longer slow start, …)
<number>

## Slide 9: FIFO Scheduling and Drop-Tail
Access to the bandwidth: first-in first-out queue
  Packets only differentiated when they arrive
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet
<number>
✗
Notes: <number>

## Slide 10: Early Detection of Congestion
<number>

## Slide 11: Bursty Loss From Drop-Tail Queuing
TCP depends on packet loss
  Packet loss is indication of congestion
  TCP additive increase drives network into loss
Drop-tail leads to bursty loss
  Congested link: many packets encounter full queue
  Synchronization: many connections lose packets at once
<number>
Notes: <number>

## Slide 12: Slow Feedback from Drop Tail
Feedback comes when buffer is completely full
  … even though the buffer has been filling for a while
Plus, the filling buffer is increasing RTT
  … making detection even slower
Better to give early feedback
  Get 1-2 connections to slow down before it’s too late!
<number>
Notes: <number>

## Slide 13: Random Early Detection (RED)
Router notices that queue is getting full
  … and randomly drops packets to signal congestion
Packet drop probability
  Drop probability increases as queue length increases
  Else, set drop probability f(avg queue length)
<number>
Average Queue Length
Drop
Probability
0 1
Notes: <number>

## Slide 14: Properties of RED
Drops packets before queue is full
  In the hope of reducing the rates of some flows
Drops packet in proportion to each flow’s rate
  High-rate flows selected more often
Drops are spaced out in time
  Helps desynchronize the TCP senders
Tolerant of burstiness in the traffic
  By basing the decisions on average queue length
<number>
Notes: <number>

## Slide 15: Problems With RED
Hard to get tunable parameters just right
  How early to start dropping packets?
  What slope for increase in drop probability?
  What time scale for averaging queue length?
RED has mixed adoption in practice
  If parameters aren’t set right, RED doesn’t help
Many other variations in research community
  Names like “Blue” (self-tuning), “FRED”…
<number>
Notes: <number>

## Slide 16: Feedback: From Loss to Notification
Early dropping of packets
  Good: gives early feedback
  Bad: has to drop the packet to give the feedback
Explicit Congestion Notification (ECN)
  Router marks the packet with an ECN bit
  Sending host interprets as a sign of congestion
  Requires participation of hosts and the routers
<number>
Notes: <number>

## Slide 17: Link Scheduling
<number>
Notes: <number>

## Slide 18: First-In First-Out Scheduling
<number>
First-in first-out scheduling
  Simple, but restrictive
Example: two kinds of traffic
  Voice over IP needs low delay
  E-mail is not that sensitive about delay
Voice traffic waits behind e-mail
Notes: <number>

## Slide 19: Strict Priority
<number>
Multiple levels of priority
  Always transmit high-priority traffic, when present
Isolation for the high-priority traffic
  Almost like it has a dedicated link
  Except for (small) delay for packet transmission
But, lower priority traffic may starve 
Notes: <number>

## Slide 20: Weighted Fair Scheduling
<number>
Weighted fair scheduling
  Assign each queue a fraction of the link bandwidth
  Rotate across queues on a small time scale
Work-conserving
  Send extra traffic from one queue if others are idle
50% red, 25% blue, 25% green
Notes: <number>

## Slide 21: Implementation Trade-Offs
<number>
FIFO
  One queue, trivial scheduler
Strict priority
  One queue per priority level, simple scheduler
Weighted fair scheduling
  One queue per class, and more complex scheduler
Notes: <number>

## Slide 22: Quality of Service Guarantees
<number>

## Slide 23: Distinguishing Traffic
Applications compete for bandwidth
  VoIP and email sharing a link
  E-mail traffic can cause congestion and losses
Principle 1: Packet marking
  So router can distinguish between classes
  E.g., Type of Service (ToS) bits in IP header
<number>
Notes: <number>

## Slide 24: Preventing Misbehavior
<number>
Applications misbehave
  VoIP sends packets faster than 1 Mbps
Principle 2: Policing
  Protect one traffic class from another
  By enforcing a rate limit on the traffic
Notes: <number>

## Slide 25: Subdividing Link Resources
<number>
Principle 3: Link scheduling
  Ensure each application gets its share
  … while (optionally) using any extra bandwidth
  E.g., weighted fair scheduling
Notes: <number>

## Slide 26: Reserving Resources, and Saying No
<number>
Traffic cannot exceed link capacity
  Deny access, rather than degrade performance
Principle 4: Admission control
  Application declares its needs in advance
  Application denied if insufficient resources available
Notes: <number>

## Slide 27: Quality of Service (QoS)
<number>
Guaranteed performance
  Alternative to best-effort delivery model
QoS protocols and mechanisms
  Packet classification and marking
  Traffic shaping
  Link scheduling
  Resource reservation and admission control
  Identifying paths with sufficient resources
Notes: <number>

## Slide 28: Conclusions
Link resource allocation
  Buffer management
  Link scheduling
Friday precept
  Practice exam questions on resource allocation
  See six questions posted on syllabus page
Next week: routing dynamics
  Routing protocol convergence
  Routing to mobile hosts
<number>
Notes: <number>