## Slide 1: Routing Convergence
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Routing Changes
Topology changes: new route to the same place
Host mobility: route to a different place
<number>

## Slide 3: Topology Changes
<number>

## Slide 4: Two Types of Topology Changes
Planned
  Maintenance: shut down a node or link
  Energy savings: shut down a node or link
  Traffic engineering: change routing configuration
Unplanned
  Failure
  E.g., fiber cut, faulty equipment, power outage, software bugs, …
<number>

## Slide 5: Detecting Topology Changes
Beaconing
  Periodic “hello” messages in both directions
  Detect a failure after a few missed “hellos”
Performance trade-offs
  Detection delay
  Overhead on link bandwidth and CPU
  Likelihood of false detection
<number>
“hello”
Notes: <number>

## Slide 6: Routing Convergence: Link-State Routing
<number>

## Slide 7: Convergence
<number>
Control plane
  All nodes have consistent information
Data plane
  All nodes forward packets in a consistent way
3
2
2
1
1
4
1
4
5
3
Notes: <number>

## Slide 8: Transient Disruptions
Detection delay
  A node does not detect a failed link immediately
  … and forwards data packets into a “blackhole”
  Depends on timeout for detecting lost hellos
<number>
3
2
2
1
1
4
1
4
5
3
Notes: <number>

## Slide 9: Transient Disruptions
<number>
Inconsistent link-state database
  Some routers know about failure before others
  Inconsistent paths cause transient forwarding loops
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
3
Notes: <number>

## Slide 10: Convergence Delay
<number>
Sources of convergence delay
  Detection latency
  Updating control-plane information
  Computing and install new forwarding tables
Performance during convergence period
  Lost packets due to blackholes and TTL expiry
  Looping packets consuming resources
  Out-of-order packets reaching the destination
Very bad for VoIP, online gaming, and video
Notes: <number>

## Slide 11: Reducing Convergence Delay
Faster detection
  Smaller hello timers, better link-layer technologies
Faster control plane
  Flooding immediately
  Sending routing messages with high-priority
Faster computation
  Faster processors, and incremental computation
Faster forwarding-table update
  Data structures supporting incremental updates
<number>
Notes: <number>

## Slide 12: Slow Convergence in Distance-Vector Routing
<number>

## Slide 13: Distance Vector: Link Cost Changes
Link cost decreases and recovery
  Node updates the distance table
  If cost change in least cost path, notify neighbors
<number>
X
Z
1
4
50
Y
1
“good
news
travels
fast”
Notes: <number>

## Slide 14: Distance Vector: Link Cost Changes
Link cost increases and failures
  Bad news travels slowly
  “Count to infinity” problem!
<number>
X
Z
1
4
50
Y
60
algorithm
continues
on!
Notes: <number>

## Slide 15: Distance Vector: Poison Reverse
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
  Still, can have problems in larger networks
<number>
X
Z
1
4
50
Y
60
algorithm
terminates
Notes: <number>

## Slide 16: Redefining Infinity
Avoid “counting to infinity”
  By making “infinity” smaller!
Routing Information Protocol (RIP)
  All links have cost 1
  Valid path distances of 1 through 15
  … with 16 representing infinity
Used mainly in small networks
<number>
Notes: <number>

## Slide 17: Reducing Convergence Time With Path-Vector Routing (e.g., Border Gateway Protocol)
<number>

## Slide 18: Path-Vector Routing
Extension of distance-vector routing
  Support flexible routing policies
  Avoid count-to-infinity problem
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
<number>
3
2
1
d
“d: path (2,1)”
“d: path (1)”
data traffic
data traffic
Notes: <number>

## Slide 19: Faster Loop Detection
Node can easily detect a loop
  Look for its own node identifier in the path
  E.g., node 1 sees itself in the path “3, 2, 1”
Node can simply discard paths with loops
  E.g., node 1 simply discards the advertisement
<number>
3
2
1
“d: path (2,1)”
“d: path (1)”
“d: path (3,2,1)”
Notes: <number>

## Slide 20: BGP Session Failure
BGP runs over TCP
  BGP only sends updates when changes occur
  TCP doesn’t detect lost connectivity on its own
Detecting a failure
  Keep-alive: 60 seconds
  Hold timer: 180 seconds
Reacting to a failure
  Discard all routes learned from neighbor
  Send new updates for any routes that change
<number>
AS1
AS2
Notes: <number>

## Slide 21: Routing Change: Before and After
<number>
0
1
2
3
(1,0)
(2,0)
(3,1,0)
0
1
2
3
(2,0)
(1,2,0)
(3,2,0)
Notes: <number>

## Slide 22: Routing Change: Path Exploration
AS 1
  Delete the route (1,0)
  Switch to next route (1,2,0)
  Send route (1,2,0) to AS 3
AS 3
  Sees (1,2,0) replace (1,0)
  Compares to route (2,0)
  Switches to using AS 2
<number>
0
1
2
3
(2,0)
(1,2,0)
(3,2,0)
Notes: <number>

## Slide 23: Routing Change: Path Exploration
Initial situation
  All ASes use direct path
Destination 0 dies
  All ASes lose direct path
  All switch to longer paths
  Eventually withdrawn
E.g., AS 2
  (2,0)  (2,1,0)  (2,3,0)  (2,1,3,0)  null
<number>
1
2
3
0
(1,0)
(1,2,0)
(1,3,0)
(2,0)
(2,1,0)
(2,3,0)
(2,1,3,0)
(3,0)
(3,1,0)
(3,2,0)
Notes: <number>

## Slide 24: BGP Converges Slowly
Path vector avoids count-to-infinity
  But, ASes still must explore many alternate paths
  … to find the highest-ranked available path
Fortunately, in practice
  Most popular destinations have stable BGP routes
  Most instability lies in a few unpopular destinations
Still, lower BGP convergence delay is a goal
  Can be tens of seconds to tens of minutes
  High for important interactive applications
<number>
Notes: <number>

## Slide 25: BGP Instability
<number>

## Slide 26: Stable Paths Problem (SPP) Instance
1
Node
  BGP-speaking router
  Node 0 is destination
Edge
  BGP adjacency
Permitted paths
  Set of routes to 0 at each node
  Ranking of the paths
2
5
5 2 1 0
0
2 1 0
2 0
1 3 0
1 0
3 0
4 2 0
4 3 0
3
4
2
1
most preferred
…
least preferred
Notes: <number>

## Slide 27: Solution to a Stable Paths Problem
5
5 2 1 0
1
Solution
  Path assignment per node
  Can be the “null” path
If node u has path uwP
  {u,w} is an edge in the graph
  Node w is assigned path wP
Each node is assigned
  Highest ranked path consistent with its neighbors
2
0
2 1 0
2 0
1 3 0
1 0
3 0
4 2 0
4 3 0
3
4
2
1
Notes: <number>

## Slide 28: SPP May Have Multiple Solutions
1
0
2
1 2 0
1 0
2 1 0
2 0
First solution
1
0
2
1 2 0
1 0
2 1 0
2 0
1
0
2
1 2 0
1 0
2 1 0
2 0
Second solution
Notes: <number>

## Slide 29: An SPP May Have No Solution
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 2 0
3 0
4
3
Notes: <number>

## Slide 30: Avoiding BGP Instability
Detecting conflicting policies
  Computationally expensive
  Requires too much cooperation
Detecting oscillations
  Observing the repetitive BGP routing messages
Restricted routing policies and topologies
  Policies based on business relationships
<number>

## Slide 31: Customer-Provider Relationship
Customer pays provider for access to Internet
  Provider exports its customer routes to everybody
  Customer exports provider routes only to its customers
d
d
provider
customer
customer
provider
Traffic to customer
Traffic from customer
advertisements
traffic
Notes: <number>

## Slide 32: Peer-Peer Relationship
Peers exchange traffic between their customers
  AS exports only customer routes to a peer
  AS exports a peer’s routes only to its customers
peer
peer
Traffic to/from the peer and its customers
d
advertisements
traffic
Notes: <number>

## Slide 33: Hierarchical AS Relationships
Provider-customer graph is directed and acyclic
  If u is a customer of v and v is a customer of w
  … then w is not a customer of u
u
v
w
Notes: <number>

## Slide 34: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Valid paths: “1 2 d” and “7 d”
Invalid path: “5 8 d”
Valid paths: “6 4 3 d” and “8 5 d”
Invalid paths: “6 5 d” and “1 4 3 d”
Notes: <number>

## Slide 35: Local Control, Global Stability
Route export
  Don’t export routes learned from a peer or provider
  … to another peer or provider
Global topology
  Provider-customer relationship graph is acyclic
  E.g., my customer’s customer is not my provider
Route selection
  Prefer routes through customers
  … over routes through peers and providers
Guaranteed to converge to unique, stable solution
Notes: <number>

## Slide 36: Conclusion
The only constant is change
  Planned topology and configuration changes
  Unplanned failure and recovery
Routing-protocol convergence
  Transient period of disagreement
  Blackholes, loops, and out-of-order packets
Routing instability
  Permanent conflicts in routing policy
  Leading to bi-stability or oscillation
<number>