## Slide 1: Mobility
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Why (and How) Things Move
<number>

## Slide 3: Physical Mobility
Device attaches to a new attachment point
<number>

## Slide 4: Multi-Homing
Device starts using a different attachment point
<number>
3G
WiFi

## Slide 5: Migration
Process or virtual machine migration
<number>

## Slide 6: Failover
Backup machine takes over after the primary fails
<number>

## Slide 7: Handling Mobility
<number>

## Slide 8: Change Address of Mobile Node?
<number>
link
session
path
name
address
A
B
a
b1
?

## Slide 9: Keeping the Address the Same
Mobility is a routing problem
  Change the routes to reach the new location
  Challenge: scalability of the routing protocol
<number>
path
a
b1
b1

## Slide 10: Changing the Address
Mobility is a directory problem
  Change the mapping of name to address
  Challenge: scalability of directory, updating neighbor
<number>
link
session
name
a
b1
b2
A
B

## Slide 11: Two Internet Design Decisions
Socket abstraction
  Connection between a pair of fixed IP addresses and port numbers
  Leads to more emphasis on routing solutions
Interface addresses
  Addresses refer to interfaces (adaptors)
  Not the host, or the service
<number>
3G
WiFi
1.2.3.4
5.6.7.8

## Slide 12: Routing Solutions
Address Stays the Same
<number>

## Slide 13: Three Examples
Ethernet
  MAC learning of the new location
IP routing
  Inject IP address(es) at new location
Mobile IP
  Stationary home agent directs traffic to new location
<number>

## Slide 14: Example #1: Ethernet
MAC learning
  Learn b1’s location when b1 sends a frame
  Soft state: timeout the cached information
<number>
a
b1
b1

## Slide 15: Making Larger Ethernet Segments
<number>
Ethernet handles mobility
  IP address and MAC address stay the same
  Switches learn to route to the new location
But, larger networks have multiple segments
  Cannot retain your IP address as you move
Solution: virtual local area networks (VLAN)
  Logical Ethernet segment spanning a campus
  E.g., interconnecting the WiFi access points

## Slide 16: Pros and Cons
Advantages
  Seamless mobility, no changes to hosts or apps
  No changes to MAC or IP addresses
Disadvantages
  Ethernet does not scale
  Long paths, state per MAC address, flooding, …
Widely used approach in campus networks
<number>

## Slide 17: Example #2: IP Routing
Node has a persistent address (e.g., 12.34.45.7)
Injected into routing protocol (e.g., OSPF)
<number>
12.34.45.0/24
12.34.45.7/32
Notes: <number>

## Slide 18: Boeing Connexion: Wide-Area Mobility
<number>
BGP
12.78.3.0/24
http://www.nanog.org/meetings/nanog31/abstracts.php?pt=NTk1Jm5hbm9nMzE=&nm=nanog31
Notes: <number>

## Slide 19: Pros and Cons
<number>
Advantages
  Seamless mobility, no MAC or IP address changes
  Traffic follows an efficient path to new location
Disadvantages
  Does not scale to large number of mobile hosts
  More routing-protocol messages
  Larger routing tables to store smaller address blocks
Notes: <number>

## Slide 20: Example #3: Mobile IP
<number>
Home network: permanent “home” of mobile (e.g., 128.119.40/24)
Permanent address: can always be used to reach mobile, e.g., 128.119.40.186
Home agent: performs mobility functions on behalf of mobile
wide area network
correspondent
Correspondent: wants to communicate with mobile
Notes: <number>

## Slide 21: Visited Network and Care-of Address
<number>
Care-of-address: in visited network
(e.g., 79,129.13.2)
wide area network
Visited network: e.g., 79.129.13/24
Permanent address: remains constant (e.g., 128.119.40.186)
Foreign agent: performs mobility functions for the mobile.
Correspondent
Notes: <number>

## Slide 22: Mobility: Registration
Foreign agent knows about mobile
Home agent knows location of mobile
<number>
wide area network
home network
visited network
1
mobile contacts foreign agent on entering visited network
2
foreign agent contacts home agent home: “this mobile is resident in my network”
Notes: <number>

## Slide 23: Mobility via Indirect Routing
<number>
wide area network
home
network
visited
network
3
2
4
1
correspondent addresses packets using home address of mobile
home agent intercepts packets, forwards to foreign agent
foreign agent receives packets, forwards to mobile
mobile replies directly to correspondent
Notes: <number>

## Slide 24: Pros and Cons
<number>
Advantages
  Seamless to the remote end-point
  No routing-protocol overhead
Disadvantages
  Overhead of running home and foreign agents
  Inefficient “triangle routing” (high “stretch”)
  Foreign agent sends “spoofed” IP source address
Notes: <number>

## Slide 25: Directory Solutions
Change the mapping of name to address
<number>

## Slide 26: Three Examples
Ethernet
  Gratuitous ARP to change the MAC address associated with an IP address
Dynamic DNS
  DNS updates to change the IP address(es) associated with a domain name
Various recent proposed designs
  Updating the remote end-point (e.g., end host, edge switch) to use a new address
<number>

## Slide 27: Example #1: Ethernet
Backup machine floods “gratuitous ARP” response
  Associates the IP address with a new MAC address
  Hosts update their ARP cache
<number>
IP 1.2.3.4
MAC m1
IP 1.2.3.4
MAC m2

## Slide 28: Ethernet Multi-Homing
Gratuitous ARP
  Balance traffic over two interfaces
  Fail over from one interface to the other
<number>
IP 1.2.3.4
MAC m1
IP 1.2.3.4
MAC m2

## Slide 29: Pros and Cons
Advantages
  Seamless change from one MAC address to another
Disadvantages
  Works only within a single Ethernet subnet
  Scalability limitations of Ethernet
Used in data-center networks
  But doesn’t help with smart phones homed to multiple administrative domains
<number>

## Slide 30: Example #2: Dynamic DNS
Dynamically update DNS
  Change the mapping of domain name to IP address
  Future DNS requests get the new addres
<number>
Name: www.nbc.com
IP: 1.2.3.4
Name: www.nbc.com
IP: 5.6.7.8

## Slide 31: Applications of Dynamic DNS
Replicated services
  Direct future requests to a different replica
  E.g., for failover, load balancing, performance, etc.
Services on dynamically-assigned IP addresses
  Residential user with a dynamic IP address
  Directs clients to the server’s current address
“Fast flux” in botnets
  Hiding phishing and malware delivery servers
  … behind constantly changing IP addresses
<number>

## Slide 32: Pros and Cons
Advantages
  No new infrastructure
  Leverages existing DNS servers
Disadvantages
  Only helps for new connections
  Overheads of updating DNS servers
  Stymied by DNS caching
<number>

## Slide 33: Example #3: Updating the End-Points
Mobile node updates the remote end-point
  Sends the remote end-point the new IP address
  Allowing ongoing connection to continue
  Can be used in conjunction with Dynamic DNS
<number>
1.2.3.4
5.6.7.8
8.9.10.11

## Slide 34: Updating the Edge Switches
Update the switches
  Hosts retain their addresses
  Switches rewrite the addresses, or encapsulate
  Used in some data-center networks
<number>
10.0.0.1
5.6.7.8
8.9.10.11
10.0.0.1
1.2.3.4
10.0.0.2

## Slide 35: Pros and Cons
Advantages
  Scalability of hierarchical addressing
  Efficiency of routing along short paths
Disadvantages
  Changes to the end host (e.g., apps, TCP, etc.)
  … or support from the edge switches
  Difficulty when both end-points move at once
Work in progress
  Used in some data centers, recent standards/projects
<number>

## Slide 36: Mobility Today
<number>
Limited network support for mobility
  E.g., within a single Ethernet subnet
  E.g., among base stations on a campus
Applications increasingly robust to mobility
  Robust to changes in IP address, and disconnections
  E.g., e-mail client contacting the e-mail server
  … and allowing reading/writing while disconnected

## Slide 37: Mobility Tomorrow
<number>
Increasing demand for seamless IP mobility
  E.g., continue a VoIP call while on the train
  E.g., virtual machine migration within and between data centers
Increasing integration of WiFi and cellular
  E.g., multi-homed cell phones that can use both networks
  E.g., servers with multiple interface cards
Need better mobility & multi-homing solutions!

## Slide 38: Conclusions
Mobility
  Change is hard
  Routing and directory solutions
  Mobility is still a moving target… 
Friday’s precept: IP routers and assignment #2
Midterm next week
  Midterm next Wednesday during lecture time
  In Frist 302, not in the lecture hall
<number>