## Slide 1: Middleboxes
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Internet Ideal: Simple Network Model
Globally unique identifiers
  Each node has a unique, fixed IP address
  … reachable from everyone and everywhere
Simple packet forwarding
  Network nodes simply forward packets
  … rather than modifying or filtering them
<number>
source
destination
IP network
Notes: <number>

## Slide 3: Internet Reality
Host mobility
  Host changing address as it moves
IP address depletion
  Multiple hosts using the same address
Security concerns
  Detecting and blocking unwanted traffic
Replicated services
  Load balancing over server replicas
Performance concerns
  Allocating bandwidth, caching content, …
Incremental deployment
  New technology deployed in stages
<number>
Notes: <number>

## Slide 4: Middleboxes
Middleboxes are intermediaries
  Interposed between communicating hosts
  Often without knowledge of one or both parties
Myriad uses
  Address translators
  Firewalls
  Traffic shapers
  Intrusion detection
  Transparent proxies
  Application accelerators
<number>
“An abomination!”
  Violation of layering
  Hard to reason about
  Responsible for subtle bugs
“A practical necessity!”
  Solve real/pressing problems
  Needs not likely to go away
Notes: <number>

## Slide 5: Firewalls
<number>
Notes: <number>

## Slide 6: Firewalls
Firewall filters packet-by-packet, based on:
  Source and destination IP addresses and port numbers
  TCP SYN and ACK bits; ICMP message type
  Deep packet inspection on packet contents (DPI)
<number>
administered
network
public
Internet
firewall
Should arriving packet be allowed in? Departing packet let out?
Notes: <number>

## Slide 7: Packet Filtering Examples
Block all packets with IP protocol field = 17 and with either source or dest port = 23.
  All incoming and outgoing UDP flows blocked
  All Telnet connections are blocked
Block inbound TCP packets with SYN but no ACK
  Prevents external clients from making TCP connections with internal clients
  But allows internal clients to connect to outside
Block all packets with TCP port of Quake
<number>
Notes: <number>

## Slide 8: Firewall Configuration
Firewall applies a set of rules to each packet
  To decide whether to permit or deny the packet
Each rule is a test on the packet
  Comparing IP and TCP/UDP header fields
  … and deciding whether to permit or deny
Order matters
  Once packet matches a rule, the decision is done
<number>
Notes: <number>

## Slide 9: Firewall Configuration Example
Alice runs a network in 222.22.0.0/16
Wants to let Bob’s school access certain hosts
  Bob is on 111.11.0.0/16
  Alice’s special hosts on 222.22.22.0/24
Alice doesn’t trust Trudy, inside Bob’s network
  Trudy is on 111.11.11.0/24
Alice doesn’t want any other Internet traffic
<number>
Notes: <number>

## Slide 10: Firewall Configuration Rules
#1: Don’t let Trudy’s machines in
  Deny (src = 111.11.11.0/24, dst = 222.22.0.0/16)
#2: Let rest of Bob’s network in to special dsts
  Permit (src=111.11.0.0/16, dst = 222.22.22.0/24)
#3: Block the rest of the world
  Deny (src = 0.0.0.0/0, dst = 0.0.0.0/0)
<number>
Notes: <number>

## Slide 11: Stateful Firewall
Stateless firewall:
  Treats each packet independently
Stateful firewall
  Remembers connection-level information
  E.g., client initiating connection with a server
  … allows the server to send return traffic
<number>
SYN
SYN
SYN-ACK
SYN-ACK

## Slide 12: A Variation: Traffic Management
Permit vs. deny is too binary a decision
  Classify the traffic based on rules
  … and handle each class differently
Traffic shaping (rate limiting)
  Limit the amount of bandwidth for certain traffic
Separate queues
  Use rules to group related packets
  And then do weighted fair scheduling across groups
<number>
Notes: <number>

## Slide 13: Clever Users Subvert Firewalls
Example: filtering dorm access to a server
  Firewall rule based on IP addresses of dorms
  … and the server IP address and port number
  Problem: users may log in to another machine
Example: filtering P2P based on port #s
  Firewall rule based on TCP/UDP port numbers
    E.g., allow only port 80 (e.g., Web) traffic
  Problem: software using non-traditional ports
    E.g., write P2P client to use port 80 instead
<number>
Notes: <number>

## Slide 14: Network Address Translation
<number>
Notes: <number>

## Slide 15: History of NATs
IP address space depletion
  Clear in early 90s that 232 addresses not enough
  Work began on a successor to IPv4
In the meantime…
  Share addresses among numerous devices
  … without requiring changes to existing hosts
Meant as a short-term remedy
  Now: NAT is widely deployed, much more than IPv6
<number>
Notes: <number>

## Slide 16: Network Address Translation
138.76.29.7
<number>
NAT
inside
outside
10.0.0.1
10.0.0.2
Problem: Local address not globally addressable
NAT rewrites the IP addresses
  Make “inside” look like single IP addr
  Change header checksums accordingly
  Outbound: Rewrite the src IP addr
  Inbound: Rewrite the dest IP addr
Notes: <number>

## Slide 17: Port-Translating NAT
Two hosts communicate with same destination
  Destination needs to differentiate the two
Map outgoing packets
  Change source address and source port
Maintain a translation table
  Map of (src addr, port #) to (NAT addr, new port #)
Map incoming packets
  Map the destination address/port to the local host
<number>
Notes: <number>

## Slide 18: Network Address Translation Example
<number>
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
138.76.29.7
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345 ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
Notes: <number>

## Slide 19: Maintaining the Mapping Table
Create an entry upon seeing an outgoing packet
  Packet with new (source addr, source port) pair
Eventually, need to delete entries to free up #’s
  When? If no packets arrive before a timeout
  (At risk of disrupting a temporarily idle connection)
Yet another example of “soft state”
  I.e., removing state if not refreshed for a while
<number>
Notes: <number>

## Slide 20: Where is NAT Implemented?
Home router (e.g., Linksys box)
  Integrates router, DHCP server, NAT, etc.
  Use single IP address from the service provider
Campus or corporate network
  NAT at the connection to the Internet
  Share a collection of public IP addresses
  Avoid complexity of renumbering hosts/routers when changing ISP (w/ provider-allocated IP prefix)
<number>
Notes: <number>

## Slide 21: Practical Objections Against NAT
Port #s are meant to identify sockets
  Yet, NAT uses them to identify end hosts
  Makes it hard to run a server behind a NAT
<number>
NAT
10.0.0.1
10.0.0.2
138.76.29.7
Requests to 138.76.29.7 on port 80
Which host should get the request???
Explicit config at NAT for incoming conn’s
Notes: <number>

## Slide 22: Principled Objections Against NAT
Routers are not supposed to look at port #s
  Network layer should care only about IP header
  … and not be looking at the port numbers at all
NAT violates the end-to-end argument
  Network nodes should not modify the packets
IPv6 is a cleaner solution
  Better to migrate than to limp along with a hack
<number>
That’s what happens when network puts power in hands of end users!
Notes: <number>

## Slide 23: Load Balancers
<number>

## Slide 24: Replicated Servers
One site, many servers
  www.youtube.com
<number>

## Slide 25: Load Balancer
Splits load over server replicas
  At the connection level
Apply load balancing policies
<number>
10.0.0.1
10.0.0.2
10.0.0.3
Virtual IP address
12.1.11.3
Dedicated IP addresses

## Slide 26: Wide-Area Accelerators
<number>
Notes: <number>

## Slide 27: At Connection Point to the Internet
Improve end-to-end performance
  Through buffering, compression, caching, …
Incrementally deployable
  No changes to end hosts or the rest of the Internet
<number>
Internet
Appliance
Appliance
Notes: <number>

## Slide 28: Example: Improve TCP Throughput
Appliance with a lot of local memory
Sends ACK packets quickly to the sender
Overwrites receive window with a large value
Or, even run a new and improved version of TCP
<number>
Internet
ACK
Appliance
Appliance
Notes: <number>

## Slide 29: Example: Compression
Compress the packet
Send the compressed packet
Uncompress at the other end
Maybe compress across successive packets
<number>
Internet
Appliance
Appliance
Notes: <number>

## Slide 30: Example: Caching
Cache copies of the outgoing packets
Check for sequences of bytes that match past data
Just send a pointer to the past data
And have the receiving appliance reconstruct
<number>
Internet
Appliance
Appliance
Notes: <number>

## Slide 31: Example: Encryption
Two sites share keys for encrypting traffic
Sending appliance encrypts the data
Receiving appliance decrypts the data
Protects the sites from snoopers on the Internet
<number>
Internet
Appliance
Appliance
Notes: <number>

## Slide 32: Tunneling
<number>
Notes: <number>

## Slide 33: IP Tunneling
IP tunnel is a virtual point-to-point link
  Illusion of a direct link between two nodes
Encapsulation of the packet inside IP datagram
  Node B sends a packet to node E
  … containing another packet as the payload
<number>
A
B
E
F
tunnel
Logical view:
Physical view:
A
B
E
F
Notes: <number>

## Slide 34: 6Bone: Deploying IPv6 over IP4
<number>
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
C
D
IPv4
IPv4
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
A-to-B:
IPv6
E-to-F:
IPv6
B-to-C:
IPv6 inside
IPv4
B-to-C:
IPv6 inside
IPv4
Notes: <number>

## Slide 35: Remote Access Virtual Private Network
Tunnel from user machine to VPN server
  A “link” across the Internet to the local network
Encapsulates packets to/from the user
  Packet from 12.1.1.73 to 12.1.1.100
  Inside a packet from 1.2.3.4 to 12.1.1.1
<number>
Internet
VPN server
12.1.1.0/24
12.1.1.73
1.2.3.4
12.1.1.1

## Slide 36: Conclusions
Middleboxes address important problems
  Getting by with fewer IP addresses
  Blocking unwanted traffic
  Making fair use of network resources
  Improving end-to-end performance
Middleboxes cause problems of their own
  No longer globally unique IP addresses
  Cannot assume network simply delivers packets
<number>
Notes: <number>

## Slide 37: Midterm Exam
10:00-10:50am Wednesday March 14
  In Frist 302 (not the lecture room!)
Open books, notes, slides, etc.
  E-readers okay, but tablets/laptops are not
Covers first five weeks of the course
  Lectures, precepts, readings, and assignments
No precept on Friday
  Enjoy your spring break!
<number>