## Slide 1: Multimedia Streaming
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Digital Audio and Video Data
<number>

## Slide 3: Challenges for Media Streaming
<number>
Large volume of data
  Many sound or image samples per second
Volume of data may vary over time
  Due to compression of the data
Cannot tolerate much delay
  For interactive applications (e.g., VoIP and gaming)
Cannot tolerate much variation in delay
  Once playout starts, need to keep playing
Though some loss is acceptable

## Slide 4: Digital Audio
Sampling the analog signal
  Sample at some fixed rate
  Each sample is an arbitrary real number
Quantizing each sample
  Round each sample to one of a finite # of values
  Represent each sample in a fixed number of bits
<number>
4 bit representation (values 0-15)
Notes: <number>

## Slide 5: Audio Examples
Speech
  Sampling rate: 8000 samples/second
  Sample size: 8 bits per sample
  Rate: 64 kbps
<number>
Compact Disc (CD)
  Sampling rate: 44,100 samples/sec
  Sample size: 16 bits per sample
  Rate: 705.6 kbps for mono, 1.411 Mbps for stereo
Notes: <number>

## Slide 6: Audio Compression
<number>
Audio data requires too much bandwidth
  Speech: 64 kbps is too high for some connections
  Stereo music: 1.411 Mbps exceeds most access rates
Compression to reduce the size
  Remove redundancy, and details user don’t perceive
Example audio formats
  Speech: GSM (13 kbps), G.729 (8 kbps), and G.723.3 (6.4 and 5.3 kbps)
  Stereo music: MPEG 1 layer 3 (MP3) at 96 kbps, 128 kbps, and 160 kbps
Notes: <number>

## Slide 7: Digital Video
<number>
Sampling the analog signal
  Sample images at fixed rate (e.g., 30 times per sec)
Quantizing each sample
  Representing an image as array of picture elements
  Each pixel is a mix of colors (red, green, and blue)
  E.g., 24 bits, with 8 bits per color
Notes: <number>

## Slide 8: Video Compression: Within Image
Image compression
  Exploit spatial redundancy (e.g., regions of same color)
  Exploit aspects humans tend not to notice
Common image compression formats
  Joint Pictures Expert Group (JPEG)
  Graphical Interchange Format (GIF)
<number>
Uncompressed: 167 KB
Good quality: 46 KB
Poor quality: 9 KB
Notes: <number>

## Slide 9: Video Compression: Across Images
Compression across images
  Exploit temporal redundancy across images
Common video compression formats
  MPEG 1: CD-ROM quality video (1.5 Mbps)
  MPEG 2: high-quality DVD video (3-6 Mbps)
<number>
Notes: <number>

## Slide 10: Streaming Over the Internet
<number>

## Slide 11: Transferring Audio and Video Data
Simplest case: just like any other file
  Audio and video data stored in a file
  File downloaded using conventional protocol
  Playback does not overlap with data transfer
A variety of more interesting scenarios
  Live vs. pre-recorded content
  Interactive vs. non-interactive
  Single receiver vs. multiple receivers
<number>
Notes: <number>

## Slide 12: Streaming Stored Audio and Video
Client-server system
  Server stores the audio and video files
  Clients request files, play them as they download, and perform VCR-like functions (e.g., rewind, pause)
Playing data at the right time
  Server divides the data into segments
  … and labels each segment with frame id
Avoiding starvation at the client
  The data must arrive quickly enough
<number>
Notes: <number>

## Slide 13: Playout Buffer
Client buffer
  Store the data as it arrives from the server
  Play data for the user in a continuous fashion
Playout delay
  Client typically waits a few seconds to start playing
  … to allow some data to build up in the buffer
  … to help tolerate some delays down the road
<number>
Notes: <number>

## Slide 14: Influence of Playout Delay
<number>
Notes: <number>

## Slide 15: Requirements for Data Transport
Delay
  Some small delay at the beginning is acceptable
  E.g., start-up delays of a few seconds are okay
Jitter
  Variability of delay within the same packet stream
  Client cannot tolerate high variation if buffer starves
Loss
  Small amount of missing data is not disruptive
  Retransmitting lost packet may take too long anyway
<number>
Notes: <number>

## Slide 16: Streaming From Web Servers
Data stored in a file
  Audio: an audio file
  Video: interleaving of audio and images in a file
HTTP request-response
  TCP connection between client and server
  Client HTTP request and server HTTP response
Client invokes the media player
  Content-type indicates encoding
  Browser launches media player
  Media player renders file
<number>
Notes: <number>

## Slide 17: Initiating Streams from Web Servers
<number>
Avoid passing all data through the Web browser
  Web server returns a meta file describing the object
  Browser launches media player and passes meta file
  Player sets up its own connection to the Web server
Notes: <number>

## Slide 18: Using a Streaming Server
<number>
Avoiding the use of HTTP (and perhaps TCP, too)
  Web server returns a meta file describing the object
  Player requests the data using a different protocol
Notes: <number>

## Slide 19: TCP is Not a Good Fit
Reliable delivery
  Retransmission of lost packets may not be useful
Adapting the sending rate
  Slowing down after loss may cause starve client
Protocol overhead
  20-byte TCP header is large for audio samples
  ACKing every other packet is a lot of overhead
<number>
Notes: <number>

## Slide 20: Better Ways of Transporting Data
User Datagram Protocol (UDP)
  No automatic retransmission of lost packets
  No automatic adaptation of sending rate
  Smaller packet header
UDP leaves many things to the application
  When to transmit the data
  Whether to retransmit lost data
  Whether to adapt the sending rate
  … or adapt quality of the audio/video encoding
<number>
Notes: <number>

## Slide 21: Recovering From Packet Loss
Loss is defined in a broader sense
  Does a packet arrive in time for playback?
  A packet that arrives late is as good as lost
Selective retransmission
  Sometimes retransmission is acceptable
  E.g., if client has not already started playing data
  Data can be retransmitted within time constraint
Could do Forward Error Correction (FEC)
  Send redundant info so receiver can reconstruct
<number>
Notes: <number>

## Slide 22: YouTube: HTTP, TCP, and Flash
Flash videos
  All uploaded videos converted to Flash format
  Nearly every browser has a Flash plug-in
  … avoids need for users to install players
HTTP/TCP
  Implemented in every browser
  Easily gets through most firewalls
Keep It Simple, Stupid
  Simplicity more important than video quality
<number>

## Slide 23: Interactive Audio and Video
<number>
Two or more users interacting
  Telephone call, video conference, video game
Strict delay constraints
  Delays over 150-200 msec are very noticeable
  … delays over 400 msec are a disaster for voice
Much harder than streaming applications
  Receiver cannot introduce much playout delay
  Difficult if network doesn’t guarantee performance
Notes: <number>

## Slide 24: Quality of Interactive Applications
<number>
The application can help
  Good audio compression algorithms
  Forward error correction
  Adaptation to the available bandwidth
But, ultimately the network is a major factor
  Long propagation delay?
  High congestion?
  Disruptions during routing changes?
Notes: <number>

## Slide 25: Multicast
<number>

## Slide 26: Multicast
Many receivers
  Receiving the same content
Applications
  Video conferencing
  Online gaming
  IP television (IPTV)
  Financial data feeds
<number>

## Slide 27: Iterated Unicast
Unicast message to each recipient
Advantages
  Simple to implement
  No modifications to network
Disadvantages
  High overhead on sender
  Redundant packets on links
  Sender must maintain list of receivers
<number>

## Slide 28: IP Multicast
Embed receiver-driven tree in network layer
  Sender sends a single packet to the group
  Receivers “join” and “leave” the tree
Advantages
  Low overhead on the sender
  Avoids redundant network traffic
Disadvantages
  Control-plane protocols for multicast groups
  Overhead of duplicating packets in the routers
<number>

## Slide 29: Multicast Tree
<number>
A
B
G
D
E
c
F

## Slide 30: Single vs. Multiple Senders
Source-based tree
  Separate tree for each sender
  Tree is optimized for that sender
  But, requires multiple trees for multiple senders
Shared tree
  One common tree
  Spanning tree that reaches all participants
  Single tree may be inefficient
  But, avoids having many different trees
<number>

## Slide 31: Multicast Addresses
Multicast “group” defined by IP address
  Multicast addresses look like unicast addresses
  224.0.0.0 to 239.255.255.255
Using multicast IP addresses
  Sender sends to the IP address
  Receivers join the group based on IP address
  Network sends packets along the tree
<number>

## Slide 32: Example Multicast Protocol
Receiver sends a “join” messages to the sender
  And grafts to the tree at the nearest point
<number>
A
B
G
D
E
c
F

## Slide 33: IP Multicast is Best Effort
Sender sends packet to IP multicast address
  Loss may affect multiple receivers
<number>
A
B
G
D
E
c
F

## Slide 34: Challenges for Reliable Multicast
Send an ACK, much like TCP?
  ACK-implosion if all destinations ACK at once
  Source does not know # of destinations
How to retransmit?
  To all? One bad link effects entire group
  Only where losses? Loss near sender makes retransmission as inefficient as replicated unicast
Negative acknowledgments more common
<number>

## Slide 35: Scalable Reliable Multicast
Data packets sent via IP multicast
  Data includes sequence numbers
Upon packet failure
  If failures relatively rare, use Negative ACKs (NAKs) instead: “Did not receive expected packet”
  Sender issues heartbeats if no real traffic. Receiver knows when to expect (and thus NAK)
<number>
Notes: <number>

## Slide 36: Handling Failure in SRM
Receiver multicasts a NAK
  Or send NAK to sender, who multicasts confirmation
Scale through NAK suppression
  If received a NAK or NCF, don’t NAK yourself
  Add random delays before NAK’ing
Repair through packet retransmission
  From initial sender
  From designated local repairer
<number>
Notes: <number>

## Slide 37: Conclusions
<number>
Digital audio and video
  Increasingly popular media on the Internet
  Video on demand, VoIP, online gaming, IPTV…
Many challenges
  Best-effort network vs. real-time applications
  Unicast routing vs. multi-party applications
Friday’s precept
  Hashing and partitioning to balance load
Notes: <number>