## Slide 1: Enterprise Networks
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Networking Case Studies
<number>
Data Center
Backbone
Enterprise
Cellular
Wireless

## Slide 3: Simple Enterprise Design
Single layer-two subnet
  Hubs and switches
  Gateway to the Internet
  Single IP address block
Local services
  DHCP
  DNS
<number>
S
S
S
G
S
DHCP server
DNS server
1.2.3.1
1.2.3.76
1.2.3.5
1.2.3.150
Internet
1.2.3.0/24
0.0.0.0/0

## Slide 4: Limitations of Simple Design
Ethernet scalability and performance
Single ISP reliability and performance
Limited IP address space
Unwanted Internet traffic
Privacy and isolation within the enterprise
Detecting and preventing bad behavior from inside
<number>
S
S
S
G
S
DHCP server
DNS server
1.2.3.1
1.2.3.76
1.2.3.5
1.2.3.150
Internet
1.2.3.0/24
0.0.0.0/0

## Slide 5: Beyond Ethernet Switching
<number>

## Slide 6: Scalability Limitations of Ethernet
Spanning tree
  Paths that are longer than necessary
  Bandwidth wasted for links not in the tree
Forwarding tables
  Bridge tables grow with number of hosts
Broadcast traffic
  ARP, DHCP, and broadcast applications
Flooding
  Frames sent to unknown destinations
<number>

## Slide 7: Hybrid of Switches and Routers
<number>
R
R
R
R
Ethernet Bridging
- Flat addressing
- Self-learning
- Flooding - Forwarding along a tree
IP Routing
- Hierarchical addressing
- Subnet configuration
- Host configuration
- Forwarding along shortest paths
R
1.2.3.192/26
1.2.3.128/26
1.2.3.0/26
1.2.3.64/26
Internet

## Slide 8: Limitations of Hybrid Design
No plug-and-play and mobility between subnets
Need consistency between IP addressing & routing
<number>
R
R
R
R
R
1.2.3.192/26
1.2.3.128/26
1.2.3.0/26
1.2.3.64/26
Internet

## Slide 9: Virtual Local Area Networks
<number>

## Slide 10: Early Days of Ethernet LANs
Thick cables snaked through cable ducts
  Every computer they passed was plugged in
All people in adjacent offices on the same LAN
  Whether they belonged together or not
Users grouped based on physical layout
  Rather than organizational structure
Security, privacy, and scalability limitations…
<number>
Notes: <number>

## Slide 11: Today’s Ethernet LANs
Changes introduced by hubs and switches
  Every office connected to central wiring closets
  Often multiple LANs (k hubs) connected by switches
  Flexibility in mapping offices to different LANs
Can group by organizational structure
  Better privacy: snooping in promiscuous mode
  Separate IP addresses: one IP subnet per LAN
  Better security: access control at IP routers
  Better load management: isolate broadcast/flooding
<number>
Notes: <number>

## Slide 12: People Move, and Roles Change
<number>
Organizational changes are frequent
  E.g., faculty office becomes a grad-student office
  E.g., graduate student becomes a faculty member
Physical rewiring is a major pain
  Requires unplugging the cable from one port
  … and plugging it into another
  … and hoping the cable is long enough to reach
Would like to “rewire” the building in software
  The resulting concept is a Virtual LAN (VLAN)
Notes: <number>

## Slide 13: Example: Two Virtual LANs
<number>
Red VLAN and Orange VLAN
Switches forward traffic as needed
R
O
RO
R
R
R
O
O
O
R
O
R
R
R
O
O
O
Notes: <number>

## Slide 14: Making VLANs Work
<number>
Changing the Ethernet header
  Adding a field for a VLAN tag
  Implemented on the bridges/switches
  … but can still interoperate with old Ethernet cards
Bridges/switches trunk links
  Saying which VLANs are accessible via which interfaces
Approaches to mapping access links to VLANs
  Each interface has a VLAN color
  Each MAC address has a VLAN color
Notes: <number>

## Slide 15: Uses of VLANs (See the Survey Paper)
Scoping broadcast traffic
Simplifying access control policies
Decentralizing network management
Enabling host mobility
<number>

## Slide 16: Problem: Limited Granularity
Limited number of VLANs
  Placing multiple groups in the same VLAN
  Reusing limited VLAN
Limited number of hosts per VLAN
  Divide a large group into multiple VLANs
One VLAN per access port
  Supporting VLANs on the end host
  Supporting multiple groups at the router
<number>

## Slide 17: Problem: Complex Configuration
Host address assignment
  Wasting IP addresses
  Complex host address assignment
Spanning tree computation
  Limitation of automated trunk configuration
  Enabling extra links to survive failures
  Distributing load over the root bridges
<number>
Open question: can we do better than VLANs?

## Slide 18: Multiple Internet Connections
<number>

## Slide 19: Motivation for Multi-Homing
Benefits of multi-homing
  Extra reliability, e.g., survive single ISP failure
  Financial leverage through competition
  Better performance by selecting better path
  Gaming the 95th-percentile billing model
<number>
ISP 1
ISP 2
1.2.3.0/24

## Slide 20: Multi-Homing Without BGP
Inbound Traffic
Ask each ISP to originate the IP prefix
… to rest of the Internet
Outbound Traffic
One ISP as a primary, the other as a backup
Or simple load balancing of all traffic
<number>
ISP 1
ISP 2
1.2.3.0/24

## Slide 21: Multi-Homing With BGP
Inbound traffic
  Originate the prefix to both providers
  Do not allow traffic from one ISP to another
Outbound traffic
  Select the “best” route for each remote prefix
  Define BGP policies based on load, performance, cost
<number>
ISP 1
ISP 2
1.2.3.0/24
BGP sessions
“Intelligent route control” or “multi-homed traffic engineering”.

## Slide 22: Interconnecting Multiple Enterprise Sites
<number>

## Slide 23: Challenges
Challenges of interconnecting multiple sites
  Performance
  Reliability
  Security
  Privacy
Solutions
  Connecting via the Internet using secure tunnels
  Virtual Private Network (VPN) service
  Dedicated backbone between sites
<number>

## Slide 24: Connecting Via the Internet
Each site connects to the Internet
  Encrypted tunnel between each pair of sites
  Packet filtering to block unwanted traffic
  But, no performance or reliability guarantees
<number>
Internet
Site 2
Site 3
Site 1

## Slide 25: Virtual Private Network (VPN)
Each site connects to a common VPN provider
  Provider allows each site to announce IP prefixes
  Separate routing/forwarding table for each customer
  Performance guarantees
<number>
VPN Provider
Site 2
Site 3
Site 1

## Slide 26: Middleboxes
<number>

## Slide 27: Enterprise Internet Connection
Multiple middleboxes
  Intrusion prevention system
  Network address translator
  Firewall
  Traffic shaper
Handling bad internal users
  Filtering IP packets with spoofed source IP addresses
  Logging which MAC address has each IP address
<number>
Internet
R
M
M
M
link

## Slide 28: Internal Middleboxes
Network divided into regions
  E.g., departments within a campus
  E.g., public computers (servers, WiFi) vs. private
Network divided by roles
  E.g., human resources vs. engineering
  E.g., faculty vs. students
Sometimes physically separate networks
  E.g., ATM machines, campus safety, media streaming
<number>

## Slide 29: Princeton Campus Network
http://www.net.princeton.edu/index.html
http://www.net.princeton.edu/statistics/
http://www.net.princeton.edu/whatsnew.html
<number>

## Slide 30: Internet Connections
Two commercial ISPs: Comcast and WindStream
Two research networks: ESnet and Internet2
Non-profits: McCarter Theater, Princeton Public Library, and Princeton Regional Schools
<number>
vgate1
WindStream
(full routes)
1 Gbps
Comcast
(full routes)
1 Gbps
Princeton Campus
1 Gbps
ESnet
1 Gbps
MAGPI/Internet2

## Slide 31: Princeton Public Internet Traffic
Traffic volumes over the past week
  Green: traffic from the Internet
  Blue: traffic to the Internet
<number>

## Slide 32: Three Internal Networks
Campus Data Network
  Connects dorms, academic and administrative buildings, campus WiFi, etc.
Princeton Private Network
  Environmental systems, power, security cameras, building locks
VoIP Network
  VoIP phones in data center, chemistry, neuroscience, Forrestal campus, and all new construction
  Separate for disaster recovery & traffic management
<number>

## Slide 33: Campus Data Network
<number>
vgate1
gigasw4
gigasw2
gigagate1
Internet
Dormnet
Applications
Data Center
Academic,
administrative
RIP
routing

## Slide 34: Data Center (Forrestal Campus)
40,000 square feet with 1800 computers
Multiple tiers of backup power
Minimizes energy for cooling and power
<number>

## Slide 35: Virtual Private Network (VPN)
Online campus resources
  E.g., some Princeton University library resources
  Not available from outside of campus
External resources with Princeton subscription
  E.g., digital libraries from ACM and IEEE
  Accessible from a Princeton IP address
Princeton VPN service (vpn.princeton.edu)
  Secure network connection layered over IP network
  … connects you to an internal Princeton machine
<number>

## Slide 36: Aruba WiFi Access Points
Adaptive radio management
  Automatically assigns channel and power settings
  Channel load balancing to distribute clients
  Coverage hole detection
<number>

## Slide 37: WiFi Anecdote (puwireless)
Single large VLAN
  Enabling seamless mobility on campus
Limited address space
  16K or 32K IP addresses
  3 hour DHCP leases
Frequently a large number of users
  Several thousand to up to 10,000
  … may soon run low on IP addresses
<number>

## Slide 38: WiFi Anecdote (puwireless), Continued
Bug in Android and IOS smart phones
  Don’t release DHCP lease on IP addresses
  Offloads ARP processing to the chipset, to avoid waking up sleeping device on ARP requests
  … but DHCP timeout is handled by the processor
So, can have IP address collisions
  DHCP lease expires, but the phone doesn’t know
  DHCP server gives the IP address to someone else
  … and both devices respond to ARP requests!
<number>
http://www.net.princeton.edu/android/android-stops-renewing-lease-keeps-using-IP-address-11236.html

## Slide 39: WiFi Anecdote (puwireless), Continued
Working with Google and Apple on the problem
Longer-term solution
  Move to larger, private address block (10.0.0.0/8)
  Use network address translation (NAT) to communicate with the public Internet
Benefits
  Avoids running out of IP addresses
  Introduces long delay before reusing an address
  Seems like a good solution, right?
<number>

## Slide 40: WiFi Anecdote (puwireless), Continued
Solution makes troubleshooting harder
  Public IP addresses shared by many users
  … due to network address translation
Example: DMCA violations
  Student downloads copyrighted material on WiFi
  Company comes to Princeton to complain
Given IP address, can OIT identify the student?
  With NAT, cannot pinpoint a unique MAC address
  … without much more detailed (flow-level) logs
<number>

## Slide 41: Conclusions
Enterprise networks
  Campuses and companies
  Access to local services and the Internet
Challenges
  IP address limitations
  Hybrid switch and routed network
  Load balancing over upstream ISPs
  Protecting users and the Internet from each other
Next time: data-center networks
<number>