## Slide 1: Backbone Networks
Jennifer Rexford
COS 461: Computer Networks
Lectures: MW 10-10:50am in Architecture N101
http://www.cs.princeton.edu/courses/archive/spr12/cos461/
Notes: <number>

## Slide 2: Networking Case Studies
<number>
Data Center
Backbone
Enterprise
Cellular
Wireless

## Slide 3: Backbone Topology
<number>

## Slide 4: Backbone Networks
Backbone networks
  Multiple Points-of-Presence (PoPs)
  Lots of communication between PoPs
  Accommodate traffic demands and limit delay
<number>
Notes: <number>

## Slide 5: Abilene Internet2 Backbone
<number>
Notes: <number>

## Slide 6: Points-of-Presence (PoPs)
Inter-PoP links
  Long distances
  High bandwidth
Intra-PoP links
  Short cables between racks or floors
  Aggregated bandwidth
Links to other networks
  Wide range of media and bandwidth
<number>
Intra-PoP
Other networks
Inter-PoP
Notes: <number>

## Slide 7: Where to Locate Nodes and Links
Placing Points-of-Presence (PoPs)
  Large population of potential customers
  Other providers or exchange points
  Cost and availability of real-estate
  Mostly in major metropolitan areas (“NFL cities”)
Placing links between PoPs
  Already fiber in the ground
  Needed to limit propagation delay
  Needed to handle the traffic load
<number>
Notes: <number>

## Slide 8: Peering
<number>
Exchange traffic between customers
  Settlement-free
Diverse peering locations
  Both coasts, and middle
Comparable capacity at all peering points
  Can handle even load
Customer A
Customer B
multiple
peering
points
Provider A
Provider B
Notes: <number>

## Slide 9: Combining Intradomain and Interdomain Routing
<number>

## Slide 10: Intradomain Routing
Compute shortest paths between routers
  Router C takes path C-F-A to router A
Using link-state routing protocols
  E.g., OSPF, IS-IS
<number>
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B

## Slide 11: Interdomain Routing
Learn paths to remote destinations
  AT&T learns two paths to Yale
Applies local policies to select a best route
<number>
AT&T
Sprint
Yale
Tier-2
Tier-3

## Slide 12: An AS is Not a Single Node
Multiple routers in an AS
  Need to distribute BGP information within the AS
  Internal BGP (iBGP) sessions between routers
<number>
AS1
AS2
eBGP
iBGP
Notes: <number>

## Slide 13: Internal BGP and Local Preference
<number>
Both routers prefer path through AS 100
… even though right router learns external path
I-BGP
AS 256
AS 300
Local Pref = 100
Local Pref = 90
AS 100
AS 200
Notes: <number>

## Slide 14: Hot-Potato (Early-Exit) Routing
<number>
Hot-potato routing
  Each router selects the closest egress point
  … based on the path cost in intradomain protocol
BGP decision process
  Highest local preference
  Shortest AS path
  Closest egress point
  Arbitrary tie break
hot potato
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dst
Notes: <number>

## Slide 15: Hot-Potato Routing
Selfish routing
  Each provider dumps traffic on the other
  As early as possible
Asymmetric routing
  Traffic does not flow on the same path in both directions
Customer A
Customer B
multiple
peering
points
Provider A
Provider B
Early-exit
routing
Notes: <number>

## Slide 16: Joining BGP and IGP Information
<number>
Border Gateway Protocol (BGP)
  Announces reachability to external destinations
  Maps a destination prefix to an egress point
    128.112.0.0/16 reached via 192.0.2.1
192.0.2.1
10.1.1.1
Notes: <number>

## Slide 17: Joining BGP and IGP Information
<number>
Interior Gateway Protocol (IGP)
  Used to compute paths within the AS
  Maps an egress point to an outgoing link
    192.0.2.1 reached via 10.1.1.1
192.0.2.1
10.1.1.1
Notes: <number>

## Slide 18: Joining BGP with IGP Information
<number>
IGP
AS 7018
AS 88
192.0.2.1
128.112.0.0/16
10.10.10.10
BGP
192.0.2.1
128.112.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
128.112.0.0/16
Next Hop = 192.0.2.1
+
Forwarding Table
128.112.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
10.10.10.10
Notes: <number>

## Slide 19: Interdomain Routing Policy
<number>

## Slide 20: Selecting a Best Path
Routing Information Base
  Store all BGP routes for each destination prefix
  Withdrawal: remove the route entry
  Announcement: update the route entry
BGP decision process
  Highest local preference
  Shortest AS path
  Closest egress point
  Arbitrary tie break
<number>

## Slide 21: Import Policy: Local Preference
Favor one path over another
  Override the influence of AS path length
Example: prefer customer over peer
AT&T
Sprint
Yale
Tier-2
Tier-3
Local-pref = 100
Local-pref = 90
Notes: <number>

## Slide 22: Import Policy: Filtering
Discard some route announcements
  Detect configuration mistakes and attacks
Examples on session to a customer
  Discard route if prefix not owned by the customer
  Discard route with other large ISP in the AS path
AT&T
Princeton
USLEC
128.112.0.0/16
Notes: <number>

## Slide 23: Export Policy: Filtering
Discard some route announcements
  Limit propagation of routing information
Examples
  Don’t announce routes from one peer to another
  Don’t announce routes for management hosts
AT&T
Princeton
Sprint
128.112.0.0/16
UUNET
network operator
Notes: <number>

## Slide 24: Export Policy: Attribute Manipulation
Modify attributes of the active route
  To influence the way other ASes behave
Example: AS prepending
  Artificially inflate AS path length seen by others
  Convince some ASes to send traffic another way
AT&T
Princeton
USLEC
128.112.0.0/16
Sprint
88 88
88
Notes: <number>

## Slide 25: Business Relationships
Common relationships
  Customer-provider
  Peer-peer
  Backup, sibling, …
Implementing in BGP
  Import policy
    Ranking customer routes over peer routes
  Export policy
    Export only customer routes to peers and providers
Notes: <number>

## Slide 26: BGP Policy Configuration
Routing policy languages are vendor-specific
  Not part of the BGP protocol specification
  Different languages for Cisco, Juniper, etc.
Still, all languages have some key features
  List of clauses matching on route attributes
  … and discarding or modifying the matching routes
Configuration done by human operators
  Implementing the policies of their AS
  Business relationships, traffic engineering, security
Notes: <number>

## Slide 27: Backbone Traffic Engineering
<number>

## Slide 28: Routing With “Static” Link Weights
Routers flood information to learn topology
  Determine “next hop” to reach other routers…
  Compute shortest paths based on link weights
Link weights configured by network operator
<number>
3
2
2
1
1
3
1
4
5
3

## Slide 29: Setting the Link Weights
How to set the weights
  Inversely proportional to link capacity?
  Proportional to propagation delay?
  Network-wide optimization based on traffic?
<number>
3
2
2
1
1
3
1
4
5
3
3

## Slide 30: Measure, Model, and Control
<number>
Topology/
Configuration
Offered
traffic
Changes to
the network
Operational network
Network-wide
“what if” model
measure
control

## Slide 31: Limitations of Shortest-Path Routing
Sub-optimal traffic engineering
  Restricted to paths expressible as link weights
Limited use of multiple paths
  Only equal-cost multi-path, with even splitting
Disruptions when changing the link weights
  Transient packet loss and delay, and out-of-order
Slow adaptation to congestion
  Network-wide re-optimization and configuration
Overhead of the management system
<number>

## Slide 32: Constrained Shortest Path First
Run a link-state routing protocol
  Configurable link weights
  Plus other metrics like available bandwidth
Constrained shortest-path computation
  Prune unwanted links (e.g., not enough bandwidth)
  Compute shortest path on the remaining graph
<number>
s
d
5, bw=10
6, bw=60
5
bw=70
3,
bw=80

## Slide 33: Constrained Shortest Path First
Signal along the path
  Source router sends a message to pin the path to destination
  Revisit decisions periodically, in case better options exist
<number>
s
d
5, bw=10
6, bw=60
5, bw=70
3, bw=80
1
2
1: 7: 20
2: 7: 53
link 7
20: 14: 78
53: 8: 42
link 14
link 8

## Slide 34: Challenges for Backbone Networks
<number>

## Slide 35: Challenges
Routing protocol scalability
  Thousands of routers
  Hundreds of thousands of address blocks
Fast failover
  Slow convergence disrupts user performance
  Backup paths for faster recovery
  E.g., backup path around a failed link
<number>

## Slide 36: Challenges
Router configuration
  Adding customers, planned maintenance, traffic engineering, access control, …
  Manual configuration is very error prone
Measurement
  Measuring traffic, performance, routing, etc.
  To detect attacks, outages, and anomalies
  To drive traffic-engineering decisions
<number>

## Slide 37: Challenges
Diagnosing performance problems
  Incomplete control and visibility
  Combining measurement data
Security
  Defensive packet and route filtering
  Detecting and blocking denial-of-service attacks
  DNS security, detecting and blocking spam, etc.
New services
  IPv6, IPTV, …
<number>

## Slide 38: Conclusions
Backbone networks
  Transit service for customers
  Glue that holds the Internet together
Routing challenges
  Interdomain routing policy
  Intradomain traffic engineering
Next time
  Cellular data networks (guest lecture)
<number>