## Slide 1: Precept 3
Host Configuration
<number>
Peng Sun
Notes: play with your computer. see network statistics on the host machine
<number>

## Slide 2: What TCP conn. running?
Commands
  netstat [-n] [-p] [-c] (Linux)
  lsof -i -P (Mac)
  ss (newer version of netstat)
Demo
  iperf: TCP-based throughput test tool
<number>
Notes: What tcp connections are running on your host?
netstat : linux, Mac, and windows. options will be slightly different across platforms.
Linux: -p: show process, -n: numeric, -c: continuous
Mac: -p doesn’t work. If you want to see which process opens which tcp connections
Small demo: emulab machines running iperf: show iperf’s TCP connection.
run iperf server on node1
run iperf client on node0
netstat -npc
<number>

## Slide 3: Demo
<number>
node0
node1
node2
10.1.1.2
10.1.1.3
10.1.2.3
10.1.2.2
node1:~>
netstat -npc
node0:~>
netstat -npc
node0:~>
iperf –c 10.1.1.3
node1:~> iperf -s

## Slide 4: Play with IP Layer
ifconfig
  show all the network interfaces
  configure IP
  configure MAC (!)
route
  show local IP routing table
  set routes: add/del
<number>
Notes: ifconfig demo:
http://linux-ip.net/html/basic-changing.html
show interface: ifconfig
change IP: ifconfig ethX down; ifconfig ethX newIP netmask 255.255.255.0 up; ifconfig;
change MAC: ifconfig ethX down; ifconfig ethX newIP hw ether 00:00:00:00:00:01 up; ifconfig;
route demo:
route –n : show IP routing table
add routes:
sudo route add -net 10.1.2.0 netmask 255.255.255.0 gw 10.1.1.3
delete routes
sudo route del –net 10.1.2.0 netmask 255.255.255.0
setup routing manually: node0 contact node2 through node1. install rules on node1.
sudo route add –net 10.1.2.0 netmask 255.255.255.0 gw 10.1.1.3 on node0
sudo route add –net 10.1.1.0 netmask 255.255.255.0 gw 10.1.2.2 on node2
Then it should ping
<number>

## Slide 5: Demo
<number>
node0
node1
node2
10.1.1.2
10.1.1.3
10.1.2.3
10.1.2.2
node0:~>
ping 10.1.2.2
node0:~> route add
-net 10.1.2.0
netmask 255.255.255.0
gw 10.1.1.3
node2:~> route add
-net 10.1.1.0
netmask 255.255.255.0
gw 10.1.2.3
connected
?
Notes: we don’t know how to reach node2
so we install a routing rule on node0. Traffic for 10.1.2.0/24 will go through node1
node1 will forward to node2.
But node2 don’t know how to reply, either.
So we need to install another rule on node2. So they can reach each other.
<number>

## Slide 6: traceroute
Why we need traceroute?
  No global information
  Want to know the forwarding path
Based on ICMP
  Internet Control Message Protocol
  Used to signal error
Adjust Time-To-Live for each hop
  When timeout, ICMP returns the IP where TTL expires.
<number>
Notes: Demo first. On own computer. traceroute www.cnn.com. explain what shows up.
show demo first. No global info. Mention more about TTL. not too long in air.
explain why traceroute is for.
nobody knows the actual path. We need to make it this way. Why?
Where it expires returns its own IP address
<number>

## Slide 7: traceroute
<number>
Server
User
ICMP TTL=1
Timeout at Rt. 1
ICMP TTL=2
Timeout at Rt. 2
ICMP TTL=3
Reply from Server
Router 1
Router 2
Notes: show demo first. No global info. Mention more about TTL. not too long in air.
explain why traceroute is for.
nobody knows the actual path. We need to make it this way. Why?
Where it expires returns its own IP address
<number>

## Slide 8
<number>
New Guy
Internet
Old Guy 1
Old Guy 2
Gateway
DHCP
I want an IP
Return IP & Gateway IP
1
2
3
3
3
If same subnet (e.g. OG1):
3. Broadcast ARP request
4. OG1 Reply ARP
5. NG caches OG1’s MAC
4
4
If outside world:
6. Send to Gateway
6
6
Notes: How your computer is connected to the world.
If in the same subnet, directly use Ethernet (MAC) to communicate
If for outside world, send to gateway
Demo:
show the empty arp table on each node
ping from one to another. show the update
<number>

## Slide 9: ARP
ARP table (cache)
1. Look up local ARP table
2. If not, broadcast to ask
3. LAN switch caches ARP to port
<number>
Notes: <number>

## Slide 10: ARP Spoofing
No protection from ARP itself
Rely on other mechanism
  Static ARP entry (perfect security. High cost of maintenance)
  Spoofing detection software
Legitimate usage
  Hotel
  Redundancy of service (takeover of bad server)
<number>
Notes: ARP spoofing
Legitimate usage:
sign up page
pretend to be the dead server, so user has seamless experience.
<number>

## Slide 11: Wireshark
http://www.wireshark.org/
Packet Capture & Analysis
  Live capture
Critical for Debug in Assign. 2
Filter
  e.g., ip / (not) arp / tcp / etc.
<number>
Notes: Start wireshark on your own laptop
close wifi
start live capture
start wifi
show the lively captured packets
<number>