## Slide 1: Ad Hoc Wireless Routing
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr14/cos461/

## Slide 2: Outline
What are Ad Hoc Networks?
Assumptions and Challenges for Routing
Four Routing Protocols: DSDV, TORA, AODV, and DSR
How well do these protocols perform?
Reference for this lecture: J. Broch, et al. “A Performance Comparison of Multi-Hop Wireless Ad Hoc Network Routing Protocols”, MOBICOMM 1998: 85-97

## Slide 3: Ad Hoc Wireless Network
Infrastructureless: No centralized administration
Nodes move freely within and out of network
Nodes act as hosts and routers
A
B
A->B?

## Slide 4: Assumptions
802.11 MAC with Distributed Coordination Function (DCF)
Physical carrier sensing
Virtual carrier sensing (RTS/CTS)
Link breakage detection
Address Resolution: ARP
Broadcasting requests and managing replies
harder in this environment.

## Slide 5: Challenges for Routing
Dynamic topology
Node mobility
Transmission ranges
Node routing preferences
A
B
C

## Slide 6: Challenges for Routing
Broadcast packets not work as well
No RTS/CTS exchanged
Collisions account for loss
Use random back-off to avoid synchronization

## Slide 7: Challenges for Routing
Managing Queues
For ARP, pace packets sent to ARP queue or
have the space to buffer many packets awaiting
ARP reply.
For transmitting packets, prioritize routing
packets in queue followed by ARP and data.

## Slide 8: Overview of Protocols
Bellman Ford variants: DSDV, AODV
DSDV – avoids loops and count-to-infinity
AODV - on-demand, no periodic updates
Link Reversal: TORA
Loop-free, quick routes, localize changes
Source Path: DSR
Packets route themselves; minimize route
advertisements and neighbor detection

## Slide 9: Destination-Sequenced Distance Vector (DSDV)
Bellman-Ford variant
Each node keeps routing table with next hop to each destination with metric and destination sequence number (SN).
A route with greater SN is chosen.

## Slide 10: DSDV
If two routes have equal SN, then lower metric route is chosen.
Each node maintains its own increasing even SN.
Updates broadcast periodically and upon SN, metric, or topological changes.

## Slide 11: DSDV
When topological change discovered:
v
y
x
z
7
1
1
1
V advertised route to Z of cost 2, SN=102
If V thinks route to Z broken, V advertises route to Z of infinite cost, SN = 103
X would put infinite metric route in routing table until it gets update from Z with SN > 103

## Slide 12: Temporally-Ordered Routing Algorithm (TORA)
“Link Reversal Algorithm” – discovers and maintains multiple routes to destination on demand and quickly
Shortest path not as important

## Slide 13: TORA
Route traffic towards desired destination.
If a node becomes blocked, pass traffic to its neighbors by setting its height greater than its neighbors.

## Slide 14: TORA
A needs a route to B
A
B
A will broadcast a QUERY packet, dest=B
B or node with route to B will broadcast UPDATE packet with height from B
In this case Z will broadcast UPDATE packet with height of 1 to B
Z

## Slide 15: TORA
A needs a route to B
A
B
Z broadcasts update creating directed link between itself and B.
All nodes receiving UPDATE packets set height to B to be greater than in received update.
Nodes broadcast UPDATE to source of QUERY
UPDATEs create directed links from A to Z and a directed acyclic graph, DAG, with B as sink
Z
U,3
U,2
U,4
U,1
U,1

## Slide 16: TORA
If route to destination no longer valid, nodes will set height to maximum value of its neighbors and UPDATE.
If no new route is found, node will send CLEAR packet to remove invalid routes.
Internet MANET Encapsulation Protocol (IMEP): for routing control messages and notification for broken/created links (BEACON/HELLO)

## Slide 17: Dynamic Source Routing (DSR)
Source based: Packet headers contain complete route of nodes to traverse in order.
Within DSR source route option
header in IP payload, before data:
IP address of X
IP address of Z
IP address of Y
IP address of B
A
Y
X
Z
B

## Slide 18: DSR Route Discovery
A needs a route to B
A broadcasts a ROUTE REQUEST, packet, dest=B using hop limit to limit propagation
If hop limit = 0, neighbor replies with ROUTE REPLY if it is B or has route to B
If no neighbor replies, A will send another request with greater hop limit to propagate the request.
In this example, X replies with a ROUTE REPLY to A.
A
Y
X
Z
B

## Slide 19: DSR Route Maintenance
Caching
Nodes maintain cache of routes from route discovery and eavesdropping.
Nodes will return ROUTE REPLY if cache contains shorter path.
If forwarding packets and route broken, node will attempt to fix broken path from cache and retransmit before dropping.

## Slide 20: DSR Route Maintenance
ROUTE ERROR packets: A sending data to B
A
Y
X
Z
B
A unicasts data to B on path discovered
Y discovers link to B is broken.
Y unicasts ROUTE ERROR packet to Z.
ROUTE ERROR packets indicate broken link.
ROUTE ERROR packets are propagated back to A.
Each node receiving ROUTE ERROR packet removes routes using the Y<->B link from its cache.

## Slide 21: Ad Hoc On-Demand Distance Vector (AODV)
Bellman Ford variant like DSDV uses SN
Like DSR, on demand route discovery: A->B
A
Y
X
Z
B
A broadcast ROUTE REQUEST, dest=B, SN=102
X and C broadcast forward the REQUEST and create reverse route to A
Z has a route to B of 1 hop and SN = 104.
C

## Slide 22: AODV
Route Discovery: A->B
A
Y
X
Z
B
4. Z will unicast ROUTE REPLY on the reverse route.
5. This creates the forward route for data.
6. A will accept route since it has greater SN.
REP
REP

## Slide 23: AODV Route Maintenance
No cache and no full routes
Only routing table entries for reverse path and forward path next hops
Routing table entries have timeouts

## Slide 24: AODV Link Detection
Periodic HELLO messages for maintaining neighbors
If don’t hear from neighbor in 3s, assume broken link

## Slide 25: AODV Broken Link
UNSOLICITED ROUTE REPLY
A
Y
X
Z
B
Upon discovering Z->B link is down, Z sends an UNSOLICITED ROUTE REPLY with infinite metric to all nodes that used the forward path.
REP
REP

## Slide 26: Performance?
Depends on the metric
Packet delivery ratio: ratio of packets sent/packets received between application layers
Routing overhead: total number of routing packets sent
Path optimality: how close to shortest path
Depends on how quickly the topology of network is changing

## Slide 27: Packet Delivery Ratio
Assume same number of nodes and constant mobility. Rank the algorithms from best to worst packet delivery ratio:
DSDV 4
TORA 3
DSR 1
AODV 2

## Slide 28: Routing Overhead
Assume same number of nodes and constant mobility. Rank the algorithms from best to worst routing overhead:
DSDV 2
TORA 4
DSR 1
AODV 3

## Slide 29: Path Optimality
Assume same number of nodes and constant mobility.
Which two algorithms have best path optimality?
DSDV, DSR
Which two algorithms have the worst?
TORA, AODV