## Slide 1: Link Layer I: ALOHA, Time-, Frequency-, and Code Division
COS 463: Wireless Networks
Lecture 4
Kyle Jamieson

## Slide 2: Review: The Data Link Layer (L2)
Enables exchange of atomic messages (frames) between end hosts
Determine start and end of bits and frames (framing)
Deliver information reliably
Control errors
Some link layers involve a shared medium
  e.g., Shared-wire Ethernet, satellite uplink, Wi-Fi
  Today: Medium access control to share the medium

## Slide 3: Medium access: The Problem
Two questions:
  How should the shared medium be divided?
  Who gets to talk on a shared medium, and when?
A medium access control (MAC) protocol specifies the above

## Slide 4: Medium access: Goals
Efficiency
  High throughput (bits/second successfully received through the channel)
    i.e. high utilization (throughput/raw channel rate)
Fairness: All hosts with data to send should get a roughly equal share of the medium over time
Latency: Want to minimize the time a host waits before being granted permission to talk on the shared medium

## Slide 5: Physical Limitation: Finite speed of light
Geosynchronous Satellite (one way)
100 ms
30,000 km
Mobile
Base station
300 m
1 μs
Wi-Fi AP
3−30 m
10−100 ns
From Princeton to...
30 km
100 μs
Trenton
300 km
1 ms
Washington,
D.C.
Yellowstone
3,000 km
10 ms

## Slide 6: Vastly Different Timescales, Same Medium Access Protocol!
100 ms
30,000 km
300 m
1 μs
3−30 m
10−100 ns
Packet Radio
(ALOHA net)
300 km
1 ms
3G/4G Cellular
Data
Wi-Fi
Satellite Communications

## Slide 7: Today
Sharing by partitioning
  Time division
  Frequency division
  Code division
Contention-based sharing
  ALOHA
  The Ethernet

## Slide 8: TDMA: Time Division Multiple Access
Channel time is divided fixed-period, repeating rounds
Each user gets a fixed-length slot (packet time) in each round (unused slots are wasted)
Out-of-band: Mechanism for allocating/de-allocating slots
e.g.: six stations, only 1, 3, and 4 have data to send
1
3
4
1
3
4
6-slot
round
Time

## Slide 9: FDMA: Frequency Division Multiple Access
Channel spectrum divided into frequency bands
Each user gets a fixed frequency band (unused frequency slots are wasted)
e.g.: six stations, only 1, 3, and 4 have data to send
frequency bands
time
FDM cable

## Slide 10: TDMA and FDMA: Considerations
Advantages
Users are guaranteed to be able to send bits, continuously (FDMA) or periodically (TDMA)
Disadvantages
Unused time slots or frequency bands reduce channel utilization
An out-of-band mechanism is needed to allocate slots or bands (which requires another channel)
Guard bands or guard times reduce channel utilization

## Slide 11: Today
Sharing by partitioning
  Time division
  Frequency division
  Code division
Contention-based sharing
  ALOHA
  The Ethernet

## Slide 12: CDMA: Code Division Multiple Access
All users transmit over the same frequencies, and at the same time:
Allows multiple users to coexist and transmit simultaneously with no interference, in theory
In practice: also performs well
  Some cellular data networks have used CDMA
Alice
(CDMA)
Cathy
Okay!
Bob

## Slide 13: Representing bits as binary levels
Let’s represent bits with two (binary) levels as follows:
  0 bit  +1 level 1 bit  −1 level
Scenario: Alice receives data from Bob and Cathy:
  TDMA e.g.: Bob sends bits 101, Cathy sends 001:
Alice
Cathy
Bob
TDMA timeslots:
+1
−1
time
TDMA timeslots:
Bob
Cathy

## Slide 14: CDMA: User codes
Assign each user a unique binary sequence of bits: code
  Call each code bit a chip (convention)
  Call the code length M
CDMA example:
Alice
Cathy
Bob
+1
−1
time
Cathy’s code ccathy
+1
−1
Bob’s code cbob

## Slide 15: CDMA: Cathy Sending
Suppose Cathy alone sends message bits 001:
Alice
Cathy
Bob
+1
−1
time
Cathy’s message
Cathy’s transmitted CDMA signal:
Algorithm (CDMA encoding):
For each message bit m:
Send m × cuser
ccathy:
+1
−1
L data bits  M × L CDMA chips
Bit rate: Factor of M slower

## Slide 16: CDMA: Assumptions
Let’s assume we have a way of:
  Synchronizing Cathy’s and Bob’s data bits in time
  Synchronizing Cathy’s and Bob’s CDMA chips in time
  Estimating and correcting the effect of the wireless channel between Cathy and Bob to Alice
Alice
Cathy
Bob

## Slide 17: What Alice Hears
Cathy’s transmitted CDMA signal:
+1
−1
Bob’s transmitted CDMA signal:
+1
−1
Alice
Cathy
Bob
What Alice hears:
+1
−1
+2
−2
Result: Neither Bob nor Cathy’s signal – interference!

## Slide 18: Tool: Correlation
+1
−1
Cathy’s code ccathy
+1
−1
Bob’s code cbob
+1
−1
1. Multiply pointwise:
Algorithm (correlation):
Multiply two signals pointwise, across time
Sum the result across time
Normalize (divide) by the signal length
Sum: 0
2. Sum across time
 Correlation: 0
3. Normalize (÷2)

## Slide 19: Tool: Correlation
+1
−1
Cathy’s code ccathy
+1
−1
1. Multiply pointwise:
Algorithm (correlation):
Multiply two signals pointwise, across time
Sum the result across time
Normalize (divide) by the signal length
Sum: 2
2. Sum across time
 Correlation: 1
3. Normalize (÷2)
Cathy’s code ccathy
+1
−1

## Slide 20: Correlating Cathy’s Code and CDMA transmission
+1
−1
Cathy’s code ccathy
+1
−1
Correlation
Cathy’s transmission
+1
−1
corr
Cathy sent: 0 0 1

## Slide 21: Listening to Cathy
Cathy’s transmission
+1
−1
Bob’s transmission
+1
−1
Alice
Cathy
Bob
Alice hears a mixture
+1
−1
+2
−2
+1
−1
Cathy’s code ccathy
+1
−1
Correlation
corr
Cathy sent: 0 0 1
Zero-correlation with Bob’s code cancels Bob’s transmission from the mixture

## Slide 22: CDMA: How to choose codes?
Let’s generalize the Alice, Bob, Cathy scenario:
  N users, each user n has code , n = 1...N
    (m = 1...Code length M)
Recall: Correlate against code to decode user n
  Correlate any user’s code against itself: ★ = 1
Goal: Ensure cancellation of all other users when correlating against (each) one
AP
User 1
User 2
User 3
User N
...
Zero mutual correlation condition: ★

## Slide 23: Example of CDMA codes
Start with the Bob / Cathy code, write as rows in a matrix
Recursive rule: given matrix M, form
e.g. four users:

## Slide 24: CDMA: Considerations
CDMA advantages:
  Sending over entire channel frequency bandwidth
    Some parts of frequency band interfered? Okay!
FDMA, TDMA, CDMA disadvantages:
  Rigid allocation of channel resources, requires advance coordination (frequency, time, code)
  Partitioning the channel  reduced rate
Can we have the best of both worlds, perhaps?

## Slide 25: Today
Sharing by partitioning
  Time division
  Frequency division
  Code division
Contention-based sharing
  Unslotted ALOHA, Slotted ALOHA
  The Ethernet

## Slide 26: Contention-based sharing
When a station has a frame to send:
  Transmit at full channel data rate B
  No a priori coordination among nodes
Two or more frames overlapping in time: collision
  Both frames lost, resulting in diminished throughput
A random access MAC protocol specifies:
  How to detect collisions
  How to recover from collisions

## Slide 27: ALOHAnet: Context
Norm Abramson, 1970 at the University of Hawaii
  Seven campuses, on four islands
  Wanted to connect campus terminals and mainframe
  Telephone costs high, so built a packet radio network

## Slide 28: Unslotted ALOHA
Simplest possible medium access control: no control at all, anyone can just transmit a packet without delay
Suppose: Probability packet begins in time interval Δt = λ × Δt
  N senders in total, sending frames of time duration 1
λ is the aggregate rate from all N senders
Individual rate λ/N for each sender

## Slide 29: Unslotted ALOHA: Performance
Suppose some node i is transmitting; let’s focus on i ’s frame
Others send in [t0−1, t0]: overlap i ’s frame start  collision
Others send in [t0, t0+1]: overlap i ’s frame end  collision
Otherwise, no collision, node i ’s frame is delivered
Therefore, vulnerable period of length 2 around i ’s frame
Vulnerable period

## Slide 30: Unslotted ALOHA: Performance
What’s the chance no one else sends in the vulnerable period (length 2)?
Vulnerable period

## Slide 31: Unslotted ALOHA: Utilization
Recall λ is the aggregate rate from all senders
  So, utilization = λ × Pr(no other transmission in 2)
= λe−2λ
λ
Utilization
1/2e ≈ 18%
Too many collisions!
Not sending fast enough

## Slide 32: Slotted ALOHA
Divide time into slots of duration 1, synchronize so that nodes transmit only in a slot
  Each of N nodes transmits with probability p in each slot
  So aggregate transmission rate λ = N × p
As before, if there is exactly one transmission in a slot, can receive; if two or more in a slot, no one can receive (collision)
...
Node N

## Slide 33: Slotted ALOHA: Utilization
Suppose N nodes, each transmit with probability p in each slot. What is the utilization as a function of aggregate rate λ = N × p?
Pr[A node is successful in a slot] = p(1−p)N−1
Pr[Success in a slot] = Np(1−p)N−1
λ
1/e ≈ 37%
Utilization

## Slide 34: ALOHA throughput: slotted versus unslotted
Unslotted ALOHA: λe−2λ
Slotted ALOHA: λe−λ
1/2e ≈ 18%
1/e ≈ 36%
Just by forcing nodes to transmit on slot boundaries, we double peak medium utilization!

## Slide 35: Today
Sharing by partitioning
  Time division
  Frequency division
  Code division
Contention-based sharing
  Unslotted ALOHA, Slotted ALOHA
  The Ethernet

## Slide 36: How did the Ethernet get built?
Bob Metcalfe, PhD student at Harvard in early 1970s
  Working on protocols for the ARPAnet
  Intern at Xerox Palo Alto Research Center (PARC), 1973
  Needed a way to network ≈100 Alto workstations in-building
  Adapted ALOHA packet radio
Metcalfe later founds 3Com, acquired by HP in April ’10 for USD $2.7 bn

## Slide 37: The Ethernet: Physical design
Coaxial cable, propagation delay τ
  Propagation speed: 3/5 × speed of light
Experimental Ethernet
  Data rate: B = 3 Mbits/s
  Maximum length: 1000 m
Propagation delay: τ

## Slide 38: Building the link: Framing bits
Goal: Move bits from one computer to another
  Sender and receiver have independent clocks
  No separate “clock signal” sent on the Ethernet
Problem: Agree on clock tick period
Problem: Agree on clock tick alignment (phase)

## Slide 39: Manchester (phase) encoding
Manchester encoding:
  Exclusive-OR of the NRZ signal and the clock signal
  “0” is a low-to-high transition; “1” is a high-to-low
Transition guaranteed on every bit
Drawback: Halves data rate

## Slide 40: Ethernet framing
Framing
  Beginning of frame determined by presence of carrier
  End of frame determined by absence of carrier
  Preamble: 10101010 produces a square wave that allows receiver to frame bits
CRC (Cyclic Redundancy Check) protects against errors on the Ether
  Does not guard against errors introduced by the tap: rely on higher-layer checksums
Destination address allows filtering at the link layer
Preamble
Destination
Source
Data
CRC
8 bits
8 bits
16 bits
4000 bits

## Slide 41: Collisions on the Ethernet
Packet of size N bits: N/B seconds on the wire
From the perspective of a receiver (B):
  Overlapping packets at B means signals sum
  Not time-synchronized: result is bit errors at B
No fate-sharing: C receives OK in this example
A
B
C
Z
Propagation delay: τ seconds

## Slide 42: Who gets to transmit, and when?
Carrier Sense Multiple Access
with Collision Detection (CSMA/CD)
Begin the transmission procedure at any time
Carrier sensing: defer if you sense that another station is transmitting
Collision detection: while sending, immediately abort your transmission if you detect another station transmitting

## Slide 43: Carrier sensing
Mechanism: measure voltage on the wire
Binary encoding: voltage depends on the data
Manchester coding: constant average voltage

## Slide 44: Collision detection
Paper isn’t clear on this point (authors did have a patent in the filing process)
Mechanism: monitor average voltage on cable
  Manchester encoding means your transmission will have a predictable average voltage V0; others will increase V0
  Abort transmission immediately if Vmeasured > V0
A
B
C
Z
Propagation delay: τ seconds

## Slide 45: When might a collision happen?
Suppose Station A begins transmitting at time 0
Assume that the packet lasts much longer than τ
All stations sense transmission and defer by time τ
  Don’t begin any new transmissions
A
B
C
Z
Propagation delay: τ seconds

## Slide 46: How long does a collision take to detect?
Suppose Station A begins transmitting at time 0
τ seconds after Z starts, A hears Z’s transmission
When does A know whether its packet collided or not?
  At time 2τ
A
B
C
Z
Propagation delay: τ seconds

## Slide 47: Collision detection and packet size
Transmit rate B bits/second
If packets take time 2τ, A will still be transmitting when Z’s packet arrives at A, so A will detect collision
  So minimum packet size = 2τB bits
    Experimental Ethernet:
      τ = 5 μs, B = 3 Mbits/s → 2τB = 30 bits
A
B
C
Z
Propagation delay: τ seconds

## Slide 48: Resolving collisions
Upon abort (carrier detect), station enters the backoff state
Key idea: the colliding stations all wait a random time before carrier sensing and transmitting again
  How to pick the random waiting time? (Should be based on how stations have data to send)
  How to estimate the number of colliding stations?
Goal: Engineer such that nodes will wait different amounts of time, carrier sense, and not collide

## Slide 49: Slotted Ethernet backoff
Backoff time is slotted (like slotted ALOHA) and random
  Station’s view of the where the first slot begins is at the end of the busy medium
  Random slot choice in contention window (CW)
Goal: Choose slot time so that different nodes picking different slots CS and defer  don’t collide

## Slide 50: Picking the length of a backoff slot
OK
Bad
Consider from the perspective of one packet at time t
  Packets before t−τ will cause packet to defer
  Packets after t+τ will not happen (why not?)
Packets beginning within time τ apart will collide
So should we pick a backoff slot length of τ?
OK
τ
τ
Cause defer
CS fail
(Won’t happen)

## Slide 51: The problem of clock skew
OK
No! Slots are timed off the tail-end of the last packet
  Therefore, stations’ clocks differ by at most τ
Suppose we use a backoff slot length of τ
  Different stations picking different slots may collide!
OK
τ
τ
τ
τ
Δ
Station B, slot 0
Station A, slot 1
0
1
2
0
1
2

## Slide 52: Picking slot time in presence of clock skew
OK
Want other station’s other slots to all be in “OK” region
  Then, transmissions in different slots won’t collide
  Worst case clock skew: τ
  So, pick a slot time of τ + τ = 2τ
OK
2τ
2τ
0
1
2
0
1
2
τ

## Slide 53: Binary Exponential Backoff
Binary exponential backoff (BEB): double CW size on each consecutive collision
Stations wait some number of slots chosen uniformly at random from CW = [0, 2m−1]
  Reset m ← 1 upon a successful transmission
  First retransmit (m = 1): pick from [0, 1]
  Second retransmit (m = 2): pick from [0, 1, 2, 3]
Observe: Stations transmitting new frames don’t take into account recent collisions, might transmit before stations in backoff

## Slide 54: Ethernet performance analysis
Divide time into:
  Variable-sized contention intervals,
  Fixed size transmission intervals (duration tpacket)
Time →
tpacket
slot time
Number of slots to acquire the Ether
Efficiency:

## Slide 55: Ethernet performance: Acquisition
What’s the probability that one station acquires the medium without a collision?
Suppose there are Q stations waiting to send
Assume stations know Q and send with probability 1/Q (BEB approximates this)
Slotted ALOHA  37% probability of successful acquisition

## Slide 56: Ethernet performance: Waiting time
W = number of slots in a contention window before acquisition of the Ether
Probability of no wait: pacquire
Probability wait one slot: (1 − pacquire)pacquire
Probability wait two slots: (1 − pacquire)2pacquire
E[slots to wait] = E[W] = (1 − pacquire)/pacquire
  = e − 1

## Slide 57: Comparing CDMA and ALOHA random access
CDMA wireless
  No interference between transmitting stations
  Adaptation to varying numbers of users possible by changing codes
  Reduced rate of individual transmissions
  Unused codes waste overall capacity
ALOHA random access
  Stations can transmit using the entire medium, at full rate if alone
  Almost-instant adaptation to varying traffic loads
  Concurrent transmissions result in collisions, reduced throughput

## Slide 58
Friday Precept
Introduction to Lab 1
Tuesday Topic:
Link Layer II: MACA and MACAW