## Slide 1: Wireless Mesh Networks
COS 463: Wireless Networks
Lecture 6
Kyle Jamieson
[Parts adapted from I. F. Akyildiz, B. Karp]

## Slide 2: Wireless Mesh Networks
Describes wireless networks in which each node can communicate directly with any other node
Traditional wireless network traffic goes through APs
Mesh networks: Remove this restriction
  Multiple paths: Mesh
router
client
Client serves as a router

## Slide 3: Distance Vector & Link State Routing
Both assume each router knows single-hop routing information:
  Address of each neighbor
  Cost of reaching each neighbor (metric)
Distance Vector: Router knows just the metric to each destination
Link State: Router knows entire network topology, computes shortest path to each destination

## Slide 4: Today
Distance Vector Routing
  New node join
  Broken link
  Route changes
Destination Sequenced Distance-Vector Routing (DSDV)
Dynamic Source Routing (DSR)
Roofnet

## Slide 5: Distance Vector Routing
Every node maintains a routing table
  For each destination in the mesh:
    The number of hops to reach the destination (metric)
    The next node on the path towards the destination
All nodes periodically, locally broadcast their routing table
  Traffic overhead due to broadcasting
C
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2
B
A
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0

## Slide 6: Distance Vector – New Node Join
D joins the network
C
B
A
D
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2

## Slide 7: Distance Vector – New Node Join
D joins the network
D’s broadcast first updates C’s table with new entry for D
(D, D, 0)
C
B
A
D
D’s routing table
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0
D | D | 1
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2

## Slide 8: Distance Vector – New Node Join
Now C broadcasts its routing table
  B and D hear and add new entries, incrementing metric (hops)
(A, B, 2)
(B, B, 1)
(C, C, 0)
(D, D, 1)
C
B
A
D
(A, B, 2)
(B, B, 1)
(C, C, 0)
(D, D, 1)
C’s routing table
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0
D | D | 1
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
D | C | 2
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2
Dest. | Next | Metric
A | C | 3
B | C | 2
C | C | 1
D | D | 0

## Slide 9: Distance Vector – New Node Join
Now B broadcasts its routing table
  A and C hear and add new entries, incrementing metric (hops)
(A, A, 1)
(B, B, 0)
(C, C, 1)
(D, C, 2)
C
B
A
D
(A, A, 1)
(B, B, 0)
(C, C, 1)
(D, C, 2)
B’s routing table
9
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0
D | D | 1
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
D | C | 2
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2
D | B | 3
Dest. | Next | Metric
A | C | 3
B | C | 2
C | C | 1
D | D | 0

## Slide 10: Today
Distance Vector Routing
  New node join
  Broken link
  Route changes
Destination Sequenced Distance-Vector Routing (DSDV)
Dynamic Source Routing (DSR)
Roofnet

## Slide 11: Distance Vector – Broken Link
Suppose link C  D breaks
C
B
A
D
Dest. | Next | Metric
… | … | …
D | C | 2
Dest. | Next | Metric
… | … | …
D | B | 3
Dest. | Next | Metric
… | … | …
D | D | 1

## Slide 12: Distance Vector – Broken Link
C hears no advertisement from D for a timeout period
  C sets D’s metric to 
Dest. | Next | Metric
… | … | …
D | C | 2
Dest. | Next | Metric
… | … | …
D | B | 3
Dest. | Next | Metric
… | … | …
D | D | 
C
B
A
D

## Slide 13: Distance Vector – Broken Link
C sets D’s metric to 
B broadcasts its routing table
  C now accepts B’s entry for D (3 < )
(D, C, 2)
(D, C, 2)
C
B
A
D
Dest. | Next | Metric
… | … | …
D | C | 2
Dest. | Next | Metric
… | … | …
D | B | 3
Dest. | Next | Metric
… | … | …
D | B | 3

## Slide 14: Broken Link: Counting to Infinity
C sets D’s metric to 
B broadcasts its routing table
C broadcasts its routing table
  B accepts C’s new metric (previous next-hop: C)
(D, C, 2)
(D, C, 2)
C
B
A
D
Dest. | Next | Metric
… | … | …
D | C | 4
Dest. | Next | Metric
… | … | …
D | B | 3
Dest. | Next | Metric
… | … | …
D | B | 3
(D, B, 3)

## Slide 15: Broken Link: Counting to Infinity
C sets D’s metric to 
B broadcasts its routing table
C broadcasts its routing table
B broadcasts its routing table
  A, C accept B’s new metric (previous next-hops: B)
(D, C, 2)
(D, C, 2)
C
B
A
D
Dest. | Next | Metric
… | … | …
D | C | 4
Dest. | Next | Metric
… | … | …
D | B | 5
Dest. | Next | Metric
… | … | …
D | B | 5
(D,3)
(D, C, 4)
(D, C, 4)

## Slide 16: Today
Distance Vector Routing
  New node join
  Broken link
  Route changes
Destination Sequenced Distance-Vector Routing (DSDV)
Dynamic Source Routing (DSR)
Roofnet

## Slide 17: Distance Vector – Route Change
D moves to another place and broadcast its routing table
C
B
A
D
17
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0
D | D | 1
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
D | C | 2
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2
D | B | 3
Dest. | Next | Metric
A | C | 3
B | C | 2
C | C | 1
D | D | 0

## Slide 18: Distance Vector – Route Change
D moves to another place and broadcast its routing table
C
B
A
D
18
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0
D | D | 1
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
D | D | 1
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2
D | B | 3
Dest. | Next | Metric
A | C | 3
B | C | 2
C | C | 1
D | D | 0
…
(D, D, 0)
…
(D, D, 0)

## Slide 19: Distance Vector – Route Change
…
(D, D, 1)
…
(D, D, 1)
D moves to another place and broadcast its routing table
B broadcast its routing table
C
B
A
D
19
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 0
D | D | 1
Dest. | Next | Metric
A | A | 1
B | B | 0
C | C | 1
D | D | 1
Dest. | Next | Metric
A | A | 0
B | B | 1
C | B | 2
D | B | 2
Dest. | Next | Metric
A | B | 2
B | B | 1
C | C | 1
D | D | 0
…
(D, D, 1)

## Slide 20: Today
Distance Vector Routing
Destination Sequenced Distance-Vector Routing (DSDV)
  New node join
  Broken link
  Route advertisement
Dynamic Source Routing (DSR)
Roofnet

## Slide 21: Destination Sequenced Distance-Vector (DSDV) Routing
  Guarantees loop freeness
  New routing table information: Sequence number
  Per-destination information
  Originated by destination
  Included in routing advertisements
Destination | Next | Metric | Seq. Nr
A | A | 0 | 550
B | B | 1 | 102
C | B | 3 | 588
D | B | 4 | 312

## Slide 22: DSDV: Route Advertisement Rule
Rules to set sequence number:
Just before node N’s broadcast advertisement:
  Node N sets:
    Seq(N)  Seq(N) + 2
Node N thinks neighbor P is no longer directly reachable
  Node N sets:
    Seq(P)  Seq(P) + 1
    Metric(P)  

## Slide 23: DSDV – New Node
(D, D, 0, 000)
C
B
A
D
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 104
C | B | 2 | 590
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 104
C | C | 1 | 590
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 104
C | C | 0 | 590
1. D broadcast for first time Send Sequence number 000
D joins the network
D’s broadcast first updates C’s table with new entry for D

## Slide 24: DSDV – New Node
C
B
A
D
2.1: Insert entry for D with same sequence number 000 2.2: Triggered broadcast of its own table
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 104
C | B | 2 | 590
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 104
C | C | 1 | 590
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 104
C | C | 0 | 590
D | D | 1 | 000
(D, D, 0, 000)
1. D broadcast for first time Send Sequence number 000

## Slide 25: DSDV – New Node
C
B
A
D
(A, B, 2, 550)
(B, B, 1, 104)
(C, C, 0, 592)
(D, D, 1, 000)
(A, B, 2, 550)
(B, B, 1, 104)
(C, C, 0, 592)
(D, D, 1, 000)
3. C increases its sequence number to 592 then broadcasts its new table.
4. B gets C’s update and updates its table
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 104
C | B | 2 | 590
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 104
C | C | 1 | 592
D | C | 2 | 000
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 104
C | C | 0 | 592
D | D | 1 | 000

## Slide 26: DSDV – New Node
C
B
A
D
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 106
C | B | 2 | 592
D | B | 3 | 000
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 106
C | C | 1 | 592
D | C | 2 | 000
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 106
C | C | 0 | 592
D | D | 1 | 000
(A, B, 1, 550)
(B, B, 0, 106)
(C, C, 1, 592)
(D, C, 2, 000)
(A, B, 1, 550)
(B, B, 0, 106)
(C, C, 1, 592)
(D, C, 2, 000)
4. B increases its own seqno and broadcasts its new table

## Slide 27: Today
Distance Vector Routing
Destination Sequenced Distance-Vector Routing (DSDV)
  New node join
  Broken link
  Route advertisement
Dynamic Source Routing (DSR)
Roofnet

## Slide 28: DSDV – Broken Link
C
B
A
D
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 106
C | B | 2 | 592
D | B | 3 | 000
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 106
C | C | 1 | 592
D | C | 2 | 000
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 106
C | C | 0 | 592
D | D | 1 | 000
Suppose link C  D breaks

## Slide 29: DSDV – Broken Link
C
B
A
D
1. Node C detects broken Link:  Increase Seq. No. by 1 (only case where not the destination sets the sequence number  odd number)
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 106
C | B | 2 | 592
D | B | 3 | 000
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 106
C | C | 1 | 592
D | C | 2 | 000
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 106
C | C | 0 | 592
D | D |  | 001

## Slide 30: DSDV: Routing Table Update Rule
Rules to update routing table entry:
Node N gets routing advertisement from neighbor Node P:
  Update routing table entry for node E when:
    Seq(E) in P’s advertisement > Seq(E) in N’s table

## Slide 31: DSDV – Broken Link
(A, A, 1, 550)
(B, B, 0, 108)
(C, C, 1, 592)
(D, C, 2, 000)
(A, A, 1, 550)
(B, B, 0, 108)
(C, C, 1, 592)
(D, C, 2, 000)
C
B
A
D
No affect on C’s entry for D (because 001 > 000)
No loop  no count to infinity
B next broadcasts its routing table
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 108
C | B | 2 | 592
D | B | 3 | 000
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 108
C | C | 1 | 592
D | C | 2 | 000
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 108
C | C | 0 | 592
D | D |  | 001

## Slide 32: Today
Distance Vector Routing
Destination Sequenced Distance-Vector Routing (DSDV)
  New node join
  Broken link
  Route advertisement
Dynamic Source Routing (DSR)
Roofnet

## Slide 33: Distance Vector – Route Advertisement
D moves to another place and broadcasts its routing table
C
B
A
D
33
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 108
C | B | 2 | 592
D | B | 3 | 000
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 108
C | C | 1 | 592
D | D | 1 | 002
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 108
C | C | 0 | 592
D | D | 1 | 002
Dest. | Next | Metric | Seq.
A | C | 3 | 550
B | C | 2 | 108
C | C | 1 | 592
D | D | 0 | 002
…
(D, D, 0, 002)
…
(D, D, 0, 002)

## Slide 34: Distance Vector – Route Advertisement
…
(B, B, 0, 110)
…
(B, B, 0, 110)
…
(B, B, 0, 110)
D moves to another place and broadcasts its routing table
B broadcasts its routing table
C
B
A
D
34
Dest. | Next | Metric | Seq.
A | A | 0 | 550
B | B | 1 | 110
C | B | 2 | 592
D | B | 2 | 002
Dest. | Next | Metric | Seq.
A | A | 1 | 550
B | B | 0 | 110
C | C | 1 | 592
D | D | 1 | 002
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 110
C | C | 0 | 592
D | D | 1 | 002
Dest. | Next | Metric | Seq.
A | B | 2 | 550
B | B | 1 | 110
C | C | 1 | 592
D | D | 0 | 002

## Slide 35: Today
Distance Vector Routing
Destination Sequenced Distance-Vector Routing (DSDV)
Dynamic Source Routing (DSR)
Roofnet

## Slide 36: Dynamic Source Routing (DSR)
No periodic “beaconing” from all nodes
When node S wants to send a packet to node D (but doesn’t know a route to D), S initiates a route discovery
S network-floods a Route Request (RREQ)
  Each node appends its own id when forwarding RREQ

## Slide 37: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Represents a node that has received RREQ for D from S
M
N
L

## Slide 38: Route Discovery in DSR
B
A
S
E
F
H
J
D
C
G
I
K
Represents transmission of RREQ
Broadcast transmission
M
N
L
[S]
[X,Y] Represents list of identifiers appended to RREQ

## Slide 39: Route Discovery in DSR
Represents transmission of RREQ
[X,Y] Represents list of identifiers appended to RREQ
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,E]
[S,C]

## Slide 40: Route Discovery in DSR
Represents transmission of RREQ
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,C,G]
[S,E,F]
Node C receives RREQ from G and H, but does not forward
it again, because node C has already forwarded RREQ once

## Slide 41: Route Discovery in DSR
Represents transmission of RREQ
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,C,G,K]
[S,E,F,J]
Nodes J and K both broadcast RREQ to node D
Since nodes J and K are hidden from each other, their
transmissions may collide

## Slide 42: Route Discovery in DSR
Represents transmission of RREQ
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
[S,E,F,J,M]
Node D does not forward RREQ, because node D
is the intended target of the route discovery

## Slide 43: Route Reply in DSR
On receiving first RREQ, D sends a Route Reply (RREP)
  RREP sent on route obtained by reversing the route in the received RREQ
  RREP includes the route from S to D over which D received the RREQ
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
RREP [S,E,F,J,D]
Represents RREP control message

## Slide 44: Dynamic Source Routing (DSR)
On receiving RREP, S caches route included therein
When S sends a data packet to D, includes entire route in packet header
Intermediate nodes use the source route included in packet to determine to whom packet should be forwarded
B
A
S
E
F
H
J
D
C
G
I
K
M
N
L
DATA [S,E,F,J,D]

## Slide 45: Today
Distance Vector Routing
Destination Sequenced Distance-Vector Routing (DSDV)
Dynamic Source Routing (DSR)
Roofnet
  Wireless mesh link measurements
  Routing and bit rate selection
  End-to-end performance evaluation

## Slide 46: Context, ca. 2000-2005
Mobile ad hoc networking research
  Mobile, hence highly dynamic topologies
  Chief metrics: routing protocol overhead, packet delivery success rate, hop count
  Largely evaluated in simulation
Roofnet, a real mesh network deployment
  Fixed, PC-class nodes
  Motivation: shared Internet access in community
  Chief metric: TCP throughput
  “Test of time” system, led to Cisco Meraki

## Slide 47: Roofnet: Design Choices
Volunteer users host nodes at home
  Open participation without central planning
  No central control over topology
Omnidirectional rather than directional antennas
  Ease of installation: no choice of neighbors/aiming
  Links interfere, likely low quality
Multi-hop routing (not single-hop hot spots)
  Improved coverage (path diversity)
  Must build a routing protocol
Goal: high TCP throughput

## Slide 48: Roofnet: Goals and non-goals
Each part of the mesh architecture had been previously examined in isolation
Paper contribution: A systematic evaluation of whether architecture can achieve goal of providing Internet access
Stated non-goals for paper:
  Throughput of multiple concurrent flows
  Scalability in number of nodes
  Design of routing protocols

## Slide 49: Roofnet deployment
Each node: PC, 802.11b card, roof-mounted omni antenna

## Slide 50: Hardware design
PC Ethernet interface provides wired Internet for user
Omnidirectional antenna in azimuthal direction
  3 dB vertical beam width of 20 degrees
    Wide beam sacrifices gain but removes the need for perfect vertical antenna orientation
802.11b radios (Intersil Prism 2.5 chipset)
  200 mW transmit power
  All share same 802.11 channel (frequency)

## Slide 51: Internet gateways
Node sends DHCP request on Ethernet then tests reachability to Internet hosts
  Success indicates node is an Internet gateway
    Gateways translate between Roofnet and Internet IP address spaces
Roofnet nodes track gateway used for each open TCP connection they originate
  If best gateway changes, open connections continue to use gateway they already do
If a Roofnet gateway fails, existing TCP connections through that gateway will fail

## Slide 52: Example: Varying link loss rates
A  C: 1 hop; high loss
A  B  C: 2 hops; lower loss
But does this happen in practice?
A
B
C
10% loss
10% loss
90% loss

## Slide 53: Hop count and throughput (1)
Minimum-hop-count routes are significantly throughput-suboptimal

## Slide 54: Hop count and throughput
Two-hop path is suboptimal
Some 3-hop paths better, some worse than 2-hop

## Slide 55: Link loss is high and asymmetric
Vertical bar ends = loss rate on 1 link in each direction
Many links asymmetric and very lossy in ≥ 1 way
Wide range of loss rates

## Slide 56: Routing protocol: Srcr
Each link has an associated metric (not necessarily 1!)
Data packets contain source routes
Nodes keep database of link metrics
  Nodes write current metric into source route of all forwarded packets
  DSR-like: Nodes flood route queries when they can’t find a route; queries accumulate link metrics
    Route queries contain route from requesting node
  Nodes cache overheard link metrics
Dijkstra’s algorithm computes source routes

## Slide 57: Link metric: Strawmen
Discard links with loss rate above a threshold?
  Risks unnecessarily disconnecting nodes
Product of link delivery rates  prob. of e2e delivery?
  Ignores inter-hop interference
    Prefers 2-hop, 0% loss route over 1-hop, 10% loss route (but latter is double throughput)
Throughput of highest-loss link on path?
  Also ignores inter-hop interference

## Slide 58: ETX: Expected Transmission Count
Link ETX: predicted number of transmissions
  Calculate link ETX using forward, reverse delivery rates
  To avoid retry, data packet and ACK must succeed
  Link ETX = 1 / (df × dr)
    df = forward link delivery ratio (data packet)
    dr = reverse link delivery ratio (ack packet)
Path ETX: sum of the link ETX values on a path

## Slide 59: Measuring link delivery ratios
Nodes periodically send broadcast probe packets
  All nodes know the sending period of probes
  All nodes compute loss rate based on how many probes arrive, per measurement interval
Nodes enclose these loss measurements in their transmitted probes
  e.g. B tells node A the link delivery rate from A to B

## Slide 60: Multi-bitrate radios
ETX assumes all radios run at same bit-rate
  But 802.11b rates: {1, 2, 5.5, 11} Mbit/s
Can’t compare two transmissions at 1 Mbit/s with two at 2 Mbit/s
Solution: Use expected time spent on a packet, rather than transmission count

## Slide 61: ETT: Expected Transmission Time
ACKs always sent at 1 Mbps, data packets 1500 bytes
Nodes send 1500-byte broadcast probes at every bit rate b to compute forward link delivery rates df(b)
  Send 60-byte (min size) probes at 1 Mbps  dr
At each bit-rate b, ETXb = 1 / (df(b) × dr)
For packet of length S, ETTb = (S / b) × ETXb
Link ETT = minb (ETTb)

## Slide 62: ETT: Assumptions
Path throughput estimate t is given by
  ti = throughput of hop i
Does ETT maximize throughput? No!
Underestimates throughput for long (≥ 4-hop) paths
  Distant nodes can send simultaneously
Overestimates throughput when transmissions on different hops collide and are lost

## Slide 63: Roofnet evaluation
TCP bulk transfers between all node pairs but always a single flow at a time
  But background traffic present: users always active
Results:
  Wide spread of end-to-end throughput across pairs
  “Chain forwarding” indeed creates interference
  Lossy links indeed useful in practice

## Slide 64: Wireless Mesh Networks: Evolving Routing
DSDV took DV out of wired (more static) networks
  Better coped with dynamism
DSR addressed protocol overheads of routing
ETX and ETT abolished hop-count as a viable metric
  Replaced it with throughput as the metric