## Slide 1: From AM Radio to Digital I/Q Modulation
COS 463: Wireless Networks
Lecture 12
Kyle Jamieson
[Parts adapted from H. Balakrishnan, M. Perrott, C. Terman]

## Slide 2: Roadmap
Analog I/Q modulation
Discrete-time processing of continuous signals
  The Digital Abstraction
  Quantization: Discretizing values
  Sequences: Discretizing time
Digital I/Q Modulation

## Slide 3: Review: AM Modulation & Demodulation
Multiplication (i.e. mixing) operation shifts in frequency
Low-pass filtering passes only the desired baseband signal at the receiver

## Slide 4: Impact of a 90º phase shift
Receiver uses sine instead of cosine: no output
  sin(2πf0t)cos(2πf0t) = ½ sin(4πf0t)
Need to synchronize phase of transmitter and receiver local oscillators (coherent demodulation)
∿
∿
Local oscillator

## Slide 5: Coherent Demodulation: Frequency-domain analysis
Transmitter and receiver oscillators phase-synchronized
Demodulated copies add constructively at baseband
∿
∿

## Slide 6: 90º Phase Shift: Frequency-domain analysis
Transmitter, receiver oscillators are offset in phase by 90º
Demodulated copies add destructively at baseband
  Zero output from receiver
Two separate channels!

## Slide 7: In-Phase/Quadrature Modulation
Modulate each with a cosine & sine, sum the result
In-Phase (I) component
Quadrature (Q) component
I, Q signals occupy the same frequency band
  One is real (for cos), one is imaginary (for sin)

## Slide 8: In-Phase/Quadrature Demodulation
Demodulate with both a sine and a cosine
  Both I and Q channels are recovered!

## Slide 9: I/Q Demodulation: 90º Phase Shift
I and Q channels get swapped at receiver
  Key observation: No information is lost!

## Slide 10: Summary of Analog I/Q modulation

## Slide 11: I/Q modulation: Wrap-up
I/Q modulation allows twice the amount of information to be sent compared to basic AM
Impact of phase offset is to swap I/Q
Impact of frequency offset is I/Q swapping (small offset)
  Or catastrophic corruption (large offset) of received signal

## Slide 12: Roadmap
Analog I/Q modulation
Discrete-time processing of continuous signals
  The Digital Abstraction
  Quantization: Discretizing values
  Sequences: Discretizing time
Digital I/Q Modulation

## Slide 13: Representing information with voltage
Encoding of pixel at location (x, y) in a Black & White picture:
  0 Volts = Black
  1 Volt = White
  0.37 V = 37% Gray
  etc...
Encoding of a picture:
  Scan points in prescribed order
  Generate a continuous voltage waveform (baseband signal)

## Slide 14: Let’s build a P2P television network
x(t)
∿
×
∿
×
Encode
Decode
One hop:
Many hops:
Decode
Encode

## Slide 15: Why did our network fail?
Transmitter doesn’t work right
Receiver doesn’t work right
Theory is imperfect
System architecture isn’t right
Answer: All of the above!
Noise, transmitter/receiver imperfections inevitable, so must design system to tolerate some amount of error

## Slide 16: Analog communications issues
Problem: It’s hard to distinguish legitimate analog waveforms from corrupted ones
  Every waveform is potentially legitimate!
Small errors accumulate at each hop
Endpoints can’t help, so need to eliminate errors at each hop

## Slide 17: Plan: Mixed Signal Architecture

## Slide 18: Discrete time, Discrete values
Continuous-time, continuous-valued waveform is being converted into a discrete-valued sequence
  Only certain values are ”allowed” to be used
Questions yet to be answered:
How many discrete values should we use?
How rapidly in time should we sample the waveform?

## Slide 19: Digital signaling
First encoding attempt:
But, what happens in the presence of noise?

## Slide 20: Big Idea: Noise Margins

## Slide 21: How many discrete values?

## Slide 22: Quantization Error
Introduce at most ½ interval length of quantization error

## Slide 23: Roadmap
Analog I/Q modulation
Discrete-time processing of continuous signals
  The Digital Abstraction
  Quantization: Discretizing values
  Sequences: Discretizing time
Digital I/Q Modulation

## Slide 24: Need for Continuous to Discrete Conversion
The boundary between analog and digital
  Real world filled with continuous-time signals
  Computers operate on discrete-time sequences
Crossing the analog to digital boundary requires conversion between the two
Real world (Hack RF)
Computer (Python)

## Slide 25: Modelling Continuous-to-Discrete Conversion
Two-step process:
Sample continuous-time signal every T seconds
  Model as multiplication of signal with impulse train
Create sequence from amplitude of scaled impulses
  Model as rescaling of time axis (T  1)

## Slide 26: Fourier Transform of Impulse Train
Impulse train in time corresponds to impulse train in frequency
  Spacing in time of T seconds corresponds to 1/T Hz spacing in frequency

## Slide 27: Frequency Domain view of Sampling
Sampling in time leads to a periodic Fourier Transform, with period 1/T

## Slide 28: Frequency Domain View of a Sequence
Conversion to sequence amounts to T = 1
Resulting Fourier Transform now periodic with period 1

## Slide 29: Summary of Continuous-to-Discrete Conversion
Sampling leads to periodicity in frequency domain

## Slide 30: The Sampling Theorem
No overlap in frequency domain (aliasing) when:
  or
We refer to the minimum 1/T that avoids aliasing as the Nyquist sampling frequency of a signal

## Slide 31: Sine Wave Example: Sampling Above Nyquist Rate
Time domain: Resulting sequence maintains same period as input signal

## Slide 32: Sine Wave Example: Sampling at Nyquist Rate
Time Domain: Resulting sequence maintains same period as input signal

## Slide 33: Sine Wave Example: Sampling at Half the Nyquist Rate
Sequence now appears as constant (zero frequency) signal
Frequency domain: Aliasing to 0

## Slide 34: Sine Wave Example: Sampling Below the Nyquist Rate
Resulting sequence is now a sine wave with a different period than the input
Frequency domain: Aliasing to a lower frequency

## Slide 35: The Issue of High Frequency Noise
Typically set sample rate to exceed desired signal’s bandwidth
Real systems can introduce noise/other interference at high frequencies
  Sampling causes noise to alias into desired frequency band

## Slide 36: Anti-Alias Filtering
Practical A/D converters include a continuous-time filter before the sampling operation
  Designed to filter out noise and interference above 1/2T in frequency, prevent aliasing

## Slide 37: Summary: Advantages of Going Digital
Allows error correction to be achieved
  Less sensitivity to radio channel imperfections
Enables compression of information
  More efficient use of the channel
Supports a wide variety of information content
  Voice, text, video can all be represented as digital bit streams

## Slide 38: Roadmap
Analog I/Q modulation
Discrete-time processing of continuous signals
Digital I/Q Modulation

## Slide 39: Digital I/Q modulation
Leverage analog communication channel to send discrete-valued symbols
  Example: Send symbol from set { -3, -1, 1, 3 } on both I and Q channels
At receiver, sample I/Q waveforms every symbol period
  Associate each sampled I/Q value with symbols from same set on both I and Q channels

## Slide 40: Constellation Diagrams
Plot I/Q samples on x-y axis
  As samples are plotted, constellation diagram eventually displays all possible symbol values
Provides a sense of how easy it is to distinguish between different symbols

## Slide 41: Sending Digital Bits
Assign bits to each I/Q symbol
  Example: I/Q = {1, 3} translates to bits 1110
  Gray coding minimizes bit errors when symbol errors are made
    Example: I/Q = {3, 3} translates to bits 1010 (one bit flip from {1, 3})

## Slide 42: The Impact of Noise
At receiver, noise perturbs sampled I/Q values
  Constellation points no longer consist of single points for each symbol
Issue: What’s the best way of matching received I/Q samples with their corresponding transmitted symbols?

## Slide 43: Symbol Selection based on Slicing
Receiver matches I/Q samples to corresponding symbols based on decision regions comprised of decision boundaries
  Choose decision boundaries to minimize symbol errors
Decision boundaries also called slicing levels

## Slide 44: Transitioning Between Symbols
Transition behavior influenced by transmit I/Q input waveforms and receive filter
  Today: Focus on what the transmitter does
  Ignore impact of noise for this analysis

## Slide 45: Transitions and the Transmitted Spectrum
Want transmitted spectrum with minimal bandwidth
Issue: Sharply changing I/Q leads to very wide bandwidth spectrum

## Slide 46: Impact of Transmit Filter
Transmit filter shapes the pulses, enables reduced bandwidth for transmitted spectrum
Next Issue: Can lead to bit errors

## Slide 47: Impact of Low Bandwidth Transmit Filter
Lowering the transmit bandwidth leads to increased bit errors

## Slide 48: Eye Diagrams
Eye Diagram: Wrap signal back onto itself in periodic time intervals, retaining all “traces”

## Slide 49: Looking at Many Symbols
Increasing the number of symbols eventually reveals all possible symbol transition trajectories
  Intuitively displays the impact of filtering on transmitted signal

## Slide 50: Assessing the Quality of an Eye Diagram
Eye diagram allows visual inspection of the impact of sample time and decision boundary choices
  Large “eye opening” implies less vulnerability to symbol errors
Sample times:

## Slide 51: Relating Eye Diagrams to Constellation
Open eye diagrams lead to tight symbol groupings in constellation
  Assumes proper sample time placement

## Slide 52: Impact of Low Transmit Bandwidth
Eye diagrams show increased inter-symbol interference (ISI)
  Also show symbol decision sensitivity to sample timing placement

## Slide 53: Digital Modulation: Summary
Digital modulation: Sends discrete-valued symbols through an analog communication channel
  Receiver must sample I/Q signals at the appropriate time
  Receiver matches I/Q sample values to corresponding symbols based on decision regions
  Constellation diagrams are a convenient tool to see likelihood of bit errors being made
Choice of transmit filter: Tradeoff between achieving a minimal bandwidth transmitted spectrum and minimal ISI
  Eye diagrams: A convenient tool to see effects of ISI and sensitivity of bit errors to sample time choice

## Slide 54
Thursday Topic:
Digital Communications II:
Receiver Processing, Performance
Friday Precept:
BER and Shannon’s Limit