## Slide 1: The Radio Channel
COS 463: Wireless Networks
Lecture 14
Kyle Jamieson
[Parts adapted from I. Darwazeh, A. Goldsmith, T. Rappaport, P. Steenkiste]

## Slide 2: Motivation
The radio channel is what limits most radio systems – the main challenge!
  Understanding its properties is therefore key to understanding radio systems’ design
There is no single radio channel, but instead variation in many different properties
  Carrier frequency, environment (e.g. indoors, outdoors, satellite, space)
Many different models covering many different scenarios

## Slide 3: Channel and Propagation Models
A channel model describes what happens
  Gives channel output power for a particular input power
  “Black Box” – no explanation of mechanism
  Requires appropriate statistical parameters (e.g. loss, fading)
A propagation model describes how it happens
  How signal gets from transmitter to receiver
  How energy is redistributed in time and frequency
  Can inform channel model parameters

## Slide 4: Modeling (from a high-level perspective)

## Slide 5: Today
Large scale channel models
  Free space model
  Two-ray ground model
Small-scale channel models
Equalization: Coping with the channel

## Slide 6: The dBm unit
If we take one milliwatt as a reference then we have a unit of absolute power called dBm:
Where P1 is the power we want to express in dBm, in Watts
Power (linear) | Power (dBm)
10 W | 40 dBm
1 W | 30 dBm
100 mW | 20 dBm
10 mW | 10 dBm
1 mW | 0 dBm
10 µW | -20 dBm
1 µW | -30 dBm
1 nW | -60 dBm
1 pW | -90 dBm

## Slide 7: Goal: Power Budget
Receiver needs a certain SINR to be able to decode the signal
Factors reducing power budget:
  Noise, attenuation (multiple sources), longer range, fading
Factors improving power budget:
  Antenna gain, transmit power
Tx Radio
Rx Radio
PRX (dBm) = PTX (dBm) + Gains (dB) – Losses (dB)

## Slide 8: Large-Scale Channel Models
Goal: Predict average received signal strength given a transmitter-receiver separation distance

## Slide 9: Transmitting in Free Space
Deliver Watts to an omnidirectional transmitting antenna
So then power density (Watts per unit area) at range d is W/m2
  Independent of wavelength (frequency)
Total spherical surface area:
unit area

## Slide 10: Idealized Receive Antenna
Effective aperture : fraction of incident power density p captured and received
    Larger antennas at greater λ capture more power
So power received is the product of the power density and effective aperture:

## Slide 11: Antenna Gain
Antennas don’t radiate power equally in all directions
  Specific to the antenna design
Model these gains in the directions of interest between transmitter, receiver:
  Transmit antenna gain Gt
  Receive antenna gain Gr

## Slide 12: Friis Free Space Channel Model
Power received is the product of the power received by idealized antennas, times transmit and receive antenna gains:

## Slide 13: Ground Reflection (Two-Ray) Propagation Model
Commonly occurs in mobile cellular environments
Near transmitter: multipath oscillation due to constructive and destructive interference
Far from transmitter (), reflection always approximately out of phase with line of sight path: rapid attenuation
Transmitter
Receiver

## Slide 14: Today
Large scale channel models
Small-scale channel models
Equalization: Coping with the channel

## Slide 15: Small-scale versus large-scale modeling
Small-scale models: Characterize the channel over at most a few wavelengths or a few seconds

## Slide 16: Radio Propagation Mechanisms
reflection
scattering
diffraction
Reflection
  Propagation wave impinges on object large compared to λ
    e.g. the surface of the Earth, buildings, walls, etc.
Diffraction
  Path from transmitter to receiver obstructed by surface with sharp irregular edges
  Waves bend around obstacle, even when LOS (line of sight) does not exist
Scattering
  Objects smaller than radio wavelength (i.e. foliage, street signs etc.)

## Slide 17: Multipath Radio Propagation
Receiver gets multiple copies of signal
  Each copy follows different path, with different path length
  Copies can either strengthen or weaken each other
    Depends on whether they are in or out of phase
Enables communication even when transmitter and receiver are not in “line of sight”
  Allows radio waves effectively to propagate around obstacles, thereby increasing the radio coverage area
Transmitter, receiver, or environment object movement on the order of λ significantly affects the outcome
  e.g. 2.4 GHz  λ = 12 cm, 900 MHz  ≈ 1 ft

## Slide 18: Sinusoidal carrier, line of sight only
Baseband transmitted signal:
  Transmitted signal:
Represent path attenuation a, length d with a complex number:
  Complex channel
Received signal: (no noise)
Receiver
Transmitter
a, d, τ

## Slide 19: Adding a reflecting path
Channel is now
Conclusion: At different λ, fading is different in frequency
Receiver
Transmitter
h1 (a1=1,d1,τ1)
h2 (a2,d2,τ2)
h1
h2

## Slide 20: Reflections cause frequency selectivity
Interference between reflected and line-of-sight radio waves results in frequency dependent fading
Coherence bandwidth Bc: Frequency range over which the channel is roughly the same (“flat”)

## Slide 21: How does frequency selectivity arise? (Another look)
Receiver
Transmitter
Path 1
Path 2

## Slide 22: How does frequency selectivity arise? (Another look)
Path 1
(shorter):
Path 2
(longer):
Sum:
Receive antenna
 Distance from receive antenna
d2−d1

## Slide 23: Stationary transmitter, moving receiver
Suppose reflecting wall, fixed transmit antenna, no other objects
  Receive antenna moving rightwards at velocity v
Two arriving signals at receiver antenna with path length difference 2(d − r(t))
Receiver
antenna

## Slide 24: How does fading in time arise?
Path length difference
If  receive ≈ 0
  Destructive interference
If  receive ≈ 2
  Constructive interference
λ/2
λ
sum
Receiver
antenna

## Slide 25: Channel Coherence Time
Radio carrier frequency
  Speed of light: c; Wavelength of the signal: λ
Change in path length difference of λ/2 moves from constructive to destructive interference
  Receiver movement of λ/4: coherence distance
  Time transmitter, receiver, or objects in environment take to move a coherence distance: channel coherence time Tc
    Walking speed (2 mph) @ 2.4 GHz: ≈ 15 milliseconds
    Driving speed (20 mph) @ 1.9 GHz: ≈ 2.5 milliseconds
    Train/freeway speed (75 mph) @ 1.9 GHz: < 1 millisecond

## Slide 26: Another perspective: Doppler Effect
Movement by the transmitter, receiver, or objects in the environment creates a Doppler Shift
v 

## Slide 27: Stationary transmitter, moving receiver: From a Doppler Perspective
Doppler Shift of a path
  vradial is the radial component of the receiver’s velocity vector along the path
    Positive with decreasing path length, negative with increasing path length
Suppose v = 60 km/h, fc = 900 MHz
  Direct path , reflection path
Receiver
antenna

## Slide 28: Stationary transmitter, moving receiver: From a Doppler Perspective
Channel Doppler Spread Ds: maximum path Doppler shift, minus minimum path Doppler shift
Suppose v = 60 km/h, fc = 900 MHz
  Direct path , reflection path
  Doppler Spread: 100 Hz
Results in sinusoidal “envelope” at frequency Ds / 2:
Receiver
antenna
Received signal
5 ms

## Slide 29: Channel Coherence Time: From a Doppler Perspective
Sinusoidal “envelope” at frequency :
Transition from 0 to peak in
  So qualitatively significant change in time
    Alternate definition of channel coherence time
Received signal

## Slide 30: What does the channel look like in time?
Receiver
Transmitter
a1,d1,τ1
a2,d2,τ2
Channel impulse response h(t)
t
τ1
a1
a1
τ2
a2
Delay spread Td

## Slide 31: Power delay profile (PDP)
Power received via the path with excess time delay is the value (height) of the discrete PDP component at
P(τ) corresponds to |h(τ)|2
P(τ)
t
0

## Slide 32: Characterizing a power delay profile
Given a PDP sampled at time steps :
Mean excess delay : Expected value of
Root mean squared (RMS) delay spread measures the spread of the power’s arrival in time
  RMS delay spread is the variance of
, where
Maximum excess delay < X dB is the greatest delay at which the PDP is greater than X dB below the strongest arrival in the PDP

## Slide 33: Example Indoor PDP Estimation
Finite bandwidth of measurement normally results in continuous PDP
PDP typically has a decaying exponential form
Environment | RMS delay spread
Indoor cell | 10 – 50 ns
Satellite mobile | 40 – 50 ns
Open area (rural) | < 0.2 𝛍s
Suburban macrocell | < 1 𝛍s
Urban macrocell | 1 – 3 𝛍s
Hilly macrocell | 3 – 10 𝛍s
Typical RMS delay spreads

## Slide 34: Indoor power delay profile

## Slide 35: Flat Fading
Slow down  sending data over a narrow bandwidth channel
  Channel is constant over its bandwidth
  Multipath is still present, so channel strength fluctuates over time
    How to model this fluctuation?
Channel
Not shown above!

## Slide 36: Rayleigh Fading Model
Random gain of kth arriving path:
Therefore, the I and Q channel components are zero-mean Gaussian distributed
So is Rayleigh-distributed
Rayleigh PDF
Channel impulse response h(t)
t
τ1
a1
τ2
a2
a3
τ3

## Slide 37: Rayleigh fading example

## Slide 38: Putting it all Together: Ray Tracing
Approximate solutions to Maxwell’s electromagnetic equations by instead representing wavefronts as particles, traveling along rays
  Apply geometric reflection, diffraction, scattering rules
    Compute angle of reflection, angle of diffraction
Error is smallest when receiver is many λ from nearest scatterer, and all scatterers are large relative to λ
Good match to empirical data in rural areas, along city streets (radios close to ground), and indoors
Completely site-specific
  Changes to site may invalidate model

## Slide 39: Today
Large scale channel models
Small-scale channel models
Equalization: Coping with the channel

## Slide 40: Problem: Inter-symbol interference (ISI)
Transmitted signal
Received signal with ISI

## Slide 41: Problem: Inter-symbol interference (ISI)
Transmitted signal
Received signal with ISI
ISI at one symbol depends on the value of other symbols

## Slide 42: One Solution: Slow down
Transmitted signal
Received signal
No ISI
1

## Slide 43: Channel Model
p(t)
Transmit filter
dk
h(t)
h*(-t)
heq(t)
yt
y[n]
Matched filter
Equalizer
Transmitter
Receiver
Wireless Channel
Composite channel (made up of pulse shape, radio channel, and matched filter)

## Slide 44: Another Solution I: Zero-forcing Equalizer
h*(-t)
heq(t)
yt
y[n]
Matched filter
Equalizer
Receiver
+
Noise: nk

## Slide 45: Preamble
Sequence of symbols known to both transmitter & receiver
Preamble
Packet body

## Slide 46: Another Solution II: MSE Equalizer
Goal: Minimizing mean-squared error (MSE) between received symbols & transmitted symbols
Assumes Receiver has a preamble

## Slide 47: Another Solution III: Decision-feedback Equalizer
Idea: Subtract the interference caused by already detected data (symbols)
w (t)
Forward filter
+
d(t)
Decision device
This part shapes the signal to work well with the decision feedback.
This part removes ISI on “future” symbols from the currently detected symbols.
Feedback filter
h*(-t)
yt
y[n]
Matched filter
+
Noise: nk
+
-

## Slide 48: Another Solution III: Decision-feedback Equalizer
The forward filter w(t) here uses a linear equalizer
  e.g., zero-forcing, MSE
The DFE has access to the symbol decisions
w (t)
Forward filter
+
d(t)
Decision device
Feedback filter
h*(-t)
yt
y[n]
Matched filter
+
Noise: nk
+
-

## Slide 49
Thursday Topic:
OFDM
Friday Precept:
Lab 4: BPSK Radio