## Slide 1: MIMO III: Channel Capacity, Interference Alignment
COS 463: Wireless Networks
Lecture 18
Kyle Jamieson
[Parts adapted from D. Tse]

## Slide 2: Today
MIMO Channel Degrees of Freedom
MIMO Channel Capacity
Interference Alignment

## Slide 3: Review: The MIMO Channel
Transmit three symbols per symbol time:
Represent the MIMO channel as
  is the MIMO channel matrix, noise
antenna separation
Send x1, x2, x3
Receive y1, y2, y3
1
2
3
1
2
3

## Slide 4: Recap: MIMO Radio Channel
MIMO link with nt transmit, nr receive antennas
MIMO radio channel itself:

## Slide 5: Recap: Zero-Forcing MIMO
Transmitter does not know H (CSI)
Each symbol time:
  Sends nt symbols (original Data), one per transmit antenna
Data arrives mixed together at receiver antennas y
Sender
Receiver

## Slide 6: Recap: Zero-Forcing MIMO
Receiver knows H (CSI)
Each symbol time:
  Receive nr mixed-up signals y
  For each of the nt transmitted symbols:
    Zero-Forcing Receiver nulls all but that symbol

## Slide 7: How Many Streams are Possible?
Received signals live in an nr-dimensional vector space
  e.g. nr = 3 receive antennas  3-D vector space:
Cancel by projection. Therefore, at most nr streams possible

## Slide 8: How Many Streams are Possible?
One spatial signature per transmit antenna
  e.g. nr = 3 receive, nt = 2 transmit antennas:
Therefore, at most nt streams possible
h1
h2

## Slide 9: How Many Streams are Possible?
Need enough strong physical paths in the wireless channel
  e.g. nr = 3, nt = 3 but two physical paths confines { hi } to a plane
At most # physical paths possible streams
h1
h2
h3

## Slide 10: How Many Streams are Possible?
Need enough strong physical paths in the wireless channel
  e.g. nr = 3, nt = 3 and three physical paths
At most # physical paths possible streams
h1
h2
h3
h1

## Slide 11: Degrees of Freedom
Figure of merit that summarizes number of streams possible is called degrees of freedom of H
Degrees of freedom = min { nt, nr, # strong paths }
h2
h3
h1

## Slide 12: Today
MIMO Channel Degrees of Freedom
MIMO Channel Capacity
  Vector Space Intuition
  Eigenmode Forcing via Singular Value Decomposition
Interference Alignment

## Slide 13: MIMO Channel Capacity: Motivation
The story so far: Copy data into each symbol time
  Looked at when this performed well, poorly
    Answer: MIMO channel conditioning  “Rich multipath environment” around sender, receiver
* * *
Today’s first topic: Is this the best bits/seconds/Hz possible?
  What’s the capacity of a MIMO channel?
    Similar question: Shannon capacity of a single-input, single-output (SISO) channel

## Slide 14: Where’s the Room for Improvement?
Suppose the transmitter knows H (CSI)
Zero-forcing receiver heard h1, h2, h3
  Power loss at receiver (due to Proj⟘) for h3
Idea: Use transmit antennas 2 and 3 to send the ideal direction
  No longer simply one symbol, one transmit antenna
h2
Send this instead of h3
h1
h3

## Slide 15: How Might We Control Directions?
Sender precodes data into actual transmission in desired directions x
Receiver processing changes accordingly
Sender
Receiver

## Slide 16: What Kind of Precoding?
Recall, we wanted to make independent channels on each wireless channel path
Suppose H were diagonal:
Then the yk channel output would only depend on xk
  Parallel, independent channels

## Slide 17: Today
MIMO Channel Degrees of Freedom
MIMO Channel Capacity
  Vector Space Intuition
  Eigenmode Transmission
Interference Alignment

## Slide 18: Singular Value Decomposition (SVD)
The insight lies in a special way of “factoring” matrix H
Any matrix H has an SVD: H  UΛV*
  Λ is a diagonal matrix (contains zeroes off-diagonal)
  U and V are unitary (UU* = U*U = VV* = V*V = I)
H
=
nt
nr
Λ
nt
nr
V*
×
nt
nt
U
×
nr
nr

## Slide 19: Interpreting the SVD Steps
Λ matrix with the singular values
  One per significant radio channel path
V* translates to the radio channel path coordinate system where channels are decoupled
U translates back, to antenna coordinate system (undoes the V* translation)
H
=
nt
nr
Λ
nt
nr
V*
×
nt
nt
U
×
nr
nr

## Slide 20: Leveraging the SVD in a Practical System
  Alone, SVD does nothing (just analyzes what H does)
  Want to put data into the radio channel coordinate system
Want here 
Insight: VV* = I (Unitary property)

## Slide 21: Leveraging the SVD in a Practical System
  Sender precodes with V, receiver “post-codes” with U*
    V is unitary, so V*V = I (same for U)
      So data sees independent channels
  This is called MIMO eigenmode transmission
Sender
Receiver
No effect

## Slide 22: A Model for Eigenmode Transmission
Performance model for the eigenmode transmitter/receiver
All channels decoupled, transmit power Pk  SNR on ith channel:
Sender
Receiver

## Slide 23: Performance: Uniform Power Division
  At high SNR (the common case in wireless LANs), with total transmit power P evenly divided over spatial paths
  Data rate =
  * * *
  How can we do better?
    Idea: Allocate different transmit powers to different radio channel paths i
    Problem we’ve seen before in 463 in OFDM context

## Slide 24: Waterfilling for MIMO Power Allocation
Physical Channel Path / Eigenmode i
μ
Allocated transmit power Pi

## Slide 25: MIMO Capacity: Takeaways
OFDM – MIMO analogy:
  A transformation (OFDM: FFT, MIMO: SVD)
  renders interfering channels in
  (OFDM: frequency, MIMO: space) independent
MIMO Eigenmode transmission:
  Transmitter sends directionally, along spatial paths of the radio channel
  Receiver listens directionally, along same spatial paths
  Achieves the MIMO channel capacity

## Slide 26: Today
MIMO Channel Degrees of Freedom
MIMO Channel Capacity
Interference Alignment

## Slide 27: Interference Alignment (IA)
Number of concurrent MIMO streams a client can send is limited by the number of antennas
  Sending more streams results in interference between streams
  Also limited by the amount of multipath in the environment
New Idea: Use MIMO precoding techniques to align interference at receivers to advantage
Requires APs cooperating via a wired backhaul
  e.g. APs owned by one organization

## Slide 28: MIMO channel representation
As before, model channel from one antenna i to another j as one complex number
Channel matrix H from a client to an AP is formed by []

## Slide 29: Uplink: Interference Between Networks
Client 1 has 2 packets for AP 1; Client 2 has a packet for AP 2
  Two-antenna APs, so each decoding in a 2-D space
Three packets form three vectors in the 2-D space at each AP
  Therefore, the APs can’t decode these 3 packets
1
2
1
2

## Slide 30: Interference alignment: Basic idea (1)
Clients transmit p2 and p3 aligned at access point (AP) 1
  They add up in their one direction
AP 1 zero-forces to decode p1, sends it over backhaul to AP 2
AP 2 subtracts p1 from the signal it receives, cancelling it
1
2
1
2

## Slide 31: Interference alignment: Basic idea (2)
AP 2 uses zero-forcing receiver to decode p2, p3
AP 2 sends p2 to AP 1 (or onward on behalf of client 1)
1
2
1
2

## Slide 32: Uplink: Sketching a Practical Protocol
Client 2 chooses v3 so that H11v2 = H21v3
  How does client 2 know H11 and H21?
    Client 1 can include in its packet header
1
2
1
2
Transmit precoding: client multiplies packet by vector v
  Changes alignment at receiver
Client 1 picks random precoding vectors v1 and v2
Client 1 begins transmission

## Slide 33: Uplink: Four Concurrent Packets?
All packets but one (p1) must align at AP 1, so AP 1 can decode
Subtract p1 from the four packets at AP 2, leaving three packets
AP 2 can only decode two packets at a time (2-d space)
  Can’t decode p3 and p4 at AP 2: Can only decode p1 and p2
1
2

## Slide 34: Downlink Interference Alignment
Clients can’t exchange frames over backhaul
Instead, align neighboring APs’ interference at each client
p2, p3 aligned:
p1, p3 aligned:
p1, p2 aligned:

## Slide 35
Thursday Topic:
Multiuser Channel Capacity