## Slide 1: Multiuser Communication and Capacity
COS 463 Wireless Networks
Lecture 19
Kyle Jamieson
Notes: Today we’ll go back to single-antenna systems and revisit questions of Capacity and communication.
2018 Notes:

## Slide 2: Review: Shannon Capacity
Capacity, or maximum rate that a Gaussian channel supports arbitrarily-low bit error rates is
Reliable communication possible at rates R < C, not possible when R > C
Notes: Today we’re going to GENERALIZE this to beyond simple links.

## Slide 3: Review: Sharing the Wireless Medium
Uplink to Alice, Cathy and Bob both want to deliver information
Contention-based: Unstructured, taking turns in time
TDMA: Scheduled turns in time
FDMA: Sharing via Different Frequency Bands
CDMA: Sharing via Different Codes
What’s the best we can do?
Alice
Cathy
Bob

## Slide 4: Today: Multiuser Capacity
Building atop Shannon capacity of a single link:
What’s the best we can do in the multiuser uplink channel?
What’s the best we can do in the multiuser downlink channel?
Notes: Building on Shannon Capacity of a single link

## Slide 5: Two-User Interference Channel
On the same frequency channel at the same time:
  Sender 1 sends signal x1 with power P1
  Sender 2 sends signal x2 with power P2
AP receives: y[m] = x1[m] + x2[m] + w[m]
  w[m] is background Gaussian Noise with variance σ2
Sender 1
Sender 2
AP
Notes: Two concurrent sender radios; one receiver radio.
Note: No radio channel, but we can model that as different powers transmitted.

## Slide 6: Extension of Capacity to Multiple Users
Single-channel Shannon capacity is a single rate (bits/s/Hz)
Generalizing for two users capacity becomes a region:
  Set of all pairs such that simultaneously,
    User 1 can communicate at rate R1 and
    User 2 can communicate at rate R2
  Tradeoff between reliable communication rates:
    If User 1 wants to increase its rate, User 2 may need to decrease its rate
Notes: TRADEOFF E.G.: in OFDM you vary the number of subcarriers you give to each user. TDMA, vary timeslots.

## Slide 7: Two-User Interference Channel: Single-User Bounds
User 2’s rate
User 1’s rate
User 1 sending alone
User 2 sending alone
Notes: Plotting rates on both axes: rate region
>>> R1 less than p2p link w/o other user
>>> R2 less than p2p link w/o other user

## Slide 8: Interference Doesn’t Help
Assumption: User 1’s data are completely independent from User 2’s data, and vice-versa
Thought exercise: Point-to-point link sending with power
  Must outperform interfering link (otherwise interference helps)
So therefore,
Notes: >>> R1 + R2 cannot exceed capacity of a p2p link with sum of the two users’ power.
(Otherwise, an interfering user would increase capacity).

## Slide 9: Two-User Interference Channel: Capacity Region
User 2’s rate
User 1’s rate
Notes: So the capacity region looks like this.
>>> Surprising part is we can operate HERE.
MAX RATE for USER 1, good rate for USER 2.
DECODE USER 2, treating USER 1 like interference.

## Slide 10: Successive Interference Cancellation (SIC)
Receiver decodes information from both senders in three stages:
Decode data of user 2, treating signal from user 1 as noise
Reconstruct user 2’s signal (x’2[m]) from decoded data and subtract from aggregate received signal y[m], cancelling it:
  y’ [m] = y [m] − x’2[m]
  = x1[m] + (x2[m] – x’2[m]) + w[m]
Decode user 1’s signal from y’[m]

## Slide 11: SIC: Choice of User Order
User 2’s rate
User 1’s rate
Notes: P2 stronger than P1
Choosing stronger user first is more practical for implementation
Choosing weaker user first gives better rate fairness

## Slide 12: Comparison with CDMA
CDMA: Every user decoded treating the other users as noise
  Achieves Point C
    But, User 1 starves
CDMA power control: Reduce power of the strong user
  Achieves Point D

## Slide 13: Comparison with TDMA/FDMA
Allocate α time- or frequency-fraction to User 1; 1 − α to User 2
Scale each user’s power according to allocated proportion
User 1 maximum rate:
User 2 maximum rate:

## Slide 14: Comparison with TDMA/FDMA
Allocate as follows:
  α time- or frequency-fraction to User 1;
  1 − α to User 2
Tuning α (time/frequency and power) to P1, P2 can achieve a point on the A-B curve (optimal)

## Slide 15: Today: Multiuser Capacity
Building atop Shannon capacity of a single link:
What’s the best we can do in the multiuser uplink channel?
What’s the best we can do in the multiuser downlink channel?
  Unknown information streams
  Taking content of the data into account
Notes: Building on Shannon Capacity of a single link

## Slide 16: Two-User Downlink Channel
On the same frequency channel at the same time:
  User 1 receives signal x1 with power P1
  User 2 receives signal x2 with power P2
AP receives: y[m] = x1[m] + x2[m] + w[m]
  w[m] is background Gaussian Noise with variance σ2
User 1
User 2
AP

## Slide 17: Superposition Coding
User 2 alone
QPSK signal
User 1 alone
QPSK signal
User 1 and 2 Superposition

## Slide 18: Decoding Strong BPSK with weak QPSK
“1”
“0”
I
Q
−1
+1
Input bit=“0”
Input bit=“1”
BPSK model
“10”
“00”
“01”
“11”
=
=
Interference-cancelled QPSK
BPSK decoding
BPSK
symbol
decisions
−
−
Received r(t)

## Slide 19: Power Difference Helps Superposition Coding
I
Q
−1
+1
Input bit=“0”
Input bit=“1”
−
Notes: explain on board X’s and O’s

## Slide 20: Today: Multiuser Capacity
Building atop Shannon capacity of a single link:
What’s the best we can do in the multiuser uplink channel?
What’s the best we can do in the multiuser downlink channel?
  Unknown information streams
  Taking content of the data into account
Notes: Building on Shannon Capacity of a single link

## Slide 21: Precoding for Known Interference
Scenario: Hide digital data in an analog TV broadcast
AP transmitting on downlink to user overhears broadcast
  Sends digital data x intended for User 1
  s is the stronger analog TV broadcast signal
Background noise w
TV receiver
TV broadcast
AP
Receives:
y = x + s + w

## Slide 22: Precoding for Known Interference
Want to distort TV broadcast signal s minimally
Suppose we want to send one of four in-phase symbols (no Q):
In-Phase
TV receiver
TV broadcast
AP
Receives:
y = x + s + w

## Slide 23: Precoding for Known Interference
Want to distort TV broadcast s minimally
Suppose we want to send one of four in-phase symbols (no Q):
Large distortion

## Slide 24: Tomlinson-Harashima Precoding
Suppose we want to send one of four in-phase symbols (no Q):
Idea: Replicate constellation across amplitudes:
Transmit closest replicated constellation point:

## Slide 25: Tomlinson-Harashima: Summary
Effect is like superposition coding
Choosing closest replicated constellation group minimizes power
  Transmitted signal depends on the interfering signal
Result: Hide digital information in the analog transmission

## Slide 26
Friday Precept:
Lab 4 Hackathon
Tuesday Topic:
Low-Power Wireless Communication