## Slide 1: End-to-End Transport Over Wireless I: Preliminaries, Split Connection
COS 463: Wireless Networks
Lecture 2
Kyle Jamieson
[Various parts adapted from S. Das, B. Karp, N. Vaidya]

## Slide 2: Today
Layering and the End-to-End Argument
Transmission Control Protocol (TCP) primer
Split Connection TCP over wireless

## Slide 3: Layering: Motivation
Re-implement every application for every new underlying transmission medium?
  Change every application on any change to an underlying transmission medium (and vice-versa)?
No! But how does the Internet design avoid this?
Applications
Transmission
media
Skype
Web
SSH
FTP
Coaxial cable
Fiber optic
Wi-Fi
?

## Slide 4: Internet solution: Intermediate layers
Intermediate layers provide a set of abstractions for applications and media
New applications or media need only implement for intermediate layer’s interface
Applications
Transmission
media
Skype
HTTP
SSH
FTP
Coaxial cable
Fiber optic
Wi-Fi
Intermediate layers

## Slide 5: Properties of layers
Service: What a layer does
Service interface: How to access the service
  Interface for the layer above
Application
Transport
Network
Link
Physical
Protocol interface: How peers communicate to implement service
  Set of rules and formats that govern the communication between two Internet hosts

## Slide 6: Physical layer (L1)
Service: Move bits between two systems connected by a single physical link
Interface: specifies how to send, receive bits
  e.g., require quantities and timing
Protocols: coding scheme used to represent bits, voltage levels, duration of a bit

## Slide 7: Data link layer (L2)
Service: End hosts exchange atomic messages
  Perhaps over multiple physical links
    But using same framing (headers/trailers)
  Arbitrates access to common physical media
  Implements reliable transmission, flow control
Interface: send messages (frames) to other end hosts; receive messages addressed to end host
Protocols: Addressing, routing, medium access control

## Slide 8: Network layer (L3)
Service: Deliver datagrams to other networks
  Cross-technology (e.g., Ethernet, 802.11, optical, …)
  Possibly includes packet scheduling/priority
  Possibly includes buffer management
  Best effort service: may drop, delay, duplicate datagrams
Interface:
  Send packets to specified internetwork destination
  Receive packets destined for end host
Protocols:
  Define inter-network addresses (globally unique)
  Construct routing tables and forward datagrams

## Slide 9: Transport layer (L4)
Service: Provide end-to-end communication between processes on different hosts
  Demultiplex communication between hosts
  Possibly reliability in the presence of errors
  Rate adaptation (flow control, congestion control)
Interface: send message to specific process at given destination; local process receives messages sent to it
Protocol: perhaps implement reliability, flow control, packetization of large messages, framing

## Slide 10: Who does what?
Five layers
  Lower three layers are implemented everywhere
  Top two layers are implemented only at end hosts
    Their protocols are end-to-end
Application
Transport
Network
Link
Physical
Network
Link
Physical
Host A
Router
Application
Transport
Network
Link
Physical
Host B

## Slide 11: Logical communication
Each layer on a host interacts with its peer host’s corresponding layer via the protocol interface
Application
Transport
Network
Link
Physical
Network
Link
Physical
Host A
Router
Application
Transport
Network
Link
Physical
Host B

## Slide 12: Physical path across the Internet
Communication goes down to physical network
Then from network peer to peer
Then up to the relevant layer
Application
Transport
Network
Link
Physical
Network
Link
Physical
Host A
Router
Application
Transport
Network
Link
Physical
Host B

## Slide 13: Protocol multiplexing
Multiplexing: Multiple overlying protocols share use of a single underlying protocol
Problem: How does the underlying protocol decide which overlying protocol messages go to?
Applications
Network
Host A
TCP
UDP
Applications
Network
Host B
TCP
UDP
???

## Slide 14: Protocol headers
Each layer attaches its own header (H) to facilitate communication between peer protocols
On reception, layer inspects and removes its own header
  Higher layers don’t see lower layers’ headers
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical
Host A
Host B
data
data
H
H
data
H
H
H
data
H
H
H
H
H
data
H
H
H
H
data
H
H
data
H
H
data
H
data
H
data

## Slide 15: Encapsulation in the Internet
Host A
application
L3 Router
L2 Switch
message
data
transport
network
link
physical
segment
data
H
datagram
H
data
H
frame
H
H
data
H
H
H
H
H
data
frame
link
physical
network
link
physical
H
H
data
H
H
H
H
H
data
H
H
data
H
H
data
H
H
H
data
H
H
H
H
H
data
H
data
H
Host B
application
data
transport
network
link
data
H
H
data
H
H
H
data
H
H
H
H
H
data
physical

## Slide 16: Protocol demultiplexing
Host A
application
Lower-layer header contains demultiplexing information
Network header contains Protocol field specifying overlying protocol
message
data
transport
network
segment
data
H
datagram
H
data
H
application
transport
network
data
H
H
data
H
Applications
Network
Host B
TCP
UDP
???
Host B

## Slide 17: Drawbacks of layering
Layer n may duplicate lower level functionality
  e.g., error recovery to retransmit lost data
Layers may need same information in headers
  e.g., timestamps, maximum transmission unit size
Layering can hurt performance
  e.g., previous lecture

## Slide 18: Layer violations
Two types:
Overlying layer examines underlying layer’s state
  e.g., transport monitors wireless link-layer to see whether packet loss from congestion or corruption
Underlying layer inspecting overlying layer’s state
  e.g., firewalls, NATs (network address translators), “transparent proxies”

## Slide 19: Today
Layering and the End-to-End Argument
  Reading: “End-to-End Arguments in System Design” by Saltzer, Reed, Clark
Transmission Control Protocol (TCP) primer
Split Connection TCP over wireless

## Slide 20: Motivation: End-to-End Argument
Five layers in the Internet architecture model
Five places to solve many of same problems:
  In-order delivery
  Duplicate-free delivery
  Reliable delivery after corruption, loss
  Encryption
  Authentication
In which layer(s) should a particular function be implemented?

## Slide 21: Example: Careful file transfer from A to B
Goal: Accurately copy file on A’s storage to B’s storage
Straw man design:
  Read file from A’s storage
  A sends packetized file to B
    Link layer resends lost or corrupted packets at each hop
  B writes file data to storage
Does this system meet the design goal? Bit errors on links no issue
A
B
data
LL ACKs

## Slide 22: Where might errors happen?
On A’s or B’s disk
In A’s or B’s RAM or CPU
In A’s or B’s software
In the RAM, CPU, or software of any router that forwards packet
Why might errors be likely?
  Drive for CPU speed and storage density: pushes hardware to EE limits, engineered to tight tolerances
    e.g., today’s disks return data that are the output of an maximum-likelihood estimation!
  Bugs abound!

## Slide 23: Solution: End-to-End verification
A keeps a checksum with the on-disk data
  Why not compute checksum at start of transfer?
B computes checksum over received data, sends to A
A compares the two checksums and resends if not equal
Can we eliminate hop-by-hop error detection?
Is a whole-file checksum, alone, enough?

## Slide 24: End-to-End Principle
Only the application at communication endpoints can completely and correctly implement a function
Processing in middle alone cannot provide function
  Processing in middle may, however, be an important performance optimization
Engineering middle hops to provide guaranteed functionality is often wasteful of effort, inefficient

## Slide 25: Perils of lower-layer implementation
Entangles application behavior with network internals
Suppose each IP router reliably transmitted to next hop
  Result: Lossless delivery, but variable delay
    ftp: Okay, move huge file reliably (just end-to-end TCP works fine, too, though)
    Skype: Terrible, jitter packets when a few corruptions or drops not a problem anyway
Complicates deployment of innovative applications
  Example: Phone network v. the Internet

## Slide 26: Advantages of lower-layer implementation
Can improve end-to-end system performance
Each application author needn’t recode a shared function
Overlapping error checks (e.g., checksums) at all layers invaluable in debugging and fault diagnosis
If end systems not cooperative (increasingly the case), only way to enforce resource allocation!

## Slide 27: End-to-end violation: Firewalls
Firewalls clearly violate the e2e principle
  Endpoints are capable of deciding what traffic to ignore
  Firewall is entangled with network, transport, apps, & vice-versa
    e.g.: New header bit to improve congestion control? Many firewalls filter all such packets!
Yet, we probably do need firewalls
Our network
X
Firewall
Internet

## Slide 28: Summary: End-to-End principle
Many functions must be implemented at application endpoints to provide desired behavior
  Even if implemented in “middle” of network
End-to-end approach decouples design of components in network interior from design of applications at edges
  Some functions still benefit from implementation in network interior at cost of entangling interior, edges
End-to-end principle is not sacred; it’s just a way to think critically about design choices in communication systems

## Slide 29: Five-minute break and Partner Exercises
The end-to-end argument is:
  A guideline for placing functions in computer systems
  A rule for placing functions in a computer system
  A debate on where to place functions in a computer system
  A debate about anonymity in computer networks
Of the following, the best example of an end-to-end argument is:
  If you laid all the web programmers in the world end to end, they would reach from Princeton to CERN
  Every byte going into the write end of a UNIX pipe eventually emerges from the pipe’s read end
  Even if a chain manufacturer tests each link before assembly, they had better test the completed chain
  All important network communication functions should be moved to the Application layer

## Slide 30: Today
Layering and the End-to-End Argument
Transmission Control Protocol (TCP) primer
  Over wired networks
  Reading: “Congestion Avoidance and Control” by Jacobson and Karels
TCP over wireless

## Slide 31: TCP: Connection-Oriented, Reliable Byte Stream Transport
Layer-four protocol for reliable transport
  Sending app offers a sequence of bytes: d0, d1, d2, …
  Receiving app sees all bytes arrive in same sequence: d0, d1, d2…
    Result: Reliable byte stream transport between endpoints on the internet
Each such byte stream is called a connection, or flow

## Slide 32: TCP’s Many End-to-End Goals
Recover from data loss
Avoid receipt of duplicated data
Preserve data ordering
Provide integrity against corruption
Avoid sending faster than receiver can accept data
Avoid congesting network

## Slide 33: Fundamental Problem: Ensuring At-Least-Once Delivery
Network drops packets, so to ensure delivery:
  Sender attaches sequence number (seqno) to each data packet sent; keeps copy of sent packet
  Receiver returns acknowledgement (ACK) to sender for each data packet received, containing seqno
Sender sets a retransmit timer on each transmission
  If timer expires < ACK returns: retransmit that packet
  If ACK returns, cancel timer, forget that packet
How long should the retransmit timer be?

## Slide 34: Fundamental Problem: Estimating RTT
Expected time for ACK to return is round-trip time (RTT)
  End-to-end delay for data to reach receiver, then its ACK to reach sender
Strawman: use fixed timer (e.g., 250 milliseconds)
  What if the route/wireless conditions change?
  What if congestion occurs at one or more routers?
Too small a value: needless retransmissions
Too large a value: needless delay detecting loss
Fixed timer violates E2E argument; details of link behavior should be left to link layer!
Hard-coded timers lead to brittle behavior as technology evolves

## Slide 35: Estimating RTT: Exponentially Weighted Moving Average (EWMA)
Measurements of RTT readily available
  Note time t when packet sent, corresponding ACK returns at time t’
  RTT measurement sample: m = t’− t
Single sample too brittle (queuing, routing dynamic)
Adapt over time, using EWMA:
  Measurement samples: m0, m1, m2, …
  fractional weight for new measurement, α
  RTTi = ((1 − α) × RTTi-1 + α × mi)
EWMA weights newest samples most
How to choose α? (TCP uses 1/8)
Is mean sufficient to capture RTT behavior over time? (more later)

## Slide 36: What is Congestion?
Sources may have sufficient proximal link capacity to send
But in the middle of the network may share capacity
Too many packets in the network  queue overflows: congestion

## Slide 37: How does TCP know congestion occurred?
How can packets get lost in wired networks?
  Almost exclusively queue buffer overflows
Packet loss is a binary signal
How does a TCP sender know that a packet loss has occurred?
  Lack of receipt of an Acknowledgement  Timeouts

## Slide 38: Retransmission and Duplicate Delivery
When sender’s retransmit timer expires, two indistinguishable cases:
  Data packet dropped en route to receiver, or
  ACK dropped en route to sender
In both cases, sender retransmits
In latter case, duplicate data packet reaches receiver!

## Slide 39: Eliminating Duplicates: Exactly-Once Delivery
Sender marks each packet with a monotonically increasing sequence number seqno
Sender includes greatest ACKed seqno in its packets
Receiver remembers only greatest received sequence number, drops received packets with smaller ones
Doesn’t guarantee delivery!
Properties: If delivered, then only once.
If undelivered, sender will not think delivered.
If ACK not seen, data may have been delivered, but sender will not know.

## Slide 40: End-to-End Integrity
Achieved by using transport checksum
Protects against things link-layer reliability cannot:
  Router memory corruption, software bugs, &c.
Covers data in packet, transport protocol header
Also should cover layer-3 source and destination!
  Misdelivered packet should not be inserted into data stream at receiver, nor should be acknowledged
  Receiver drops packets w/failed transport checksum

## Slide 41: Today
Networking primer/review
Transmission Control Protocol (TCP) primer
TCP over wireless

## Slide 42: Running TCP on Wireless Links
Generally, TCP interprets packet loss as queue congestion
  TCP sender reduces congestion window
Wireless links have higher bit error rates, frame loss rates
On wireless links, packet loss can also occur due to random channel errors, or cellular or WLAN handoffs
  Temporary loss not due to congestion
  Reducing window may be too conservative
  Leads to poor throughput

## Slide 43: Wireless can also Cause Packet Loss
Bob
Alice
Dave
Cathy
Shared wireless medium leads to a collision of Bob and Cathy’s packets at Alice

## Slide 44: Wired & Wireless Mix: Best TCP sender strategy becomes unclear
Wired links:
Congestion loss
Link loss
Frequent
(queue drop)
Wireless link:
Frequent
(collision)
Frequent
(multipath, interference)
Rare
Slow down!
Maintain rate
loss
loss
?

## Slide 45
Fundamental question:
How to differentiate between
Loss due to congestion
Loss due to wireless link itself
Hard to do:
TCP is fundamentally an “end-to-end”
protocol: only sees a loss

## Slide 46: Two Broad Approaches
Mask wireless losses from TCP sender
  Then TCP sender will not slow down
  Split Connection Approach
  TCP Snoop
Explicitly notify TCP sender about cause of packet loss

## Slide 47: Split Connection Approach
Also called Indirect TCP (I-TCP)
Divide the TCP connection into two parts:
  TCP connection between content server and AP
  Another connection between AP and mobile host
  No real end-to-end connection
No changes to the TCP endpoint at the content server
Wireless
(One hop)
Multi-hop Wired Internet
Access point (AP)
Mobile
Content server

## Slide 48: Split Connection: TCP Implementation
Application
Transport
Network
Link
Physical
Maintain state for both “halves” of each end-to-end “connection” at the AP
Wireless link
Retransmit
Per-TCP connection state
TCP
Reliable transport
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical

## Slide 49: Split Connection: Considerations
Connection between AP and mobile need not be TCP
  Could be e.g., Selective Repeat over UDP
Assume that the wireless part is just one hop (traditional cellular or wireless LAN)
Assumes wireless losses not caused by too many packets in the network
  But that’s not always true (e.g. collisions)
    Sender should slow down, but doesn’t

## Slide 50: Split Connection: State Migration
Consequence of breaking end-to-end connection:
  On handoff from AP 1 to AP 2, connection state must move from AP 1 to AP 2
Wireless
(One hop)
Multi-hop Wired Internet
AP 1
Mobile
Content server
AP 2

## Slide 51: Split Connection: Advantages
No changes needed in wired network or content servers
Transmission errors on the wireless link do not propagate into the fixed network
  Local recovery from errors
Possibility of using custom (optimized) transport protocol for the hop between AP and mobile

## Slide 52: Split Connection: Critique
Loss of end-to-end semantics:
  ACK at TCP sender no longer means that receiver must have received that packet
    TCP no longer reliable if crash/bug at AP
Large buffer space may be needed at AP
AP must maintain per-TCP connection state
State must be forwarded to new AP on handoff
  May cause higher handoff latency

## Slide 53
Precepts
Python Intro & Programming Exercises
Location: Friend Center, Room 003
Tuesday Lecture
Transport over Wireless II: Snoop
and Explicit Loss Notification