## Slide 1: Bit Rate Adaptation and Rateless Codes
COS 463: Wireless Networks
Lecture 10
Kyle Jamieson
[Parts adapted from H. Balakrishnan, M. Vutukuru]

## Slide 2: Today
Bit Rate Adaptation
  Modulation
  Bit error rate (BER) and signal to noise ratio (SNR)
  Adapting modulation and error control coding
Rateless Codes: Spinal Codes

## Slide 3: What is modulation?
Modulate means to change. Change what?
  The amplitude and phase (angle) of a radio carrier signal
Digital modulation: Use only a finite set of choices (i.e., symbols) for how to change the carrier and phase
amplitude
phase
symbol
In-phase (I)
Quadrature (Q)

## Slide 4: From information bits to symbols…
Pick two symbols (binary)
  The information bit decides which symbol you transmit
  Phase shift of 180 degrees between the two symbols, so called binary phase shift keying
I
Q
Input bit=“0”
Input bit=“1”

## Slide 5: …and back to bits!
Received BPSK constellation
“0”
“1”
Decision region
Decision boundary
Received symbols

## Slide 6: From bits to symbols, twice as fast
I
Q
Input
bits=“00”
Input
bits=“10”
Sending log2 4 = 2 bits/symbol
Input
bits=“11”
Input
bits=“01”
Quadrature phase shift keying (QPSK)

## Slide 7: …and back to bits, twice as fast!
Received QPSK constellation
“00”
“11”
“10”
“01”

## Slide 8: Change modulations, increase bitrate
Binary Phase-Shift
Keying (BPSK)
Quadrature Phase-Shift
Keying (QPSK)
16-Quadrature Amplitude
Modulation (16-QAM)

## Slide 9: The wireless channel
Received signal: r(t) = s(t) + noise
I
Q
−1
+1
Input bit=“0”
Input bit=“1”
Transmitted signal: s(t)

## Slide 10: Signal­ to ­Noise Ratio (SNR)
Signal-to-Noise Ratio (SNR) measures power ratio between a signal of interest and background noise:
SNR (dB) | SNR
30 | 1,000
20 | 100
10 | 10
0 | 1 (equal)
-10 | 0.1
-20 | 0.01
-30 | 0.001
SNR is often expressed in decibels (dB), 10 times the base-10 logarithm of a quantity:

## Slide 11: Visualizing Signal to Noise Ratio
Signal view:
Constellation
view:

## Slide 12: Modulation adaptation

## Slide 13: Bit Rate Adaptation in the Physical Layer
source bits
Channel encoder
Modulation (BPSK, QPSK, …)
k bits
n bits
Code rate: R = k/n
Demodulation
source bits
Channel decoder
n bits
k bits

## Slide 14: 802.11: adapt code rate, modulation

## Slide 15: BER vs SNR

## Slide 16: Packetized throughput
Throughput = delivery rate × bitrate = (1 − BER)n × bitrate
n = 1500 × 8 bits

## Slide 17: Link/PHY checks packet integrity
Link layer
packet
Physical layer
  Change modulation
  Change coding rate
Network layer
Frame checksum: pass only entirely correct frames
BER
Packet delivery rate = (1−BER)n
Throughput = delivery rate × bitrate = (1 − BER)n × bitrate
n = 1500 × 8 bits

## Slide 18: Delivery rate vs BER
Throughput = delivery rate × bitrate = (1 − BER)n × bitrate

## Slide 19: BER vs SNR
Let’s go back to the BER vs SNR graph
  For each modulation: What are the SNRs required for BER < 10-5?
BPSK: 7 dB; QPSK: 12 dB; 16-QAM: 20 dB; 64-QAM: 26 dB

## Slide 20: Fixed-rate codes require channel adaptation
7 dB
12 dB
26 dB
Throughput = delivery rate × bitrate = (1 − BER)n × bitrate
n = 1500 × 8 bits

## Slide 21: Fixed-rate codes require channel adaptation

## Slide 22: Existing rate adaptation algorithms
SNR/BER-based
Frame-based
Estimate frame loss rate
at each bit rate
Data
ACK
Data
Lookup table:
SNR/BER  best rate
SNR using preamble

## Slide 23: Today
Bit Rate Adaptation
Rateless Codes: Spinal Codes

## Slide 24: Rateless codes: Motivation (1)
Sender transmits information at a rate higher than the channel can sustain
  At first glance, this sounds disastrous!
Receiver extracts information at the rate the channel can sustain at that instant
  No adaptation loop is needed!

## Slide 25: Rateless codes: Motivation (2)
Setting: Multicast or unicast links
Sender sends a potentially limitless stream of encoded bits
Receiver(s) collect bits until they are reasonably sure that they can recover the content from the received bits, then send STOP feedback to sender
Automatic adaptation: Receivers with larger loss rate need longer to receive the required information

## Slide 26: Today
Bit Rate Adaptation
Rateless Codes: Spinal Codes
  Encoder structure
  Decoder structure

## Slide 27: Spinal encoder: Computing the spines
Start with a hash function h and an initial random v-bit state s0
  Sender and receiver agree on h and s0 a priori
Sender divides its n-bit message M into k-bit chunks mi
h maps the state and a message chunk into a new state
  The v-bit states s1, …, s⌈n/k⌉ are the spines

## Slide 28: Spinal encoder: Information flow
Observe: State si contains information about chunks m1, …, mi
  A stage’s state depends on the message bits up to that stage
So only state s⌈n/k⌉ has information about entire message

## Slide 29: Spinal encoder: Computing the spines
Each spine seeds a pseudorandom number generator RNG
RNG generates a sequence of c-bit numbers xi,l called symbols
Encoder output is a series of passes, each of ⌈n/k⌉ symbols

## Slide 30: Spinal encoder: RNG to symbols
A constellation mapping function translates c-bit numbers xi,l from the RNG to in-phase (I) and quadrature (Q)
  Generates in-phase (I) and quadrature (Q) components independently from two separate xi,l
Uniform
Truncated Gaussian

## Slide 31: Today
Bit Rate Adaptation
Rateless Codes: Spinal Codes
  Encoder structure
  Decoder structure
    “Maximum-likelihood” decoding
    Practical “Bubble” Decoder
    Puncturing for higher rate
    Performance

## Slide 32: Decode by replaying the encoder
Sender transmits “1”, “0”:
h
s0
1
h
0


h
s0
0
×
×


Instead of inverting the hash function, the decoder replays all four possibilities:
Transmitted symbols
h
0
h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×


   Replayed symbol
  × Received symbol

## Slide 33: Decode by measuring distance
How to decide between the four possible messages?
Measure total distance between:
  Received symbols, corrupted by noise (×), and
  Replayed symbols ()
Sum across stages: the distance increases at first incorrect symbol
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×


   Replayed symbol
  × Received symbol

## Slide 34: Adding additional passes
Recall: The encoder sends multiple passes over the same message blocks

## Slide 35: Adding additional passes
What’s a reasonable strategy for decoding now?
Take the average distance from the replayed symbol (), across all received symbols (×, ×)
  Intuition: As number of passes increases, noise and bursts of interference average out and impact the metric less
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×


×
×
×
×
×
×
×
×
   Replayed symbol
  × Received symbol

## Slide 36: The Maximum Likelihood (ML) decoder
Consider all 2n possible messages that could have been sent
  The ML decoder minimizes probability of error
Pick the message M′ that minimizes the vector distance between:
  The vector of all received constellation points y
  The vector of constellation points sent if M′ were the message, x(M′)
In further detail:
  xt,l(M′): tth constellation point sent in the lth pass for M′
  yt,l: tth constellation point received in the lth pass

## Slide 37: ML decoding over a tree
Observe: Hypotheses whose initial stages share the same symbol guesses are identical in those stages
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
s0
0
h
1
×
×


h
s0
1
h
1
×
×



## Slide 38: ML decoding over a tree
Observe: Hypotheses whose initial stages share the same symbol guesses are identical in those stages
Therefore we can merge these initial identical stages:
h
s0
0
h
0
×
×


h
s0
1
h
0
×
×


h
1
×

h
1
×


## Slide 39: ML decoding over a tree
General tree properties:
  n/k levels, one per spine
  Branching factor 2k (per choice of k-bit message chunk)
Let s′t be the tth spine value associated with all messages that share s′t
We find cost of a particular message by summing costs on path from root to leaf
h
0
h
0
×
×


h
s0
1
h
0
×
×


h
1
×

h
1
×

✔
✔
✔
s1
s2

## Slide 40: ML decoding over a tree: Multiple passes
Suppose the sender transmits L passes, in a poor channel
Average (sum) metric across passes, and label branches
However, the tree has 2n leaves to compare so this approach is still impracticable (too computationally demanding)
h
0
h
0✔
×
×


h
s0
1
h
0
×
×


h
1
×

h
1
×

✔
✔
s1
s2

## Slide 41: Efficiently exploring the tree
Observation: Suppose the ML message M* and some other message M′ differ only in the ith bit
  Only symbols including and after index ⌈i/k⌉ will disagree
  So the earlier the error in M′, the larger the cost
  Can show that the “runners-up” to M* differ only in the last O(log n) bits
Consider the best 100 leaves in the ML tree:
  Tracing back through the tree, they will have a common ancestor with M* in O(log n) steps
  This suggests a strategy in which we only keep a limited number of ancestors

## Slide 42: “Bubble” decoder
Maintain a beam of B tree node possibilities to explore at each stage, each to a certain depth d
Expand each ancestor, score every child, propagate best child score for each ancestor, pick B best survivors
Example: B = d = 2, k = 1 (lighter color = better score)
beam

## Slide 43: Adjusting the rate
Spinal codes as described so far uses different numbers of passes to adjust the rate
Two problems in Spinal codes as described so far:
  Must transmit one full pass, so max out at k bits/symbol
    Increase k? No: Decoding cost is exponential in k
  Sending L passes reduces rate to k/L—abrupt drop
    Introduces plateaus in the rate versus SNR curve

## Slide 44: Puncturing for higher and finer-grained rates
Idea: Systematically skip some spines
  Sender and receiver agree on the pattern beforehand
  Receiver can now attempt a decode before a pass concludes
Decoder algorithm unchanged, missing symbols get zero score
Max rate of this puncturing: 8∙k bits/symbol

## Slide 45: Framing at the link layer
Sender and receiver need to maintain synchronization
  Sender uses a short sequence number protected by a highly redundant code
Unusual property of Spinal codes: Shorter message length n is more efficient
  This is in opposition to the trend most codes follow
  Divide the link-layer frame into shorter checksum-protected code blocks
If half-duplex radio, when should sender wait for feedback?
  For more information, see RateMore (MobiCom ‘12)

## Slide 46: Today
Bit Rate Adaptation
Rateless Codes: Spinal Codes
    Encoder structure
    Decoder structure
    Performance

## Slide 47: Methodology
Software simulation: Simulated wireless channel (additive white Gaussian noise and Rayleigh fading)
Hardware platform: Airblue (FPGA based platform)
  Real 10, 20 MHz bandwidth channels in 2.4 GHz ISM band
Gap to capacity: How much more noise could a capacity-achieving code tolerate at same rate?
  Smaller gap is better
  e.g.: This code achieves six bits/symbol at 20 dB SNR, for a 2 dB gap to capacity
Rate (bits per symbol)
0
2
4
6
8
2 dB

## Slide 48: Spinal codes: Higher rate on AWGN channel
Simulated AWGN channel: no link-layer performance effects here
LDPC envelope: Choose best-performing rated LDPC code at each SNR to mimic the best a rate adaptation strategy could do
Strider+: Strider + puncturing: finer rate control, but significant gap to capacity

## Slide 49: Rateless codes can “hedge their bets”
Constant SNR means constant average noise power
  But, noise impacting any particular symbol(s) may be higher or lower
Rated codes must be risk averse (send at lower rate)
Rateless codes can decode with fewer symbols when noise is momentarily lower
But this result requires perfect and instantaneous feedback so the rateless code knows when to stop

## Slide 50: Spinal codes: Better at sending short messages
Longer code block means more opportunities to prune correct path
  So Spinal codes achieves better performance (smaller gap to capacity) with smaller code block length n
We can see artifacts due to puncturing at higher SNRs

## Slide 51: Spinal Codes: Conclusion
Spinal Codes give performance close to Shannon capacity
Eliminate the need to run a bit rate adaptation algorithm
Simpler design and better performance
Link layer design more open, incurs overhead between transmissions

## Slide 52: Midterm format
Timing: 60 minutes in a 90 minute timeslot
Exam is closed book, closed Internet, closed electronic devices; calculators not permitted
True/False/Don’t Know questions
  One point for a correct T/F response
  No effect for a don’t know response or no response
  Minus one point for an incorrect T/F response
  Rescaled as a section with a zero floor
Short answer questions
  One to two, each on a theme

## Slide 53
Next week’s precepts:
Lab 2
Tuesday, March 12, 11:00 AM:
In-Class Midterm
Next Thursday:
[Part III: Wireless from the PHY Upwards]
Signals and Systems Preliminaries