## Slide 1: Part III: Wireless from the Physical Layer, up Preliminaries: Radio Communication, Modulation, and Filtering
COS 463: Wireless Networks
Lecture 11
Kyle Jamieson
[Parts adapted from H. Balakrishnan, M. Perrot, C. Sodini , P. Steenkiste]

## Slide 2: Radio Frequency (RF)
Electromagnetic signal that propagates through space
  Transmitted at some carrier frequency fc
  Travels at the speed of light (c)
Wavelength in air:
fc range: (beyond) 3 KHz to 300 GHz (or, λ = 100 km to 1 mm)

## Slide 3: Today
Introduction to Signals: The Frequency Domain
  Modulation and Demodulation
Introduction to Filtering
AM Radio
Signals and Noise

## Slide 4: Information Transmission
Goal: Move information (voice, video, data etc.), encoded in signals (e.g., electromagnetic, optical, acoustic)
  Over some channel (physical medium, e.g., free space, fiber, coax)
Transmitter
Channel
Receivers
Input
Output
Information
Signal
Information
Signal

## Slide 5: Key Tool: Fourier Series
Suppose x(t) is our information signal
A periodic waveform x(t) can be represented as a sum of weighted (an) sinusoids of different frequencies ωn:
x(t)
t
= a0 + a1 ×
t
+ a2 ×
+ a3 ×
+ ⋯
sin(ω1t)
sin(ω2t)
sin(ω3t)

## Slide 6: Frequency Domain View
Idea: plot the weights an versus the frequencies ωn:
x(t)
t
frequency
a1
a2
a3
a0
ω0
ω1
ω2
ω3

## Slide 7: Fourier Transform
Fourier series deals with periodic signals
Fourier transform deals with non-periodic signals
Notation:
Time
Frequency
Amplitude
Amplitude

## Slide 8: Fourier Transform of cosine wave

## Slide 9: Key Tool: The Impulse Function
An impulse of area A at time t0 is denoted:
Defined in terms of its properties when combined with other (information carrying) signals
Aδ(t-t0)
t
t0
A

## Slide 10: Today
Introduction to Signals: The Frequency Domain
  Modulation and Demodulation
Introduction to Filtering
AM Radio
Signals and Noise

## Slide 11: Motivation for Modulation
Physical medium of wireless channel usually free space
Radio wavelength inversely proportional to frequency (1 GHz  30 cm, while 1 KHz  30 km wavelength)
Since antenna, component size related to wavelength:
  Want to move signal to higher frequency for smaller devices
Higher frequency signals can send more data, further

## Slide 12: Sinusoidal carrier signal
RF signal propagates away from transmitter at light speed c
At an instant in time: signal “looks” sinusoidal in space
At a point in space: signal oscillates sinusoidally in time
c
Transmitter

## Slide 13: Goal of Modulation
Given an information signal
Example: Voice signal with 4 KHz bandwidth
Shift information signal to the carrier frequency
Example: 900 MHz carrier frequency
 Information signal modulates (changes) the carrier signal
0
Magnitude
4 kHz
Voice
signal
900 MHz
-900 MHz
-4 kHz
Frequency

## Slide 14: Carrier signal parameters
Amplitude
Wavelength
t
Phase
The information signal modulates the carrier’s parameters:

## Slide 15: Goal of Demodulation
Given a transmitted signal,
Example: Voice signal centered at 900 MHz
Recover the original signal from the transmission.
Example: 4 KHz bandwidth voice signal centered at 0 Hz
0
Magnitude
4 kHz
Voice
signal
900 MHz
-900 MHz
-4 kHz
Frequency

## Slide 16: Impulse: Sampling Property
Multiplication of a function x(t) with an impulse at time t0:
Results in scaling the impulse by the value of x(t) at t0
t
t0
A
x(t)
t
t0
x(t0)
t
t0
δ(t-t0)
×
=

## Slide 17: Impulse: Convolution in Time
Convolution of a function x(t) with an impulse at time t0:
Results in a time shift of x(t) by t0
t
t0
A
x(t)
t
t
t0
δ(t-t0)
*
=
0

## Slide 18: Impulse: Convolution in Frequency
Convolve function X(f) with impulse at frequency f0:
Results in a frequency shift of X(f) by f0
f
f0
A
X(f)
f
f
f0
δ(f−f0)
*
=
0

## Slide 19: Duality of Convolution and Multiplication
Multiplication in time leads to convolution in frequency:
Convolution in time leads to multiplication in frequency:

## Slide 20: Modulation: Introduction
Given a data signal (e.g. cosine wave) at frequency f1 (e.g., 1 Hz)
Modulate it with carrier at frequency f2 (e.g., 10 Hz)
cos(2πt)
cos(2π10t)
frequency (Hz)
frequency (Hz)
Magnitude
Magnitude

## Slide 21: Transmitter: Principle of Modulation
f1+f2 = 11 Hz Cosine
f1−f2 = 9 Hz Cosine
Frequency (Hz)
Magnitude
Time (s)
Magnitude
Time Domain
Frequency Domain
Modulate the carrier with the data: cos(2πt) × cos(2π10t)
⨂
data signal
carrier
modulated
signal
Transmitter:

## Slide 22: Demodulation: Motivation
Receiver wants to recover the original data signal
  Multiplies modulated signal containing f1−f2 and f1 + f2 by copy of carrier
⨂
???
carrier
modulated signal
Receiver:
f1+f2 = 11 Hz Cosine
f1−f2 = 9 Hz Cosine
Frequency (Hz)
Magnitude
Modulated signal:
Carrier:
Frequency (Hz)
Magnitude

## Slide 23: Receiver: Principle of Demodulation
Receiver multiplies modulated signal by copy of carrier signal,
  Frequency shift of by the convolution property
Result contains original signal and higher frequency sinusoids:
Frequency (Hz)
Magnitude
Frequency Domain
How to remove the higher frequency sinusoids?
⨂
carrier
modulated signal
Receiver:

## Slide 24: Today
Introduction to Signals: The Frequency Domain
Introduction to Filtering
AM Radio
Signals and Noise

## Slide 25: The Concept of Filtering
With input, filter produces output signal y(t) by convolution with a filter response h(t)
So, in the frequency domain, the filter multiplies each input frequency f by
  Y(f) = X(f)H(f)
x(t)
h(t)
y(t)
X(f)
H(f)
Y(f)

## Slide 26: Example Input Signal to Filter
Input signal: Sum of three sinusoids (10, 50, 90 Hz)
time (s)
h(t)
y(t)
f (Hz)
↕︎𝓕
10 Hz
50 Hz
90 Hz

## Slide 27: Low Pass Filter Example
H(f) = 1 below 20 Hz, approaches 0 above 20 Hz
time (s)
h(t)
y(t)
f (Hz)
↕︎𝓕
f (Hz)
0
1
20 Hz
10 Hz
50 Hz
90 Hz
H(f)

## Slide 28: Low Pass Filter Output
H(f) = 1 below 20 Hz, approaches 0 above 20 Hz
time (s)
h(t)
f (Hz)
↕︎𝓕
f (Hz)
0
1
20 Hz
10 Hz
50 Hz
90 Hz
time (s)
↕︎𝓕
H(f)

## Slide 29: High Pass Filter Example
H(f) = 0 below 70 Hz, approaches 1 above 70 Hz
time (s)
h(t)
y(t)
f (Hz)
↕︎𝓕
f (Hz)
0
1
70 Hz
10 Hz
50 Hz
90 Hz
H(f)

## Slide 30: High Pass Filter Output
H(f) = 0 below 70 Hz, approaches 1 above 70 Hz
time (s)
h(t)
f (Hz)
↕︎𝓕
f (Hz)
0
1
70 Hz
10 Hz
50 Hz
90 Hz
H(f)
f (Hz)
time (s)

## Slide 31: Bandpass Filter: Motivation
Want to receive exclusively a certain frequency band of interest
  In presence of other communication on adjacent channels
RF Transmitter
RF Receiver
0
Magnitude
4 kHz
Voice signal
900 MHz
Frequency
0
Magnitude
900 MHz
Frequency

## Slide 32: Bandpass Filter Output
H(f) = 0 below 30 Hz, above 70 Hz, approaches 1 elsewhere
time (s)
h(t)
f (Hz)
↕︎𝓕
f (Hz)
0
1
70 Hz
10 Hz
50 Hz
90 Hz
H(f)
f (Hz)
time (s)
30 Hz

## Slide 33: Today
Introduction to Signals
Introduction to Filtering
AM Radio
Signals and Noise

## Slide 34: AM Radio Transmitter
Time domain view:
Carrier signal (f0 Hz):
x(t)
Carrier signal:
Frequency domain view:
Carrier signal (f0 Hz):

## Slide 35: Demodulation: Frequency Domain View
Transmitter:
Receiver:

## Slide 36: Demodulation: Time Domain View
Receiver:
Transmitter:

## Slide 37: Impact of a frequency offset
Frequency offset ε at receiver corrupts the output signal r(t)

## Slide 38: Stretch Break and Partner Exercise: FDM-AM
Using the principle of superposition and the AM radio circuits we’ve just seen:
  Draw a circuit to transmit frequency division-multiplexed amplitude modulation (FDM-AM) of the voice signals A, B, and C at frequencies , , and , respectively
  Plot the radio-frequency spectrum of your circuit’s output (the transmitted FDM-AM signal)
  Describe how a receiver would tune in to and demodulate just Signal B
0
Signal A
Magnitude
Frequency
0
Signal B
Magnitude
Frequency
0
Signal C
Magnitude
Frequency
Voice signals:

## Slide 39: Today
Introduction to Signals: The Frequency Domain
Introduction to Filtering
AM Radio
Signals and Noise

## Slide 40: The Issue of Noise
Noise: Unpredictable, corrupting signal that adds to desired signal
  For RF receiver, mostly comes from analog receiver amplifier circuitry
Undesired signals also add to and corrupt desired signal
RF Receiver
0
Magnitude
900 MHz
Frequency
Desired signal
Noise

## Slide 41: Energy Transfer in Wireless Communication
Receiver antenna captures a limited amount of desired signal’s energy
  Depending on antenna size, distance, environment
RF Receiver
0
Magnitude
900 MHz
Frequency
Desired signal
Noise
RF Transmitter

## Slide 42: Signal versus Noise
Moving transmitter closer to receiver generally increases desired signal energy
Noise from analog receiver circuitry remains unchanged
Next few lectures: How is system performance impacted?
RF Receiver
0
Magnitude
900 MHz
Frequency
Desired signal
Noise
RF Transmitter

## Slide 43: Definition of Power, Energy
Given a signal x[n]:
Energy
Power

## Slide 44: Signal­ to ­Noise Ratio (SNR)
Signal-to-Noise Ratio (SNR) measures power ratio between a signal of interest and background noise:
SNR (dB) | SNR
30 | 1,000
20 | 100
10 | 10
0 | 1 (equal)
-10 | 0.1
-20 | 0.01
-30 | 0.001
SNR is often expressed in decibels (dB), 10 times the base-10 logarithm of a quantity:

## Slide 45: Visualizing Signal to Noise Ratio
Signal view:
Constellation
view:

## Slide 46: Summary
Impulse function is an important concept for frequency domain “picture” analysis
  Shifting, sampling properties of impulse explain modulation and demodulation
“Picture analysis” of modulation and filtering
  Modulation shifts in frequency (convolution with impulses)
  Filtering multiplies in frequency

## Slide 47
Good luck with the
remainder of your midterms!
Tuesday, March 25 lecture:
From AM Radio to Digital I/Q Modulation