## Slide 1: The Radio Channel
COS 463: Wireless Networks
Lecture 14
Kyle Jamieson
[Parts adapted from I. Darwazeh, A. Goldsmith, T. Rappaport, P. Steenkiste]

## Slide 2: Radio Channel: Motivation
The radio channel is what limits most communications systems – the main challenge!
  Understanding its properties is therefore key to understanding radio systems’ design
There is variation in many different properties
  Carrier frequency, environment (e.g. indoors, outdoors, satellite, space)
Many different models covering many different scenarios

## Slide 3: Channel and Propagation Models
A channel model describes what happens
  Gives channel output power for a particular input power
  “Black Box” – no explanation of mechanism
  Requires appropriate statistical parameters (e.g. loss, fading)
A propagation model describes how it happens
  How signal gets from transmitter to receiver
  How energy is redistributed in time and frequency
  Can inform channel model parameters

## Slide 4: Today
Large scale channel model
  Friis Free space model
    How much power delivered from omnidirectional transmitter to omnidirectional receiver, in free space?
Small-scale channel models

## Slide 5: Transmitting in Free Space
Deliver Watts to an omnidirectional transmitting antenna
So then power density (Watts per unit area) at range d is W/m2
  Independent of wavelength (frequency)
Total spherical surface area:
unit area

## Slide 6: Idealized Receive Antenna
Effective aperture : fraction of incident power density p captured and received:
    Larger antennas at greater λ capture more power
Therefore, power received is the product of the power density and effective aperture:

## Slide 7: Antenna Gain
Antennas don’t radiate power equally in all directions
  Specific to the antenna design
Model these gains in the directions of interest between transmitter, receiver:
  Transmit antenna gain Gt
  Receive antenna gain Gr

## Slide 8: Friis Free Space Channel Model
Power received is the product of the power received by idealized antennas, times transmit and receive antenna gains:

## Slide 9: Today
Large scale channel models
Small-scale channel models
  Multi-path propagation
  Motion and channel coherence time

## Slide 10: Small-scale versus large-scale modeling
Small-scale models: Characterize the channel over at most a few wavelengths or a few seconds

## Slide 11: Multipath Radio Propagation
Receiver gets multiple copies of signal
  Each copy follows different path, with different path length
  Copies can either strengthen or weaken each other
    Depends on whether they are in or out of phase
Enables communication even when transmitter and receiver are not in “line of sight”
  Allows radio waves effectively to propagate around obstacles, thereby increasing the radio coverage area
Transmitter, receiver, or environment object movement on the order of λ significantly affects the outcome
  e.g. 2.4 GHz  λ = 12 cm, 900 MHz  ≈ 1 ft

## Slide 12: Radio Propagation Mechanisms
Reflection
Scattering
Diffraction
Refraction
  Propagation wave changes direction when impinging on different medium
Reflection
  Propagation wave impinges on large object (compared to λ)
Scattering
  Objects smaller than λ (i.e. foliage, street signs etc.)
Diffraction
  Transmission path obstructed by surface with sharp irregular edges
  Waves bend around obstacle, even when line of sight does not exist
Refraction

## Slide 13: Today
Large scale channel models
Small-scale channel models
  Multi-path propagation
    Frequency-domain view
    Time-domain view
  Motion and channel coherence time

## Slide 14: Sinusoidal carrier, line of sight only
Suppose transmitter is distance d (propagation time delay τ = d / c) away from receiver (where c is the speed of light)
Radio frequency transmitted signal:
  Carrier frequency fc corresponds to radio wavelength λ
  Baseband transmitted signal in one symbol period:
How to model the effect of the channel?
Receiver
Transmitter
d, τ
λ

## Slide 15: Sinusoidal carrier, line of sight only: Signal Attenuation
Represent channel’s amplitude attenuation with a real number a
Models, e.g. attenuation due to two refractions and partial reflection as the signal passes through an indoor wall
Receiver
Transmitter
a, d, τ

## Slide 16: Sinusoidal carrier, line of sight only: Signal Phase Shift
Received signal travels distance d
One wavelength corresponds to a 360˚ (2π radian) phase shift
Represent path’s phase shift with an angle (real number) θ = 2π⋅ d / λ
  “Abstract away” distance and wavelength into (one) phase shift θ
Receiver
Transmitter
a, θ
λ

## Slide 17: Sinusoidal carrier, line of sight only: Channel Model
Wireless channel h attenuates by a, phase-shifts by θ
  Therefore,
Received baseband signal: (no noise)
Receiver
Transmitter
a, θ
I
Q
x
y
Rotate by θ
Scale by a
x
y

## Slide 18: Line-of-sight plus reflecting path: Motivation
What if reflections (e.g., indoor walls) introduce a second path?
Wireless channel becomes the superposition of the direct path’s channel h1 and the reflection path’s channel h2
Receiver
Transmitter
h1 (a1, θ1)
h2 (a2, θ2)

## Slide 19: Line-of-sight plus reflecting path: Channel Model
Channel is now
Receiver
Transmitter
h1 (a1, θ1)
h2 (a2, θ2)
h1
h2
I
Q
h2
h

## Slide 20: Line-of-sight plus reflecting path: Channel Model
Phase difference between paths
  Depends on wavelength and path length difference
So, depends on wavelength (frequency) as well as channel attenuation
Receiver
Transmitter
h1 (a1, θ1)
h2 (a2, θ2)
h1
h2
I
Q
Δθ

## Slide 21: Reflections cause frequency selectivity
Interference between reflected and line-of-sight radio waves results in frequency dependent fading
Coherence bandwidth Bc: Frequency range over which the channel is roughly the same (“flat”)

## Slide 22: Practical Frequency-Selective Fading
One 2.4 GHz Wi-Fi channel is centered at 2412 MHz and spans a 20 MHz bandwidth
Observe: Frequency-selective fading
[D. Halperin]
Recall, phase shift for kth path
  Received phase difference between paths depends on wavelength
Channel spans 2402–2422 MHz
  Lowest wavelength (2402 MHz): 12.49 cm
  Highest wavelength (2422 MHz): 12.39 cm
    Just one millimeter wavelength difference
      Almost the same. Contradiction?

## Slide 23: Practical Frequency-Selective Fading
[D. Halperin]
Channel spans 2402–2422 MHz
  Lowest wavelength (2402 MHz): 12.49 cm
  Highest wavelength (2422 MHz): 12.39 cm
Recall, causes additive vs. destructive fading
For Wi-Fi, so, e.g., , equals:
  160×12.49 cm wavelengths
  161×12.39 cm wavelengths
So we move from e.g. constructive to destructive, to constructive fading from lowest to highest wavelength

## Slide 24: Radio Channels are “Reciprocal”
Forward channel (T to R) is
Switch T and R roles, changing nothing else:
  Reverse channel (R to T) is
  The reverse radio channel is “reciprocal”
Practical radio receiver circuitry induces differences between ,
Receiver R
Transmitter T
a1,d1,τ1
a2,d2,τ2

## Slide 25: Putting it all Together: Ray Tracing
Approximate solutions to Maxwell’s electromagnetic equations by instead representing wavefronts as particles, traveling along rays
  Apply geometric reflection, diffraction, scattering rules
    Compute angle of reflection, angle of diffraction
Error is smallest when receiver is many λ from nearest scatterer, and all scatterers are large relative to λ
Good match to empirical data in rural areas, along city streets (radios close to ground), and indoors
Completely site-specific
  Changes to site may invalidate model

## Slide 26: Today
Large scale channel models
Small-scale channel models
  Multi-path propagation
    Frequency-domain view
    Time-domain view
  Motion and channel coherence time

## Slide 27: What does the channel look like in time?
Receiver
Transmitter
a1,d1,τ1
a2,d2,τ2
Channel impulse response h(t)
t
τ1
a1
a1
τ2
a2
Delay spread Td

## Slide 28: Power delay profile (PDP)
Power received via the path with excess time delay is the value (height) of the discrete PDP component at
P(τ) corresponds to |h(τ)|2
P(τ)
t
0

## Slide 29: Characterizing a power delay profile
Given a PDP sampled at time steps :
Mean excess delay : Expected value of
Root mean squared (RMS) delay spread measures the spread of the power’s arrival in time
  RMS delay spread is the variance of
, where
Maximum excess delay < X dB is the greatest delay at which the PDP is greater than X dB below the strongest arrival in the PDP

## Slide 30: Example Indoor PDP Estimation
Finite bandwidth of measurement normally results in continuous PDP
PDP typically has a decaying exponential form
Environment | RMS delay spread
Indoor cell | 10 – 50 ns
Satellite mobile | 40 – 50 ns
Open area (rural) | < 0.2 𝛍s
Suburban macrocell | < 1 𝛍s
Urban macrocell | 1 – 3 𝛍s
Hilly macrocell | 3 – 10 𝛍s
Typical RMS delay spreads

## Slide 31: Indoor power delay profile

## Slide 32: Flat Fading
Slow down  sending data over a narrow bandwidth channel
  Channel is constant over its bandwidth
  Multipath is still present, so channel strength fluctuates over time
    How to model this fluctuation?
Channel
Not shown above!

## Slide 33: Rayleigh Fading Model
Random gain of kth arriving path:
Therefore, the I and Q channel components are zero-mean Gaussian distributed
So is Rayleigh-distributed
Rayleigh PDF
Channel impulse response h(t)
t
τ1
a1
τ2
a2
a3
τ3

## Slide 34: Rayleigh fading example

## Slide 35: Today
Large scale channel models
Small-scale channel models
  Multi-path propagation
  Motion and channel coherence time

## Slide 36: Stationary transmitter, moving receiver
Suppose reflecting wall, fixed transmit antenna, no other objects
  Receive antenna moving rightwards at velocity v
Two arriving signals at receiver antenna with a path length difference of 2(d − r(t))
Receiver
antenna

## Slide 37: How does fading in time arise?
Path length difference
If  receive ≈ 0
  Destructive interference
If  receive ≈ 2
  Constructive interference
λ/2
λ
sum
Receiver
antenna

## Slide 38: Stretch Break and In-Class Question
In the preceding example, the reflected wave and direct wave travel in opposite directions
  What happens if we move the reflecting wall to the left side of the transmitter?
    What is the nature of the multipath fading, both over time and over frequency?
v
Transmit antenna
Wall
r(t)
d

## Slide 39: Channel Coherence Time
A change in path length difference of λ / 2 transitions from constructive to destructive interference
  Receiver movement of λ/4: coherence distance
  Duration of time that transmitter, receiver, or objects in environment take to move a coherence distance: channel coherence time Tc
    Walking speed (2 mph) @ 2.4 GHz: ≈ 15 milliseconds
    Driving speed (20 mph) @ 1.9 GHz: ≈ 2.5 milliseconds
    Train/freeway speed (75 mph) @ 1.9 GHz: < 1 millisecond

## Slide 40: Another perspective: Doppler Effect
Movement by the transmitter, receiver, or objects in the environment creates a Doppler Shift
v 

## Slide 41: Stationary transmitter, moving receiver: From a Doppler Perspective
Doppler Shift of a path
  vradial is radial component of receiver’s velocity vector along the path
    Positive with decreasing path length, negative with increasing path length
Suppose v = 60 km/h, fc = 900 MHz
  Direct path , reflection path
Receiver
antenna

## Slide 42: Stationary transmitter, moving receiver: From a Doppler Perspective
Channel Doppler Spread Ds: maximum path Doppler shift, minus minimum path Doppler shift
Suppose v = 60 km/h, fc = 900 MHz
  Direct path , reflection path
  Doppler Spread: 100 Hz
Results in sinusoidal “envelope” at frequency Ds / 2:
Receiver
antenna
Received signal
5 ms

## Slide 43: Channel Coherence Time: From a Doppler Perspective
Sinusoidal “envelope” at frequency :
Transition from 0 to peak in
  So qualitatively significant change in time
    Alternate definition of channel coherence time
Received signal

## Slide 44
Thursday Topic:
Receiver Designs for
the Wireless Channel