## Slide 1: Receiver Designs for the Radio Channel
COS 463: Wireless Networks
Lecture 15
Kyle Jamieson
[Parts adapted from C. Sodini, W. Ozan, J. Tan]

## Slide 2: Today
Delay Spread and Frequency-Selective Fading
Time-Domain Equalization
Orthogonal Frequency Division Multiplexing

## Slide 3: Last Time: Multipath causes Delay Spread
Receiver
Transmitter
a1,τ1
a2,τ2
Power Delay Profile P(t)
t
τ1
a1
τ2
a2
Channel delay spread Td

## Slide 4: Last Time: Multipath causes Frequency Selectivity
Interference between reflected and line-of-sight radio waves results in frequency dependent fading

## Slide 5: Problem: Inter-symbol interference (ISI)
Transmitted signal
Received signal with ISI

## Slide 6: Problem: Inter-symbol interference (ISI)
Transmitted signal
Received signal with ISI
ISI at one symbol depends on the value of other symbols

## Slide 7: Today
Delay Spread and Frequency-Selective Fading
Time-Domain Equalization
Orthogonal Frequency Division Multiplexing

## Slide 8: Wideband System Design
p(t)
Transmit pulse filter
Data dk
h(t)
p*(−t)
heq(t)
yt
y[n]
Received data
Matched filter
Equalizer
Transmitter
Receiver
Channel
Composite channel f between data and received signal y[n] is made up of the transmit pulse shape, radio channel, and matched filter

## Slide 9: Zero-Forcing Equalizer
p*(−t)
heq(t)
yt
y[n]
Matched filter
Equalizer
Receiver:
+
Receiver front-end noise: nk
Received
Received
Information
Noise

## Slide 10: Today
Delay Spread and Frequency-Selective Fading
Time-Domain Equalization
Orthogonal Frequency Division Multiplexing

## Slide 11: Simple Solution: Increase symbol time
Choose symbol time Ts ≫ channel delay spread Td
Transmitted signal Received signal
1
(double) Ts
No ISI
(at receiver)

## Slide 12: Symbol time determines frequency bandwidth
t
Symbol time
T
2T
t
f
W/2
f
W
Slowing down by a factor of two halves the frequency bandwidth of the sender’s signal

## Slide 13: A narrowband signal “fits into” the coherence bandwidth
Over what frequency range is the channel approximately the same? This is the coherence bandwidth
Coherence bandwidth Wc

## Slide 14: Wideband versus OFDM
Time
Frequency
Frequency selective fading
distorts wide-band signals
Multipath causes ISI
Wideband Signal
Narrowband
signals
Longer symbol time Ts
Time
Frequency
OFDM Signal

## Slide 15: FDMA: Frequency Division Multiple Access
Channel frequency bandwidth divided into smaller sub-bands
Each data gets own frequency sub-band (sinusoidal carrier)
But need to add quiet guard sub-bands in between each sub-band
  To mitigate inter-sub band interference
frequency bands
time
FDM signal
(guard)
(guard)
(guard)

## Slide 16: Long sinusoids, different frequencies
Baseband signal (In-Phase part)
Modulate amplitude/phase of each above subcarrier to send information
Different frequencies on different subcarriers don’t mutually interfere
Symbol time Ts

## Slide 17: Integer-Multiple Frequencies
Suppose N subcarriers and N complex valued data symbols
  X[k] (0 ≤ k < N) are the complex-valued data we want to send
Goal: for integers k from 0 to N−1:
  cosine at frequency 2πk/N on the I channel
  sine at frequency 2πk/N on the Q channel
So (as before) let each subcarrier be the time-domain (indexed by n) signal:

## Slide 18: OFDM Subcarriers are “Orthogonal”
Integer-multiple frequencies so peaks of each subcarrier coincide in frequency with zeros of other subcarriers
  No guard bands required!

## Slide 19: Generating an OFDM Signal
How to generate this type of signal:
By Euler’s formula,
  This is the (familiar) Inverse DFT
    Transmit time domain signal x[n] = DFT−1{ X[k] }
    So has an efficient hardware implementation

## Slide 20: Transmitting one OFDM symbol in time
OFDM symbol time Ts

## Slide 21: Receiving an OFDM signal
Apply the DFT to each OFDM symbol individually, to recover data:
Time
Frequency
One OFDM symbol
x[0]…x[N−1]

## Slide 22: What about the wireless channel?
Channel impulse response h(t) is a function of time
  Impulse has an infinite bandwidth
Effect of a very narrowband channel is one complex number h
  Subcarrier eventually arrives on all paths, e.g. h = h1+h2:
Channel impulse response h(t)
t
τ1
a1
τ2
a2
Delay spread Td
Receiver
Transmitter
h1
h2

## Slide 23: What about the wireless channel?
Channel used at each subcarrier’s discrete frequency location
e.g. with three subcarriers:
k=1
k=2
k=3

## Slide 24: Estimating the Channel
Transmit known a OFDM preamble symbol p[n]
  In frequency domain on frequency k denote preamble P[k]
After DFT on the preamble, the receiver hears frequency domain value Y[k]
Receiver computes channel estimate on kth subcarrier: H[k] = Y[k] / P[k]
Aside: To compute channel impulse response: DFT−1{ H[k] } = h[n]

## Slide 25: Problem: Inter-OFDM Symbol Interference

## Slide 26: Problem: Receiver synchronization
1
2
3
Receiver:
1
2
3
Receiver’s view of Symbol 1 contains actual Symbols 1 and 2

## Slide 27: Interference solution: Inter-symbol guard interval
Guard interval between adjacent symbols mitigates adjacent symbol interference

## Slide 28: Synchronization solution: Cyclic prefix
Receiver:
Symbol OK!
Ns, Ts
Nfft, Tfft

## Slide 29: OFDM signal: Frequency-Domain view
Uniform power in the frequency domain over the OFDM signal bandwidth

## Slide 30: OFDM signal: Time Domain View
Many low-frequency sinusoids in the time domain
Occasionally in time, many will all constructively interfere
  Result: High ratio of peak power / average power

## Slide 31: Peak to Average Power & Transmit Amplifiers
Transmit power amplifier sits just before the transmit antenna
Peak power in non-linear region causes signal distortion
  So lower input signal level:
Typical Transmit Power Amplifier Response (Vout / Vin)
High peak to average power ratio (PAPR)  Low average power level 
    Signal mostly uses fewer levels in discrete representation, so high quantization error (another form of distortion)
Put peak power here

## Slide 32: An OFDM Modem
P/S
QAM decoder
invert channel
=
frequency
domain
equalizer
S/P
quadrature amplitude modulation (QAM) encoder
N-IFFT
add cyclic prefix
P/S
D/A +
transmit filter
N-FFT
S/P
remove cyclic prefix
TRANSMITTER
RECEIVER
N subchannels
N complex samples
N complex samples
N subchannels
Receive filter
+
A/D
multipath channel
Bits
00110

## Slide 33: Packet detection
OFDM uses two identical, repeated symbols s1, s2 in the preamble for packet detection:
Receiver radio is always listening, receiving samples
  Call this received sample stream r[n]
s2
Preamble
Packet body
s1

## Slide 34: Searching for the preamble in noise
Suppose each preamble symbol is of length L
Receiver computes
Angle of each term in the sum is random
Sum of complex numbers with random angle ≈ 0
  c[0] ≈ 0
s2
s1
background noise
Packet body
r[n]:
L
Computing c[0]:

## Slide 35: Search window encounters preamble
Suppose preamble at position n0
Receiver computes
∡(zz*) = 0, so angle of each term in the sum is ≈ 0
Sum of complex numbers with ≈ 0 angle is large
  c[n0] is large
s2
s1
background noise
Packet body
r[n]:
L
Computing c[n0]:
n0

## Slide 36: Schmidl-Cox Packet Detection
Normalize power fluctuations in r[n], by measuring power:
Schmidl-Cox Packet Detection signal: m[n] = c[n] / p[n]
Packet detection metric m[n]
Time samples n

## Slide 37: A Closer Look at Carrier Frequency Offset
Limited precision of frequency oscillators
Up-convert baseband signal sn to passband signal
Down-convert passband signal yn back to baseband:
()

## Slide 38: Estimating Carrier Frequency Offset
Because of carrier frequency offset,
Consider the kth term in sum:
  This is equal to
    So all terms have the same angle
So, carrier frequency offset estimator
s2
s1
background noise
Packet body
r[n]:
L
Computing c[n0]:
n0

## Slide 39: Sample Clock Offset
The transmitter and receiver may sample the signal at slightly different rates, leading to a sample time offset ζ
All subcarriers experience the same sampling delay, but travel over different frequencies

## Slide 40: Correcting Sample Clock Offset in the Frequency Domain
Sample clock offset : slope
Residual CFO: intersection with y-axis
f
⦟ H

## Slide 41: Example: IEEE 802.11a, 802.11g
OFDM with up to 48 subcarriers
  Subcarrier spacing is 312.5 KHz
  Subcarriers modulated: BPSK, QPSK, 16-QAM, or 64-QAM
Uses a convolutional code at a rate of ½, 2/3, ¾ , or 5/6 to provide forward error correction
Results in data rates of 6, 9, 12, 18, 24, 36, 48, and 54 MBps
Cyclic prefix is 25% of a symbol time (16 vs 64)

## Slide 42: Per-subcarrier Bit Rate Choice

## Slide 43
Tuesday Topic:
MIMO I: Spatial Diversity
Friday Precept:
Lab 4: Single-carrier transceiver
on the HackRF hardware