## Slide 1: COS 461: Computer Networks
Mike Freedman
Spring 2020
Lectures: MW 1:30-2:50pm in Richardson 002
http://www.cs.princeton.edu/courses/archive/spring20/cos461/

## Slide 2: Protocol Layers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame
SONET frame

## Slide 3: Link = Medium + Adapters

## Slide 4: What is a Link?
Communication Medium
Network Adapter

## Slide 5: Broadcast Links: Shared Media

## Slide 6: Adaptors Communicating
Sending side
  Encapsulates packet in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
packet
frame
adapter
adapter
link layer protocol
packet

## Slide 7: Link-Layer Services
Encoding
  Represent the 0s and 1s
Framing
  Encapsulate packet into frame, adding header/trailer
Error detection
  Receiver detecting errors with checksums
Error correction
  Receiver optionally correcting errors
Flow control
  Pacing between sending and receiving nodes

## Slide 8: Addresses

## Slide 9: Medium Access Control Address
Identify the sending and receiving adapter
  Unique identifier for each network adapter
  Identifies the intended receiver(s) of the frame
  … and the sender who sent the frame

## Slide 10: Medium Access Control Address
MAC address (e.g., 00-15-C5-49-04-A9)
  Numerical address used within a link
  Unique, hard-coded in the adapter when it is built
  Flat name space of 48 bits
Hierarchical allocation: Global uniqueness!
  Blocks: assigned to vendors (e.g., Dell) by the IEEE
  Adapters: assigned by the vendor from its block
Broadcast address (i.e., FF-FF-FF-FF-FF-FF)
  Send the frame to all adapters

## Slide 11: As an Aside: Promiscuous Mode
Normal adapter: receives frames sent to
  The local MAC address
  Broadcast address FF-FF-FF-FF-FF-FF
Promiscuous mode
  Receive everything, independent of destination MAC
Useful for packet sniffing
  Network monitoring
  E.g., wireshark, tcpdump

## Slide 12: Why Not Just Use IP Addresses?
Links can support any network protocol
  Not just for IP (e.g., IPX, Appletalk, X.25, …)
  Different addresses on different kinds of links
An adapter may move to a new location
  So, cannot simply assign a static IP address
  Instead, must reconfigure the adapter’s IP address
Must identify the adapter during bootstrap
  Need to talk to the adapter to assign it an IP address

## Slide 13: Who Am I: Acquiring an IP Address
????
DHCP server
Dynamic Host Configuration Protocol (DHCP)
  Broadcast “I need an IP address, please!”
  Response “You can have IP address 1.2.3.4.”
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98
1.2.3.6

## Slide 14: Who Are You: Discovering the Receiver
Address Resolution Protocol (ARP)
  Broadcast “who has IP address 1.2.3.6?”
  Response “0C-C4-11-6F-E3-98 has 1.2.3.6!”
71-65-F7-2B-08-53
1.2.3.4
1.2.3.5
0C-C4-11-6F-E3-98
1.2.3.6
1A-2F-BB-76-09-AD

## Slide 15: Sharing the Medium

## Slide 16: Collisions
Single shared broadcast channel
  Avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98

## Slide 17: Multi-Access Protocol
Divide the channel into pieces
  in frequency vs. in time
17

## Slide 18: Multi-Access Protocol
Take turns
  Do not transmit w/o token
  With token, transmit for up to some max time/length
  Pass token to right
Punt
  Let collisions happen
  … and detect and recover from them
18

## Slide 19: Like Human Conversation…
Carrier sense
  Listen before speaking
  …and don’t interrupt!
Collision detection
  Detect simultaneous talking
  … and shut up!
Random access
  Wait for a random period of time
  … before trying to talk again!
19

## Slide 20: Carrier Sense Multiple Access
Listen for other senders
  Then transmit your data
Collisions can still occur
  Propagation delay
  Wasted transmission

## Slide 21: CSMA/CD Collision Detection
Detect collision
  Abort transmission
  Jam the link
Wait random time
  Transmit again
Hard in wireless
  Must receive data while transmitting

## Slide 22: Comparing the Three Approaches
Channel partitioning is
  (a) Efficient/fair at high load, inefficient at low load
  (b) Inefficient at high load, efficient/fair at low load
“Taking turns”
  (a) Inefficient at high load
  (b) Efficient at all loads
  (c) Robust to failures
Random access
  (a) Inefficient at low load
  (b) Efficient at all load
  (c) Robust to failures
22

## Slide 23: Comparing the Three Approaches
Channel partitioning is
  (a) Efficient/fair at high load, inefficient at low load
  (b) Inefficient at high load, efficient/fair at low load
“Taking turns”
  (a) Inefficient at high load
  (b) Efficient at all loads
  (c) Robust to failures
Random access
  (a) Inefficient at low load
  (b) Efficient at all load
  (c) Robust to failures
23

## Slide 24: Ethernet

## Slide 25: Ethernet
Dominant wired LAN technology
First widely used LAN technology
Kept up with speed race: 10 Mbps – 40 Gbps
Metcalfe’s
Ethernet
sketch
25

## Slide 26: Ethernet Uses CSMA/CD
Carrier Sense: wait for link to be idle
  Channel idle: start transmitting
  Channel busy: wait until idle
Collision Detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission, and send jam signal
Random Access: exponential back-off
  After collision, wait random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again
26

## Slide 27: Limitations on Ethernet Length
Latency depends on physical length of link
  Time to propagate a packet from one end to other
Suppose A sends a packet at time t
  And B sees an idle line at a time just before t+d
  … so B happily starts transmitting a packet
B detects a collision, and sends jamming signal
  But A doesn’t see collision till t+2d
latency d
A
B
27

## Slide 28: Limitations on Ethernet Length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  … and keep an eye out for a possible collision
Imposes restrictions on Ethernet
  Maximum length of the wire: 2500 meters
  Minimum length of the packet: 512 bits (64 bytes)
latency d
A
B
28

## Slide 29: Ethernet Frame Structure
Sending adapter encapsulates packet in frame
Preamble: synchronization
  Seven bytes with pattern 10101010, followed by one byte with pattern 10101011
  Used to synchronize receiver, sender clock rates
29

## Slide 30: Ethernet Frame Structure
Addresses: source and destination MAC addresses
  Adaptor passes frame to network-level protocol
    If destination is local MAC address or broadcast address
  Otherwise, adapter discards frame
Type: indicates the higher layer protocol
  Usually IP
  But also Novell IPX, AppleTalk, …
CRC: cyclic redundancy check
  Checked at receiver
  If error is detected, the frame is simply dropped
30

## Slide 31: Unreliable, Connectionless Service
Connectionless
  No handshaking between send and receive adapter
Unreliable
  Receiving adapter doesn’t send ACKs or NACKs
  Packets passed to network layer can have gaps
  Gaps can be filled by transport protocol (e.g., TCP)
  Otherwise, the application will see the gaps
31

## Slide 32: Summary: Multiple Layers
Different devices switch different things
  Network layer: packets (routers)
  Link layer: frames (bridges and switches)
  Physical layer: electrical signals (repeaters and hubs)
Application
Transport
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data
32

## Slide 33: Conclusion
Links
  Connect two or more network adapters
  … each with a unique address
  … over a shared communication medium
Coming next
  Network layer (IP)