## Slide 1: Queue Management
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/

## Slide 2: Last lecture: Congestion Control
?
?
logical link
physical
path
name
address
What can end-points do to collectively to make
good use of shared underlying resources?
Notes: This week, we’ll talk about how to share resources. Today we’ll talk about what the end-points can do in a distributed fashion, from the edge of the network. On Wednesday, we’ll talk about what the lower-level elements can do.

## Slide 3: Today: Queue Management
What can individual links do to make good use of shared underlying resources?
logical link
physical
path
name
address
?
Notes: This week, we’ll talk about how to share resources. Today we’ll talk about what the end-points can do in a distributed fashion, from the edge of the network. On Wednesday, we’ll talk about what the lower-level elements can do.

## Slide 4: Packet Queues

## Slide 5: Router
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane

## Slide 6: Line Cards (Interface Cards, Adaptors)
Packet handling
  Packet forwarding
  Buffer management
  Link scheduling
  Packet filtering
  Rate limiting
  Packet marking
  Measurement
to/from link
to/from switch
lookup
Receive
Transmit

## Slide 7: Queue Management Issues
Scheduling discipline
  Which packet to send?
  Some notion of fairness? Priority?
Drop policy
  When should you discard a packet?
  Which packet to discard?
Goal: balance throughput and delay
  Huge buffers minimize drops, but add to queuing delay (thus higher RTT, longer slow start, …)

## Slide 8: FIFO Scheduling and Drop-Tail
Access to the bandwidth: first-in first-out queue
  Packets only differentiated when they arrive
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet
✗

## Slide 9: Early Detection of Congestion

## Slide 10: Bursty Loss From Drop-Tail Queuing
TCP depends on packet loss
  Packet loss is indication of congestion
  TCP additive increase drives network into loss
Drop-tail leads to bursty loss
  Congested link: many packets encounter full queue
  Synchronization: many connections lose packets at once

## Slide 11: Slow Feedback from Drop Tail
Feedback comes when buffer is completely full
  … even though the buffer has been filling for a while
Plus, the filling buffer is increasing RTT
  … making detection even slower
Better to give early feedback
  Get 1-2 connections to slow down before it’s too late!

## Slide 12: Random Early Detection (RED)
Router notices that queue is getting full
  … and randomly drops packets to signal congestion
Packet drop probability
  Drop probability increases as queue length increases
  Else, set drop probability f(avg queue length)
Average Queue Length
Drop
Probability
0 1

## Slide 13: Properties of RED
Drops packets before queue is full
  In the hope of reducing the rates of some flows
Tolerant of burstiness in the traffic
  By basing the decisions on average queue length
Which of the following are true?
  (Y) Drops packet in proportion to each flow’s rate
  (M) High-rate flows selected more often
  (C) Helps desynchronize the TCP senders
  (A) All of the above
Notes: D: All of the above

## Slide 14: Properties of RED
Drops packets before queue is full
  In the hope of reducing the rates of some flows
Tolerant of burstiness in the traffic
  By basing the decisions on average queue length
Which of the following are true?
  (Y) Drops packet in proportion to each flow’s rate
  (M) High-rate flows selected more often
  (C) Helps desynchronize the TCP senders
  (A) All of the above
Notes: D: All of the above

## Slide 15: Problems With RED
Hard to get tunable parameters just right
  How early to start dropping packets?
  What slope for increase in drop probability?
  What time scale for averaging queue length?
RED has mixed adoption in practice
  If parameters aren’t set right, RED doesn’t help
Many other variations in research community
  Names like “Blue” (self-tuning), “FRED”…

## Slide 16: From Loss to Notification

## Slide 17: Feedback: From loss to notification
Early dropping of packets
  Good: gives early feedback
  Bad: has to drop the packet to give the feedback
Explicit Congestion Notification
  Router marks the packet with an ECN bit
  Sending host interprets as a sign of congestion

## Slide 18: Explicit Congestion Notification
Needs support by router, sender, AND receiver
  End-hosts check ECN-capable during TCP handshake
ECN protocol (repurposes 4 header bits)
  Sender marks “ECN-capable” when sending
  If router sees “ECN-capable” and congested, marks packet as “ECN congestion experienced”
  If receiver sees “congestion experienced”, marks “ECN echo” flag in responses until congestion ACK’d
  If sender sees “ECN echo”, reduces cwnd and marks “congestion window reduced” flag in next packet
Notes: Why extra ECN flag? Congestion could happen in either direction, want sender to react to forward direction
Why CRW ACK? ECN-echo could be lost, but we ideally only respond to congestion in forward direction

## Slide 19: ECN Questions
Why separate ECN experienced and echo flags?
  (Y) Detect reverse path congestion with “experienced”
  (M) Congestion could happen in either direction, want sender to react to forward direction
  (C) Both of the above

## Slide 20: ECN Questions
Why separate ECN experienced and echo flags?
  (Y) Detect reverse path congestion with “experienced”
  (M) Congestion could happen in either direction, want sender to react to forward direction
  (C) Both of the above
Why “echo” resent & “congestion window reduced” ACK?
  (Y) Congestion in reverse path can lose ECN-echo, still want to respond to congestion in forward path
  (M) Only should apply backoff once per cwnd
  (C) Both of the above

## Slide 21: ECN Questions
Why separate ECN experienced and echo flags?
  (Y) Detect reverse path congestion with “experienced”
  (M) Congestion could happen in either direction, want sender to react to forward direction
  (C) Both of the above
Why “echo” resent & “congestion window reduced” ACK?
  (Y) Congestion in reverse path can lose ECN-echo, still want to respond to congestion in forward path
  (M) Only should apply backoff once per cwnd
  (C) Both of the above

## Slide 22: Link Scheduling

## Slide 23: First-In First-Out Scheduling
First-in first-out scheduling
  Simple, but restrictive
Example: two kinds of traffic
  Voice over IP needs low delay
  E-mail is not that sensitive about delay
Voice traffic waits behind e-mail
23

## Slide 24: Strict Priority
Multiple levels of priority
  Always transmit high-priority traffic, when present
Isolation for the high-priority traffic
  Almost like it has a dedicated link
  Except for (small) delay for packet transmission
But, lower priority traffic may starve 
24

## Slide 25: Weighted Fair Scheduling
Weighted fair scheduling
  Assign each queue a fraction of the link bandwidth
  Rotate across queues on a small time scale
50% red, 25% blue, 25% green
25

## Slide 26: Weighted Fair Scheduling
If non-work conserving (resources can go idle)
  Each flow gets at most its allocated weight
WFQ is work-conserving
  Send extra traffic from one queue if others are idle
  Results in (Y) higher or (M) lower utilization than non-work conserving?
WFQ results in max-min fairness
  Maximize the minimum rate of each flow
26
Notes: Results in higher

## Slide 27: Max-Min Fairness
Maximize the minimum rate of each flow
  Allocate in order of increasing demand
  No flow gets more than demand
  The excess, if any, is equally shared
27
10
8
2
10
Rate Demanded/Allocated
Flows sorted by demand
2
8
10
2
2
2
Total = 6
Notes: Results in higher

## Slide 28: Max-Min Fairness
Maximize the minimum rate of each flow
  Allocate in order of increasing demand
  No flow gets more than demand
  The excess, if any, is equally shared
28
10
8
2
10
Rate Demanded/Allocated
Flows sorted by demand
8
10
2
2
2
f = 4:
min(8, 4) = 4
min(10, 4) = 4
min(2, 4) = 2
4
4
2
Total = 10
4
4
2
Notes: Results in higher

## Slide 29: Weighted Fair Queueing
Link 1, ingress
Link 1, egress
Link 2, ingress
Link 2, egress
Link 3, ingress
Link 3, egress
Scheduler
flow 1
flow 2
flow n
Classifier
WFQ slides credit: Nick McKeown (Stanford)

## Slide 30: Bit-by-Bit Fair Queueing
Flow 1
Flow N
Classification
Bit-by-bit round robin
Question: What is a “flow”?
Flow 5-tuple: protocol, IP source/dest, port src/dest
Question: How can we give weights?
Protocol class, bit markings, prefixes, etc.
Notes: One connection: IP source/dest, TCP port/dest
Aggregate of traffic called a class; members have same requirements (all video, bit-torrent, traffic to a particular domain, etc)

## Slide 31: Bit-by-Bit Weighted Fair Queueing
Flows allocated different rates by servicing different number of bits for each flow during each round.
1
w1 = 0.1
w3 = 0.3
R1
C
w4 = 0.3
w2 = 0.3
Order of service for the four queues:
… f1, f2, f2, f2, f3, f3, f3, f4, f4, f4, f1,…

## Slide 32: Packet vs. “Fluid” System
Bit-by-bit FQ is not implementable:
…In real packet-based systems:
  One queue is served at any given time
  Packet transmission cannot be preempted
Goal: A packet scheme close to fluid system
  Bound performance w.r.t. fluid system

## Slide 33: First Cut: Simple Round Robin
Serve a packet from non-empty queues in turn
  Lets assume all flows have equal weight
Variable packet length  get more service by sending bigger packets
Unfair instantaneous service rate (esp. with variable weights)
  E.g. 500 flows: 250 with weight 1, 250 with weight 10
  Each round takes 2,750 packet times
  What if a packet arrives right after its “turn”?
Notes:   Q1: What about different packet sizes? How might you mitigate the problem? What if you knew mean pkt size?

## Slide 34: Packet-by-packet Fair Queuing (Weighted Fair Queuing)
Deals better with variable size packets and weights
Key Idea:
Determine the finish time of packets in bit-by-bit system, assuming no more arrivals
Serve packets in order of finish times

## Slide 35: Implementing WFQ
Challenge: Determining finish time is hard
Idea: Don’t need finish time. Need finish order.
The finish order is a lot easier to calculate.

## Slide 36: Finish order
In what order do the packets finish?
1
w1 = 0.1
w3 = 0.3
R1
C
w4 = 0.3
w2 = 0.3
Order of service for the four queues:
… f1, f2, f2, f2, f3, f3, f3, f4, f4, f4, f1,…
L1
L2
L3
L4
Increasing Li/wi
Does not change with future packet arrivals!

## Slide 37: Bit-by-bit System Round
Round – One complete cycle through all the queues sending wi bits per queue
1
w1 = 0.1
w3 = 0.3
R1
C
w4 = 0.3
w2 = 0.3
Order of service for the four queues:
… f1, f2, f2, f2, f3, f3, f3, f4, f4, f4, f1,…
L1
L2
L3
L4
w1 = 1
w3 = 3
w4 = 3
w2 = 3
Question: How long does a round take?
Notes: Makes sense that this is doable because we saw that the GPS order does not depend on future events

## Slide 38: Bit-by-bit System Round
Round – One complete cycle through all the queues sending wi bits per queue
1
w1 = 0.1
w3 = 0.3
R1
C
w4 = 0.3
w2 = 0.3
Order of service for the four queues:
… f1, f2, f2, f2, f3, f3, f3, f4, f4, f4, f1,…
L1
L2
L3
L4
w1 = 1
w3 = 3
w4 = 3
w2 = 3
R(t) = # of rounds at time t
C = link rate
B(t) = set of backlogged flows
Notes: Makes sense that this is doable because we saw that the GPS order does not depend on future events

## Slide 39: Bit-by-bit System Round
Round – One complete cycle through all the queues sending wi bits per queue
1
w1 = 0.1
w3 = 0.3
R1
C
w4 = 0.3
w2 = 0.3
Order of service for the four queues:
… f1, f2, f2, f2, f3, f3, f3, f4, f4, f4, f1,…
L1
L2
L3
L4
w1 = 1
w3 = 3
w4 = 3
w2 = 3
  Question: How many rounds does it take to serve a packet of length L from flow i?
Notes: Makes sense that this is doable because we saw that the GPS order does not depend on future events

## Slide 40: Bit-by-bit System Round
Round – One complete cycle through all the queues sending wi bits per queue
1
w1 = 0.1
w3 = 0.3
R1
C
w4 = 0.3
w2 = 0.3
Order of service for the four queues:
… f1, f2, f2, f2, f3, f3, f3, f4, f4, f4, f1,…
L1
L2
L3
L4
w1 = 1
w3 = 3
w4 = 3
w2 = 3
Packet of length L takes L/wi rounds to serve
Notes: Makes sense that this is doable because we saw that the GPS order does not depend on future events

## Slide 41: Round (aka. “Virtual Time”) Implementation of WFQ
  Question: What is finish round of kth packet – Fik?

## Slide 42: Round (aka. “Virtual Time”) Implementation of WFQ
Assign a start/finish round to each packet at arrival
 serve packets in order of finish rounds
(Flow i backlogged)
k
……
k-1
(Flow i empty)
k
Suppose kth packet of flow i arrives at time a
Start round
of kth packet
Finish round
of (k-1)th packet
Round number
at time a

## Slide 43: Putting it All Together
For kth packet of flow i arriving at time a:
  Question: How to compute R(a)?
Simple approximation:
Set R(a) to start or finish round of packet currently in service

## Slide 44: Implementation Trade-Offs
FIFO
  One queue, trivial scheduler
Strict priority
  One queue per priority level, simple scheduler
Weighted fair scheduling
  One queue per class, and more complex scheduler
44

## Slide 45: Quality of Service Guarantees

## Slide 46: Distinguishing Traffic
Applications compete for bandwidth
  E-mail traffic can cause congestion/losses for VoIP
Principle 1: Packet marking
  So router can distinguish between classes
  E.g., Type of Service (ToS) bits in IP header
46

## Slide 47: Preventing Misbehavior
Applications misbehave
  VoIP sends packets faster than 1 Mbps
Principle 2: Policing
  Protect one traffic class from another
  By enforcing a rate limit on the traffic
47

## Slide 48: Subdividing Link Resources
Principle 3: Link scheduling
  Ensure each application gets its share
  … while (optionally) using any extra bandwidth
  E.g., weighted fair queuing
48

## Slide 49: Reserving Resources, and Saying No
Traffic cannot exceed link capacity
  Deny access, rather than degrade performance
Principle 4: Admission control
  Application declares its needs in advance
  Application denied if insufficient resources available
49

## Slide 50: Quality of Service (QoS)
Guaranteed performance
  Alternative to best-effort delivery model
QoS protocols and mechanisms
  Packet classification and marking
  Traffic shaping
  Link scheduling
  Resource reservation and admission control
  Identifying paths with sufficient resources
50