## Slide 1: Routing
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/

## Slide 2: Routing: Mapping Link to Path
logical link
physical
path
name
address

## Slide 3: Data and Control Planes
Switching
Fabric
Processor
Line card
Line card
Line card
Line card
Line card
Line card
data plane
control plane

## Slide 4: Routing vs. Forwarding
Routing: control plane
  Computing paths the packets will follow
  Routers talking amongst themselves
  Creating the forwarding tables
Forwarding: data plane
  Directing a data packet to an outgoing link
  Using the forwarding tables
4

## Slide 5: Three Issues to Address
What does the protocol compute?
  E.g., shortest paths
What algorithm does the protocol run?
  E.g., link-state routing
How do routers learn end-host locations?
  E.g., injecting into the routing protocol
5

## Slide 6: What Does the Protocol Compute?
6

## Slide 7: Different Types of Paths
Static model
  What is computed, not how computation performed
Trade-offs
  State to represent the paths
  Efficiency of the paths
  Ability to support multiple paths
  Complexity of path computation
7

## Slide 8: Spanning Tree
One tree that reaches every node
  Single path between each pair of nodes
  No loops, so can support broadcast easily
  But, paths are long, and some links not used
8

## Slide 9: Shortest Paths
Shortest path(s) between pairs of nodes
  A shortest-path tree rooted at each node
  Min hop count or min sum of edge weights
  Multipath routing is limited to Equal Cost MultiPath

## Slide 10: Local Policy at Each Hop
1 d
1 2 d
2 1 d
2 d
3 2 d
3 4 d
4 d
5 4 d
6 4 d
6 5 4 d
10
Is (3 2 d) chosen path?
  (Y) True
  (M) False
Locally best path
  Local policy: each node picks the path it likes best
  … among the paths chosen by its neighbors
2
3
1
4
d
5
6

## Slide 11: Local Policy at Each Hop
Locally best path
  Local policy: each node picks the path it likes best
  … among the paths chosen by its neighbors
11
1 d
1 2 d
2 1 d
2 d
3 2 d
3 4 d
4 d
5 4 d
6 4 d
6 5 4 d
2
3
1
4
d
5
6
1 d
1 2 d
2 1 d
2 d
4 d
3 2 d
3 4 d
5 4 d
6 4 d
6 5 4 d
2
3
1
4
d
5
6

## Slide 12: End-to-End Path Selection
End-to-end path selection
  Each node picks its own end to end paths
  … independent of what other paths other nodes use
  More state and complexity in the nodes
12

## Slide 13: How to Compute Paths?
13

## Slide 14: Spanning Tree Algorithm
Elect a root
  The switch with the smallest identifier
  And form a tree from there
Algorithm
  Repeatedly talk to neighbors
    “I think node Y is the root”
    “My distance from Y is d”
  Update based on neighbors
    Smaller id as the root
    Smaller distance d+1
root
One hop
Three hops
Used in Ethernet LANs
14

## Slide 15: Spanning Tree Example: Switch #4
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
  Notation: (my root, my distance, my ID)
Switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  Thinks #2 is root and it’s one hop away
Switch #4 hears from #7
  Receives (2, 1, 7) from 7
  But, this is a longer path, so 4 prefers 4-2 over 4-7-2
  And removes 4-7 link from the tree
3
5
6
7
15
1
2
4

## Slide 16: Shortest-Path Problem
Compute: path costs to all nodes
  From a given source u to all other nodes
  Cost of the path through each outgoing link
  Next hop along the least-cost path to s
3
2
2
1
1
4
1
4
5
3
u
s
6
16

## Slide 17: Link State: Dijkstra’s Algorithm
Flood the topology information to all nodes
Each node computes shortest paths to other nodes
S = {u}
for all nodes v
if (v is adjacent to u)
D(v) = c(u,v)
else D(v) = ∞
add w with smallest D(w) to S
update D(v) for all adjacent v:
D(v) = min{D(v), D(w) + c(w,v)}
until all nodes are in S
Initialization
Loop
Used in OSPF and IS-IS

## Slide 18: Link-State Routing Example
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
18

## Slide 19: Link-State Routing Example (cont.)
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
3
2
2
1
1
4
1
4
5
3
19

## Slide 20: Link State: Shortest-Path Tree
Shortest-path tree from u
Forwarding table at u
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
v
(u,v)
w
(u,w)
x
(u,w)
y
(u,v)
z
(u,v)
link
s
(u,w)
t
(u,w)
20
dest

## Slide 21: Link State: Shortest-Path Tree
Find shortest path t to v
Forwarding table entry at t
(Y) (t,x) (M) (t, s)
Distance from t to v
(Y) 6 (M) 7 (C) 8 (A) 9
Rounds to find shortest path
(Y) 5 (M) 6 (C) 7 (A) 8
4
1
3
4
1
1
1
1
5
2
u
v
w
x
y
z
s
t
21
Notes: 1: B (t,s), gets to X in 4
2: B: 7
3: A (non-negative weights)

## Slide 22: Link State: Shortest-Path Tree
Find shortest path t to v
Forwarding table entry at t
(Y) (t,x) (M) (t, s)
Distance from t to v
(Y) 6 (M) 7 (C) 8 (A) 9
Rounds to find shortest path
(Y) 5 (M) 6 (C) 7 (A) 8
4
1
3
4
1
1
1
1
5
2
u
v
w
x
y
z
s
t
22
Rounds: Add s (distance 2), w (distance 3), x (distance 4), z (distance 5), equi-distance to u or y (distance 6)
So could be 5 (via y) or 6 (via u then y)
Notes: 1: B (t,s), gets to X in 4
2: B: 7
3: A (non-negative weights)

## Slide 23: Distance Vector: Bellman-Ford Algo
Define distances at each node x
  dx(y) = cost of least-cost path from x to y
Update distances based on neighbors
  dx(y) = min {c(x,v) + dv(y)} over all neighbors v
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
du(z) = min{ c(u,v) + dv(z),
c(u,w) + dw(z)}
Used in RIP and EIGRP
23

## Slide 24: Distance Vector Example
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
dy(z) = 1
dx(z) = 4
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
dv(z) = min{ 2+dy(z), 1+dx(z) }
= 3

## Slide 25: Distance Vector Example (Cont.)
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
dw(z) = min{ 1+dx(z), 4+ds(z),
2+du(z) }
= 5
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
du(z) =
(Y) 5 (M) 6 (C) 7

## Slide 26: Distance Vector Example (Cont.)
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
dw(z) = min{ 1+dx(z), 4+ds(z),
2+du(z) }
= 5
3
2
2
1
1
4
1
4
5
3
u
v
w
x
y
z
s
t
du(z) = min{ 3+dv(z), 2+dw(z) }
= 6

## Slide 27: Path-Vector Routing
Extension of distance-vector routing
  Support flexible routing policies
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
3
2
1
d
“d: path (2,1)”
“d: path (1)”
data traffic
data traffic
Used in BGP
27

## Slide 28: Path-Vector: Flexible Policies
Each node can apply local policies
  Path selection: Which path to use?
  Path export: Which paths to advertise?
2
3
1
2
3
1
Node 2 prefers “2, 3, 1” over “2, 1”
Node 1 doesn’t let 3 hear the path “1, 2”
28

## Slide 29: End-to-End Signaling
Establish end-to-end path in advance
  Learn the topology (as in link-state routing)
  End host or router computes and signals a path
    Signaling: install entry for each circuit at each hop
    Forwarding: look up the circuit id in the table
1
2
1: 7
2: 7
link 7
1: 14
2: 8
link 14
link 8
Used in MPLS with RSVP
29

## Slide 30: Source Routing
Similar to end-to-end signaling
  But the data packet carries the hops in the path
End-host control
  Tell the end host the topology
  Let the end host select the end-to-end path
Variations of source routing
  Strict: specify every hop
  Loose: specify intermediate points
    Used in IP source routing (but almost always disabled)
30

## Slide 31: Learning Where the Hosts Are
31

## Slide 32: Finding the Hosts
Building a forwarding table
  Computing paths between network elements
  … and figuring out where the end-hosts are
How to find the hosts?
  Learning/flooding
  Injecting into the routing protocol
  Dissemination using a different protocol
  Directory service
32

## Slide 33: Learning and Flooding
When a frame arrives
  Inspect the source address
  Associate address with the incoming interface
When the frame has an unfamiliar destination
  Forward out all interfaces
  … except incoming interface
A
B
C
D
Switch learns how to reach A
A
B
C
D
When in doubt, shout!
Used in Ethernet LANs
33

## Slide 34: Inject into Routing Protocol
Treat the end host (or subnet) as a node
  And disseminate in the routing protocol
  E.g., flood information about where addresses attach
3
2
2
1
1
4
1
4
5
3
u
s
6
Used in OSPF and IS-IS, especially in enterprise networks
. . .
34

## Slide 35: Disseminate With Another Protocol
Distribute using another protocol
  One router learns the route
  … and shares the information with other routers
learn a route to d
(e.g., via BGP)
disseminate route to other routers
Internal BGP (iBGP) used in backbone networks
35

## Slide 36: Directory Service
Contact a service to learn the location
  Look up the end-host or subnet address
  … to determine the label to put on the packet
s
d
i
e
directory
“Host d is at egress e”
Encapsulate packet to send to egress e
Used in some
data centers
36

## Slide 37: Conclusions: Many Different Solutions
Ethernet LAN and home networks
  Spanning tree, MAC learning, flooding
Enterprise
  Link-state routing, injecting subnet addresses
Backbone
  Link-state routing inside, path-vector routing with neighboring domains, and iBGP dissemination
Data centers
  Many different solutions, still in flux
37