## Slide 1: Interdomain Routing
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/
peer
peer
advertisements
traffic

## Slide 2: How to avoid BGP Instability
Detecting conflicting policies
  CON: Computationally expensive
  CON: Requires too much cooperation
Detecting oscillations
  Observing the repetitive BGP routing messages
  CON: Requires dynamic, stateful analysis
Restricted routing policies and topologies
  Policies based on business relationships
2

## Slide 3: AS (Autonomous System) Business Relationships
3

## Slide 4: Customer-Provider Relationship
Customer pays provider for access to Internet
  Provider exports its customer routes to everybody
  Customer exports provider routes only to its customers
d
d
provider
customer
customer
provider
Traffic to customer
Traffic from customer
advertisements
traffic
4

## Slide 5: Peer-Peer Relationship
Peers exchange traffic between their customers
  AS exports only customer routes to a peer
  AS exports a peer’s routes only to its customers
peer
peer
Traffic to/from the peer and its customers
d
advertisements
traffic
5

## Slide 6: Hierarchical AS Relationships
Provider-customer graph is directed and acyclic
  If u is a customer of v and v is a customer of w
  … then w is not a customer of u
u
v
w
6

## Slide 7: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Path 1 2 d
Path 7 d
Path 5 8 d
Path 6 4 3 d
Path 8 5 d
Path 6 5 d
Path 1 4 3 d
7

## Slide 8: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Path 1 2 d
Path 7 d
Path 5 8 d
Path 6 4 3 d
Path 8 5 d
Path 6 5 d
Path 1 4 3 d
8
Y) Valid M) Invalid
Valid
Valid
Invalid
Valid
Valid
Invalid
Invalid

## Slide 9: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Valid paths: “1 2 d” and “7 d”
Invalid path: “5 8 d”
9

## Slide 10: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Valid paths: “6 4 3 d” and “8 5 d”
Invalid paths: “6 5 d” and “1 4 3 d”
10

## Slide 11: Local Control, Global Stability: “Gao-Rexford Conditions”
Route export
  Don’t export routes learned from a peer or provider to another peer or provider
Global topology
  Provider-customer relationship graph is acyclic
  E.g., my customer’s customer is not my provider
Route selection
  Prefer routes through customers over routes through peers and providers
Guaranteed to converge to unique, stable solution
11

## Slide 12: How do we implement Interdomain Routing Policy?

## Slide 13: Selecting a Best Path
Routing Information Base
  Store all BGP routes for each destination prefix
  Withdrawal: remove the route entry
  Announcement: update the route entry
BGP decision process
  Highest local preference
  Shortest AS path
  Closest egress point
  Arbitrary tie break

## Slide 14: Import Policy: Local Preference
Favor one path over another
  Override the influence of AS path length
Example: prefer customer over peer
AT&T
Sprint
Princeton
Tier-2
Tier-3
Local-pref = 100
Local-pref = 90

## Slide 15: Import Policy: Filtering
Discard some route announcements
  Detect configuration mistakes and attacks
Examples on session to a customer
  Discard route if prefix not owned by the customer
  Discard route with other large ISP in the AS path
AT&T
Princeton
USLEC
128.112.0.0/16

## Slide 16: Export Policy: Filtering
Discard some route announcements
  Limit propagation of routing information
Examples
  Don’t announce routes from one peer to another
  Don’t announce routes for management hosts
AT&T
Princeton
Sprint
128.112.0.0/16
UUNET
network operator

## Slide 17: Export Policy: Attribute Manipulation
Modify attributes of the active route
  To influence the way other ASes behave
Example: AS prepending
  Artificially inflate AS path length seen by others
  Convince some ASes to send traffic another way
AT&T
Princeton
USLEC
128.112.0.0/16
Sprint
88 88
88

## Slide 18: Reflect Business Relationships
Common relationships
  Customer-provider
  Peer-peer
  Backup, sibling, …
ISP terminology:
  Tier-1 (~15 worldwide): No settlement or transit
  Tier-2 ISPs: Widespread peering, still buy transit
Policies implementing in BGP, e.g.,
  Import: Ranking customer routes over peer routes
  Export: Export only customer routes to peers and providers

## Slide 19: BGP Policy
Tier 1 ISPs?
Y. U, W
M. U, X
C. X, Y, Z
Which path may packets take (given commercial policies)?
Y. Red
M. Blue
C. Green
A. Orange
Notes: Tier 1: UW (no providers)
Which paths: Orange

## Slide 20: BGP Policy
Tier 1 ISPs?
Y. U, W
M. U, X
C. X, Y, Z
Which path may packets take (given commercial policies)?
Y. Red
M. Blue
C. Green
A. Orange
Notes: Tier 1: UW (no providers)
Which paths: Orange

## Slide 21: BGP Policy
Tier 1 ISPs?
Y. U, W
M. U, X
C. X, Y, Z
Which path may packets take (given commercial policies)?
Y. Red
M. Blue
C. Green
A. Orange
Notes: Tier 1: UW (no providers)
Which paths: Orange

## Slide 22: BGP Policy
Tier 1 ISPs?
Y. U, W
M. U, X
C. X, Y, Z
Which path may packets take (given commercial policies)?
Y. Red
M. Blue
C. Green
A. Orange
Notes: Tier 1: UW (no providers)
Which paths: Orange

## Slide 23: BGP Policy Configuration
Routing policy languages are vendor-specific
  Not part of the BGP protocol specification
  Different languages for Cisco, Juniper, etc.
Still, all languages have some key features
  List of clauses matching on route attributes
  … and discarding or modifying the matching routes
Configuration done by human operators
  Implementing the policies of their AS
  Business relationships, traffic engineering, security

## Slide 24: How do backbone AS operate?
Backbone Topology

## Slide 25: Backbone Networks
Backbone networks
  Multiple Points-of-Presence (PoPs)
  Lots of communication between PoPs
  Accommodate traffic demands and limit delay

## Slide 26: Abilene Internet2 Backbone

## Slide 27: Points-of-Presence (PoPs)
Inter-PoP links
  Long distances
  High bandwidth
Intra-PoP links
  Short cables between racks or floors
  Aggregated bandwidth
Links to other networks
  Wide range of media and bandwidth
Intra-PoP
Other networks
Inter-PoP

## Slide 28: Where to Locate Nodes and Links
Placing Points-of-Presence (PoPs)
  Large population of potential customers
  Other providers or exchange points
  Cost and availability of real-estate
  Mostly in major metropolitan areas (“NFL cities”)
Placing links between PoPs
  Already fiber in the ground
  Needed to limit propagation delay
  Needed to handle the traffic load

## Slide 29: Peering
Exchange traffic between customers
  Settlement-free
Diverse peering locations
  Both coasts, and middle
Comparable capacity at all peering points
  Can handle even load
Customer A
Customer B
multiple
peering
points
Provider A
Provider B

## Slide 30: Combining Intradomain and Interdomain Routing

## Slide 31: Intradomain Routing
Compute shortest paths between routers
  Router C takes path C-F-A to router A
Using link-state routing protocols
  E.g., OSPF, IS-IS
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B

## Slide 32: Interdomain Routing
Learn paths to remote destinations
  AT&T learns two paths to Yale
Applies local policies to select a best route
AT&T
Sprint
Princeton
Tier-2
Tier-3

## Slide 33: An AS is Not a Single Node
Multiple routers in an AS
  Need to distribute BGP information within the AS
  Internal BGP (iBGP) sessions between routers
AS1
AS2
eBGP
iBGP

## Slide 34: Internal BGP and Local Preference
Both routers prefer path through AS 100
… even though right router learns external path
I-BGP
AS 256
AS 300
Local Pref = 100
Local Pref = 90
AS 100
AS 200

## Slide 35: Hot-Potato (Early-Exit) Routing
Hot-potato routing
  Each router selects the closest egress point
  … based on the path cost in intradomain protocol
BGP decision process
  Highest local preference
  Shortest AS path
  Closest egress point
  Arbitrary tie break
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dst

## Slide 36: Hot-Potato Routing
Selfish routing
  Each provider dumps traffic on the other
  As early as possible
Asymmetric routing
  Traffic does not flow on same path in both directions
Customer A
Customer B
multiple
peering
points
Provider A
Provider B
Early-exit
routing

## Slide 37: Joining BGP and IGP Information
Border Gateway Protocol (BGP)
  Announces reachability to external destinations
  Maps a destination prefix to an egress point
    128.112.0.0/16 reached via 192.0.2.1
Interior Gateway Protocol (IGP)
  Used to compute paths within the AS
  Maps an egress point to an outgoing link
    192.0.2.1 reached via 10.10.10.10
192.0.2.1
10.10.10.10

## Slide 38: Joining BGP with IGP Information
IGP
AS 7018
AS 88
192.0.2.1
128.112.0.0/16
BGP
192.0.2.1
128.112.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
128.112.0.0/16
Next Hop = 192.0.2.1
+
(Y) True (M) False
The FIB of internal routers are of size O(all dest prefixes known to ISP)
The FIB of internal routers point to border router to neighbor ISP
10.10.10.10
Notes: Questions:
FIB of size: TRUE
Point to neighbor ISP: False (point to next hop internal router)

## Slide 39: Joining BGP with IGP Information
IGP
AS 7018
AS 88
192.0.2.1
128.112.0.0/16
BGP
192.0.2.1
128.112.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
128.112.0.0/16
Next Hop = 192.0.2.1
+
(Y) True (M) False
The FIB of internal routers are of size O(all dest prefixes known to ISP)
The FIB of internal routers point to border router to neighbor ISP
TRUE
FALSE
10.10.10.10
Notes: Questions:
FIB of size: TRUE
Point to neighbor ISP: False (point to next hop internal router)

## Slide 40: Joining BGP with IGP Information
IGP
AS 7018
AS 88
192.0.2.1
128.112.0.0/16
BGP
192.0.2.1
128.112.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
destination
next hop
128.112.0.0/16
Next Hop = 192.0.2.1
+
Forwarding Table
128.112.0.0/16
destination
next hop
10.10.10.10
192.0.2.0/30
10.10.10.10
10.10.10.10

## Slide 41: Backbone Traffic Engineering

## Slide 42: Routing With “Static” Link Weights
Routers flood information to learn topology
  Determine “next hop” to reach other routers…
  Compute shortest paths based on link weights
Link weights configured by network operator
3
2
2
1
1
3
1
4
5
3

## Slide 43: Setting the Link Weights
How to set the weights
  Inversely proportional to link capacity?
  Proportional to propagation delay?
  Network-wide optimization based on traffic?
3
2
2
1
1
3
1
4
5
3
3

## Slide 44: Measure, Model, and Control
Topology/
Configuration
Offered
traffic
Changes to
the network
Operational network
Network-wide
“what if” model
measure
control

## Slide 45: Limitations of Shortest-Path Routing
Sub-optimal traffic engineering
  Restricted to paths expressible as link weights
Limited use of multiple paths
  Only equal-cost multi-path, with even splitting
Disruptions when changing the link weights
  Transient packet loss and delay, and out-of-order
Slow adaptation to congestion
  Network-wide re-optimization and configuration
Overhead of the management system

## Slide 46: Constrained Shortest Path First
Run a link-state routing protocol
  Configurable link weights
  Plus other metrics like available bandwidth
Constrained shortest-path computation
  Prune unwanted links
  (e.g., not enough bw)
  Compute shortest path on the remaining graph
s
d
5, bw=10
6, bw=60
5
bw=70
3,
bw=80

## Slide 47: Conclusions
Interdomain routing
  Business relationships reflected in interdomain routing, leads to more stable paths
  Peering and transit key ideas between providers, peers, and customer AS
Backbone networks
  Transit service for customers
  Combine inter and intradomain routing
  Glue that holds the Internet together