## Slide 1: Interdomain Routing Security
Mike Freedman
COS 461: Computer Networks
http://www.cs.princeton.edu/courses/archive/spr20/cos461/

## Slide 2: Interdomain Routing
AS-level topology
  Nodes are Autonomous Systems (ASes)
  Edges are links and business relationships
1
2
3
4
5
6
7
Client
Web server

## Slide 3: Border Gateway Protocol (BGP)
ASes exchange reachability information
  Destination: block of addresses (an “IP prefix”)
  AS path: sequence of ASes along the path
Policies configured by network operators
  Path selection: which of the paths to use?
  Path export: which neighbors to tell?
1
2
3
d
“I can reach d”
“I can reach d
via AS 1”
data traffic
data traffic

## Slide 4: BGP Session Security

## Slide 5: TCP Connection Underlying BGP Session
BGP session runs over TCP
  TCP connection between neighboring routers
  BGP messages sent over TCP connection
  Makes BGP vulnerable to attacks on TCP
BGP session
physical link

## Slide 6: Attacks on Session Security
Confidentiality
  Eavesdropping by tapping the link
  Inferring routing policies and stability
Integrity
  Tampering by dropping, modifying, adding packets
  Changing, filtering, or replaying BGP routes
Availability
  Resetting the session or congesting the link
  Disrupting communication and overloading routers

## Slide 7: Defending Session Security is Easy
BGP routing information is propagated widely
  Confidentiality isn’t all that important
Two end-points have a business relationship
  Use known IP addresses and ports to communicate
  Can agree to sign and encrypt messages
Limited physical access to the path
  Direct physical link, often in same building
Low volume of special traffic
  Filter packets from unexpected senders
  Can give BGP packets higher priority

## Slide 8: Validity of the routing information: Origin authentication

## Slide 9: IP Address Ownership and Hijacking
IP address block assignment
  ICANN -> Regional Internet Registries -> ISPs
Proper origination of a prefix into BGP
  By the AS who owns the prefix
  … or, by its upstream provider(s) in its behalf
However, what’s to stop someone else?
  Prefix hijacking: another AS originates the prefix
  BGP does not verify that the AS is authorized
  Registries of prefix ownership are inaccurate

## Slide 10: Prefix Hijacking
Blackhole: data traffic is discarded
Snooping: data traffic is inspected, then redirected
Impersonation: traffic sent to bogus destinations
1
2
3
4
5
6
7
12.34.0.0/16
12.34.0.0/16

## Slide 11: Hijacking is Hard to Debug
The victim AS doesn’t see the problem
  Picks its own route, might not learn the bogus route
May not cause loss of connectivity
  Snooping, with minor performance degradation
Or, loss of connectivity is isolated
  E.g., only for sources in parts of the Internet
Diagnosing prefix hijacking
  Analyzing updates from many vantage points
  Launching traceroute from many vantage points

## Slide 12: Sub-Prefix Hijacking
Originating a more-specific prefix
  Every AS picks the bogus route for that prefix
  Traffic follows the longest matching prefix
1
2
3
4
5
6
7
12.34.0.0/16
12.34.158.0/24

## Slide 13: How to Hijack a Prefix
The hijacking AS has
  Router with BGP session(s)
  Configured to originate the prefix
Getting access to the router
  Network operator makes configuration mistake
  Disgruntled operator launches an attack
  Outsider breaks in to the router and reconfigures
Getting other ASes to believe bogus route
  Neighbor ASes do not discard the bogus route
  E.g., not doing protective filtering

## Slide 14: YouTube Outage on Feb 24, 2008
YouTube (AS 36561): 208.65.152.0/22
Pakistan Telecom (AS 17557)
  Government order to block access to YouTube
  Announces 208.65.153.0/24 to PCCW (AS 3491)
  All packets to YouTube get dropped on the floor
Mistakes were made
  AS 17557: announce to everyone, not just customers
  AS 3491: not filtering routes announced by AS 17557
Lasted 100 minutes for some, 2 hours for others

## Slide 15: Timeline (UTC Time)
18:47:45: First evidence of hijacked /24 route in Asia
18:48:00: Several big trans-Pacific providers carrying route
18:49:30: Bogus route fully propagated
20:07:25: YouTube advertising /24 to attract traffic back
20:08:30: Many (but not all) providers are using valid route
20:18:43: YouTube announces two more-specific /25 routes
20:19:37: Some more providers start using the /25 routes
20:50:59: AS 17557 starts prepending (“3491 17557 17557”)
20:59:39: AS 3491 disconnects AS 17557
21:00:00: Videos of cats flushing toilets are available again!

## Slide 16: Another Example: Spammers
Spammers sending spam
  Form a (bidrectional) TCP connection to mail server
  Send a bunch of spam e-mail, then disconnect
But, best not to use your real IP address
  Relatively easy to trace back to you
Could hijack someone’s address space
  But you might not receive all the (TCP) return traffic
How to evade detection
  Hijack unused (i.e., unallocated) address block
  Temporarily use the IP addresses to send your spam

## Slide 17: BGP AS Path

## Slide 18: Bogus AS Paths
Remove ASes from the AS path
  E.g., turn “701 3715 88” into “701 88”
Motivations
  Attract sources that normally try to avoid AS 3715
  Help AS 88 look like it is closer to the Internet’s core
Who can tell that this AS path is a lie?
  Maybe AS 88 does connect to AS 701 directly
701
88
3715
?

## Slide 19: Bogus AS Paths
Add ASes to the path
  E.g., turn “701 88” into “701 3715 88”
Motivations
  Trigger loop detection in AS 3715
    Denial-of-service attack on AS 3715
    Or, blocking unwanted traffic coming from AS 3715!
  Make your AS look like is has richer connectivity
Who can tell the AS path is a lie?
  AS 3715 could, if it could see the route
  AS 88 could, but would it really care?
701
88

## Slide 20: Bogus AS Paths
Adds AS hop(s) at the end of the path
  E.g., turns “701 88” into “701 88 3”
Motivations
  Evade detection for a bogus route
  E.g., by adding the legitimate AS to the end
Hard to tell that the AS path is bogus…
  Even if other ASes filter based on prefix ownership
701
88
3
18.0.0.0/8
18.0.0.0/8

## Slide 21: Invalid Paths
AS exports a route it shouldn’t
  AS path is a valid sequence, but violated policy
Example: customer misconfiguration
  Exports routes from one provider to another
Interacts with provider policy
  Provider prefers customer routes
  Directing all traffic through customer
Main defense
  Filtering routes based on prefixes and AS path
BGP
data

## Slide 22: Missing/Inconsistent Routes
Peers require consistent export
  Prefix advertised at all peering points
  Prefix advertised with same AS path length
Reasons for violating the policy
  Trick neighbor into “cold potato”
  Configuration mistake
Main defense
  Analyzing BGP updates or traffic
  for signs of inconsistency
src
dest
Bad AS
data
BGP

## Slide 23: BGP Security Today
Applying “best common practices”
  Securing the session (authentication, encryption)
  Filtering routes by prefix and AS path
  Packet filters to block unexpected control traffic
This is not good enough
  Depends on vigilant application of practices
  Doesn’t address fundamental problems
    Can’t tell who owns the IP address block
    Can’t tell if the AS path is bogus or invalid
    Can’t be sure the data packets follow the chosen route

## Slide 24: Proposed Enhancements to BGP

## Slide 25: Secure BGP
Public Key Signature: Anyone who knows v’s public key can verify that the message was sent by v.
a1
a2
v
a3
m
IP Prefix
  Origin Authentication + cryptographic signatures
Notes: In the last slide, attacker announced a path that doesn’t’ exist
The next security mechansim we consider
V authorizes a1 to send the path (v,Prefix)
Add the security property pr ovided “can’t announce paths that don’t exist (no announced)

## Slide 26: Secure BGP
Public Key Signature: Anyone who knows v’s public key can verify that the message was sent by v.
a1
a2
v
a3
m
IP Prefix
a1: (v, Prefix)
a1: (v, Prefix)
m: (a1, v, Prefix)
  Origin Authentication + cryptographic signatures
Notes: In the last slide, attacker announced a path that doesn’t’ exist
The next security mechansim we consider
V authorizes a1 to send the path (v,Prefix)
Add the security property pr ovided “can’t announce paths that don’t exist (no announced)

## Slide 27: “Secure BGP”
Route attestations
  Distributed as an attribute in BGP update message
  Signed by each AS as route traverses the network
Address attestations
  Claim the right to originate a prefix
  Signed and distributed out-of-band
  Checked through delegation chain from ICANN
S-BGP can validate
  AS path indicates the order ASes were traversed
  No intermediate ASes were added or removed
  Proper ASes originate prefixes

## Slide 28: S-BGP Deployment Challenges
Complete, accurate registries of prefix “owner”
Public Key Infrastructure
  To know the public key for any given AS
Cryptographic operations
  E.g., digital signatures on BGP messages
Need to perform operations quickly
  To avoid delaying response to routing changes
Difficulty of incremental deployment
  Hard to have a “flag day” to deploy S-BGP

## Slide 29: Incrementally Deployable Solutions?
Backwards compatible
  No changes to router hardware or software
  No cooperation from other ASes
Incentives for early adopters
  Security benefits for ASes that deploy the solution
  … and further incentives for others to deploy
What kind of solutions are possible?
  Detecting suspicious routes
  … and then filtering or depreferencing them

## Slide 30: Detecting Suspicious Routes
Monitoring BGP update messages
  Use past history as an implicit registry
E.g., AS that announces each address block
  Prefix 18.0.0.0/8 usually originated by AS 3
E.g., AS-level edges and paths
  Never seen the subpath “7018 88 1785”
Out-of-band detection mechanism
  Generate reports and alerts
  Internet Alert Registry: http://iar.cs.unm.edu/
  Prefix Hijack Alert System: http://phas.netsec.colostate.edu/

## Slide 31: Avoiding Suspicious Routes
Soft response to suspicious routes
  Prefer routes that agree with the past
  Delay adoption of unfamiliar routes when possible
Why is this good enough?
  Some attacks will go away on their own
  Let someone else be the victim instead of you
  Give network operators time to investigate
How well would it work?
  If top ~40 largest ASes applied the technique
  … most other ASes are protected, too

## Slide 32: What About Packet Forwarding?

## Slide 33: Control Plane vs. Data Plane
Control plane
  BGP security concerns validity of routing messages
  I.e., did the BGP message follow the sequence of ASes listed in the AS-path attribute
Data plane
  Routers forward data packets
  Supposedly along path chosen in the control plane
  But what ensures that this is true?

## Slide 34: Data-Plane Attacks, Part 1
Drop packets in the data plane
  While still sending the routing announcements
Easier to evade detection
  Especially if you only drop some packets
  Like, oh, say, BitTorrent or Skype traffic
Even easier if you just slow down some traffic
  How different are normal congestion and an attack?
  Especially if you let traceroute packets through?

## Slide 35: Data-Plane Attacks, Part 2
Send packets in a different direction
  Disagreeing with the routing announcements
Direct packets to a different destination
  E.g., one the adversary controls
What to do at that bogus destination?
  Impersonate the legitimate destination
  Snoop on traffic and forward along to real destination
How to detect?
  Traceroute? Longer than usual delays?
  End-to-end checks, like site certificate or encryption?

## Slide 36: Data-Plane Attacks are Harder
Adversary must control a router along the path
  So that the traffic flows through him
How to get control a router
  Buy access to a compromised router online
  Guess the password, exploit router vulnerabilities
  Insider attack (disgruntled network operator)
Malice vs. greed
  Malice: gain control of someone else’s router
  Greed: say, Verizon DSL blocks Skype to encourage me to use (Verizon) landline phone

## Slide 37: What’s the Internet to Do?

## Slide 38: BGP is So Vulnerable
Several high-profile outages
  http://merit.edu/mail.archives/nanog/1997-04/msg00380.html
  http://www.renesys.com/blog/2005/12/internetwide_nearcatastrophela.shtml
  http://www.renesys.com/blog/2006/01/coned_steals_the_net.shtml
  http://www.renesys.com/blog/2008/02/pakistan_hijacks_youtube_1.shtml
  http://www.theregister.co.uk/2010/04/09/china_bgp_interweb_snafu/
Many smaller examples
  Blackholing a single destination prefix
  Hijacking unallocated addresses to send spam
Why isn’t it an even bigger deal?
  Really, most big outages are configuration errors
  Most bad guys want the Internet to stay up

## Slide 39: BGP is So Hard to Fix
Complex system
  Large, with around 40,000 ASes
  Decentralized control among competitive Ases
Hard to reach agreement on the right solution
  S-BGP with PKI, registries, and crypto?
  Who should be in charge of running PKI & registries?
  Worry about data-plane attacks or just control plane?
Hard to deploy the solution once you pick it
  Hard enough to get ASes to apply route filters
  Now you want them to upgrade to a new protocol

## Slide 40: Conclusions
Internet protocols designed based on trust
  Insiders are good guys, bad guys on the outside
Border Gateway Protocol is very vulnerable
  Glue that holds the Internet together
  Hard for an AS to locally identify bogus routes
  Attacks can have very serious global consequences
Proposed solutions/approaches
  Secure variants of the Border Gateway Protocol
  Anomaly detection, with automated response
  Broader focus on data-plane availability