## Slide 1: Precept 3
  Main topic:
  - Cyclic redundancy check (CRC)
  Breakout rooms:
  Reminder: participation is part of your grade
  What types of errors can be detected?
  Is there a pattern in how errors are detected?

## Slide 2: Cyclic redundancy check (CRC)
Most popular method error detecting code at L2
  Found in Ethernet, Wi-Fi, token ring, many many others
Often implemented in hardware at the link layer
Represent k-bit messages as degree k − 1 polynomials
  Each coefficient in the polynomial is either zero or one, e.g.:
1 0 1 1 1 0
k = 6 bits of message
M(x) = 1x5 + 0x4 + 1x3 + 1x2 + 1x + 0

## Slide 3: Modulo-2 Arithmetic
Addition and subtraction are both exclusive-or without carry or borrow
110
101110
110
111
110
1
011
000
110
1
0
1
Multiplication example:
Division example:
110
1101
0000
11010
110100
101110
110

## Slide 4: CRC at the sender
M(x) is our message of length k
  e.g.: M(x) = x5 + x3 + x2 + x (k = 6)
Sender and receiver agree on a generator polynomial G(x) of degree g − 1 (i.e., g bits)
  e.g.: G(x) = x3 + 1 (g = 4)
Calculate padded message T(x) = M(x)∙xg−1
  i.e., right-pad with g − 1 zeroes
  e.g.: T(x) = M(x)∙x3 = x8 + x6 + x5 + x4
1 0 1 1 1 0
1 0 0 1
1 0 1 1 1 0
0 0 0

## Slide 5: CRC at the sender
Divide padded message T(x) by generator G(x)
  The remainder R(x) is the CRC:
1 0 1 1 1 0
0 0 0
1 0 0 1
1
1 0 0 1
0 1 0 1
0
1
0 0 0 0
1 0 1 0
1 0 0 1
0 1 1 0
0
0 0 0 0
1 1 0 0
1
1
1 0 0 1
1 0 1 0
1 0 0 1
0 1 1
R(x) = x + 1

## Slide 6: CRC at the sender
The sender transmits codeword C(x) = T(x) + R(x)
  i.e., the sender transmits the original message with the CRC bits appended to the end
  Continuing our example, C(x) = x8 + x6 + x5 + x4 + x + 1
1 0 1 1 1 0
0 1 1

## Slide 7: Properties of CRC codewords
Remember: Remainder [ T(x)/G(x) ] = R(x)
What happens when we divide C(x) / G(x)?
C(x) = T(x) + R(x) so remainder is
  Remainder [ T(x)/G(x) ] = R(x), plus
  Remainder [ R(x)/G(x) ] = R(x)
  Recall, addition is exclusive-or operation, so:
    Remainder [ C(x)/G(x) ] = R(x) + R(x) = 0

## Slide 8: Detecting errors at the receiver
Divide received message C′(x) by generator G(x)
  If no errors occur, remainder will be zero
1 0 1 1 1 0
0 1 1
1 0 0 1
1
1 0 0 1
0 1 0 1
0
1
0 0 0 0
1 0 1 0
1 0 0 1
0 1 1 0
0
0 0 0 0
1 1 0 1
1
1
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0  no error detected

## Slide 9: Detecting errors at the receiver
Divide received message C′(x) by generator G(x)
  If errors occur, remainder may be non-zero
1 0 1 1 1 1
0 1 1
1 0 0 1
1
1 0 0 1
0 1 0 1
0
1
0 0 0 0
1 0 1 1
1 0 0 1
0 1 0 0
0
0 0 0 0
1 0 0 1
1
1
1 0 0 1
0 0 0 1  error detected

## Slide 10: Detecting errors at the receiver
Divide received message C′(x) by generator G(x)
  If errors occur, remainder may be non-zero
1 0 1 1 1 1
0 1 0
1 0 0 1
1
1 0 0 1
0 1 0 1
0
1
0 0 0 0
1 0 1 1
1 0 0 1
0 1 0 0
0
0 0 0 0
1 0 0 1
1
1
1 0 0 1
0 0 0 0  undetected error!
How many errors can the CRC detect?
☟
How do we choose generator G(x)?

## Slide 11: Detecting errors with the CRC
The error polynomial E(x) = C(x) + C′(x) is the difference between the transmitted and received codeword
  E(x) tells us which bits the channel flipped
We can write the received message C′(x) in terms of C(x) and E(x): C′(x) = C(x) + E(x), so:
  Remainder [C′(x) / G(x) ] = Remainder [ E(x) / G(x) ]
When does an error go undetected?
  When Remainder [ E(x) / G(x) ] = 0

## Slide 12: Detecting single-bit errors w/CRC
Suppose a single-bit error in bit-position i: E(x) = xi
  Choose G(x) with ≥ 2 non-zero terms: xg−1 and 1
  Remainder [ xi / (xg−1 + ⋯ + 1) ] ≠ 0, e.g.:
Therefore a CRC with this choice of G(x) always detects single-bit errors in the received message
0 0 1 0 0 0
1 0 0 1
1
1 0 0 1
1

## Slide 13: Error detecting code: CRC
Far less overhead than error correcting codes
  Typically 16 to 32 bits on a 1,500 byte (12 Kbit) frame
Error detecting properties are more complicated
  But in practice, “missed” bit errors are exceedingly rare

## Slide 14: Breakout rooms
What types of errors can be detected?
Is there a pattern in how errors are detected?
Extra time: Can you provide an example of an error detection?

## Slide 15: Error detecting properties of the CRC
The CRC will detect:
  All single-bit errors
    Provided G(x) has two non-zero terms

## Slide 16: Error detecting properties of the CRC
The CRC will detect:
  All single-bit errors
    Provided G(x) has two non-zero terms
  All burst errors of length ≤ g − 1
    Provided G(x) begins with xg−1 and ends with 1
    Similar argument to previous property
  All double-bit errors
    With conditions on the frame length and choice of G(x)
  Any odd number of errors
    Provided G(x) contains an even number of non-zero coefficients
Pattern: errors that manifest as remainders are detected