## Slide 1
Network Access Control
COS 316: Principles of Computer System Design
Lecture 16
Wyatt Lloyd

## Slide 2: Controlling Which Packets Get Delivered
Objects: the things being accessed
  Services (possibly) running at the destination host machine
  Identified by fields in the packet headers
  E.g., destination IP address and TCP port number address
Subjects: entity requesting access to an object

## Slide 3: Controlling Which Packets Get Delivered
Objects: the things being accessed
  Services (possibly) running at the destination host machine
  Identified by fields in the packet headers
  E.g., destination IP address and TCP port number address
Subjects: entity requesting access to an object
  Sender of the packet on the source host machine
  Identified by fields in the packet headers
  E.g., source IP address, source TCP port number, …

## Slide 4: The Guard Model
“Is the subject allowed to access the object?”

## Slide 5: Network Administrator Sets the Policy

## Slide 6: Policy Language: Access Control Rule
An access control rule has two parts
  Match: pattern on packet header fields and location
  Action: permit (forward) or deny (drop)
Block external initiation of a TCP connection
    Match: external link, TCP protocol, TCP SYN flag
  Action: deny
Allow traffic from Princeton clients
  Match: internal link, source IP in 128.112.*.*
  Action: permit
SYN

## Slide 7: Policy Language: Access Control Lists
Access control list (ACL)
  List of rules, possibly overlapping
  Ordered list to disambiguate overlaps
Example:
Priority | Match | Action
1 | Src=1.2.3.4, Dest=5.6.7.8 | Deny
2 | Dest=1.2.3.8, Dport=53 | Allow
3 | Dest=1.2.3.* | Deny
4 | Src=1.2.3.7, Dport=100 | Allow
5 | Dport=100 | Deny

## Slide 8: Geometric Interpretation of Access Control List
Overlapping shapes
  Rules are multi-dimensional rectangles
  Higher-priority rules on top of lower-priority
Example with 4-bit addresses
Src
Dest
0 15
0
15
Pri | Match | Action
1 | Src=1***, Dest=1*** | Permit
2 | Src=****, Dest=10** | Deny

## Slide 9: Applying an Access Control List
Classifying a packet
  Packet header: Src=1000, Dest=1011
  Find the highest-priority matching rule
Apply the associated action
Src
Dest
0
0
15
15
Pri | Match | Action
1 | Src=1***, Dest=1*** | Permit
2 | Src=****, Dest=10** | Deny

## Slide 10: Simple Packet Classification Algorithm
Classification problem
  Given a packet (e.g., Src=1000, Dest=1011)
  … and an Access Control List
  Find the highest-priority matching rule
Simple algorithm
  Scan rules in priority order
  Stop after the first match
What is running time?
Pri | Match | Action
1 | Src=1***, Dest=1*** | Permit
2 | Src=****, Dest=10** | Deny
3 | Src=****, Dest=**** | Permit

## Slide 11: Special Case: One-Dimensional Prefix Matching
Pri | Match | Action
1 | Dest=110* | Deny
2 | Dest=0100 | Permit
3 | Dest=1*** | Permit
4 | Dest=**** | Deny
0
1
1
0
1
0
0
Binary Trie
Notes: Tries are ideal for longest prefix matching, which is what IP routing uses. Tries are not a perfect fit for highest-priority rule wins, but provide a nice intuition here.
Students: I want you to know how to look things up in a trie, but I do not expect you to know how to construct one.

## Slide 12: Multi-Dimensional Classification
Src
Dest
01
00
00
10
11
11
01
10
Pri | Match | Action
1 | Src=01, Dest=** | Deny
2 | Src=**, Dest=01 | Deny
3 | Src=11, Dest=11 | Deny
4 | Src=**, Dest=** | Permit

## Slide 13: Multi-Dimensional Classification
Build a compact classifier
  By finding small “cuts”
(**, 0*)
(**,1*)
Src
Dest
00
00
11
11
01
10
01
10
(two-bit Src, two-bit Dest)
(**, 00)
(**, 01)
…
…
Notes: These are even more complex to construct, so I definitely don’t expect you to know how to construct them!

## Slide 14: Multi-Dimensional Classification
Classify a packet
  By traversing the trie
(**, 0*)
(**,1*)
Src
Dest
00
00
11
11
01
10
01
10
(**, 00)
(**, 01)
…
…
Packet with (10, 01)

## Slide 15: Packet Classification: CAM Hardware
Random Access Memory
  Given a memory address
  … return the data word stored at that address
00 01 10 11
Content-Addressable Memory
  Given some key
  … find the data word (if any) associated with the key
b
a
d
c
1010 | b
0110 | a
1110 | d
0001 | c

## Slide 16: Packet Classification: Ternary CAM Hardware
Ternary Content-Addressable Memory (TCAM)
  Ternary: 0, 1, or * (wildcard)
  Matching pattern can have wildcards
  Entries in the TCAM in priority order
110* | b
0100 | a
1*** | d
**** | c
0
1
2
3

## Slide 17: Packet Classification: Ternary CAM Hardware
Ternary Content-Addressable Memory (TCAM)
  Ternary: 0, 1, or * (wildcard)
  Matching pattern can have wildcards
  Entries in the TCAM in priority order
110* | b
0100 | a
1*** | d
**** | c
0
1
2
3
1010
priority
d

## Slide 18: Packet Classification in Practice
Software access control
  End-host network stack and software switches
  Using algorithms for multi-dimensional packet classification
  With optional caching of “popular” classification results
Hardware access control
  High-speed switches and network interface cards
  Using Ternary Content Addressable Memory (TCAM)
  With small TCAMs to reduce chip area and power consumption

## Slide 19: Dynamic Access Control
So far, we have discussed static ACLs
  Configured by a network administrator
  Based on network administrator knowledge of (in)valid traffic
More sophisticated policies are dynamic
  Adapted to the ongoing traffic (e.g., stateful firewall, SYN cookies)
  Adapted to the routing protocol (e.g., reverse path forwarding)

## Slide 20: Internet Clients and Servers
request
response
client server
request
response
Request-response protocols
  Client initiates communication by sending a request message
  Server accepts the request and sends a response message

## Slide 21: Stateful Firewall: Protecting Clients
Most user devices act as a client
  Sending DNS requests to look up domain names
  Sending TCP SYN packets to start TCP connections
  Sending HTTP requests to retrieve Web pages
They should not receive unsolicited traffic
  They should only receive response traffic
  … from requests they sent recently
Stateful firewall
  Remember recent client request traffic
  … and permit (only) the associated response traffic

## Slide 22: Stateful Firewall: Example
By default, firewall denies all traffic destined to IP address 1.2.3.4
Then, the client sends a packet to open a TCP connection to 5.6.7.8
The firewall, on seeing the packet, adds a new “permit” rule
… allowing the return traffic from server 5.6.7.8 to client 1.2.3.4
(Removing the rule when the connection ends or after a timeout)
IP: 1.2.3.4
Port 1024
IP: 5.6.7.8
Port 80

## Slide 23: SYN Cookies: Protecting Servers
Denial-of-service attacks on servers
  Malicious clients overloading the server
  … degrading performance of legit clients
Challenging to prevent
  Servers are supposed to receive traffic!
Adversary’s goal
  Overwhelm the server
  … without investing much effort
  Idea: asymmetric attack!

## Slide 24: SYN Cookies: SYN Flooding Attacks
SYN
SYN-ACK
TCP handshake to start a connection
  Client sends a small SYN packet
  Server allocates resources and sends a SYN-ACK
  Client (supposedly) continues the communication
Transmission Control Block

## Slide 25: SYN Cookies: SYN Flooding Attacks
SYN
SYN-ACK
Asymmetric attack
  Client sends a 40-byte SYN packet
  Server does a lot of work
Crafty adversary
  Send from a spoofed source IP address (hard to trace!)
  Send from compromised hosts (very little overhead for adversary!)
Transmission Control Block

## Slide 26: SYN Cookies: Push the Work to the Client
Server ensures the client has some “skin in the game”
  Server puts a cryptographic “SYN cookie” in the SYN-ACK
  Client must return the cookie in its ACK packets
  Server verifies the cookie before dedicating resources
Deny any ACK packets that fail the cookie check
SYN
Transmission Control Block
SYN-ACK ACK

## Slide 27: Denial-of-Service Attacks are Common

## Slide 28: Wider Range of Detection Techniques
Traffic measurement
  Identify anomalous traffic destined to the server
  Identify command-and-control for botnets
Known suspicious IP addresses or entire networks
Known suspicious other header fields (ports, Time-to-Live)
Tracing attack traffic across the Internet back to the origin
Comparing analysis across different victims
Enforcement all comes down to access control!

## Slide 29: Conclusions
Internet security is challenging
  Attackers can easily send unwanted traffic
  ... that can compromise or overwhelm the destination computer
Access control is a crucial defense
  Blocking unwanted traffic based on packet header fields
  Static access control policy when possible, dynamic when necessary
Enforcing access control lists
  Software algorithms for multi-dimensional packet classification
  Ternary Content Addressable Memory (TCAMs)