## Slide 1: In-Network Traffic Obfuscation
Jennifer Rexford
Princeton University
Notes: Users understandably worry about their privacy when they access the Internet. Yet, many proposed techniques for protecting user privacy are difficult to deploy in practice – due to poor performance, or a reliance on savvy users, or a dependence on cooperation from multiple networks along the path between communicating end-points. In this talk, we explore how programmable network devices can enable a new generation of privacy solutions that can obfuscate the user’s traffic inside the network, at line rate.

## Slide 2: Privacy Threats
Network traffic reveals sensitive information
?
Internet
Notes: Network traffic contains privacy-sensitive information. An adversary watching Internet traffic can learn a great deal about the users: who they are, what sites they communicate with, and even what content they download.

## Slide 3: Privacy Threats
Network traffic reveals sensitive information
Encryption protocols protect the confidentiality of data
But, the packet header fields still reveal a lot
  The identities of communicating end-points
  The size of the exchanged content
Notes: Encryption protocols like TLS provide confidentiality of data, but they do not hide sensitive meta-data such as the identities of endpoints. Specifically, an Internet Protocol (IP) address can still be used to pinpoint and identify a user and device communicating on the Internet. Often, knowing that a user is communicating with a particular other user or web site is enough information to compromise user privacy. On top of the IP addresses, the amount of data transferred between the end-points is revealing, too, enabling traffic-analysis attacks like web fingerprinting.

## Slide 4: Practical Challenges
IPSec tunnels
  Computationally expensive
Tor overlay
  Performance overhead
  Users running special software
Network-layer anonymity systems
  E.g., Hornet, Taranet, PHI, LAP, Dovetail, …
  Cooperation from multiple ASes along the path
Notes: Unfortunately, existing approaches for anonymous communications either introduce high performance overhead (e.g., for IPSec tunnels and Tor), or face significant deployment challenges due to requiring multiple ASes along the path to cooperate and users to deploy special software.

## Slide 5: An Opportunity
Programmable data-plane hardware
  Offload privacy functionality to the network
Benefits
  High speed
  Ease of deployment
  Avoid relying on end users
But, limited memory and processing
Notes: Programmable switch hardware creates an opportunity to build a high-performance privacy service by offloading privacy functionality to the network. This can offer advantages such as high speed, ease of deployment, and avoiding a reliance on end users to run special applications. Nevertheless, programmable switch hardware has limited memory and processing resources, posing challenges for implementing cryptographic algorithms that are commonly used in privacy applications. This begs the question: can we leverage programmable data planes to design a readily-deployable anonymity system that balances the privacy/performance trade-off?

## Slide 6: Other Opportunities
Widespread encryption of payload (e.g., TLS)
  Data plane does not need to encrypt the whole packet
  Simply need to obfuscate the packet-header fields
Growing ubiquity of IPv6 in the Internet core
  Can carry packet metadata related to encryption
Importance of UDP-based transfers
  Request-response protocols like DNS and NTP
  Connection migration in WireGuard VPN and QUIC
Notes: Fortunately, we do not need to rely on the data plane to do everything. We can leverage several other opportunities:
First, because packet payloads are often encrypted (e.g., using TLS), we need only worry about obfuscating certain IP and TCP header fields.
Second, we can take advantage of the increasing ubiquity of IPv6 in the network core; IPv6 addresses have 128 bits, offering enough room to store metadata for specific types of encryption over IPv4 addresses
Third, some important data transfers that need privacy protection are “connectionless”, including request-response protocols like DNS and NTP. Other ”connection-oriented” protocols can be treated like connectionless protocols because they include “connection migration” capabilities. WireGuard is a UDP-based, connectionless VPN protocol that supports IP mobility by allowing an end-point’s address to change frequently across the life of a connection. Also, QUIC, the relatively new transport protocol from Google, has a IP address migration capability that allows a client to change its address during the course of an ongoing connection.
These capabilities, in conjunction with programmable data planes, are tremendous enablers for in-network obfuscation of traffic.

## Slide 7: Trusted Edge Networks
Edge network
  Providing extra privacy for users as a value-added service
  All hosts run unmodified applications
?
Internet
Trusted
edge
client
servers
Notes: So, where should we provide the in-network privacy protections? We envision an edge network, such as an enterprise or access network, that offers privacy protection to its customers as a value-added service while allowing its customers (and other Internet hosts) to run unmodified applications. The goal is to obfuscate the customer’s traffic over the Internet. Of course, this doesn’t help for the case where the customer’s own access network is the adversary, but it can protect a large collection of users from threats deeper inside the Internet.

## Slide 8: Challenges
Obscuring the packet-header fields at line rate
Delivering return traffic without cooperation
Not relying on symmetric routing
Working with unmodified applications and protocols
Avoiding performance penalties
7
Internet
Trusted edge
client
servers
Notes: Protecting user privacy inside the network faces several practical challenges that we will overcome in this talk…

## Slide 9: Two Trusted Edge Networks
Trusted
edge
Internet
TCP + UDP
TCP + UDP
Trusted
edge
?
Trisha Datta, Nick Feamster, Jennifer Rexford, and Liang Wang, "SPINE: Surveillance Protection in the Network Elements." in FOCI 2019.
SPINE: Per-packet traffic encryption in switches in the two trusted edge networks with no need for end-host support, for both connectionless and connection-oriented traffic.
Notes: Two unmodified hosts communicate through two trusted entities—typically two ASes or two ISPs, yet these ASes need not be distinct or even independent. They could, in fact, be two topologically disjoint fragments of the same AS (such as two branches of a large company). The adversary resides in between these two entities and can observe all traffic that traverses the intermediate part (or parts) of the network that it controls. In this setting, we show how a stateless switch (or set of switches) at the borders of the two trusted networks can encrypt, and decrypt, the IP addresses – and other header fields like TCP sequence and acknowledgment numbers -- to protect against an adversary between them.

## Slide 10: Connectionless Traffic
Internet
UDP
DNS, NTP, or WireGuard server
Trusted
edge
?
Liang Wang, Hyojoon Kim, Prateek Mittal, and Jennifer Rexford, "Programmable In-Network Obfuscation of Traffic," in arXiv 2020.
PINOT: In-network encryption of connectionless traffic between a trusted network and public connectionless services (e.g., DNS, NTP, and WireGuard VPN).
UDP
Notes: Often, though, users communicate with public services, like the Domain Name System, or Network Time Protocol, or VPN services. Here we want a ”one sided” solution that works when just one trusted network encrypts and decrypts the client’s IP address and other header fields. In this setting, we focus on connectionless protocols where each UDP packet is handled independently by the two end-points.

## Slide 11: Connection-Oriented QUIC Traffic
Internet
UDP
QUIC server
Trusted
edge
?
UDP
QUIC client
MIMIQ: Flexible client IP address randomization via QUIC’s connection-migration and programmable switches, with unmodified client apps and QUIC server.
Yashodhar Govil, Liang Wang, and Jennifer Rexford, "MIMIQ: Masking IPs with Migration in QUIC,” in FOCI 2020.
Notes: Still, many applications -- such as Web browsing and video streaming -- rely on a client maintaining a connection with a remote server across multiple packets. In this setting, we consider how the trusted network can, with support from an agent on the client machine, support communication with an unmodified QUIC server.

## Slide 12: Family of Solutions
 | Target traffic | Encryption | Scenario | Key Idea
SPINE [FOCI’19] | All | IP/TCP header | Two trusted edge ASes | P4, IPv6 encoding
PINOT [arXiv] | Connectionless | Client IP | One edge AS | P4, IPv6 encoding, line-rate encryption
MIMIQ [FOCI’20] | Connections | Client IP | One edge AS | P4, QUIC migration
Notes: Here’s a summary of the three scenarios we have considered so far.

## Slide 13: SPINE: Shared Keys
Trusted
edge
Internet
TCP + UDP
TCP + UDP
Trusted
edge
SPINE
SPINE
(key, version number)
Notes: First we will look at Spine, where hosts in two trusted networks (such as two branches of a large company) communicate. Traffic leaving the sending network has its headers encrypted, and the traffic entering the receiving network is decrypted. This is possible because the switches in the two trusted networks use shared secret keys to encrypt and decrypt the traffic, as installed by a central controller. In practice, the key changes over time, through key rotation, so each key is associated with a version number. Packets in flight carry the version number so the receiving switch knows which key to use to decrypt the incoming packet. Fortunately, packets stay in flight for a short period of time, so the switches need not remember many keys.

## Slide 14: SPINE: Per-Packet Nonce
Per-packet nonce
  Encrypt(ip, key) = ip XOR Hash(key, nonce)
  The nonce is a randomly-generated bit string
  … carried in the data packet (so it is public)
Each packet carries
  Key version number
  Nonce
So, the receiving switch can decrypt the packet
  Even if packets arrive at different receiving switches
Notes: In Spine, the sending switch encrypts the packet headers based on the shared key and a randomly-generated nonce that is carried in the packet. So, each data packet carries the key version number and the nonce, to enable the receiving switch to decrypt the packet headers. Since Spine has a different nonce (essentially a different one-time pad) for each packet, the adversary cannot easily take advantage of known plaintext attacks.
All SPINE routers in the two trusted entities (e.g., R1 and R2 in Figure 1) use the same k for encryption so that packets can exit the sending entity at one of several exit points and enter the receiving entity at one of several entry points (in contrast to IPSEC tunnels which establish point-to-point channels). Also, note that the switches do not need to maintain state at the packet or flow level, unlike (say) a network address translation (NAT) box.

## Slide 15: SPINE: IPv6
Challenges
  Sending encryption metadata
  Discerning which traffic is SPINE traffic
  Ensuring successful routing
Solution: IPv6 addresses
  Carry information for receiving switch to decrypt the IPv4 header
  Use a separate address block for routing the traffic
Encrypted IPv4 Address
Reserved IPv6 Prefix
New IPv6 Address
Version #
Nonce

## Slide 16: SPINE: P4 Data Plane
Trusted
Edge #1
R1
R2
Trusted
Edge #2
Check IPv6 Dst Addr  Decrypt if necessary
Set forwarding port
Check IPv4 Dst Addr  Encrypt if necessary
Parse headers
Deparse headers
SPINE Tables
Central Controller
SPINE Program
Routing Tables
SPINE
SPINE

## Slide 17: SPINE: Summary
Simple data-plane encryption
  Only the header fields (e.g., IP addresses, TCP seq/ack)
  Stateless (nonce and key version carried in packets)
Limitations
  Cooperation from sending and receiving networks
  P4 prototype running only on a software switch
  Encryption scheme (SipHash) difficult for line-rate hardware

## Slide 18: PINOT: One Trusted Edge Network
Client in a trusted network
  Using connectionless public services (e.g., DNS, NTP, WireGuard)
Intermediate
ASes
UDP
DNS, NTP, or WireGuard server
Trusted AS
?
UDP
Notes: To support clients talking to unmodified servers, we focus first on connectionless services like DNS, NTP, and the WireGuard VPN service. These services are an important special case. First,
DNS recursive resolvers are typically operated by the users’ Internet service provider or third-party services (e.g., Google and Cloudflare). Since DNS requests and responses are in cleartext, DNS recursive resolvers or any on-path eavesdroppers can learn the IP address of a user and the domain the user visited. Such information can be further used for inferring users’ browsing behaviors, fingerprinting and tracking users, or deanonymizing Tor users.
NTP is widely used for synchronizing the clocks of computer systems. A scanner may exploit NTP to discover active IPv6 and IPv4 hosts and conduct unauthorized vulnerability scans. The vulnerability information of hosts is publicly available and can easily be gathered by attackers during reconnaissance, posing security threats to the scanned hosts.
There are privacy concerns with third-party VPN providers. A recent report shows that 25 out of 123 VPN services collect client IP addresses [31]. The IP information could be sold to advertising companies to facilitate delivering of personalized ad content (i.e., IP targeting ads) [17]. Besides, VPN services may unintentionally leak clients’ IP information [34]. We focus on WireGuard, a UDPbased, connectionless VPN protocol being added to the Linux kernel [15]. WireGuard leverages a special mechanism to achieve good IP mobility: it assumes a peer’s public IP address can change frequently, and maintains a peer address table to record the source IP address in the latest packet received from the peer for future commutations. This mechanism enables us to obfuscate peer (user) IP addresses in WireGuard traffic without disrupting connectivity.

## Slide 19: PINOT: Improvements Over SPINE
Better line-rate crypto
  SipHash solution (Spine) and AES are too expensive
  Two-round Even-Mansour (2EM) is a good compromise (see paper)
Mapping server address to IPv6
  Client sends an IPv4 packet
  Client IP encrypted into IPv6 address
  Server IP mapped into IPv6 address for known services
Hardware switch prototype (on Barefoot Tofino)
  Deployed in the Princeton campus network!

## Slide 20: PINOT: Princeton Deployment
Notes: In our testbed at Princeton, we have a /64 IPv6 address block assigned to our Barefoot Tofino switch. The end host runs client applications including DNS, NTP, and WireGuard. The Barefoot switch automatically translates a target server address into an IPv6 equivalent using preinstalled rules. We used dig to send DNS queries for A record for domains selected from the top 1 million domains to each of the 374 public DNS resolvers we found that had both IPv4 and IPv6 addresses. All returned A records are consistent with the results when we did not use PINOT. We also experimented with WireGuard. Here, too, we are successful in maintaining a VPN connection despite changing the client IP address on each packet. We see some degradation in throughput (from 8.3 Gbps to 6.7 Gbps), due to the overhead of the remote WireGuard server needing to update its local address table on each change – not due to PINOT itself.

## Slide 21: PINOT: Summary
Privacy for connectionless services
  DNS, NTP, and WireGuard VPN services
  Line-rate IP address encryption in the Barefoot Tofino
  Deployment on the Princeton campus network
Limitations
  Need to determine the remote server’s IPv6 address
  Encryption consumes non-trivial switch resources
  Only for connectionless public services

## Slide 22: MIMIQ: Connection-Oriented
Connection-oriented services
  Multiple packets in the same connection
  Using the increasingly popular QUIC protocol
Internet
QUIC
QUIC server
Trusted edge
?
QUIC
QUIC client
Notes: Next, we explore how to handle connection-oriented services, still without requiring support from the remote end-point or its edge network. This is challenging because we need a collection of packets between the same client-server pair to be delivered successfully, in both directions, while still preventing an adversary on the path from recognizing that the packets belong together. We do this by capitalizing on features in the increasingly popular QUIC protocol, while leveraging programmable switches in the trusted network to ensure return traffic from the server reaches the right client.

## Slide 23: MIMIQ: Connection Migration
QUIC connection migration
  QUIC clients can change their IP addresses
  … within the lifetime of a single connection
Designed for client mobility, but useful for privacy!
1.1.1.1
2.2.2.2
Internet

## Slide 24: MIMIQ: Client Unlinkability
QUIC encryption
  Packet payload
  Other header fields (e.g., sequence/ACK numbers)
  Information used in migration (e.g., new connection ID)
QUIC congestion control
  QUIC restarts congestion control upon migration
  Migrated connection looks like a new connection
  … but, at some (modest) performance penalty
Notes: For example, suppose the client-server pair have a 50 msec round-trip time and we migrate every 25 packets, we see about a 10% performance penalty. Yet, this seems to be frequent enough to break traffic-analysis attacks.

## Slide 25: MIMIQ: Evade Fingerprinting
Client
srcIP = 1.1.1.1
Server
Long flows provide sufficient information:
Client is visiting a specific site and page
Client
?
srcIP = 1.1.1.1
srcIP = 1.1.1.2
srcIP = 1.1.1.3
Short flows contain less information:
Can’t reliably make decisions
Server

## Slide 26: MIMIQ: Dynamic IP Addresses
Avoid address collisions
  Avoid assigning an IP address to multiple clients at the same time
  … and wait to reuse an IP address to deliver in-flight packets
Address allocation server
Trusted edge
Address allocation server
  Assign random unique IPs to clients
  No need for cryptographic operations
  Similar to a DHCP server!

## Slide 27: MIMIQ: Deliver Return Traffic
Deliver return traffic to clients
  Client IP addresses keep changing
  … so switches need to update their forwarding rules
Internet
QUIC server
QUIC
“IP learning”
1.2.3.4
1.2.0.0/16
Runs using Mininet and the Chromium QUIC implementation with unmodified server!

## Slide 28: MIMIQ: Deliver Return Traffic
Larger trusted network
  Embed edge switch IDs in the client IP addresses
  Enables small forwarding table in border switch
  Change ID assignments and sets of bits over time
Internet
QUIC server
QUIC
1.2.0.0/16
1.2.3.4
S3
1.2.3.5
1.2.7.1
S7
1.2.3.*
1.2.7.*
border switch

## Slide 29: In-Network Traffic Obfuscation
 | Target traffic | Encryption | Scenario | Key Idea
SPINE [FOCI’19] | All | IP/TCP header | Two trusted edge ASes | P4, IPv6 encoding
PINOT [arXiv] | Connectionless | Client IP | One edge AS | P4, IPv6 encoding, line-rate encryption
MIMIQ [FOCI’20] | Connections | Client IP | One edge AS | P4, QUIC migration
Notes: Stepping back, we have a family of different solutions that vary in what kind of traffic they can handle, whether the remote edge network needs to cooperate, how we change the IP addresses, and what role the programmable switch plays in the solution. More generally, we think in-network obfuscation of traffic is an exciting research direction.

## Slide 30: Conclusion
In-network traffic obfuscation
  Practical user privacy
  With good performance and ease of deployability
  Leveraging programmable switches (and other trends)
More generally
  Internet security and privacy are hugely important
  Programmable switches offer a deployment path
  This is just the beginning!

## Slide 31: Thanks to My Collaborators
Liang Wang
Hyojoon Kim
Prateek Mittal
Nick Feamster
Trisha Datta
Yashodovar Govil
Notes: Will add pictures when I have reliable Internet connectivity again!