## Slide 1: Closing the Loop: Network Control in the Data Plane
Jennifer Rexford
Princeton University

## Slide 2: Traditional Network Management
1. Measure
(load, performance, traffic, failures)
2. Analyze
(traffic matrix, route optimization, anomaly detection, fault localization)
3. Configure
(reconfigure tunnels, link weights, access control lists)

## Slide 3: Limitations of Traditional Network Management
Measurement mismatches
  Overhead of collecting many device-local measurements
  Simplistic statistics (counts, samples) not tailored to the task
Indirect control
  Configuration of complex protocols and mechanisms
  Separate configuration of many distributed devices
Complex reasoning
  Many separate software components and protocols
  Software bugs, configuration errors, and protocol interactions

## Slide 4: Closing the Loop
An integrated approach
Efficient measurement
  Measurement tailored to the task
  Data analysis in the data plane
Direct control
  Control actions in the data plane
Correct by construction
  Device-local programs synthesized from network-wide goals
Network-wide goals
(objectives and constraints)
Compiler
Device-local programs
(measure and control)

## Slide 5: Protocol Independent Switch Architecture (PISA)
Data plane designed for programmability
  Parsing, match-action tables, actions, registers
  Barefoot/Intel (Arista, NoviFlow, Stordis), Xilinx, Netronome, Pensando, Netcope
  P4 programming language
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table

## Slide 6: Example Network-Wide Goals
Alleviating microbursts
Performance-aware routing
Denial-of-service attack mitigation
Block hosts with old OSes
<Insert your “app” here>

## Slide 7: Alleviating Microbursts: ConQuest [CoNext’19]
Small timescale traffic bursts
  Clog the packet queues
  Cause packet delay and loss
Manage microbursts to handle
  Bursty workloads
  Low-cost switches (shallow buffers)
  High link utilization
Goal: penalize the most responsible flows
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Microbursts

## Slide 8: Microburst Management Policy
Active queue management
  Mark each packet probabilistically
  In proportion to its flow’s contribution to the heavy queue
55%
10%

## Slide 9: Detecting Heavy Flows in the Queue
For each flow, how many packets are in the queue?
P4 data structure challenges
  Updating on packet arrival and departure
  Per-flow state (key and count)
Key | Count
 | 1
 | 5
 | 1
 | 1
 | 2
 | 1

## Slide 10: ConQuest: Processing Each Packet Only Once
S1 | S2 | S3 | S4 | …
Memory access
Flow | ~Count
 | 1
 | 5
 | 1
 | 1
Slice traffic into time windows
Each snapshot records T=4 packets
Queue
Egress
B
B
Historical Departures
D
B
A
C
C
D
B
B
B
A
B
B
I enqueued at t=5
I dequeued at t=14
Why am I waiting?
?
A
B
C
D

## Slide 11: ConQuest: Round-Robin Snapshots
Clean and Reuse the snapshots in the data plane!
Read
Read
Write
Clean
Read
Read
Read

## Slide 12: ConQuest: Avoiding Per-Flow State
Compact data structures
  With limited memory and processing
  … at the expense of lower accuracy
Estimate per-flow counts per snapshot
  With accurate estimates for large flows
Count-Min Sketch per snapshot
  C columns indexed by hash functions
  Increment hashi(flowid) in column I
  Estimate is the min of the C counts
Count-Min Sketch [CM ‘05]
C columns
B Buckets
f
+1
+1
+1

## Slide 13: ConQuest in Action on the Princeton Campus
Performance symptoms
  Big neuroscience data transfers
  High loss with low average load
  Router with limited measurements
Microburst analytics on Tofino
  Microbursts on a small timescale
  Caused by PerfSONAR active probes
Recent deployment with AT&T
Internet2
Mirrored traffic
Tofino
Network TAPs
Neuroscience
Institute
See https://p4campus.cs.princeton.edu/ web site for more details!

## Slide 14: ConQuest: Closing the Control Loop
Testbed with P4-enabled Barefoot Tofino, 4 snapshots
Smart early congestion notification (ECN)
  Baseline: mark all packets when the queue is long
  ConQuest: flow-based ECN to mark flows causing others to wait
100G
10G
Sender
Receiver
Send 1M TCP flows
+ synthetic bursts

## Slide 15: ConQuest: Evaluating the Control Loop
Flow-based ECN reduces Flow Completion Time
Queue remains short, bursty flow effectively suppressed
11%

## Slide 16: Toward Verified Closed-Loop Control
Explore more control-loop examples
  DDoS mitigation, blocking unwanted OSes, etc.
Evaluate under realistic conditions
  Hardware switches and operational networks
Identify unifying language constructs
  Traffic queries integrated with control actions
Verify the compiler
  Ensure the P4 programs are “correct by construction”
Pronto project (ONF, Stanford, Princeton, Cornell): https://vimeo.com/447287550

## Slide 17: Thank you!