## Slide 1: Networks Capable of Change
Jennifer Rexford Princeton University

## Slide 2: The Great Success of the Internet
IP network
Best-effort packet delivery
Arbitrary applications
Programmability: determines who can effect change, and where
Notes: One lesson is the end-to-end principle (whenever possible

## Slide 3: Innovation Above, Below, and Alongside
Applications
Media
Internet
Hosts
Notes: But, ironically, the Internet did not plant the seeds of its own reinvention

## Slide 4: But, Limited Innovation “Inside” the ’Net
Over specified
  Slow protocol standardization
  Standards in fixed-function hardware
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Few people can innovate
  Equipment vendors write the code
  Long delays for new features
But, the inside of the network does need to change
Notes: Needs to change because of performance, reliability, security, and more. And unique needs in different settings.

## Slide 5: We Are Desperate to Innovate Inside
Platforms
Research
  Active networks, overlay networks, SDN, NFV
  Testbeds such as PlanetLab, Orbit, Emulab, GENI
Control plane
Interface
Data plane
NOX, FlowVisor, Beacon, POX, ONOS, Ryu, Frenetic
Quagga, XORP, Bird
ForCES, OpenFlow, P4
Click, Open vSwitch, NetFPGA

## Slide 6: What Works? When? What Doesn’t Work? Why?
And what have we learned along the way?
I
Notes: In our insatiable drive to make networks more programmable… what works and what doesn’t, and why?
Keepin’ it real: technology push, application pull, incremental deployment, building community, etc. While

## Slide 7: Keeping it Real
Staying in touch with reality
  Real data, software, and users
  Technology push and market pull
  Changing what you can
Shaping the future reality
  Creating new artifacts
  Building community
  Enabling new kinds of change
Ambition
Pragmatism
Notes: Long-term goal, short-term steps, and a healthy dose of patience
Ironically, change to the Internet doesn’t happen at “Internet speed”
Yet, “changing what you can” can lead to a local minima.
Artifacts: data, use cases, open-source software
Community: consortia, standards, white papers, conferences – help make more substantive change inevitable

## Slide 8: A 25-Year Retrospective
Graduate school [’91-’96]
  Programmable multi-computer networks
AT&T [’96-’05]
  Active networks (as an observer)
  Programmable management plane
  Routing Control Platform  4D architecture
Princeton [’05-present]
  OpenFlow (initially as an observer)
  Programmable control plane
  Programmable data plane
Notes: In a talk like this, I am obliged to show my age and dwell on the past.
The goal of discussing this journey is to share the twists and turns, the failures and lapses in judgment, the successes, the accidents of timing, and the lessons learned
And a lesson, particularly for students, about how research careers are a circuitous journey.
We all join conversations already in progress, and these conversations have many participants.
All of these projects involved a lot of people. In a few cases, I’ll point to individual people who drove key turns in the story, but will summarize the rest at the end

## Slide 9: Multicomputer Routers [’91-’96]
Multicomputers
  Many small processors
  Regular network topologies
Diverse workloads
  Best-effort and real-time
  FFTs, matrix computations, etc.
Programmable router hardware
  Routing and flow control
  Customized virtual networks
Notes: So, in my PhD I worked on a programmable router chip, a simulator to evaluate different routing and flow control strategies, and so on.

## Slide 10: You Can’t Win Them All
Got the trends wrong
  Moore’s law wasn’t over (yet)
  Applications were the hard part
Challenges in evaluating research
  Few real applications
  Custom chips lagged behind
Should I have been more patient?
  Moore’s law is coming to an end
  Data centers are like multicomputers
Notes: In short, like many graduate students, by the end of grad school I desperately wanted to escape my dissertation!
But, I realized it before I finished, and started to pivot my research area.
But I could have switched to tea, and been patient! 

## Slide 11: Hey, Computer Networks! [’94-’96]
Real applications
  World-wide web
Real data
  Internet measurement studies
Real (power) users
  System and network administrators
Real software
  E.g., the x-kernel
Real hardware
  ATM switches (hmmm, like multicomputer routers!)

## Slide 12: An ATM Interlude at AT&T [’96-’99]
ATM Switches
(scheduling, shaping)
ATM Networks
(routing, signaling)
IP Over ATM
(flow switching)
IP Not Over ATM
(the Internet)
Collecting traffic and configuration data  Managing a network is hard! Hmmm…
Similar ideas in OpenFlow!
Notes: Joke about “A lot of rejected SIGCOMM submissions” in section on ATM networks
Before “IP Not Over ATM”, segue with “And then I moved into a research area – where I still am today – that I like to call ‘IP Not Over ATM’”.

## Slide 13: Meanwhile… Active Networks [’96-’01]
Application pull
  Custom functionality inside the network
  Enabling research experimentation
Two models
  Capsules: carrying code in packets
  Programmable router: installing code in routers
Key contributions
  Programmability to enable innovation
  Demultiplexing packets to software programs
  Unified architecture for middleboxes
Who is the programmer?
What about performance?
Notes: The technology wasn’t quite ready to offer programmability at reasonable performance
And we weren’t quite ready for end users or even network services
Going back to (re)read these papers is edifying. Everything is coming full circle now, with NFV and programmable data planes. Just be patient!

## Slide 14: ISP Network Management [’96-’04]
A quest for reality
  Real users (network operators)
  Real data (topologies, workloads)
Network management
  Traffic engineering
  Planned maintenance
  Attack mitigation
Programmability above the network
  Network-management software
  Taking existing routers as a given
measure
optimize
control
Notes: I found my passion. Real users, real data, real problems. Yay.
Network administrators holding the Internet together with duct tape and coffee. The unsung heroes.
Measurement, not just to understand (Internet topology, traffic, and performance), but also to drive decisions. About how the network should adapt.

## Slide 15: TE With Existing Routing Protocols
Given traffic matrix and topology
Compute per-link integer weight
To minimize network-wide congestion
3
2
2
1
1
3
1
4
5
3
3

## Slide 16: Real Deployment, Real Challenges
Measure (collect or infer traffic matrix)
Optimize
(tune link weights, model protocols)
Control
(avoid disruptions during update)
Notes: Measure: direct measurement from all ingress points, or inference from link-load statistics
Optimize: link weights with even splitting, computationally hard, plus modeling peculiarities of the routing protocol
Control: changing weights would cause transient performance disruption
Working the night shift…

## Slide 17: Bloated Control and Management
FIB
FIB
FIB
Packet filters
Data
plane
OSPF
BGP
Link metrics
OSPF
BGP
OSPF
BGP
Routing policies
Control
plane
Shell scripts
Traffic Eng
Databases
Planning tools
OSPF
SNMP
Netflow
Configs
Management
plane
Notes: We want happy packets, but that depends on the data-plane configuration coming from above.
The control plane is a bunch of distributed protocols with knobs we can turn and (limited) dials we can read.
We can only do the management plane, where we must “invert” the control plane to model what it will do, and set knobs based on the peculiarities of the protocols and the limitations of the dials. This is super annoying.

## Slide 18: Tired of Working Backwards
Network Control Point (NCP)
  Bell Systems Technical Journal (Sep 1982)
  Separating network control from network action
  Centralization for flexibility, scaling, and more
What would that look like in an ISP?
  Network-wide route control
How to work with legacy routers?
  Trick them using standard control-plane protocols
Notes: Configuration interfaces are slow and non-standard. Idea: use the standard protocols to talk to the routers.

## Slide 19: Separate Routing From Routers [FDNA’04]
Network-wide computation
  Input: BGP-learned routes
  Output: router forwarding tables
Incremental deployment
  No changes to routers
  No cooperation from neighbors
High-end server is enough [NSDI’05]
  Servers are better than routers
  Amortize overhead across routers
  Replication for fault tolerance
ISP
iBGP
RCP

## Slide 20: In Search of Use Cases
Security
  Blocking of DoS attacks
Virtual Private Networks
  Customer-controlled routing
Interactive applications
  Hitless maintenance
Notes: Three applications, all needing to control which traffic goes to what egress point in AT&T’s backbone
Anecdote about Sony Everquest, and tens of thousands of players dying at once

## Slide 21: Interactive Applications (VoIP, Gaming)
Planned maintenance on an edge router
  Drain traffic off of an edge router
  Before bringing it down for maintenance
d
egress 1
egress 2
RCP
use egress 2

## Slide 22: 4D Architecture [’04-’05]
Thinking bigger (Hui Zhang sabbatical, 100x100 project)
  An RCP-like approach makes sense
  … even if you can change the routers!
  Applications beyond ISP route control
Notes: Decision: all management and control
Dissemination: communication to/from the routers
Discovery: topology and traffic monitoring
Data: packet handling
100x100 project with Hui Zhang, Nick McKeown, and others. Hui Zhang, Dave Maltz, and others built an enterprise network 4D architecture

## Slide 23: Moving to Princeton [’05-present]
Popping up a level
  Networks that inherently easier to manage
  Revisiting old questions
Wanting ways to “make it real”
  Learning about PlanetLab (Larry Peterson)
  Programmability and virtualization
  Pragmatic take on active networks
  Still, a gap for network protocols research
Internet
Notes: Other people in academia were grappling with how to “make it real”, too
Slices and slivers PlanetLab transformed distributed systems work (fraction of papers with real code rather than just simulation)
What about networking?

## Slide 24: OpenFlow (initially as an observer) [’07-’08]
Ethane project at Stanford [SIGCOMM’07]
  Enterprise access control with central controller
  … installing rules in the data plane
Generalized data plane [CCR’08]
  Merchant silicon chipsets
  Easy to explain to outsiders
Programmable control plane
  Deploy in campus networks
  Run experiments and normal services
Match | Action
1**001 | forward(1)
**1111 | forward(2)
****** | drop

## Slide 25: Hey, Programming Languages!
Match-making by Jonathan Smith
  Network that adapts to new threats
  Programming languages + networking
Programming abstractions for OpenFlow
  Building on the early software of others
  OpenFlow, Mininet, Nox, example apps, etc.
  Learning by doing, and reflecting on the pain
Notes: For me, programming languages was the piece that was always missing…

## Slide 26: OpenFlow is Not a Linguistic Formalism
Images by Billy Perkins
The Good
  Network-wide visibility
  Direct control over the switches
  Simple data-plane abstraction
The Bad
  Low-level programming interface
  Functionality tied to hardware
  Explicit resource control
The Ugly
  Non-modular, non-compositional
  Challenging distributed programming
[Slide from Nate Foster]

## Slide 27: Frenetic: Programmable Control Plane
Measure
(query abstractions)
Compose
(parallel, sequential)
Control
(consistent updates)
Load balancing
Routing
Monitoring
Network-Wide Programs
+
(
)
>>
Notes: Apps drive abstractions, and abstractions support apps

## Slide 28: Consistent Updates: Abstraction
Simple abstraction
  Update entire configuration at once
Cheap verification
  If P1 and P2 satisfy an invariant
  Then the invariant always holds
Run-time system does the rest
  A schedule of low-level updates
  Using only OpenFlow commands!
Policy P1
Policy P2

## Slide 29: Consistent Updates: Two Phases
Version numbers
  Stamp packet with version number (VLAN tag)
Unobservable updates
  Add rules for P2 in the interior
One-touch updates
  Add rules to stamp packets with version # P2 at the edge
Remove old rules
  Wait for some time, then remove all version # P1 rules

## Slide 30: OpenFlow Use Cases
Wide range of uses cases
  Server load balancing
  Heavy-hitter detection
  Denial-of-service attack mitigation
  Middlebox traffic steering
  Seamless end-host mobility
Cloud provider killer use cases
  Traffic engineering in private backbones (Google)
  Network virtualization in multi-tenant data centers (Nicira)
Programming
Abstractions
Use Cases
Notes: This time, different kinds of networks… Still a similar set of “application pull” scenarios. By now you should know I only have a few ideas for apps… ;)

## Slide 31: OpenFlow Limitations
OpenFlow 1.0
  One rule table
  Limited headers and actions
  Sending packets to the controller
Later version of OpenFlow
  More tables, headers, actions
  But, still never enough
  Where does it stop?!?
Version | Date | # Headers
OF 1.0 | Dec ‘09 | 12
OF 1.1 | Feb ‘11 | 15
OF 1.2 | Dec ‘11 | 36
OF 1.3 | Jun ‘12 | 40
OF 1.4 | Oct ‘13 | 41
Notes: But, OpenFlow was not a panacea. It was an API of compromise.
Pragmatic in limited programmability, and pragmatic now because of changes in hardware trends

## Slide 32: Programmable Data Planes (as observer)
Data plane designed for programmability
  RMT paper at SIGCOMM’13 (from Stanford and TI)
  A performance-first variant of active networking
Stages
Deparser
Parser
Memory
Persistent State
ALU
Match-
Action
Table
Notes: Pragmatic in limited programmability, and pragmatic now because of changes in hardware trends

## Slide 33: P4 Language [’14-’18]
Protocol independence
  Configure a packet parser
  Define typed match+action tables
Target independence
  Program without knowledge of switch details
  Rely on compiler to configure the target switch
Reconfigurability
  Change parsing and processing in the field
Networking
Languages
Hardware
[CCR’14, p4.org]
Notes: A group of us came together to think about the language for programming such devices. Not just an API for installing rules, but a language.
Setting up the P4 Consortium with Nick McKeown, and later Amin Vahdat (Google) joined us

## Slide 34: P4 Programs: Network Telemetry
Streaming analytics in the data plane
  Heavy-hitters [HashPipe, SOSR’17]
  TCP performance [Dapper, SOSR’17]
  Microbursts [ConQuest, CoNext’19]
  Attack detection [BeauCoup, SIGCOM’20]
  Hardware-efficient data structures
General telemetry platform
  Query-driven telemetry [Sonata, SIGCOMM’18]
  Optimize use of switch resources
  Compilation to switch-level programs
measure
analyze
control
Notes: Finally can answer questions directly that previously were impossible, or relied on inference.
Still, doing it efficiently is challenging. A range of papers (from us and others) on compact data structures.
A coming together of measurement and analysis. I had always thought of them as separate. But that’s because I was never allowed to change how data collection is done.
Now we don’t have to settle for whatever data the switch vendor deigns to give us. We can decide what to collect, based on the analysis questions we want to answer.

## Slide 35: P4 Programs: Performance-Aware Routing
Performance-aware routing in the data plane [HULA, SOSR’16]
  Link performance statistics
  Distance-vector protocol
  Grouping packets into flowlets
S5
S6
S7
Best Next-Hop | Path Utilization
S6 | 50%
S7 | 10%
… | …
S0
S1
Dest
Switch
Data
Data
Probe
Probe
S0
Probe
Data
Dest Switch | Timestamp | Next-Hop
S10 | 1 | S6
S0 | 17 | S7
… | … | …
0
1
…
h(flowid)
Notes: And there’s more… multiple clases of traffic, policies that avoid undesirable paths, preventing forwarding loops, fast failure recovery, and more

## Slide 36: Ongoing Work: Closing the Loop
Three-stage control loop
Integrating the stages
measure
analyze/
optimize
control
Network-wide goals
(objectives, constraints)
Separate abstractions for each stage
Compiler
Device-local programs
(measure, control)
Notes: HULA is an example, but just the beginning….

## Slide 37: Pushing, Pushing, Pushing
FIB
FIB
FIB
Packet filters
Data
plane
OSPF
BGP
Link metrics
OSPF
BGP
OSPF
BGP
Routing policies
Control
plane
Shell scripts
Traffic Eng
Databases
Planning tools
OSPF
SNMP
Netflow
Configs
Management
plane
Programmable Management Plane
Programmable Control Plane
Programmable Data Plane
Notes: Summarize the evolution: management plane, control plane, data plane… all eventually yielding

## Slide 38: Lessons Learned: Keeping it Real
Identify compelling use cases
  Someone who is struggling
  E.g., network admins, application designers
Interdisciplinary collaboration
  Multi-faceted problems and technical constraints
  Distributed systems, programming languages, computer architecture, compact data structures, software engineering
Knowing some history
  Many ideas come around multiple times
  Different kinds of networks, and different constraints

## Slide 39: Lessons Learned: Keeping it Real
Don’t fight what you can’t change
  Control-plane protocols (RCP)
  Packet-processing hardware (OpenFlow)
  Line-rate packet processing (P4)
Fight to enable new kinds of change
  Build, deploy, and share prototype systems
  Articulate a vision (4D, OpenFlow, and P4 papers)
  Foster community (HotSDN/SOSR, P4 Consortium, tutorials)
Notes: Community is all about people…

## Slide 40: Thank You!
Many collaborators and colleagues
  Grad school (esp advisor Kang Shin)
  AT&T (esp Albert Greenberg)
  Princeton and beyond (esp David Walker and Nate Foster)
  (See the following bibliography slides)
Research group at Princeton
  Past and present students and postdocs

## Slide 41: Bibliography: Multicomputer Routers
Collaborators: Stuart Daniel, Jim Dolter, Wu-chang Feng, Ashish Mehra, Kang Shin
“A programmable routing controller for flexible communication in point-to-point networks” (ICCD’95)
“SPIDER: Flexible and efficient communication support for point-to-point distributed systems” (ICDCS’94)
“Hardware support for controlled interaction of guaranteed and best-effort communication” (PDRTS’94)

## Slide 42: Bibliography: Network Management Software
Collaborators: Jay Borkenhagen, Nick Feamster, Anja Feldmann, Bernard Fortz, Albert Greenberg, Tim Griffin, Carsten Lund, Nick Reingold, Renata Teixeira, Mikkel Thorup, Fred True
“NetScope: Traffic engineering for IP networks” (IEEE Network, 2000)
“Deriving traffic demands for operational IP networks: Methodology and experience (SIGCOMM’00, ToN June 2001)
“Traffic engineering with traditional routing protocols” (IEEE Communication, 2002)
“Route optimization in IP networks” (Handbook of Optimization in Telecommunications, 2006)
“Network-wide prediction of BGP routes” (SIGMETRCS’04, ToN 2007)

## Slide 43: Bibliography: Routing Control Platform
Collaborators: Matthew Caesar, Donald Caldwell, Nick Feamster, Aman Shaikh, Jacobus van der Merwe
“The case for separating routing from routers” (FDNA’04)
“Design and implementation of a Routing Control Platform” (NSDI’05)
“Dynamic connectivity management with an intelligent route service control point” (INM’06, by van der Merve and others)

## Slide 44: Bibliography: 4D Architecture
Collaborators: Albert Greenberg, Gisli Hjalmtysson, David Maltz, Andy Myers, Geoffrey Xie, Jibin Zhan, Hui Zhang
“Network-wide decision making: Toward a wafer-thin control plane” (HotNets’04)
“A clean-slate 4D approach to network control and management” (CCR, October 2005)

## Slide 45: Bibliography: OpenFlow and SDN
“OpenFlow: Enabling innovation in campus networks” (CCR, April 2008, by McKeown, Anderson, Balakrishnan, Parulkar, Peterson, Rexford, Shenker, and Turner)
“The road to SDN: An intellectual history of programmable networks” (ACM Queue, December 2013 by Feamster, Rexford, and Zegura)

## Slide 46: Bibliography: Frenetic
Collaborators: Nate Foster, Michael Freedman, Arjun Guha, Rob Harrison, Naga Katta, Christopher Monsanto, Josh Reich, Mark Reitblatt, Cole Schlesinger, Alec Story, David Walker
“Frenetic: A network programming language” (ICFP’11)
“Abstractions for network update” (SIGCOMM’12)
“Languages for software-defined networks” (IEEE Communications, February 2013)
“Composing software-defined networks” (NSDI’13)

## Slide 47: Bibliography: P4 Language and Apps
“P4: Programming protocol-independent packet processors” (CCR, July 2014, by Bosshart, Daly, Gibb, Izzard, McKeown, Rexford, Schlessinger, Talayco, Vahdat, Varghese, Walker)
P4 Consortium, http://www.p4.org
“HULA: Scalable load balancing using programmable data planes” (SOSR’16, Katta, Hira, Kim, Sivaraman, Rexford)
“Sonata: Query-driven streaming network telemetry” (SIGCOMM’18, Gupta, Harrison, Canini, Feamster, Rexford, Willinger)
“Catching the microburst culprits with Snappy” (SelfDN’18, Chen, Landau-Feibish, Koral, Rexford, Rottenstreich)
“Dapper: Data plane performance diagnosis of TCP” (SOSR’17, Ghasemi, Benson, Rexford”
“Heavy-hitter detection entirely in the data plane” (SOSR’17, Sivaraman, Narayana, Rottenstreich, Muthukrishnan, Rexford)

## Slide 48: Bibliography: Compositional Network Architecture
Collaborator: Pamela Zave
“The compositional nature of the Internet” (CACM, to appear)
“The design space of network mobility” (SIGCOMM eBook on Recent Advances in Networking, August 2013)
”Compositional network mobility” (Working Conference on Verified Software, May 2013)
”The geomorphic view of networking: A network model and its uses” (Workshop on Middleware for Next Generation Internet Computing, December 2012)