## Slide 1: Composing Software Defined Networks
Jennifer Rexford
Princeton University
http://frenetic-lang.org
With Joshua Reich, Chris Monsanto, Nate Foster, and David Walker
To appear at Network Systems Design and Implementation, April 2013

## Slide 2: Software Defined Networking (SDN)
Controller Platform
Controller Application
Network-wide visibility and control
Direct control via open interface
But, how should we write controller applications?
Notes: Network-wide visibility and control
Direct control via an open interface

## Slide 3: Combining Many Networking Tasks
Controller Platform
Route + Monitor + FW + LB
Monolithic application
Hard to program, test, debug, reuse, port, …
Notes: But, real networks perform a wide variety of tasks
Routing, network monitoring, firewalls, server load balancing, etc.

## Slide 4: Modular Controller Applications
Controller Platform
LB
Route
Monitor
FW
Easier to program, test, and debug
Greater reusability and portability
A module for each task

## Slide 5: Beyond Multi-Tenancy
Controller Platform
Slice 1
Slice 2
Slice n
...
Each module controls a different portion of the traffic
Relatively easy to partition rule space, link bandwidth, and network events across modules
Notes: Simple case: multi-tenancy
Each module controls a different subset of the traffic
Relatively easy to partition traffic, rule space, and bandwidth resources
We want to write a single application out of modules that affect the handling of same traffic

## Slide 6: Modules Affect the Same Traffic
Controller Platform
LB
Route
Monitor
FW
How to combine modules into a complete application?
Each module partially specifies the handling of the traffic

## Slide 7: Parallel Composition [ICFP’11, POPL’12]
Controller Platform
Route on dest prefix
Monitor on source IP
+
dstip = 1.2/16  fwd(1)
dstip = 3.4.5/24  fwd(2)
srcip = 5.6.7.8  count
srcip = 5.6.7.9  count
srcip = 5.6.7.8, dstip = 1.2/16  fwd(1), count
srcip = 5.6.7.8, dstip = 3.4.5/24  fwd(2), count
srcip = 5.6.7.9, dstip = 1.2/16  fwd(1), count
srcip = 5.6.7.9, dstip = 3.4.5/24  fwd(2), count
Notes: From ICFP’11 and POPL’12
Also useful when two modules affect the handling of non-overlapping traffic or different switches/ports

## Slide 8: Example: Server Load Balancer
Spread client traffic over server replicas
  Public IP address for the service
  Split traffic based on client IP
  Rewrite the server IP address
Then, route to the replica
clients
1.2.3.4
load balancer
server replicas
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 9: Sequential Composition [new!]
Controller Platform
Routing
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
srcip = 0*, dstip = 1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip = 1*, dstip = 1.2.3.4  dstip = 10.0.0.2, fwd(2)
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 10: Dividing the Traffic Over Modules
Predicates
  Specify which traffic traverses which modules
  Based on input port and packet-header fields
Routing
Load Balancer
Monitor
Routing
dstport != 80
dstport = 80
>>
+

## Slide 11: High-Level Architecture
Controller Platform
M1
M2
M3
Composition Spec

## Slide 12: Partially Specifying Functionality
A module should not specify everything
  Leave some flexibility to other modules
  Avoid tying the module to a specific setting
Example: load balancer plus routing
  Load balancer spreads traffic over replicas
  … without regard to the network paths
Load Balancer
Routing
>>
Avoid custom interfaces between modules

## Slide 13: Abstract Topology Views
Present abstract topology to the module
  Concise: implicitly encodes the constraints
  General: can represent a variety of constraints
  Intuitive: looks just like a normal network
  Safe: prevents the module from overstepping
13
Real network
Abstract view

## Slide 14: Separation of Concerns
Hide irrelevant details
  Load balancer doesn’t see the internal topology or any routing changes
Routing view
Load-balancer view

## Slide 15: Ex. #1: Pass-Through of Packets
Simplified input
  Merged set of input ports
  E.g., all traffic from Internet
No forwarding action
  Firewall: pass-through or drop a packet
  Load balancer: pass-through and rewrite dest
Forwarding performed by another module
  Routing module controls all packet forwarding
Load balancer,
Firewall

## Slide 16: Ex. #2: Joint Control of Forwarding
Division of labor
  One module picks the egress point
  Other module picks the path
Learning and routing
Learning
Routing

## Slide 17: Ex. #2: Joint Control of Forwarding
Virtual packet headers
  Learning module selects an egress point
  Routing module forwards on virtual output port
Learning and routing
Learning
Routing

## Slide 18: Ex. #3: Many-to-One Mapping
Left: learning switch on MAC addresses
Middle: ARP on gateway, plus simple repeater
Right: shortest-path forwarding on IP prefixes
IP Core
Ethernet
IP Core
Gateway
Ethernet

## Slide 19: High-Level Architecture
Controller Platform
View Definitions
M1
M2
M3
Composition Spec

## Slide 20: Conclusions
Modularity is crucial
  Ease of writing, testing, and debugging
  Separation of concerns, code reuse, portability
Language abstractions
  Parallel and sequential composition
  Abstract topology views and virtual headers
Ongoing work
  Imperative Python-like programming language
  Complete run-time system and example apps