## Slide 1: Enabling Innovation Inside the Network
Jennifer Rexford
Princeton University
http://www.cs.princeton.edu/~jrex

## Slide 2: The Internet: A Remarkable Story
Tremendous success
  From research experiment to global infrastructure
Brilliance of under-specifying
  Network: best-effort packet delivery
  Hosts: arbitrary applications
Enables innovation
  Apps: Web, P2P, VoIP, social networks, …
  Links: Ethernet, fiber optics, WiFi, cellular, …

## Slide 3: Inside the ‘Net: A Different Story…
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Over specified
  Slow protocol standardization
Few people can innovate
  Equipment vendors write the code
  Long delays to introduce new features

## Slide 4: Do We Need Innovation Inside?
Many boxes (routers, switches, firewalls, …), with different interfaces.
Notes: Enterprise network.

## Slide 5: Networks are Hard to Manage
Operating a network is expensive
  More than half the cost of a network
  Yet, operator error causes most outages
Buggy software in the equipment
  Routers with 20+ million lines of code
  Cascading failures, vulnerabilities, etc.
The network is “in the way”
  Especially a problem in data centers
  … and home networks

## Slide 6: Software Defined Networks
control plane: distributed algorithms
data plane: packet processing

## Slide 7: Software Defined Networks
decouple control and data planes

## Slide 8: Software Defined Networks
decouple control and data planes by providing open standard API

## Slide 9: (Logically) Centralized Controller
Controller Platform

## Slide 10: Protocols  Applications
Controller Platform
Controller Application

## Slide 11: Benefits of SDN
Faster pace of innovation
  Less dependence on vendors and standards
Easier interoperability
  Compatibility only in the “wire” protocol
Simpler management
  Network-wide visibility, and direct control
Simpler, cheaper equipment
  Minimal software, simple forwarding hardware

## Slide 12: A Major Trend in Networking
Entire backbone
runs on SDN
Bought for $1.2 x 109
(mostly cash)

## Slide 13: Creating Foundation for Networking
Today: a domain, not a discipline
  Alphabet soup of protocols
  Header formats and bit twiddling
  Preoccupation with existing artifacts
Tomorrow: from practice, to principles
  Intellectual foundation for networking
  Identify the key abstractions
  … and support them efficiently
To build networks worthy of society’s trust

## Slide 14: OpenFlow
http://openflow.org

## Slide 15: Data Plane: Packet Processing
Simple packet-handling rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 16: Control Plane: Programmability
Events from switches
Topology changes,
Traffic statistics,
Arriving packets
Commands to switches
(Un)install rules,
Query statistics,
Send packets
Controller Platform
Controller Application

## Slide 17: Seamless Mobility/Migration
See host sending traffic at new location
Modify rules to reroute the traffic

## Slide 18: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*
src=1*

## Slide 19: Example SDN Applications
Seamless mobility/migration
Server load balancing
Dynamic access control
Using multiple wireless access points
Energy-efficient networking
Adaptive traffic monitoring
Denial-of-Service attack detection
Network virtualization
See http://www.openflow.org/videos/

## Slide 20: Programming SDNs
http://frenetic-lang.org

## Slide 21: Programming SDNs
Images by Billy Perkins
The Good
  Network-wide visibility
  Direct control over the switches
  Simple data-plane abstraction
The Bad
  Low-level programming interface
  Functionality tied to hardware
  Explicit resource control
The Ugly
  Non-modular, non-compositional
  Programmer faced with challenging distributed programming problem

## Slide 22: Network Control Loop
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 23: Language-Based Abstractions
SQL-like query language
OpenFlow
Switches
Consistent updates
Module Composition

## Slide 24: Combining Many Networking Tasks
Controller Platform
Monitor + Route + FW + LB
Monolithic application
Hard to program, test, debug, reuse, port, …
Notes: But, real networks perform a wide variety of tasks
Routing, network monitoring, firewalls, server load balancing, etc.

## Slide 25: Modular Controller Applications
Controller Platform
LB
Route
Monitor
FW
Easier to program, test, and debug
Greater reusability and portability
A module for each task

## Slide 26: Beyond Multi-Tenancy
Controller Platform
Slice 1
Slice 2
Slice n
...
Each module controls a different portion of the traffic
Relatively easy to partition rule space, link bandwidth, and network events across modules

## Slide 27: Modules Affect the Same Traffic
Controller Platform
LB
Route
Monitor
FW
How to combine modules into a complete application?
Each module partially specifies the handling of the traffic

## Slide 28: Parallel Composition
Controller Platform
Route on destination
Monitor on source
+
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
srcip = 5.6.7.8  count
srcip = 5.6.7.8, dstip = 1.2.3.4  fwd(1), count
srcip = 5.6.7.8, dstip = 3.4.5.6  fwd(2), count
srcip = 5.6.7.8  count
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
Notes: From ICFP’11 and POPL’12

## Slide 29: Example: Server Load Balancer
Spread client traffic over server replicas
  Public IP address for the service
  Split traffic based on client IP
  Rewrite the server IP address
Then, route to the replica
clients
1.2.3.4
load balancer
server replicas
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 30: Sequential Composition
Controller Platform
Routing
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
srcip = 0*, dstip = 1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip = 1*, dstip = 1.2.3.4  dstip = 10.0.0.2, fwd(2)
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 31: Dividing the Traffic Over Modules
Predicates
  Specify which traffic traverses which modules
  Based on input port and packet-header fields
Routing
Load Balancer
Monitor
Routing
dstport != 80
dstport = 80
>>
+

## Slide 32: Partially Specifying Functionality
A module should not specify everything
  Leave some flexibility to other modules
  Avoid tying the module to a specific setting
Example: load balancer plus routing
  Load balancer spreads traffic over replicas
  … without regard to the network paths
Load Balancer
Routing
>>

## Slide 33: Topology Abstraction
Present an abstract topology
  Information hiding: limit what a module sees
  Protection: limit what a module does
  Abstraction: present a familiar interface
33
Real network
Abstract view

## Slide 34: High-Level Architecture
Controller Platform
M1
M2
M3
Main
Program

## Slide 35: Reading State: Query Language
Applications read state
  Traffic counters in switches
  Packets sent to the controller
Minimize controller overhead
  Filter using high-level patterns
  Limit the amount of data
Controller platform
  Installs rules, reads counters, handle packets
Select(bytes) *
Where(inport:2) *
GroupBy([dstmac]) *
Every(60)
Select(packets) *
GroupBy([srcmac]) *
SplitWhen([inport]) *
Limit(1)
Learning Host Location
Traffic Monitoring

## Slide 36: Writing Policies: Consistent Updates
Transition from policy P1 to P2
  Security: new access control lists
  Routing: new shortest paths
Transient policy violations
  Packets in flight during policy change
  Loops, blackholes, unauthorized traffic
Consistent update semantics
  Packets experience either P1 or P2
  … but never a mixture of the two
CHANGE
We Can Believe In

## Slide 37: Language-Based Abstractions
SQL-like query language
OpenFlow
Switches
Consistent updates
Module Composition

## Slide 38: Many Challenging Questions Remain
Maturing the technology
  Measuring and controlling end hosts
  Heterogeneous switch hardware
  Distributed and replicated controllers
  Multiple administrative domains
Applying SDN in new settings
  Enterprise networks
  Cellular core and radio access networks
  Internet eXchange Points and transit networks

## Slide 39: Conclusion
SDN is exciting
  Enables innovation
  Simplifies management
  Rethinks networking
SDN is happening
  Practice: useful APIs and good industry traction
  Principles: start of higher-level abstractions
Great opportunity
  Practical impact on future networks
  Placing networking on a strong foundation

## Slide 40: Learn More
SDN and OpenFlow
  www.openflow.org
  www.opennetworking.org
  www.opennetsummit.org
  conferences.sigcomm.org/sigcomm/2012/hotsdn.php
Frenetic language
  www.frenetic-lang.org
  www.cs.princeton.edu/~jrex/papers/frenetic12.pdf
  github.com/frenetic-lang