## Slide 1: Programming Languages for Software Defined Networks
Jennifer Rexford and David Walker
Princeton University
http://frenetic-lang.org
Joint work with the research groups of Nate Foster (Cornell) and Arjun Guha (Umass-Amherst), and several students and post-docs at Princeton

## Slide 2: Today’s Networks are a Mess!
Many boxes (routers, switches, firewalls, …), with different interfaces.
Notes: Enterprise network.

## Slide 3: Software Defined Networks
control plane: distributed algorithms
data plane: packet processing

## Slide 4: Software Defined Networks
decouple control and data planes

## Slide 5: Software Defined Networks
decouple control and data planes by providing open standard API

## Slide 6: Simple, Open Data-Plane API
Prioritized list of rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 7: (Logically) Centralized Controller
Controller Platform

## Slide 8: Protocols  Applications
Controller Platform
Controller Application

## Slide 9: Seamless Mobility
See host sending traffic at new location
Modify rules to reroute the traffic

## Slide 10: Server Load Balancing
Pre-install load-balancing policy
Split traffic based on source IP
src=0*,
dst=1.2.3.4
src=1*,
dst=1.2.3.4
10.0.0.1
10.0.0.2

## Slide 11: Example SDN Applications
Seamless mobility and migration
Server load balancing
Dynamic access control
Using multiple wireless access points
Energy-efficient networking
Adaptive traffic monitoring
Denial-of-Service attack detection
Network virtualization
See http://www.openflow.org/videos/

## Slide 12: A Major Trend in Networking
Entire backbone
runs on SDN
Bought for $1.2 x 109
(mostly cash)

## Slide 13: Programming SDNs
http://frenetic-lang.org

## Slide 14: Programming SDNs
Images by Billy Perkins
The Good
  Network-wide visibility
  Direct control over the switches
  Simple data-plane abstraction
The Bad
  Low-level programming interface
  Functionality tied to hardware
  Explicit resource control
The Ugly
  Non-modular, non-compositional
  Programmer faced with challenging distributed programming problem

## Slide 15: Network Control Loop
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 16: Language-Based Abstractions
SQL-like query language
OpenFlow
Switches
Consistent updates
Module Composition

## Slide 17: Combining Many Networking Tasks
Controller Platform
Monitor + Route + FW + LB
Monolithic application
Hard to program, test, debug, reuse, port, …
Notes: But, real networks perform a wide variety of tasks
Routing, network monitoring, firewalls, server load balancing, etc.

## Slide 18: Modular Controller Applications
Controller Platform
LB
Route
Monitor
FW
Easier to program, test, and debug
Greater reusability and portability
A module for each task

## Slide 19: Beyond Multi-Tenancy
Controller Platform
Slice 1
Slice 2
Slice n
...
Each module controls a different portion of the traffic
Relatively easy to partition rule space, link bandwidth, and network events across modules
Notes: Simple case: multi-tenancy
Each module controls a different subset of the traffic
Relatively easy to partition traffic, rule space, and bandwidth resources
We want to write a single application out of modules that affect the handling of same traffic

## Slide 20: Modules Affect the Same Traffic
Controller Platform
LB
Route
Monitor
FW
How to combine modules into a complete application?
Each module partially specifies the handling of the traffic

## Slide 21: Parallel Composition
Controller Platform
Route on destination
Monitor on source
+
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
srcip = 5.6.7.8  count
srcip = 5.6.7.8, dstip = 1.2.3.4  fwd(1), count
srcip = 5.6.7.8, dstip = 3.4.5.6  fwd(2), count
srcip = 5.6.7.8  count
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
Notes: From ICFP’11 and POPL’12

## Slide 22: Sequential Composition
Controller Platform
Routing
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
srcip = 0*, dstip = 1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip = 1*, dstip = 1.2.3.4  dstip = 10.0.0.2, fwd(2)
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 23: Dividing the Traffic Over Modules
Predicates
  Specify which traffic traverses which modules
  Based on input port and packet-header fields
Routing
Load Balancer
Monitor
Routing
Non-web
dstport != 80
Web traffic
dstport = 80
>>
+

## Slide 24: Abstract Topology: Load Balancer
Present an abstract topology
  Information hiding: limit what a module sees
  Protection: limit what a module does
  Abstraction: present a familiar interface
24
Real network
Abstract view

## Slide 25: High-Level Architecture
Controller Platform
M1
M2
M3
Main
Program

## Slide 26: Reading State: Query Language
Applications read state
  Traffic counters in switches
  Packets sent to the controller
Minimize controller overhead
  Filter using high-level patterns
  Limit the amount of data
Controller platform
  Installs rules
  Reads counters
  Handles packets
Select(bytes)
Where(inport:2)
GroupBy([dstmac])
Every(60)
Select(packets)
GroupBy([srcmac])
SplitWhen([inport])
Limit(1)
Learning Host Location
Traffic Monitoring

## Slide 27: Writing Policies: Consistent Updates
Transition from policy P1 to P2
  Security: new access control lists
  Routing: new shortest paths
Transient policy violations
  Packets in flight during policy change
  Loops, blackholes, unauthorized traffic
Consistent update semantics
  Packets experience either P1 or P2
  … but never a mixture of the two
CHANGE
We Can Believe In

## Slide 28: Frenetic Abstractions
Query language
OpenFlow
Switches
Consistent updates
Module Composition

## Slide 29: Frenetic Software: Try it Out!
Pyretic
  Python-based language and run-time system
  Software on github under a BSD-style license
  http://www.frenetic-lang.org/pyretic/
  Software development led by Princeton
  Used in SDN MOOC, and PyResonance and SDX projects
Frenetic-OCaml
  OCaml-based language and run-time system
  Software on github under GNU general public license v3
  https://github.com/frenetic-lang/frenetic
  Software development led by Cornell and UMass-Amherst