## Slide 1: Software-Defined Networks
Jennifer Rexford
Princeton University
http://frenetic-lang.org
Joint work with the research groups of David Walker (Princeton), Nate Foster (Cornell), and Arjun Guha (Umass)

## Slide 2: The Internet Enables Innovation
… in end-host applications

## Slide 3: Inside the ‘Net: A Different Story…
Closed equipment
  Software bundled with hardware
  Vendor-specific interfaces
Over specified
  Slow protocol standardization
Few people can innovate
  Equipment vendors write the code
  Long delays to introduce new features

## Slide 4: Do We Need Innovation Inside?
Many boxes (routers, switches, firewalls, …), with different interfaces.
Notes: Enterprise network.

## Slide 5: Software Defined Networks
control plane: distributed algorithms
data plane: packet processing

## Slide 6: Software Defined Networks
decouple control and data planes

## Slide 7: Software Defined Networks
decouple control and data planes by providing open standard API

## Slide 8: Simple, Open Data-Plane API
Prioritized list of rules
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller

## Slide 9: (Logically) Centralized Controller
Controller Platform

## Slide 10: Protocols  Applications
Controller Platform
Controller Application

## Slide 11: Example SDN Applications
Seamless mobility and migration
Server load balancing
Dynamic access control
Using multiple wireless access points
Energy-efficient networking
Blocking denial-of-service attacks
Adaptive traffic monitoring
Network virtualization
Steering traffic through middleboxes
<Your app here!>

## Slide 12: A Major Trend in Networking
Entire backbone
runs on SDN
Bought for $1.2 x 109
(mostly cash)

## Slide 13: SDN makes it possible to program the network…
… but it does not make it easy

## Slide 14: Network Control Loop
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 15: Language-Based Abstractions
SQL-like query language
OpenFlow
Switches
Consistent updates
Module Composition

## Slide 16: Combining Many Networking Tasks
Controller Platform
Monitor + Route + FW + LB
Monolithic application
Hard to program, test, debug, reuse, port, …
Notes: But, real networks perform a wide variety of tasks
Routing, network monitoring, firewalls, server load balancing, etc.

## Slide 17: Modular Controller Applications
Controller Platform
LB
Route
Monitor
FW
A module for each task

## Slide 18: Parallel Composition
Controller Platform
Route on destination
Monitor on source
+
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
srcip = 5.6.7.8  count
srcip = 5.6.7.8, dstip = 1.2.3.4  fwd(1), count
srcip = 5.6.7.8, dstip = 3.4.5.6  fwd(2), count
srcip = 5.6.7.8  count
dstip = 1.2.3.4  fwd(1)
dstip = 3.4.5.6  fwd(2)
Notes: From ICFP’11 and POPL’12

## Slide 19: Sequential Composition
Controller Platform
Routing
Load Balancer
>>
dstip = 10.0.0.1  fwd(1)
dstip = 10.0.0.2  fwd(2)
srcip = 0*, dstip=1.2.3.4  dstip=10.0.0.1
srcip = 1*, dstip=1.2.3.4  dstip=10.0.0.2
srcip = 0*, dstip = 1.2.3.4  dstip = 10.0.0.1, fwd(1)
srcip = 1*, dstip = 1.2.3.4  dstip = 10.0.0.2, fwd(2)
Notes: Load balancer splits traffic sent to public IP address over multiple replicas, based on client IP address, and rewrites the IP address

## Slide 20: Abstract Topology: Load Balancer
Present an abstract topology
  Information hiding: limit what a module sees
  Protection: limit what a module does
  Abstraction: present a familiar interface
20
Real network
Abstract view

## Slide 21: Reading State: Query Language
Applications read state
  Traffic counters in switches
  Packets sent to the controller
Minimize controller overhead
  Filter using high-level patterns
  Limit the amount of data
Controller platform
  Installs rules
  Reads counters
  Handles packets
Select(bytes)
Where(inport:2)
GroupBy([dstmac])
Every(60)
Select(packets)
GroupBy([srcmac])
SplitWhen([inport])
Limit(1)
Learning Host Location
Traffic Monitoring

## Slide 22: Writing Policies: Consistent Updates
Transition from policy P1 to P2
  Security: new access control lists
  Routing: new shortest paths
Transient policy violations
  Packets in flight during the change
  Loops, blackholes, unauthorized traffic
Consistent update semantics
  Packets experience either P1 or P2
  … but never a mixture of the two
CHANGE
We Can Believe In

## Slide 23: Conclusion
SDN is exciting
  Enables innovation
  Simplifies management
  Rethinks networking
SDN is happening
  Practice: industry traction, cool apps
  Principles: higher-level abstractions
Great opportunity
  Practical impact
  Strong foundations