## Slide 1: Programming Abstractions for Future SDN Switches
Jennifer Rexford
Princeton University

## Slide 2: Software-Defined Networking
Controller
App 1
App 2
Logically-centralized controller
Simple data-plane interface

## Slide 3
Prioritized list of rules
  Priority: disambiguate overlapping patterns
  Pattern: match packet header bits
  Actions: drop, forward, modify, send to controller
  Counters: number of bytes and packets
Priority | Pattern | Actions | Counters
3 | srcip=1.0.*.* | Forward(1) | 3, 4500
2 | dstip=1.2.3.4, dstport=80 | dstip:=10.0.0.1, Forward(2) | 5, 6018
1 | srcport=25 | Send to controller | 1, 512
0 | * | Drop | 2, 1024
1.0

## Slide 4: Enabling New SDN Applications
Wide-area traffic engineering
Network virtualization for multi-tenant data centers
Steering traffic through middleboxes
Seamless mobility and migration
Server load balancing
Dynamic access control
Using multiple wireless access points
Energy-efficient networking
Blocking denial-of-service attacks
Adaptive traffic monitoring
<Your app here!>

## Slide 5: Limitations of OpenFlow 1.0
Most switches can do much more
  Multiple stages of match-action tables
  E.g., Ethernet, IP, access control lists (ACLs)
Many applications need much more
  Multiple policies (e.g., ACL, routing, monitoring)
  Matching on more header fields
Limited TCAM space in legacy switches
  E.g., a few thousand rules in the wide TCAM
MAC
learning
Access control
IP

## Slide 6: Over the Past Five Years…
Version | Date | # Headers
OF 1.0 | Dec 2009 | 12
OF 1.1 | Feb 2011 | 15
OF 1.2 | Dec 2011 | 36
OF 1.3 | Jun 2012 | 40
OF 1.4 | Oct 2013 | 41
Proliferation of header fields
Multiple stages of heterogeneous tables
Still not enough (e.g., VXLAN, NVGRE, STT, …)
Notes: OF 1.4 did stop for lack of wanting more, but just to put on the breaks.
This is natural and a sign of success of OpenFlow:
enable a wider range of controller apps
expose more of the capabilities of the switch
E.g., adding support for MPLS, inter-table meta-data, ARP/ICMP, IPv6, etc.
New encap formats arising much faster than vendors spin new hardware

## Slide 7: Where does it stop?!?
Notes: Simplicity would be nice, but it just isn’t practical

## Slide 8: Future SDN Switches
Configurable packet parser
  Not tied to a specific header format
Flexible match+action tables
  Multiple tables (in series and/or parallel)
  Able to match on all defined fields
General packet-processing primitives
  Copy, add, remove, and modify
  For both header fields and meta-data
Notes: This may sound like a pipe dream (pun intended), and certainty this won’t happen overnight.
But, there are promising signs of progress in this direction…

## Slide 9: We Can Do This!
New generation of switch ASICs
  Intel FlexPipe
  Barefoot RMT [SIGCOMM’13]
  Cisco Doppler
But, programming these chips is hard
  Custom, vendor-specific interfaces
  Low-level, akin to microcode programming
Notes: Offering this kind of functionality at reasonable cost…

## Slide 10: We need a higher-level interface
To tell the switch how we want it to behave

## Slide 11: Three Goals
Protocol independence
  Configure a packet parser
  Define a set of typed match+action tables
Target independence
  Program without knowledge of switch details
  Rely on compiler to configure the target switch
Reconfigurability
  Change parsing and processing in the field

## Slide 12: “Classic” OpenFlow (1.x)
Target Switch
SDN Control Plane
Installing and querying rules

## Slide 13: “OpenFlow 2.0”
Target Switch
SDN Control Plane
Populating:
Installing and querying rules
Compiler
Configuring:
Parser, tables, and control flow
Parser & Table Configuration
Rule Translator
Notes: Two modes: (i) configuration and (ii) populating
Compiler configures the parser, lays out the tables (cognizant of switch resources and capabilities), and translates the rules to map to the hardware tables
The compiler could run directly on the switch (or at least some backend portion of the compiler would do so)

## Slide 14: P4 Language
Programming Protocol-Independent Packet Processing (p4.org)
With Pat Bosshart, Glen Gibb, Martin Izzard, and Dan Talayco (Barefoot Networks), Dan Daly (Intel), Nick McKeown (Stanford), Cole Schlesinger and David Walker (Princeton), Amin Vahdat (Google), and George Varghese (Microsoft)
http://www.sigcomm.org/node/3503

## Slide 15: Simple Motivating Example
Data-center routing
  Top-of-rack switches
  Two tiers of core switches
  Source routing by ToR
Hierarchical tag (mTag)
  Pushed by the ToR
  Four one-byte fields
  Two hops up, two down
up1
up2
down1
down2
ToR
ToR

## Slide 16: Header Formats
Header
  Ordered list of fields
  A field has a name and width
header ethernet {
fields {
dst_addr : 48;
src_addr : 48;
ethertype : 16;
}
}
header mTag {
fields {
up1 : 8;
up2 : 8;
down1 : 8;
down2 : 8;
ethertype : 16;
}
}
header vlan {
fields {
pcp : 3;
cfi : 1;
vid : 12;
ethertype : 16;
}
}

## Slide 17: Parser
State machine traversing the packet
  Extracting field values as it goes
parser start { parser vlan {
ethernet; switch(ethertype) {
} case 0xaaaa : mTag;
case 0x800 : ipv4;
parser ethernet { . . .
switch(ethertype) { }
case 0x8100 : vlan;
case 0x9100 : vlan; parser mTag {
case 0x800 : ipv4; switch(ethertype) {
. . . case 0x800 : ipv4;
} . . .
} }
}

## Slide 18: Typed Tables
Describe each packet-processing stage
  What fields are matched, and in what way
  What action functions are performed
  (Optionally) a hint about max number of rules
table mTag_table {
reads {
ethernet.dst_addr : exact;
vlan.vid : exact;
}
actions {
add_mTag;
}
max_size : 20000;
}
Notes: Compiler uses this to
- determine what kind of memory (width, height), and what kind (TCAM, SRAM)
- reject rules that violate the type
The “add_mTag” is an “action function”.
In other kinds of tables, multiple different action functions may be allowed.

## Slide 19: Action Functions
Custom actions built from primitives
  Add, remove, copy, set, increment, checksum
action add_mTag(up1, up2, down1, down2, outport) {
add_header(mTag);
copy_field(mTag.ethertype, vlan.ethertype);
set_field(vlan.ethertype, 0xaaaa);
set_field(mTag.up1, up1);
set_field(mTag.up2, up2);
set_field(mTag.down1, down1);
set_field(mTag.down2, down2);
set_field(metadata.outport, outport);
}
Notes: Push mTag on the packet
Copy the ethertype of the VLAN header to correctly identify the next level of header
Make the VLAN header point to the mTag
Set the four fields of the mTag
Ensure the packet goes to the right egess port

## Slide 20: Control Flow
Flow of control from one table to the next
  Collection of functions, conditionals, and tables
For a ToR switch:
ToR
From core
(with mTag)
From local hosts
(with no mTag)
Source
Check
Table
Local
Switching
Table
Egress
Check
mTag
Table
Miss: Not Local
Notes: Source check (one rule per port): verify mTag only on ports to the core (actions: fault, strip and record metadata, pass)
Local switching: checks if destination is local, and otherwise goes to mTag table
mTag table: add mTag
Egress check: has someone set the outport

## Slide 21: Control Flow
Flow of control from one table to the next
  Collection of functions, conditionals, and tables
Simple imperative representation
control main() {
table(source_check);
if (!defined(metadata.ingress_error)) {
table(local_switching);
if (!defined(metadata.outport)) {
table(mTag_table);
}
table(egress_check);
}
}
Notes: Source check (one rule per port): verify mTag only on ports to the core (actions: fault, strip and record metadata, pass)
Local switching: checks if destination is local, and otherwise goes to mTag table
mTag table: add mTag
Egress check: verify egress is resolved, do not retag packets received with tag, reads egress, etc.

## Slide 22: P4 Compilation
Notes: This is a rich area, and so far we have only touched the surface…

## Slide 23: P4 Compiler
Parser
  Programmable parser: translate to state machine
  Fixed parser: verify the description is consistent
Control program
  Target-independent: table graph of dependencies
  Target-dependent: mapping to switch resources
Rule translation
  Verify that rules agree with the (logical) table types
  Translate the rules to the physical tables
Notes: Parser:
Programmable parser: translate parser description into a state machine
Fixed parser: verify that the parser description is consistent with the target processor
Control program
Table graph: dependencies on processing order, opportunities for parallelism
Mapping to switch resources: physical tables, types of memory, sizes, combining tables
Rule translation
Verify rules agree with the types
Translate rules into the physical tables

## Slide 24: Compiling to Target Switches
Software switches
  Directly map the table graph to switch tables
  Use data structure for exact/prefix/ternary match
Hardware switches with RAM and TCAM
  RAM: hash table for tables with exact match
  TCAM: for tables with wildcards in the match
Switches with parallel tables
  Analyze table graph for possible concurrency

## Slide 25: Compiling to Target Switches
Applying actions at the end of pipeline
  Instantiate tables that generate meta-data
  Use meta-data to perform actions at the end
Switches with a few physical tables
  Map multiple logical tables to one physical table
  “Compose” rules from the multiple logical tables
  … into “cross product” of rules in physical table

## Slide 26: Recent Progress
P4 language consortium
  Latest specification on January 28, 2015
  http://p4.org/spec/p4-latest.pdf
ONF Protocol-Independent Forwarding
  Designing an intermediate representation
  https://www.opennetworking.org/images/stories/downloads/sdn-resources/white-papers/OF-PI__A_Protocol_Independent_Layer_for_OpenFlow_v1-1.pdf
Compilation for reconfigurable switches
  “Concurrent NetCore: From policies to pipelines” (Schlesinger, Greenberg, and Walker, ICFP’14)
  “Compiling packet programs to reconfigurable switches” (Yan, Jose, Varghese, and McKeown, NSDI’15)

## Slide 27: Compiling Path Queries
With Srinivas Narayana, Mina Tahmasbi Arashloo, and David Walker (Princeton)
http://dl.acm.org/authorize.cfm?key=N71306

## Slide 28: SDN “Control Loop”
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 29: SDN “Control Loop”
Read
state
OpenFlow
Switches
Write
policy
Compute Policy

## Slide 30: Traditional Traffic Monitoring
Measure traffic at single location
  SNMP and RMON
  Netflow and sFlow
  OpenFlow rule counters
Actively probe along a path
  Ping and traceroute
But, cannot easily answer questions about the flow of traffic over paths, over time

## Slide 31: Our Goals
Ask network-wide questions using concise, declarative queries,
Not worry about interactions of measurements with the network’s forwarding policy,
Not worry about interactions between different measurements,
Not have to infer the results from indirect observations of traffic and forwarding policy,
Have control over the network resources used for measurement, and
Be able to use commodity SDN switch hardware.

## Slide 32: Path Query Language
Query traffic along a path
  Regular expression on packet location and headers
  Collect packets or aggregate statistics
Simple example
  Packets reaching switch S1, then S2 with a source IP address in 10.0.0.0/16
S1
S2
  switch=S1 ^ (switch=S2 & srcip=10.0.0.0/16)

## Slide 33: Example: Firewall Evasion
Capture packets evading a firewall
    ingress()
    ^
    (switch != FW)*
    ^
    egress()
0 or more
repetitions
ingress
egress
ingress
ingress
egress
egress

## Slide 34: Example: Traffic Matrix
Switch-level traffic matrix
 | E1 | E2 | ...
I1 | 250 | 100 | ...
I2 | 120 | 95 | ...
... | ... | ... | ...
I1
E1
I2
I3
E2
E3

## Slide 35: Example: Traffic Matrix
Switch-level traffic matrix:
  ingress()
  ^
  (true)*
  ^
  egress()
Count all packets, going from any ingress to any egress.
Flow | #pkts
* | 1000

## Slide 36: Example: Traffic Matrix
Switch-level traffic matrix:
  groupby(ingress(),
  [switch])
  ^
  (true)*
  ^
  groupby(egress(),
  [switch])
Group counts by
packet’s ingress and egress switch!
Flow | #pkts
sw=I1, sw=E1 | 250
sw=I1, sw=E2 | 100
... | ...

## Slide 37: Measuring Traffic on Paths
Could record path information in packets
But, too much state!
[{sw: S1
port: 1
srcmac: ...
srcip: ...
...}]
[{sw: S1, ...},
{sw: S2
port: 3
srcmac: ...
...}]
[{sw: S1, ...},
{sw: S2, ...},
{sw: S3
port: 2
...}]

## Slide 38: Measuring Traffic on Paths
Could send every packet to a collector
Too much bandwidth and state!

## Slide 39: Measuring Traffic on Paths
Queries tell us what we need to know
  Only record the path state needed by query
Queries are regular expressions
  Easily represented as finite state automata
Q0
Q1
Q2
switch=S1
switch=S2, dstip=10.0.0.0/16
  switch=S1 ^ (switch=S2 & srcip=10.0.0.0/16)

## Slide 40: Measure Traffic on Paths
Distribute the DFA over the switches
  Packets carry their current DFA state
  Match-action tables implement transitions
E.g., using VLAN tag or MPLS label
Q0
Q1
Q2
switch=S1
switch=S2, dstip=10.0.0.0/16

## Slide 41: Query Compilation
Q0
Q1
Q2
switch=S1, srcip=10.0.0.1
switch=S2, dstip=10.0.0.3
Switch | Match | Action
S1 | state=Q0, srcip=10.0.0.1 | state=Q1
S2 | state=Q1, dstip=10.0.0.3 | state=Q2
S2 | state=Q1, dstip=10.0.0.3 | count
DFA transition
DFA accept

## Slide 42: Query Compilation
Leveraging multi-stage tables
Table types
  Customized to the header fields and number of state transitions the query needs
Supporting multiple queries
  Combine to form a single DFA
  Or, better yet, leverage even more tables!
Input tagging and capture
Forwarding policy
Output tagging and capture

## Slide 43: Path Query Prototype
Pyretic language
  Supports high-level policies and composition
Ragel state machine compiler
Pyretic run-time system
  Extended to support multi-stage tables (Open vSwitch with Nicira extensions)
Performance optimizations
  To reduce compilation time
Single-threaded on Intel Xeon E3
  With 3.4 Ghz CPU and 32 GB of memory

## Slide 44: Performance Evaluation
Many queries
  Traffic matrix, congested link diagnosis, DDoS source detection, packet loss detection, firewall evasion, slice isolation
Several topologies
  Stanford campus and fat-tree topologies
Metrics (and Stanford results)
  Compilation time: < 10 sec
  Number of tags: < 200 tags
  Number of rules: < 1K rules
Acceptable for human time-scale

## Slide 45: Conclusion
Future SDN switches
  Programmable parsing
  Reconfigurable match-action tables
Programming abstractions
  Controller tells the switch how to behave
  Header format, parsing graph, table types, graph, measurement queries, …
Efficient compilation
  P4 compiler (Princeton ICFP’14, Stanford NSDI’15)
  Path queries compiler (Princeton HotSDN’14)
Much more left to do !