## Slide 1: Toward Self-Driving Networks
Jennifer Rexford

## Slide 2: Self-Driving Network
Complete control loop
Examples
  Direct traffic over the paths with the best performance
  Block or slow heavy-hitter flows
  Block or slow flows responsible for microbursts in packet queues
Now possible in the data plane!
measure
analyze
control

## Slide 3: PISA: Protocol Independent Switch Architecture
Match+Action
Memory
ALU
Programmable
Parser
Programmer declares which
headers are recognized
Programmer declares what tables are
needed and how packets are processed
All stages are identical – makes PISA a good “compiler target”
Notes: PISA chips are also built around a pipeline. But in PISA, all the pipeline stages are all IDENTICAL. They initially don’t know anything about protocols – they are sitting waiting to receive instructions from the compiler.
The basic operations of each stage is called “Match + Action” – In each stage, there is a set of memories which match on headers,
Depending on the match, an action is applied to the header by an ALU. And then the header is passed to the next stage, and so on.
A PISA chip is initially blank – it doesn’t know about any protocols.
The P4 programmer tells the programmable parser what packet headers it should recognize.
If a new header is developed, we add it to the set of headers the parser recognizes.
Let’s take a closer look at how a packet is processed …..

## Slide 4: P4 Programming Language
High-level goals
  Reconfigurability in the field
  Protocol independence
  Target independence
Declarative language
  Specify packet pipeline
  Headers, parsing, metadata
  Tables, actions, control flow
action ipv4_forward(macAddr_t dstAddr, egressSpec_t port) {
standard_metadata.egress_spec = port;
hdr.ethernet.srcAddr = hdr.ethernet.dstAddr;
hdr.ethernet.dstAddr = dstAddr;
hdr.ipv4.ttl = hdr.ipv4.ttl - 1;
}
table ipv4_lpm {
key = { hdr.ipv4.dstAddr: lpm; }
actions = { ipv4_forward, drop; }
size = 1024;
default_action = drop();
}
apply {
if (hdr.ipv4.isValid()) {ipv4_lpm.apply(); }
}

## Slide 5: The P4 Community is Growing
P4-capable devices
P4 Language Consortium (p4.org)
  ~100 members (~75 companies)
  Working groups (language, API, architecture, and applications)
  P4 language and related specs
  Open-source software and tutorials
  P4 workshops and developer days

## Slide 6: But, a Constrained Computational Model
Packet
parser
Match | Action
m1 | a1
registers
Match-action
tables
Match | Action
m1 | a1
registers
Match-action tables
. . .
metadata
Small amount of memory
Pipelined computation
Limited computation
headers
Limited # of bits

## Slide 7: Design compact data structures and streaming algorithms

## Slide 8: Hop-by-Hop Utilization-aware Load-balancing Architecture
Naga Katta, Mukesh Hira, Changhoon Kim, Anirudh Sivaraman, and Jennifer Rexford
http://conferences.sigcomm.org/sosr/2016/papers/sosr_paper67.pdf
HULA

## Slide 9: HULA Multipath Load Balancing
Load balancing entirely in the data plane
  Collect real-time, path-level performance statistics
  Group packets into “flowlets” based on time & headers
  Direct each new flowlet over the current best path
S1
S2
S3
S4
ToR 10
ToR 1
Data

## Slide 10: Path Performance Statistics
Using the best-hop table
  Update the best next-hop upon new probes
  Assign a new flowlet to the best next-hop
S1
S3
S4
Best-hop table
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
Data
Data
Probe
Probe

## Slide 11: Flowlet Routing
Flowlet table
S1
S3
S4
Using the flowlet table
  Update the next hop if enough time has elapsed
  Update the timestamp to the current time
Forward the packet to the chosen next hop
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
0
1
…
h(flowid)
Data
Data

## Slide 12: Putting it all Together Using P4
data packet
current best next-hop S3
chosen next-hop
Update next-hop (if enough time elapsed) and time
Dest ToR | Timestamp | Next-Hop
ToR 10 | 1 | S2
ToR 0 | 17 | S4
… | … | …
Best Next-Hop | Path Utilization
S3 | 50%
S4 | 10%
… | …
0
1
…
Dest ToR
0
1
…
h(flowid)

## Slide 13: Heavy Hitter Detection Entirely in the Data Plane
Vibhaalakshmi Sivaraman, Srinivas Narayana, Ori Rottenstreich, S. Muthukrishnan, and Jennifer Rexford
https://conferences.sigcomm.org/sosr/2017/papers/sosr17-heavy-hitter.pdf
HashPipe

## Slide 14: Heavy-Hitter Detection
Heavy hitters
  The k largest trafic flows
  Flows exceeding threshold T
Space-saving algorithm
  Table of (key, value) pairs
  Evict the key with the minimum value
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Table scan

## Slide 15: Approximating the Approximation
Evict minimum of d entries
  Rather than minimum of all entries
  E.g., with d = 2 hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
K4 | 10
K5 | 1
K6 | 5
New Key K7
Multiple memory accesses

## Slide 16: Approximating the Approximation
Divide the table over d stages
  One memory access per stage
  Two different hash functions
Id | Count
K1 | 4
K2 | 2
K3 | 7
New Key K7
Id | Count
K4 | 10
K5 | 1
K6 | 5
Going back to the first table

## Slide 17: Approximating the Approximation
Rolling minimum across stages
  Avoid recirculating the packet
  … by carrying the minimum along the pipeline
Id | Count
K1 | 4
K2 | 10
K3 | 7
New Key K7
Id | Count
K4 | 2
K5 | 1
K6 | 5
Id | Count
K1 | 4
K7 | 1
K3 | 7
Id | Count
K2 | 10
K5 | 1
K6 | 5
(K2, 10)

## Slide 18: P4 Prototype and Evaluation
Id | Count
K1 | 4
K2 | 10
K3 | 7
Id | Count
K4 | 2
K5 | 1
K6 | 5
New Key K7
(K2, 10)
Hash on packet header
Packet metadata
Conditional updates to compute minimum
Register arrays
High accuracy with overhead proportional to # of heavy hitters

## Slide 19: Catching the Microburst Culprits With Snappy
Xiaoqi Chen, Shir Landau Feibish, Yaron Koral, Jennifer Rexford, and Ori Rottenstreich
http://www.cs.princeton.edu/~jrex/papers/snappy18.pdf

## Slide 20: Short-Lived Spikes in Buffer Occupancy

## Slide 21: Microbursts are Expensive
Microbursts cause performance degradation
  Packet loss
  Packet delay
But, simultaneously want to have
  Support bursty workloads
  Use low-cost switches (with shallow buffers)
  Maintain high link utilization
Only possible by micromanaging the microbursts!

## Slide 22: Detecting Heavy Flows in the Queue
For each flow, how many packets are in the queue?
Data structure challenges
  Per-flow state (key and count)
  Updating on packet arrival and departure
Key | Count
 | 1
 | 5
 | 1
 | 1
 | 2
 | 1

## Slide 23: Multiple, Approximate Snapshots of the Queue
Avoiding per-flow state
  Approximate data structure (e.g., Count-Min)
  Packet checks its flow’s status, and acts
Avoiding updates on packet departure
  Packet’s departure time is known at arrival time
  Implicitly handle departures in small batches
Count-Min Sketch [CM ‘05]
C columns
B Buckets
f
+1
+1
+1

## Slide 24: Multiple Snapshots Across the Pipeline
Snap 2:
Read
Snap 1:
Read
Snap h:
Read
length
Snap 3:
write

## Slide 25: Conclusion
Self-driving networks
  Integrate measure, analyze, and control
  Implement directly in the network devices
Enabled by programmable switches
  Parsing, processing, and state
Approximate data structures
  Good accuracy with limited resources
  Enables a ``control loop” inside the network