## Slide 1: Synthesizing Load-Sensitive Routing Protocols for Programmable Switches
Jennifer Rexford Princeton University
With Kuo-Feng Hsu, Ryan Beckett, Ang Chen, Praveen Tammana, and David Walker
http://www.cs.princeton.edu/~jrex/papers/contra.pdf

## Slide 2: Intradomain Routing Goals
Routing Constraints (e.g., service chain)
Traffic Engineering (e.g., min latency, max throughput)
Fast Adaptation (e.g., failures, load changes)

## Slide 3: Programmable Data Plane as an Enabler
Protocol-Independent Switch Architecture (PISA)
  Programmable data plane at line speed
  Programmed using a standard language (e.g., P4)
Stages
Deparser
Parser
Memory
Persistent State
ALU
Match-
Action
Table
Notes: Pragmatic in limited programmability, and pragmatic now because of changes in hardware trends

## Slide 4: Load-Sensitive Routing in the Data Plane
Programmable switch hardware as an enabler
  Fine-grained link metrics (e.g., utilization, queuing)
  Flexible computation (e.g., path metrics, best path)
  State across packets (e.g., to group packets into flowlets)
0.3
0.2
0.3

## Slide 5: Load Balancing in the Data Plane
Existing solutions (e.g., Conga, HULA)
  Specific topologies (e.g., data-center leaf-spine)
  Specific path metrics (e.g., “least utilized shortest path”)
  No routing constraints (e.g., no support for service chaining)
…
…

## Slide 6: Contra Goals
General
  Wide range of metrics
  Flexible path constraints
  Arbitrary topologies
Distributed
  No central controller
  Stable, avoids oscillation
  Converges to best paths
Performant
  Responsive to changing metrics
  Low traffic and switch overhead
  Mitigates forwarding loops
  Avoids out-of-order packets
Implementable
  Using programmable data planes

## Slide 7: Synthesizing the Routing Protocol
Compiler
High-Level Routing Policy
P4 code
P4 code

## Slide 8: Policy Language
Routing policy: a function that ranks network paths
  Matching on paths using regular expressions
  Computing and comparing path metrics
  if (.* W .*)
  then path.util
  else ∞
  if (path.util < 0.8)
  then (1, 0, path.util)
  else (2, path.len, path.util)
Waypoint W with min utilization
Min utilization under light load, otherwise shortest
Notes: Lower scores are better
Infinite mean the path is not used
Regular expressions on path properties is not a new idea

## Slide 9: Family of Routing Protocols
Distance vector routing
  Flexible routing constraints and metrics
  Implementable in modern data planes
Monitor path performance
Enforce path constraints
Compare and select paths
Pin groups of packets to a path
Prevent forwarding loops
building blocks
0.2
0.3
path probe: 0.3
data packets

## Slide 10: Challenge #1: Support Non-Isotonic Policies
Nodes rank paths differently
Propagating the locally best metric is not enough
  B chooses B-C-D
  So, A must use A-B-C-D
  But, A would have preferred A-B-D
A
D
B
0.2
  if (A B D)
  then 0
  else path.util
C
0.1
0.1
0.1
Notes: In each step, the paths obey the constraints - S-B-D
S-D
S-A-D

## Slide 11: Solution: Decompose the Policy
Decompose into multiple isotonic policies (where possible)
Separate probes
  One probe for “then” and one for “else”
  Each node makes its own decision
  Tag packets based on the chosen branch
  if (A B D)
  then 0
  else path.util
A
D
B
0.2
C
0.1
0.1
0.1

## Slide 12: Challenge #2: Compute Policy-Compliant Paths Efficiently
Shape of a path affects its ranking
  Convert regular expressions to DFAs
  Carry current DFA state in the probes
B
C
A
D
  if (A B D)
  then 0
  else if (B .* D)
  then path.util
  else ∞
0
1
2
3
D
B
A
0
1
2
D
B
not B

## Slide 13: Solution #2: Join With the Topology
Some automaton transitions cannot happen
  Disallowed by the network topology
  E.g., D-A-B cannot happen (no D-A edge)
Product graph
  Node: (node id, state in DFA 1, state in DFA 2)
  Edge: valid edge in the topology, and valid transition in each DFA
  Determines how to tag and duplicate probes
B
C
A
D

## Slide 14: Product Graph
B
C
A
D
0
1
2
3
D
B
A
0
1
2
D
B
not B
Topology
DFA1
DFA2
(D0, 1, 1)
(B0, 2, 2)
(C0, -, 1)
(B1, -, 2)
(A0, -, 1)
(A1, 3, -)
0.5
0.4
0.2
0.1
0.3
dst | tag | metric | ntag | nhop
D | B0 | 0.3 | D0 | D
D | B1 | 0.2 | C0 | C
Table at B
B’s best path
Used by A
Notes: Note: ensures DFAs are satisfied even during transients

## Slide 15: Challenge #3: Forwarding loops
Forwarding loops easily arise
  Non-hierarchical topology
  Distance-vector routing
A
S
D
B
0.1
0.1
0.1
0.7
0.2
A
S
D
B
0.5
0.1
0.1
0.7
0.2
A receives probes from B after A-D link metric increases
A
S
D
B
0.5
0.1
0.1
0.7
0.2
D sends probes to A and S, and A propagates probes to B and S
Persistent loop!
Notes: B sends probe (0.1) to A that arrives late, after A-D has gone up to 0.5

## Slide 16: Solution: Version Numbers on Probes
Strawman: path-vector routing
  Larger overhead
  Hard to do in data plane
Alternative: probe version numbers
  Identify and avoid using outdated probes
  Inspired by DSDV and Babel
Probe frequency
  Old probes propagate, before new probes sent
A
S
D
B
0.5
0.1
0.1
0.7
0.2
probe i
probe i+1
Notes: B sends probe (0.1) to A that arrives late, after A-D has gone up to 0.5
Probe period larger than half RTT

## Slide 17: Challenge #4: Interaction With Flowlet Switching
Prevent out-of-order packets in a flow
  Group packets with small interarrival times
Strawman solution: pin the flowlet
  Maintain (flowlet id, next-hop, time) for each flowlet
  If small time gap for next packet, use the pinned next-hop
  … otherwise, use the currently best next-hop
small gap
Notes: Also, helps improve stability

## Slide 18: Policy Violations Under Flowlet Pinning
Flowlet switching
  Is not policy aware
  Node timeouts at different times
C
A
E
S
  if (S C E F D + S A E B D)
  then path.util
  else ∞
F
B
D
path 1
path 2
Packets reaching E on path 2 are (still) pinned to path 1
 S-C-E-B-D policy violation!
Notes: Initially path 1 is better, and each node pins the flowlet
Path 2 becomes better, and node S switches to path 2
Packets reach node E before the flowlet entry expires
Causing some packets in flight to traverse an invalid path

## Slide 19: Solution: Flowlet Switching Per Path Constraint
Extend flowlet definition
  Before: maintain (flowlet id, next-hop, time) per flowlet
  After: include policy tag as part of the “match”
C
A
E
S
F
B
D
path 1
path 2
Packet reaching E must continue to obey the same constraint

## Slide 20: Evaluating the Contra Prototype
Contra prototype
  Written in 7485 lines of F#
  Generates switch-local P4 programs
Experimental setup
  Topologies: data centers, random graphs, ISPs
  Workloads: web search and cache
  Performance metric: flow completion time (FCT)
  Comparisons: equal-cost multipath, Hula, and SPAIN
Simulation (in ns-3) and emulation (in CloudLab)
Compiler
High-Level
Routing Policy
P4 code

## Slide 21: Contra in Data-Center Networks
Fat-tree topologies with “widest shortest path” routing
  Outperforms equal-cost multipath (esp. on asymmetric topologies)
  Performs very similarly to Hula
Flow completion time
for Web search workload
over 32 hosts with one failed link

## Slide 22: Contra on Arbitrary Topologies
Abilene topology with “minimum utilization” routing
  Outperforms shortest-path routing significantly
  Outperforms static load balancing over multipath paths (SPAIN)
Flow completion time
for Web search workload

## Slide 23: Contra Protocol Dynamics
Very few transient loops
  Less than 0.025% of packets
Load balance
  Much less imbalance than ECMP

## Slide 24: Conclusions
Performance-aware distance-vector routing
  High-level policies in a declarative language
  Compiler to synthesize data-plane programs
Good performance
  Scales to large networks topologies
  Performs comparable to systems tailored to specific topology/policy
Future work
  Compile Contra P4 programs for high-speed hardware data planes

## Slide 25: Backup Slides

## Slide 26: Challenge #2: Routing Constraints
Packets in flight violate constraint
  Packet follows S-B-S-A-D
A
S
D
B
0.2
0.1
0.1
0.9
0.1
0.1
A
S
D
B
0.2
0.1
0.1
0.1
0.1
0.7
A
S
D
B
0.2
0.1
0.1
0.3
0.1
0.7
Packet: S-B
Packet: S-B-S
Packet: S-B-S-A-D
  if (.* B .* A .*)
  then ∞
  else path.util
Notes: In each step, the paths obey the constraints - S-B-D
S-D
S-A-D