## Slide 1: Programmable Network Telemetry in the Data Plane
Jennifer Rexford

## Slide 2: Telemetry is Critical for Network Management
Security
  Heavy hitters, SYN floods, port scans, superspreaders, DNS reflection, DNS tunneling, OS fingerprinting, …
Performance
  Packet loss and delay, microbursts, round-trip times, TCP root cause analysis, path performance, video QoE, …
Grand challenge: a general-purpose network telemetry platform

## Slide 3: Sonata: Spark-Like Query Abstraction
victimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
DNS Response Traffic
From Unique DNS Servers
To a Single Victim
Exceeds a Threshold
1
2
3
4
5
6
7
😵
DNS
Victim
DNS
SIGCOMM’18 paper with Arpit Gupta, Marco Canini, Nick Feamster, and Walter Willinger

## Slide 4: Sonata Query-Driven Collection and Analysis
Query partitioning
Compiling operators to P4
  Filter “udp.srcport = 53”: match-action table
  Reduce “dstip, sum”: hash-indexed register array
  Filter “count > Th”: comparison action
Optimizing the data plane
  Minimize tuples sent to Spark
tuples

## Slide 5: Compiling a Sonata Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2
Notes: In reality, the compilation can be optimized such that two match action tables can occupy the same stage as long as the values do not depend on one another. For example the actions in the first map table and actions in the first lookup for the distinct operator could be coalesced into a single table in the first stage. But as described before the two tables implementing distinct and reduce cannot be executed in the same stage due to the data dependency.

## Slide 6: Greater Generality: Traffic Across a Switch
Traffic across a single switch
  Packet modifications: .filter(srcip_in != srcip_out)
  Queuing delay: .filter(queue.len_out > T)
  Packet loss: .lost(count, [srcip_in])
SwitchScope (Ross Teixeira)
Richer packet tuples
Synchronizing time epochs
More complex compilation

## Slide 7: Greater Generality: Traffic Across a Path
Statistics over a path
  End-to-end delay
  Maximum queuing delay
  Maximum link utilization
“Reduce’’ on link metrics
  Using inband network telemetry
Predicates over path properties
  Traversing a given link
  Avoiding a firewall
  Traffic matrix
“Regular expression” on paths
  Using DFA over the switches
Path Queries (Srinivas Narayana, Mina Arashloo, David Walker)

## Slide 8: Greater Generality: Traffic Across a Network
Network-wide statistics
  Heavy-hitters for the whole network
Think locally
  Counting of significant flows
  Reporting of significant counts
Act globally
  Combining results across switches
  Computing adaptive thresholds
Communication
State
Herd (Rob Harrison, Shir Landau-Feibish, Arpit Gupta, Ross Teixeira, Muthu Muthukrishnan)

## Slide 9: Greater Generality: Approximate Queries
Sonata
  Computing exact answers to queries
  Using significant data-plane resources
  … and sending some tuples to Spark
Goal: many queries in the data plane
  With limited memory accesses per packet
  … by computing approximate answers
General query model
  Identify keys where # distinct items > threshold
  E.g., superspreaders (srcip sending to too many dstip)
BeauCoup (Danny Chen, Shir Landau-Feibish, and Mark Braverman)
Coupon Collector Problem

## Slide 10: Conclusion
Network telemetry is important
  Crucial for good performance and security
Toward a general platform
  High-level query language
  Efficient compilation to the data plane
  From single switch, to path, to network-wide
  With approximate answers to scale to more queries
Using Tofino switches and the Princeton campus network
Eventually “closing the loop” for automated network control!