## Slide 1: Higher-Order Telemetry in the Data Plane
Jennifer Rexford Princeton University

## Slide 2: Programmability Top-to-Bottom and End-to-End
NIC
NIC
Kernel stack
User space
vSwitch
DPDK
XDP/eBPF
5G Mobile
Network
DoS Mitigation
Traffic Engineering
Load
Balancing
…
Overlay Virtualization
Controller

## Slide 3: Closing the Control Loop
Measure (dials)
Adapt (knobs)
Analyze
Traffic, performance, attacks, failures, etc.
Drop, mark, rate-limit, reroute, etc.

## Slide 4: Key Enabler: Network Telemetry
Measure (dials)
Adapt (knobs)
Analyze
Traffic, performance, attacks, failures, etc.
Drop, mark, rate-limit, reroute, etc.

## Slide 5: Data-Plane Telemetry Today
Counts based on network identifiers
“67,845 bytes between 1.2.3.4 and 5.6.7.8”
Path measurements of individual packets
“Queueing delay of 25 msec from 1.2.3.4 to 5.6.7.8”

## Slide 6: Higher-Order Telemetry in the Data Plane
End-to-end performance for network services
“50 msec round-trip time to Netflix”
In the data plane for efficiency, privacy, and direct action!

## Slide 7: Higher-Order Data-Plane Telemetry: Performance
From traffic counts to end-to-end performance
  Traffic counts: # bytes, # packet losses, …
  Performance: round-trip-time
  Challenge: join a packet with its ACK
Example use cases
  Service Level Agreement violations
  BGP interception attacks
  CDN replica selection
  Video QoE inference

## Slide 8: Higher-Order Data-Plane Telemetry: Names
From network identifiers to high-level names
  Identifiers: IP addresses, TCP/UDP port numbers, …
  Names: domain names (e.g., *.netflix.com)
  Challenge: join DNS response with subsequent data packets
Example use cases
  Traffic volume by site name or class
  Intrusion Detection System bypass
  IoT device fingerprinting
  DNS tunneling detection
www.netflix.com

## Slide 9: Data-Plane Challenges
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table
Limited parsing depth
Limited number of registers
Registers and processing divided across stages

## Slide 10: Round-Trip Time Monitoring
Client
Server
Vantage Point
Handshake RTT
SYN
SYN/ACK
ACK
SEQ
ACK
Per-packet RTT
SEQ
Continuous per-packet RTT
ACK
...
……

## Slide 11: RTT Challenges: Correctness and Efficiency
Packet retransmission
Packet reordering
Multiple packets in flight
Packets never ACKed
Long round-trip times
SYN floods and port scans
Many active connections
…
Vagaries of TCP traffic
Data-plane limitations

## Slide 12: Matching a Packet With its ACK
Insert into table
s→d, 10000, 1500
200 ms
d→s, 11500
300 ms
Client
Server
Data (SEQ)
ACK
eACK = SEQ# + len
ACK# == eACK?
Flow ID, expected ACK | Timestamp
{sIP, sPort, dIP, dPort}, 11500
200
Match, sample, delete
300 - 200 = 100 ms
Packet table

## Slide 13: Ensuring Correctness
Flow table
  Track sequence number range for valid samples
  Avoid taking inappropriate RTT measurements
Packet Table
Flow ID, expected ACK | Timestamp
Flow Table
Flow ID | Measurement Range
{sIP, sPort, dIP, dPort}, 11500
200
{sIP, sPort, dIP, dPort}
[8000, 11500]
s→d, 10000, 1500
300 ms

## Slide 14: Ensuring Efficiency
Reducing memory pressure
  Lazy eviction of packets that never produce RTT samples
  Lazy eviction of inactive flows from flow table
  No RTT samples for handshake packets (e.g., SYN flood)
Packet Table
Flow ID, expected ACK | Timestamp
Flow Table
Flow ID | Measurement Range
{sIP, sPort, dIP, dPort}, 11500
200
{sIP, sPort, dIP, dPort}
[18000, 22500]
s*→d*, 10000, 1500
400 ms
Recirculate (and perhaps evict!)
{s*IP, s*P, d*IP, d*P}
[3000, 5000]
Hash collision

## Slide 15: Round-Trip Time Monitoring in the Wild
Princeton campus traffic (p4campus.cs.princeton.edu)
  Collects vast majority of viable RTT samples (vs. tcptrace)
Prototype in progress on the Intel Tofino switch
Evaluating practical use cases
Campus WiFi performance
Detecting BGP interceptions

## Slide 16: Network Telemetry by Domain Name

## Slide 17: Network Telemetry by Domain Name

## Slide 18: DNS Response Message and Application Traffic
“www.netflix.com is 5.6.7.8”
“Address of www.netflix.com?”
5.6.7.8
1.2.3.4
DNS
Data traffic between 1.2.3.4 and 5.6.7.8

## Slide 19: DNS Telemetry Monitoring Challenges
Long domain names
Variable-length names
Browser DNS caching
Long-lived application sessions
Many clients and services
Vagaries of DNS and applications
Data-plane limitations

## Slide 20: Storing DNS Response Data
Domain Name | dID
*.netflix.com | 0
*.nflvideo.net | 0
*.edu | 1
* | 2
P a r s
e r
(cIP, sIP) | Time | dID
1.2.3.4, 5.6.7.8 | 101 | 0
Client: 1.2.3.4 Name: www.netflix.com
Time: 101
Server: 5.6.7.8
match-action rules
DNS Response Map
Limits on domain name parsing
<15char>.<15char>.<15char>.<15char>
(four parts, each at most 15 characters)
Lazy eviction of stale
DNS Response data
(100 sec timeout)
Domain IDs: Never store the domain names in DNS responses!

## Slide 21: Counting Data Traffic by Service
P a r s
e r
(cIP, sIP) | Time | dID
1.2.3.4, 5.6.7.8 | 101 103 | 0
Client: 1.2.3.4
Server: 5.6.7.8 Time: 103
Length: 243 bytes
DNS Response Map
Packets | Bytes
0+1 | 0+243
0
1
2
Traffic Statistics
3
Maintaining freshness!
Counting traffic by service!

## Slide 22: Tofino Prototype and Deployment
Tofino prototype (github.com/jkim117/Meta4)
  Parses up to four 15-byte name labels
  100-second DNS response timeout
  2-stage, 216 entry DNS response table
Princeton deployment highlights
  8-11am: 33% Skype/Microsoft Teams
  3-3:15pm: 16% Steam Games, 12% Facebook
  DNS tunneling and IoT device fingerprinting use cases

## Slide 23: Conclusion
Network telemetry
  Enables the network “control loop”
Higher-order telemetry
  Performance (e.g., RTT)
  Services (e.g., domain names)
Enables a rich set of use cases
Possible in high-speed data planes!

## Slide 24: Thank You!
Jennifer Rexford
http://www.cs.princeton.edu/~jrex
X. Chen, H. Kim, J. Aman, W. Chang, M. Lee, J. Rexford, “Measuring TCP round-trip time in the data plane,” ACM SIGCOMM Workshop on Secure Programmable Network Infrastructure, SPIN 2020. https://p4campus.cs.princeton.edu/pubs/rtt20_paper.pdf
S. Sengupta, H. Kim, J. Rexford, “Fast and accurate passive round-trip time measurement in the data plane,” May 2021. https://p4campus.cs.princeton.edu/pubs/P4-RTT.pptx
J. Kim, H. Kim, J. Rexford, “Analyzing traffic by domain name in the data plane,” May 2021.
https://p4campus.cs.princeton.edu/pubs/Meta4_sigconf-latest.pdf
Learn More