## Slide 1: Network Telemetry in the Data Plane
Jennifer Rexford

## Slide 2: Network Telemetry
Knowing what’s going on in the network
  To detect, diagnose, and fix the problem
  For better performance, security, and reliability
Measure (dials)
Adapt (knobs)
Analyze
Traffic, performance, attacks, failures, etc.
Drop, mark, rate-limit, reroute, etc.

## Slide 3: Example Telemetry Questions
Performance
  Why are web downloads so slow right now?
  What is causing this link to be congested?
  Are service-level agreements (SLAs) being violated?
  What is the video Quality-of-Experience (QoE) for Netflix clients?
Security
  Are any customers victims of DNS amplification attacks?
  Why are lightly loaded links experiencing bursty packet loss?
Network engineering
  What is the offered load (“traffic matrix”) for the network?

## Slide 4: Traffic Measurement in Traditional Networks
One-size-fits-all measurement
  Coarse-grained counters (e.g., SNMP)
  Packet/flow sampling (e.g., Netflow)
Complex analysis of incomplete data
  Overhead to backhaul data to a collector
  Indirect inference of important metrics
measurement
analysis

## Slide 5: Data-Plane Programmability for the Win
Collect the data you need: customized to analysis
Analyze the data in place: measurement + analysis
Enable closed-loop control: take direct action
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table

## Slide 6: Network Telemetry Using Data-Plane State
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table
Local registers
(data structures)
Packet metadata
(piggyback statistics)

## Slide 7: Bridging the Gap
Expressive query languages
Efficient measurement and analysis
Programming languages
Compact data structures

## Slide 8: Recent Projects
Expressive languages
  Map-reduce for network telemetry (Sonata)
  Regular expressions on paths (Path Queries)
  Elastic data-plane data structures (P4All)
  Control inside the data plane (Lucid)
Efficient data structures
  Heavy-hitter detection (HashPipe, Precision)
  Microburst analytics (ConQuest)
  Multiple count-distinct queries (BeauCoup)
  Round-trip times (P4RTT)
  Traffic by domain name (Meta4)

## Slide 9: Recent Projects
Expressive languages
  Map-reduce for network telemetry (Sonata)
  Regular expressions on paths (Path Queries)
  Elastic data-plane data structures (P4All)
  Control inside the data plane (Lucid)
Efficient data structures
  Heavy-hitter detection (HashPipe, Precision)
  Microburst analytics (ConQuest)
  Multiple count-distinct queries (BeauCoup)
  Round-trip times (P4RTT)
  Traffic by domain name (Meta4)

## Slide 10: Sonata: Query-Driven Streaming Network Telemetry
Arpit Gupta, Rob Harrison, Marco Canini, Nick Feamster, Jennifer Rexford, and Walter Willinger
SIGCOMM’18

## Slide 11: Flexible Telemetry for Network Management
Many analysis questions
  Performance diagnosis
  Cyber attack detection
  Traffic engineering
Familiar query language
  Packet as a tuple
  Dataflow operators
  E.g., Spark-like queries
E.g., DNS reflection attacks
👺
😵
Src: Victim
Dst: DNS
Src: Victim
Dst: DNS
Src: DNS
Dst: Victim
Src: DNS
Dst: Victim
DNS
DNS
Attacker
Victim
DNS Response Traffic
From Unique DNS Servers
To a Single Victim
Exceeds a Threshold

## Slide 12: Spark-Like Query Language
victimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
DNS Response Traffic
From Unique DNS Servers
To a Single Victim
Exceeds a Threshold
1
2
3
4
5
6
7
Notes: Let’s see how this type of monitoring query might be expressed in a modern data flow-like language.
[🌀] On line two we see a filter operator that specifies DNS Traffic,
[🌀] lines 3-4 to narrow that down to traffic from unique DNS servers,
[🌀] line 5 further narrows the query down to a single Victim, and
[🌀] lines 6-7 determine when the number of unique DNS servers contacting that single victim exceeds a threshold.
This query is easy to express in a high-level language, and easy to compute at a modern stream processor. But how does executing this query scale?

## Slide 13: Query-Driven Collection and Analysis
Scalability challenges
  Many packets and flows
  Many queries
  Many switches
Query-driven collection
  Integrate collection and analysis
  Customize collection to the query
  Fine-grained with low overhead
Query partitioning
tuples

## Slide 14: Compiling Individual Operators
filter(p)
Stream of Elements
Elements Statisfying
Predicate (p)
Match | Action
p | 
udp.sport == 53 | 
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Notes: Let's start by looking at what it takes to compile individual operators to match-action tables, one at a time.
[🌀] The filter operator takes [🌀] a stream of elements as input, and returns[🌀] the set of elements that satisfy some predicate p.
We can implement this in a [🌀] match-action table by simplying supply p as the match component.
If we return to the [🌀] DNS reflection query I described in the beginning, we see that the predicate performs an exact match on the UDP source port. We would implement this [🌀] directly in the match-action table as shown.

## Slide 15: Compiling Individual Operators
filter(p)
Stream of Elements
Elements Statisfying
Predicate (p)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
control ingress {
apply(filter_map_table);
...
apply(reduce_table);
if (m.reduce_table_sum > Th) {
apply(report_table)
}
Notes: The filter operator can also be used to apply a conditional predicate, as we see in the last line of this query.
In this case, we would instead choose to implement the filter in the control flow between match-action tables in the pipeline. [🌀] If we look at this code block, we see that the match-action tables that each operator compiles to is applied in the control flow of the processing pipeline. After the reduce_table is applied, the final filter’s predicate is supplied in conditional control flow that then conditionally applies the table that performs the reporting to the stream processor, when the predicate is satisfied.

## Slide 16: Compiling Individual Operators
map(f)
Match | Action
 | f
* | m.dstIP = p.dstIP m.srcIP = p.srcIP
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of Elements
Result of Applying
Function f to Each Element
1
2
3
4
5
6
7
Notes: Similar to filter, [🌀] The map operator also takes [🌀] a stream of elements as input and [🌀] returns the set of elements with a function(f) applied to each element.
We can implement that, in general, [🌀] as the action body of a match-action table where the function f, if supported by the data plane, is applied.
Returning to our example query [🌀] , the function applied here is simply a projection of the entire original packet to a single dstIP, srcIP pair. In this case, [🌀] we would just store the values from the packet in metadata for subsequent processing. However, other actions such as decrementing a TTL field are possible.

## Slide 17: Compiling Individual Operators
reduce(f)
Match | Action
* | idx = hash(m.dstIP)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of Elements
Result of Applying
Function f Over All Elements
Registers
Match | Action
* | stateful[idx] += 1
1
2
3
4
5
6
7
Notes: The [🌀] reduce operator also takes [🌀] a stream of elements as input and returns [🌀] a single result that is the application of the function f over all elements. Naturally, we break up the stream into windows of size (w) seconds to compute this function over a finite stream.
Unlike map and filter, the reduce function requires some stateful memory to store the intermediate value of the function between the arrival of successive elements. Just like with the map operator, the function to be applied must still be executable in the data plane.
Like the map operator, we would also apply the function f in the action body of a match-action table, but since stateful memory is implemented as a hash-table in PISA switches, we must first compute an index into the hash table before looking up the value stored in it.
In the case of our example query, [🌀] the first table computes an index by hashing the key of interest, in this case dstIP. Since lookup into the hash-table depends on the value of the index, both the value in the hash table in the index cannot be looked up in the same table. The second table applies the function (sum) to the intermediate value and the next element (1).

## Slide 18: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
Registers
Filter Map
Filter
D1
D2
Map
R1
R2
Notes: In reality, the compilation can be optimized such that two match action tables can occupy the same stage as long as the values do not depend on one another. For example the actions in the first map table and actions in the first lookup for the distinct operator could be coalesced into a single table in the first stage. But as described before the two tables implementing distinct and reduce cannot be executed in the same stage due to the data dependency.

## Slide 19: Partitioning Decisions
Query Planner
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Target Resources?
Reduce Load?
Notes: So we’ve seen how a [🌀] single query, is compiled to a sequence of match action tables in the data plane. However, we want to run [🌀] several different queries concurrently. Now we must consider, for all of the operators in all of the queries that can be compiled to the data plane, which ones do we actually choose to offload to the data plane? Determining the answer to that question is the [🌀] job of the query planner which takes into consideration two questions? First, [🌀] does the target have enough remaining resources and to offload a partitioning to the data plane and Second, [🌀] does this partitioning reduce the load on the stream processor optimally?

## Slide 20: Query Compilation
Constraints: packet header vector, registers, ALUs, stages
Optimization: integer linear program
Objective: minimize tuples sent to controller
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table

## Slide 21: Experimental Results
Wide range of queries
  Performance, security, traffic engineering
Realistic traffic
  CAIDA packet traces
Practical data-plane model
  16 stages, 8 stateful operations, 8 Mb stateful memory
Significant scalability benefits
  Orders of magnitude fewer tuples sent to stream processor

## Slide 22: Sonata Limitations
Simple data structures
  Rather than compact data structures
Separate resources per query
  Rather than statistical multiplexing
Recompilation of queries
  Rather than run-time reconfigurability
Single switch
  Rather than network-wide telemetry
BeauCoup
Some initial work (PacketScope, Carpe)

## Slide 23: BeauCoup: Answering Many Network Traffic Queries, One Memory Update at a Time
Xiaoqi Chen, Shir Landau-Feibish, Mark Braverman, and Jennifer Rexford
SIGCOMM’20

## Slide 24: Count-Distinct Queries
Internet
DDoS:
Are there many Source IPs sending to one particular Destination IP?
Select DstIP where distinct(SrcIP)>1000
Key
Attribute
Threshold

## Slide 25: Many Queries
Query | Key | Attribute | Threshold
DDoS | DstIP | SrcIP | 1000
Worm | SrcIP | DstIP | 300
PortScan | SrcIP,DstIP | DstPort | 100
… | … | … | …
Internet
DDoS?
Worm?
Port Scan?
…
Different keys/attrs, need multiple data structures

## Slide 26: Many Queries
I have 42 queries
Run 42 data structures?
I can’t…
Spec for today’s commodity programmable switch:
XX Tbps aggregated throughput
YY MB data-plane memory
Can only access ZZ bytes of memory per packet
(True for CPU, FPGA, etc., as well… Moore’s law!)

## Slide 27: Coupon Collector Problem
Four different coupons, collect all of them
Random draws
How many total draws are required?
C
D
A
B
?

## Slide 28: BeauCoup coupon collector
f(10.0.1.15) -> Coupon
f(10.0.1.33) -> Coupon
f(10.0.1.15) -> Coupon
f(10.0.1.42) -> No Coupon
f(SrcIP) -> Coupon
?
Mapping
Select DstIP where distinct(SrcIP)>100
Collect different coupons
C
B
C
C
D
A
B
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
SrcIP: 10.0.1.33
DstIP: 162.249.4.107
SrcIP: 10.0.1.42
DstIP: 162.249.4.107
Key: 162.249.4.107
Coupons:

## Slide 29: BeauCoup Coupon Collector
Generalization: (m, p, n)-coupon collector
m*p<1, most packets collect no coupon
f(SrcIP) -> Coupon
?
m=8 coupons in total
stop at n=4 different coupons
Example:
(m=8, p=1%, n=4)
Given a new SrcIP, each coupon is drawn with probability 1%

## Slide 30: Stacking Queries With the Same Attribute
q1: f(SrcIP) -> Coupon . m1=4, p1=1/8
?
Hash function
h1(SrcIP) -> [0,1)
1
1/4
1/2
3/4
0
q1 #1
q1 #2
q1 #3
q1 #4
4 coupons for q1
q2: f(SrcIP) -> Coupon . m2=3, p2=1/16
?
q2 #1
q2 #2
q2 #3
3 coupons for q2
…
…

## Slide 31: BeauCoup Design
Multiple queries
  Same attribute: divide the hash output space
  Different attributes: arbitrate if multiple queries activate a coupon
Sharing memory space
  Single coupon table: (Query, Key)  coupon bit vector
  Statistical multiplexing of the register arrays
Updating the set of queries at runtime
  Match-action rules for selecting coupons
  Change the match-action rules at runtime

## Slide 32: BeauCoup Design
The installed rules represent query set Q
Update queries on the fly, without recompiling P4
Table rules
Header field tuples
Key, Attribute, Threshold
Code Generator
Query Compiler
(m,p,n)
Rules Generator
P4 Compiler
Data plane program
Static
program
Dynamic
rules
Query set Q = {q1, q2, …}
code
Programmable Switch
Packets
Alerts

## Slide 33: Conclusion
Network telemetry
  For network administrators
  For closed-loop network control
Programmable data planes
  Telemetry customized to the tasks at hand
  Both fine-grained and efficient
Flexible query interface
  Sonata: map-reduce queries compiled to the data plane
  BeauCoup: supporting multiple (approximate) queries efficiently

## Slide 34: Ongoing Work: Higher-Order Telemetry
Performance
  Round-trip times (e.g., 50 msec latency)
  Challenge: matching TCP packet with an ACK
  https://p4campus.cs.princeton.edu/pubs/P4-RTT.pptx
Site names
  Traffic by domain name (e.g., www.netflix.com)
  Challenge: matching DNS response with the data traffic
  https://p4campus.cs.princeton.edu/pubs/Meta4_sigconf-latest.pdf
Talk at the May 2021 P4 Workshop: https://www.youtube.com/watch?v=2zLxBYZ3Xiw

## Slide 35: Backup Slides

## Slide 36: One Hash Function for Each Attribute
q1: f(SrcIP) -> Coupon . m1=4, p1=1/8
?
q6: g(DstIP) -> Coupon . m6=3, p6=1/8
?
h1(SrcIP) ->
1
1/4
1/2
3/4
0
q1 #1
q1 #2
q1 #3
q1 #4
…
h2(DstIP) ->
1
1/4
1/2
3/4
0
q6 #1
q6 #2
q6 #3
…

## Slide 37: TCAM for Selecting a Coupon
Packet
SrcPort: 25012
DstPort: 443
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
hA(SrcPort)=101010…
hB(DstPort)=111010…
hC(SrcIP)=1010111…
hD(DstIP)=0101011…
Match hA(SrcPort) | Query#,Coupon#
000***** | (5,1)
001***** | (5,2)
010***** | (5,3)
01101*** | (9,1)
… | …
Match hB(DstPort) | Query#,Coupon#
… | …
Match hC(SrcIP) | Query#,Coupon#
… | …
Match hD(DstIP) | Query#,Coupon#
000***** | (6,1)
001***** | (6,2)
010***** | (6,3)
01101*** | (8,1)
… | …
No coupon
q6 #3
Collect coupon (q6, #3)
No coupon
No coupon
Random tiebreak if >1 coupons

## Slide 38: Coupon collector table
Q , Key | Coupons
q4: 8.8.8.8:53 | 
q4: 1.1.1.1:53 | 
q5: 10.0.0.1 | 
q6: 10.0.1.33 | 
q6: 10.0.1.15 | 
1
4
2
3
1
4
2
3
1
2
3
4
3
1
2
3
1
2
3
2
Packet
SrcPort: 25012
DstPort: 443
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
q6 #3
q6: SrcIP
q6 Coupon #3
Key: 10.0.1.15
Query q6
Key 10.0.1.33
3
Packet
SrcPort: 27000
DstPort: 443
SrcIP: 10.0.1.33
DstIP: 4.3.2.1
q6 #1
q6 Coupon #1
Key: 10.0.1.33
1
q6: DstIP, 1000
SrcIP 10.0.1.33 is sending to >1000 distinct DstIPs.
Space efficiency:
Keys from all queries multiplexed into one table
Only keep rows for “active keys” (at least one coupon)
Clear rows after timeout