## Slide 1: Pronto: Verifiable, Closed-Loop Control of 5G Networks
Nate Foster and Jennifer Rexford
With Stanford University (Sachin Katti, Nick McKeown) and the Open Networking Foundation (Guru Parulkar, Larry Peterson, Oguz Sunay)

## Slide 2: Programmability Top-to-Bottom and End-to-End
NIC
NIC
Kernel stack
User space
Kernel stack
User space
DPDK
XDP/eBPF
DPDK
XDP/eBPF
BGP
Traffic Engineering
Load
Balancing
…
Overlay Virtualization
SDN Controller

## Slide 3: Programmability Top-to-Bottom and End-to-End
NIC
NIC
Kernel stack
User space
Kernel stack
User space
DPDK
XDP/eBPF
DPDK
XDP/eBPF
BGP
Traffic Engineering
Load
Balancing
…
Overlay Virtualization
SDN Controller
Compile
Compile
Compile
Partition
Compile
Specified Behavior

## Slide 4: Programmability Enables Closed-Loop Control
Measure (dials)
Adapt (knobs)
Analyze
Traffic, performance, attacks, failures, etc.
Drop, mark, rate-limit, reroute, etc.

## Slide 5: Programmability Enables Network Verification
Two approaches...
Static: analyze network programs to check important properties prior to deployment (e.g., reject a data-plane configuration that creates a routing loop)
Dynamic: instrument network programs to automatically enforce important properties (e.g., reject a packet that would violate slice isolation)

## Slide 6: Pronto’s Premise
NIC
NIC
Kernel stack
User space
Kernel stack
User space
DPDK
XDP/eBPF
DPDK
XDP/eBPF
BGP
Traffic Engineering
Load
Balancing
…
Overlay Virtualization
SDN Controller
Networks, for the first time, will be
  Programmable top-to-bottom
  Programmable end-to-end
  Defined entirely by software
Because of open-source, we (the research community) get to take part.
This creates new possibilities
  Closed-loop network control
  Real-time verification and fixing
  Networks correct by construction
5G Mobile
Network
5G is being redefined by software, too!

## Slide 7: High Level Objectives
“We will create and deploy the first network—including 5G—under verifiable closed-loop control as an exemplar for others in government, industry, and education to replicate.”
“Pronto will be an operational network that is deployed in a production environment, carries real traffic, and runs innovative edge services.”
…and then we demonstrate new research ideas on top

## Slide 9: Pronto Summary
Enable network owners to make their networks programmable
Research
Develop
Deploy
Edge-controlled, programmable network at three universities and ONF, including Tofino switches, P4-NICs, servers
ONF open-source Aether platform

## Slide 10: ONF Aether Platform https://opennetworking.org/aether/

## Slide 11: Aether is Operational
Drones, IoT devices, and mobile phones as end-user devices
A rack of 2x2 SDN fabric, CPU (and GPU) servers at each edge location forming the edge cloud
A multi-cloud platform for 4G/5G connectivity
4G/5G small cells serving real traffic for Internet access and edge applications

## Slide 12: Aether Software Architecture: Current Status
Central Cloud
Aether Connected Edge
Tofino switch
Tofino Switch
Tofino Switch
INT
INT
INT
Stratum
Stratum
Stratum
Fabric Control
Telemetry
Collection & Analytics
4G/5G Core User Plane
fabric.p4
fabric.p4
fabric.p4
Aether Connectivity Control (ACC)
Aether Management Platform (AMP)
Kubernetes
Tofino switch
INT
Stratum
fabric.p4
µONOS SD-RAN Controller
RAN Control
RAN
Pronto Generation & Verification
ONOS
(ACE)
SDN Substrate
SD-Core
Operational Platform
SD-RAN
Operational Platform
Operational Control
Lifecycle Mgmt
Monitoring / Logging
4G/5G Core Control Plane

## Slide 13: Aether has been operational since December 2019 Now running 2x2 Pods at Stanford, Princeton, Cornell
Aether Management Platform (AMP)
Aether Connectivity Control (ACC)
Aether Connected Edge (ACE)
ONF
Intel
Ciena
AT&T
ONF
Telefonica
Turk Telekom
NTT
Google Cloud
US West
Cornell
Princeton
Stanford

## Slide 14: Aether Empowering Autonomous Drone Flight Research at Stanford

## Slide 15: Pronto at Stanford Flight Lab
Aether Management Platform
5G SD-Core Control
ONOS (Highly Available)
ONOS (Highly Available)
ONOS (Highly Available)
SD-Fabric Control
INT
Control
5G SD-Core UPF Control
Edge Cloud Platform
Closed-Loop Control
Verification
Telemetry Collection
5G SD-Core UPF
Motion Capture
Command Control
Drone location information
delivered to the Motion Capture app
Leveraging input from Motion Capture App,
The Command Control app makes decisions
for next waypoint location of each drone
and sends them to the drones via CBRS
small cell

## Slide 16: Pronto Demonstrations
Deep programmability
New network capabilities
Fine-grained (packet-level) visibility
Closed-loop control
Run-time packet-level verification
Cloud managed
Top-down and end-to-end programmable
Infrastructure: switches, NICs, 5G small cells
Platform: cloud automation, cloud management
Connectivity: 5G connectivity
Under 1 sec reaction time
Operational resilience against maintenance, hardware and software failures, congestion, vulnerabilities, and attacks
Applied to production-grade 5G networks
Virtualized, disaggregated, SDN and distributed cloud-based, top-down and end-to-end programmable 5G networks

## Slide 17: DEMONSTRATIONS OF PRONTO’S OPERATIONAL NETWORK
Introduction: https://youtu.be/KjdXEOUMnOI
Demo 1: Resolving hardware and software failures: https://youtu.be/CUdOSv0mUmM
Demo 2: Runtime software upgrades: https://youtu.be/K44KgMNFcZc
Demo 3: Detecting and blocking microburst congestion: https://youtu.be/XW_pgPMvuqw
Demo 4: Resiliency against DoS and exfiltration attacks: https://youtu.be/lLhffmr4YbY
Demo 5a: Automated deployment of the new Stanford edge: https://youtu.be/04sq4kQ6ySw
Demo 5b: Centralized management of all Pronto and Aether networks: https://youtu.be/FAVyonQMSuc

## Slide 18: Closed-Loop Network Control
Joint work with Xiaoqi Chen, Shir Landau-Feibish, Joon Kim, Robert MacDavid, and John Sonchack

## Slide 19: Real-Time Mitigation of Microbursts
ONOS (Highly Available)
ONOS (Highly Available)
ONOS (Highly Available)
SD-Fabric Control
INT
Control
5G SD-Core UPF Control
Edge Application
DoS attack: edge application causes unexpected congestion
Without closed-loop control: disrupts the drone flight
Command Control
5G SD-Core UPF
Motion Capture

## Slide 20: ConQuest: Alleviating Microbursts [CoNext’19]
Small timescale traffic bursts
  Clog the packet queues
  Cause packet delay and loss
Manage microbursts to handle
  Bursty workloads
  Shallow-buffer switches
  High link utilization
Closed-loop control
  Identify the responsible flows
  … and drop or rate-limit them
https://opennetworking.org/p4/conquest-flow-level-queue-analysis-in-p4/

## Slide 21: Detecting Heavy Flows in the Queue
For each flow, how many packets are in the queue?
Data-plane implementation challenges
  Updating on packet arrival and departure
  Per-flow state (key and count)

## Slide 22: Updating Data Structure Once Per Packet
Slice traffic into time windows
Each snapshot records T=4 packets
Enqueued at time 5
Dequeued at time 14

## Slide 23: Avoiding Per-Flow State
Compact data structures
  With limited memory and processing
  … at the expense of loss in accuracy
Estimate per-flow counts per snapshot
  With accurate estimate for large flows
Count-Min Sketch per snapshot
  C columns indexed by hash functions
  Increment hashi(flowid) in column i
  Estimate is the min of the C counts

## Slide 24: Real-Time Mitigation of Microbursts
ONOS (Highly Available)
ONOS (Highly Available)
ONOS (Highly Available)
SD-Fabric Control
INT
Control
5G SD-Core UPF Control
Closed-loop control
Edge Application
DoS attack: edge application causes unexpected congestion
Without closed-loop control: disrupts the drone flight With closed-loop control: uninterrupted connectivity
Command Control
5G SD-Core UPF
Motion Capture
ConQuest
https://youtu.be/XW_pgPMvuqw

## Slide 25: Runtime Network Verification
Joint work with Sundararajan Renganathan, Bruce Spang, Megan Jung, Guru Parulkar, Sachin Katti, and Nick McKeown

## Slide 26
ONOS (Highly Available)
ONOS (Highly Available)
ONOS (Highly Available)
SD-Fabric Control
INT
Control
5G SD-Core UPF Control
5G SD-Core UPF
Command Control
Motion Capture
Real-Time Mitigation of Data Exfiltration
Exfiltration attack: introduce bug that broadcasts locations of drones
Without runtime verification: drone locations known by attacker With runtime verification: drone locations only known by command/control application
https://youtu.be/lLhffmr4YbY

## Slide 27: Runtime Verification
Idea: wrap switches with runtime monitors
Add checking logic to decide whether to accept or reject each packet
✔
❌

## Slide 28: Network-Wide Runtime Verification
Can also apply this idea to the network as a whole
Checking function needs to be generalized to take a sequence of packets
Now it becomes easy to check network-wide reachability properties
✔
❌

## Slide 29: Optimization: From Packets to Telemetry
Of course, keeping track of a sequence of packets would be expensive...
Instead, we can record just the data we need for checking as telemetry
✔
❌

## Slide 30: Optimization: Inlining Checking Code
Inlining checking logic enables verifying at each hop rather than all at the end
Enables runtime enforcement of additional properties (e.g., loop freedom)
Can also reduce the amount of telemetry data that must be maintained
✔
❌
✔
❌
✔
❌
✔
❌
✔
❌

## Slide 31: P4 Implementation of Slice Isolation
#include <core.p4>
#include <v1model.p4>
const bit<16> TYPE_IPV4 = 0x800;
const bit<16> TYPE_COLOR = 0x9999;
const bit<16> TYPE_SRCROUTING = 0x1234;
#define MAX_HOPS 9
/*************************************************************************
*********************** H E A D E R S ***********************************
*************************************************************************/
typedef bit<9> egressSpec_t;
typedef bit<48> macAddr_t;
typedef bit<32> ip4Addr_t;
header ethernet_t {
macAddr_t dstAddr;
macAddr_t srcAddr;
bit<16> etherType;
}
header srcRoute_t {
bit<1> bos;
bit<15> port;
}
header ipv4_t {
bit<4> version;
bit<4> ihl;
bit<8> diffserv;
bit<16> totalLen;
bit<16> identification;
bit<3> flags;
bit<13> fragOffset;
bit<8> ttl;
bit<8> protocol;
bit<16> hdrChecksum;
ip4Addr_t srcAddr;
ip4Addr_t dstAddr;
}
header color_t {
bit<8> packet_color;
bit<16> etherCType;
}
struct metadata {
bool first_hop;
bit<8> old_color;
}
struct headers {
ethernet_t ethernet;
color_t color;
srcRoute_t[MAX_HOPS] srcRoutes;
ipv4_t ipv4;
}
/*************************************************************************
*********************** P A R S E R ***********************************
*************************************************************************/
parser MyParser(packet_in packet,
out headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) {
state start {
transition parse_ethernet;
}
state parse_ethernet {
packet.extract(hdr.ethernet);
transition select(hdr.ethernet.etherType) {
TYPE_COLOR : parse_color;
TYPE_SRCROUTING: parse_srcRouting;
default: accept;
}
}
state parse_color {
packet.extract(hdr.color);
transition select(hdr.color.etherCType) {
TYPE_SRCROUTING : parse_srcRouting;
default: accept;
}
}
state parse_srcRouting {
packet.extract(hdr.srcRoutes.next);
transition select(hdr.srcRoutes.last.bos) {
1: parse_ipv4;
default: parse_srcRouting;
}
}
state parse_ipv4 {
packet.extract(hdr.ipv4);
transition accept;
}
}
/*************************************************************************
************ C H E C K S U M V E R I F I C A T I O N *************
*************************************************************************/
control MyVerifyChecksum(inout headers hdr, inout metadata meta) {
apply { }
}
/*************************************************************************
************** I N G R E S S P R O C E S S I N G *******************
*************************************************************************/
control MyIngress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) {
action drop() {
mark_to_drop(standard_metadata);
}
action srcRoute_nhop() {
standard_metadata.egress_spec = (bit<9>)hdr.srcRoutes[0].port;
hdr.srcRoutes.pop_front(1);
}
action srcRoute_finish() {
hdr.ethernet.etherType = TYPE_IPV4;
}
action update_ttl(){
hdr.ipv4.ttl = hdr.ipv4.ttl - 1;
}
action addColor() {
meta.first_hop = true;
hdr.color.setValid();
hdr.color.etherCType = hdr.ethernet.etherType;
hdr.ethernet.etherType = 0x9999;
}
action removeColor() {
hdr.ethernet.etherType = hdr.color.etherCType;
hdr.color.setInvalid();
}
table debug {
key = { hdr.srcRoutes[0].isValid() : exact;
hdr.color.isValid() : exact; }
actions = { }
}
apply {
debug.apply();
if (hdr.srcRoutes[0].isValid()) {
if (!hdr.color.isValid()) {
addColor();
}
if (hdr.srcRoutes[0].bos == 1) {
removeColor();
srcRoute_finish();
}
srcRoute_nhop();
if (hdr.ipv4.isValid()) {
update_ttl();
}
} else {
drop();
}
}
}
/*************************************************************************
**************** E G R E S S P R O C E S S I N G *******************
*************************************************************************/
control MyEgress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) {
action drop() {
mark_to_drop(standard_metadata);
}
action setColor(bit<8> switchColor) {
if (meta.first_hop) {
hdr.color.packet_color = switchColor;
} else {
meta.old_color = hdr.color.packet_color;
hdr.color.packet_color = switchColor;
}
}
table colors {
actions = { setColor; NoAction; }
default_action = NoAction();
}
apply {
colors.apply();
if (!meta.first_hop && meta.old_color != hdr.color.packet_color) {
drop();
}
}
}
/*************************************************************************
************* C H E C K S U M C O M P U T A T I O N **************
*************************************************************************/
control MyComputeChecksum(inout headers hdr, inout metadata meta) {
apply { }
}
/*************************************************************************
*********************** D E P A R S E R *******************************
*************************************************************************/
control MyDeparser(packet_out packet, in headers hdr) {
apply {
packet.emit(hdr.ethernet);
packet.emit(hdr.color);
packet.emit(hdr.srcRoutes);
packet.emit(hdr.ipv4);
}
}
/*************************************************************************
*********************** S W I T C H *******************************
*************************************************************************/
V1Switch(MyParser(), MyVerifyChecksum(), MyIngress(), MyEgress(), MyComputeChecksum(), MyDeparser()) main;
= Untrusted user code
= Trusted checking code

## Slide 32: Aether Properties
Packets forwarded to leaf switch corresponding to configured subnets
Bridged packets to learned MAC address sent to corresponding output port
Packets processed by ECMP table only forwarded to infrastructure ports
All packets sent to ONOS controller are unmodified
VLAN bridging isolation
Service chain isolation
Loop freedom

## Slide 33
ONOS (Highly Available)
ONOS (Highly Available)
ONOS (Highly Available)
SD-Fabric Control
INT
Control
5G SD-Core UPF Control
5G SD-Core UPF
Command Control
Motion Capture
Real-Time Mitigation of Data Exfiltration
Exfiltration attack: introduce bug that broadcasts locations of drones
Without runtime verification: drone locations known by attacker With runtime verification: drone locations only known by command/control application
https://youtu.be/lLhffmr4YbY

## Slide 34: Conclusions
Deep programmability
  Top to bottom
  End-to-end
Closed-loop control
  Measure, analyze, adapt
  Customized to the use case
Verification
  Runtime enforcement
  Optimizations to reduce overhead
Operational deployment
  ONF Aether platform
  Multiple deployment sites
prontoproject.org
aetherproject.org