## Slide 1: Networks That Do What They’re Told
Jennifer Rexford
Princeton University

## Slide 2: Networking Holy Grail: Intent-Based Management
Tell the network what to do
  At a high level
  In a declarative way
  For the network as a whole
And the network simply does it
  At a low level
  With specific mechanisms
  Across many network devices

## Slide 3: Why Has This Been So Hard for So Long?
The network is not designed to be managed
  Limited visibility into traffic, performance, etc.
  Hard-to-tune protocols and mechanisms on devices
Bolting-on network management
  Measure: read whatever “dials” are available
  Analyze: try to infer what you cannot see
  Adapt: tune whatever “knobs” are available
What could go wrong? ;)
measure
adapt
analyze

## Slide 4: Why I am Optimistic: Deep Programmability
NIC
NIC
Kernel stack
User space
vSwitch
DPDK
XDP/eBPF
5G Mobile
Network
DoS Mitigation
Traffic Engineering
Load
Balancing
…
Overlay Virtualization
SDN Controller

## Slide 5: Adding New “Dials”
Traffic
Performance
Cyberattacks
Failures
Signal strength
<Your measurement here>

## Slide 6: Adding New “Knobs”
Drop
Mark
Rate-limit
Reroute
Hand-off
<your knob here>

## Slide 7: Designing the Network Control Loop
Measure (dials)
Adapt (knobs)
Analyze

## Slide 8: Example #1: Microbursts
Small timescale traffic bursts
  Long queues caused by incast, attacks, etc.
  Lead to high packet delay and loss
  … despite low average link utilization
5x
3x
1x
16:00:00
0:00:00
8:00:00
16:00:00
Time in day (24h)
Queue Length
Microbursts

## Slide 9: Example #1: Microburst Measurement
Data-plane measurement and analysis
  Backlog in the queue
  A flow’s own contribution to the queue
55%
10%
ConQuest: https://opennetworking.org/p4/conquest-flow-level-queue-analysis-in-p4/

## Slide 10: Example #1: Microburst Mitigation
Data-plane adaptation
  Drop or mark an arriving packet probabilistically
  Based on its flow’s contribution to the queue
55%
10%

## Slide 11: Example #2: Distributed Denial-of-Service Attacks
DDoS attacks
  DNS reflection attack
  SYN flooding
  HTTP flooding
  Slowloris attack
Overwhelm the victim
  Exhausting network and server resources
😵
Victim
DNS
DNS
👺
Attacker
. . .

## Slide 12: Example #2: DDoS Detection
Data-plane measurement and analysis
  Identify suspected victim destinations (key DstIP)
  … receiving traffic from distinct senders (attribute SrcIP)
  … in excess of a threshold (threshold T)
select DstIP where distinct(SrcIP) > T
Key
Attribute
Threshold
BeauCoup: https://blog.apnic.net/2021/01/07/beaucoup-answering-many-network-traffic-queries-one-memory-update-at-a-time/

## Slide 13: Example #2: DDoS Mitigation
Data-plane adaptation
  Drop or rate-limit packets to suspected victims
  Run stateful firewall for suspected victims
  Pushback upstream toward the senders
DNS
DNS
👺
Attacker
. . .

## Slide 14: Example #3: Path Performance
Network path diversity
Load balancing to achieve good performance
  Track the performance (load, loss, delay) of paths
  Split traffic effectively over the multiple paths

## Slide 15: Example #3: Path Performance Monitoring
Data-plane tracking of path performance
  E.g., lowest maximum link utilization
  E.g., minimum end-to-end latency or loss
30%
25%
20%
50%
20%
10%
10%
30%
30%
10%
50%
Probes along reverse path

## Slide 16: Example #3: Performance-Aware Load Balancing
Data-plane adaptation to direct traffic over the best path
  Sending packets in the forward direction
  … along the path with the best performance
Contra: "A programmable system for performance-aware routing” (NSDI’20)
30%
25%
20%
50%
20%
10%

## Slide 17: Enabler: Programmable Data Planes
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table
p4.org

## Slide 18: Challenges: Resource Limitations
Limited
depth
Limited
# bits
Limited
# rules
Limited # registers
and # of accesses
Limited ALU
operations
Stages
Deparser
Parser
Memory
Registers
ALU
Match-
Action
Table

## Slide 19: Solution: Compact Data Structures
Approximate analysis is fine
  Microbursts: size estimate for just the large flows
  DDoS: rough count for large #s of distinct sources
  Path performance: rough estimates for best paths
Data structures can fit in data-plane registers
  Sketch (e.g., Bloom filter, count-min sketch, etc.)
  Small hash table (e.g., cache of the popular keys)

## Slide 20: Back to Example #1: Microburst Mitigation
For each flow, how many packets are in the queue?
P4 data structure challenges
  Updating on packet arrival and departure
  Per-flow state (key and count)
Key | Count
 | 1
 | 5
 | 1
 | 1
 | 2
 | 1

## Slide 21: Approximate Answers
For each flow, how many packets are in the queue?
Approximation is fine
  Just the current packet
  Just if the packet belongs to a big flow
  Just a rough count of the traffic volume
  Just a rough sense of the time window

## Slide 22: Approximate Counting: Sketch
Compact data structures
  With limited memory and processing
  … at the expense of lower accuracy
Estimate per-flow counts per snapshot
  With accurate estimates for large flows
Count-Min Sketch
  C columns indexed by hash functions
  Increment hashi(flowid) in column I
  Estimate is the min of the C counts
Count-Min Sketch [CM ‘05]
C columns
B Buckets
f
+1
+1
+1

## Slide 23: Approximate Time: Multiple Snapshots
Divide time into windows
Count the traffic in each snapshot
  One count-min sketch per snapshot
  Aggregate the counts (e.g., 2 + 3 packets)
  Retire old snapshots, and start new ones
3 green
2 green

## Slide 24: ConQuest in Action on the Princeton Campus
Performance symptoms
  Big neuroscience data transfers
  High loss with low average load
  Router with limited measurements
Microburst analytics on Tofino
  Microbursts on a small timescale
  Caused by PerfSONAR probes
Deployment in AT&T backbone
Internet2
Mirrored traffic
Tofino
Network TAPs
Neuroscience
Institute
See https://p4campus.cs.princeton.edu/ web site for more details!

## Slide 25: ConQuest in Action in the ONF Aether Pod
ONOS (Highly Available)
ONOS (Highly Available)
ONOS (Highly Available)
SD-Fabric Control
INT
Control
5G SD-Core UPF Control
Edge Application
DoS attack: edge application causes unexpected congestion
Without closed-loop control: disrupts the drone flight
Command Control
5G SD-Core UPF
Motion Capture
prontoproject.org

## Slide 26: ConQuest in Action in the ONF Aether Pod
ONOS (Highly Available)
ONOS (Highly Available)
ONOS (Highly Available)
SD-Fabric Control
INT
Control
5G SD-Core UPF Control
Closed-loop control
Edge Application
DoS attack: edge application causes unexpected congestion
Without closed-loop control: disrupts the drone flight With closed-loop control: uninterrupted connectivity
Command Control
5G SD-Core UPF
Motion Capture
ConQuest
Demo video: https://www.youtube.com/watch?v=XW_pgPMvuqw

## Slide 27: The Pieces are Gradually Coming Together
Expressive programming languages
Efficient data structures
Programmable
network devices

## Slide 28: Grand Challenge: Synthesize the Control Loop
High-level goals
Compiler
Switch OS
switch
Controller
Switch OS
switch
NIC
NIC
vSwitch
NIC
NIC
vSwitch
Distributed software
control loop

## Slide 29: Thank You
jrex@cs.princeton.edu
https://www.cs.princeton.edu/~jrex/
To learn more
ConQuest: https://www.cs.princeton.edu/~jrex/papers/conquest19.pdf
BeauCoup: https://www.cs.princeton.edu/~jrex/papers/beaucoup20.pdf
Contra: https://www.cs.princeton.edu/~jrex/papers/contra20.pdf
P4Campus: https://p4campus.cs.princeton.edu/
Pronto: https://prontoproject.org/ and Aether: https://opennetworking.org/aether/