## Slide 1: Bamboozling Certificate Authorities with BGP
Henry Birge-Lee, Yixin Sun, Anne Edmundson, Jennifer Rexford, Prateek Mittal
Notes: Expand acronym in the title.

## Slide 2: Digital certificates as a root of trust
Root of trust on the internet
Bootstraps trust on first time connections
The keys to all web encryption

## Slide 3
Doug Madory, BGP / DNS Hijacks Target Payment Systems https://blogs.oracle.com/internetintelligence/bgp-dns-hijacks-target-payment-systems
Notes: Add slide title. Say BGP hijack. Need a takeaway text on this slide.

## Slide 4
Border Gateway Protocol (BGP) attacks compromise this root of trust
Doug Madory, BGP / DNS Hijacks Target Payment Systems https://blogs.oracle.com/internetintelligence/bgp-dns-hijacks-target-payment-systems
Notes: Focus on the transition.

## Slide 5: Overview
Domain Control Validation
BGP Attacks
Quantifying Vulnerability
Countermeasures
Takeaways

## Slide 6: Domain Control Verification
Could I get a certificate for example.com?
(Certificate Signing Request)
Certificate Authority
Server at example.com
Owner of example.com

## Slide 7: Domain Control Verification
Upload <content> to example.com/verify.html
(Domain Control Verification Challenge)
Certificate Authority
Server at example.com
Owner of example.com

## Slide 8: Domain Control Verification
Server modifications
Certificate Authority
Server at example.com
Owner of example.com

## Slide 9: Domain Control Verification
I did it!
HTTP GET example.com/verify.html
Certificate Authority
Server at example.com
Owner of example.com

## Slide 10: Domain Control Verification
Here is your certificate
Certificate Authority
Server at example.com
Owner of example.com
HTTP 200 OK: <content>

## Slide 11: Where BGP Comes In
I did it!
HTTP GET example.com/verify.html
Certificate Authority
Server at example.com
Adversary posing as owner of example.com
If an adversary can see this request it can generate a response
Adversary’s server
HTTP 200 OK: <content>
Notes: Consider how exactly BGP comes in. Adversaries can launch BGP attacks tot spoof a response.

## Slide 12: Overview
Domain Control Validation
BGP Attacks
Quantifying Vulnerability
Countermeasures
Takeaways

## Slide 13: Original BGP route to victim
AS 1
AS 3
AS 4
AS 2
Certificate Authority
Adversary
AS containing
example.com

## Slide 14: Original BGP route to victim
Certificate Authority
Adversary
I own 2.2.2.0/23
AS containing
example.com
AS 1
AS 3
AS 4
AS 2

## Slide 15: BGP route to victim under sub-prefix attack
Certificate Authority
Adversary
I own sub-prefix 2.2.2.0/24
AS containing
example.com
I own 2.2.2.0/23
AS 1
AS 3
AS 4
AS 2

## Slide 16: BGP route to victim under sub-prefix attack
Certificate Authority
Adversary
I own sub-prefix 2.2.2.0/24
AS containing
exmaple.com
I own 2.2.2.0/23
AS 4
HTTP GET example.com/verify.html
goes to adversary
AS 1
AS 3
AS 2

## Slide 17: BGP route to victim under sub-prefix attack
Certificate Authority
Adversary
I own sub-prefix 2.2.2.0/24
AS containing
example.com
I own 2.2.2.0/23
Routers prefer more specific announcements
Global visibility
Connectivity broken
Not very stealthy
AS 1
AS 3
AS 4
AS 2

## Slide 18: A local (equally-specific prefix) attack
AS 5
Certificate Authority
Adversary
AS containing
example.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
A. Gavrichenkov. Breaking HTTPS with BGP hijacking. Black Hat USA Briefings, 2015

## Slide 19: A local (equally-specific prefix) attack
AS 5
Certificate Authority
Adversary
AS containing
example.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
A. Gavrichenkov. Breaking HTTPS with BGP hijacking. Black Hat USA Briefings, 2015
Hijacked portion
Unaffected portion

## Slide 20: A local (equally-specific prefix) attack
Certificate Authority
Adversary
AS 5
AS 1
AS 3
AS 4
AS containing
example.com
I own 2.2.2.0/23
I own 2.2.2.0/23
Equally specific announcements compete for traffic
Announcement localized
Local broken connectivity
Potentially stealthy
A. Gavrichenkov. Breaking HTTPS with BGP hijacking. Black Hat USA Briefings, 2015

## Slide 21: A local (equally-specific prefix) attack
Adversary
AS 1
AS 3
AS 4
AS containing
example.com
I own 2.2.2.0/23
I own 2.2.2.0/23
Equally specific announcements compete for traffic
Announcement localized
Local broken connectivity
Potentially stealthy
Not all ASes can perform
Certificate Authority
AS 2
A. Gavrichenkov. Breaking HTTPS with BGP hijacking. Black Hat USA Briefings, 2015

## Slide 22: AS path poisoning
Adversary
I can get to 2.2.2.0/24 through AS 4
Certificate Authority
AS 1
AS 3
AS 4
AS 2
I own 2.2.2.0/23
AS containing
example.com

## Slide 23: AS path poisoning
Everyone sees announcement but looks less suspicious
Connectivity preserved
Almost any AS can perform
Very stealthy
Perfect setup to intercept traffic with certificate
Adversary
I can get to 2.2.2.0/24 through AS 4
Certificate Authority
AS 1
AS 3
AS 4
AS 2
I own 2.2.2.0/23
AS containing
example.com

## Slide 24: Ethical framework for launching real-world attacks
Hijack only our own prefixes
Domains run on our own prefixes
No real users attacked
Approached trusted CAs for certificates

## Slide 25: Results from real world attacks
 | Let’s Encrypt | GoDaddy | Comodo | Symantec* | GlobalSign
Time to issue certificate | 35 seconds | < 2 min | < 2 min | < 2 min | < 2 min
Human interaction | No | No | No | No | No
Multiple Vantage Points | Not yet | No | No | No | No
Validation Method Attacked | HTTP | HTTP | Email | Email | Email
*At time of experiments Symantec was still a trusted CA
Notes: Mention covers two thirds of CA market!!!!!!!
In your speech, can mention that these 5 CA control XX market share etc (or are the top 5 CAs etc if thats true)
Highlight some aspects of the slide in color for emphasis
I typically have a key “take away” pop up box that appears in an animation, summarizing the main point in such “Results slides”

## Slide 26: Results from real world attacks
 | Let’s Encrypt | GoDaddy | Comodo | Symantec | GlobalSign
Time to issue certificate | 35 seconds | < 2 min | < 2 min | < 2 min | < 2 min
Human interaction | No | No | No | No | No
Multiple Vantage Points | No | No | No | No | No
Validation Method Attacked | HTTP | HTTP | Email | Email | Email
All studied CAs were vulnerable
*At time of experiments Symantec was still a trusted CA
Notes: In your speech, can mention that these 5 CA control XX market share etc (or are the top 5 CAs etc if thats true)
Highlight some aspects of the slide in color for emphasis
I typically have a key “take away” pop up box that appears in an animation, summarizing the main point in such “Results slides”

## Slide 27: Additional Attacks
More targets:
  Authoritative DNS servers
  Mail servers
Attacking CA prefixes:
  Reverse (victim domain -> CA) traffic also vulnerable
Certificate Authority
DNS
Certificate Authority
Notes: Add BGP attacker to blackhat icons.

## Slide 28: Overview
Domain Control Validation
BGP Attacks
Quantifying Vulnerability
Countermeasures
Takeaways

## Slide 29: Quantifying Vulnerability
How many domains are vulnerable?
How many adversaries can launch attacks?

## Slide 30: Quantifying Vulnerability
How many domains are vulnerable?
How many adversaries can launch attacks?
1.8 million certificates via Certificate Transparency
Common names resolved to IPs
Recorded the BGP routes used for IPs at time of signing

## Slide 31: Vulnerability of domains: sub-prefix attacks
Any AS can launch
Only prefix lengths less than /24 vulnerable

## Slide 32: Vulnerability of domains: sub-prefix attacks
Any AS can launch
Only prefix lengths less than /24 vulnerable (filtering)
72% of Domains Vulnerable
28% of Domains Unaffected

## Slide 33: Resilience to equally-specific prefix attacks
Certificate Authority
Affected
Adversary
AS containing
exmaple.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
AS 5

## Slide 34: Resilience to equally-specific prefix attacks
Adversary
AS containing
exmaple.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
Certificate Authority
Resilient
AS 2
Notes: An equally-specific prefix attack will not be effective in all cases. Depending on the topological relationship between the CA, victim, and attacker, sometimes a CA is resilient to the attack.

## Slide 35: Resilience to equally-specific prefix attacks
Adversary
AS containing
exmaple.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
Certificate Authority
Resilient
AS 2
Probability a CA will be resilient to attacks on a domain
Notes: Consider referencing counter-raptor and the original DSN paper.

## Slide 36: Resilience of domains assuming random CA
Notes: Consider Assuming all ASes can be adversaries.

## Slide 37: Resilience of domains assuming random CA
Median
Median resilience is .57
43% chance of attack viability
Notes: Add emphasis on key phrases in color. BGPsec: our work serves as motivation for BGPsec.
Can add here that you are engaging with Symantec and LetsEncrypt + potentially an open source community effort etc.

## Slide 38: Choosing an affected CA
CA 2
Adversary
AS containing
example.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
CA 1
Around 100 CAs
Any one can sign any for domain

## Slide 39: Vulnerability of Domains: Equally-specific attacks
Notes: Mention CAA records in the presentation

## Slide 40: Vulnerability of Domains: Equally-specific attacks
Median resilience drops from .57 to .25
Median
Notes: Mention the chance of attack now goes to 75%

## Slide 41: Overview
Domain Control Validation
BGP Attacks
Quantifying Vulnerability
Countermeasures
Takeaways

## Slide 42: Multiple Vantage Points
AS 5
Certificate Authority
Adversary
AS containing
exmaple.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
Notes: Consider circling two components of the internet that are developed.

## Slide 43: Multiple Vantage Points
Certificate Authority
Adversary
AS containing
exmaple.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
Remote Vantage Point
Notes: Consider circling two components of the internet that are developed.

## Slide 44: Multiple Vantage Points
Certificate Authority
Adversary
AS containing
exmaple.com
I own 2.2.2.0/23
I own 2.2.2.0/23
AS 1
AS 3
AS 4
Hijacked portion
Unaffected portion
Remote Vantage Point
Only sign certificate if all vantage points and CA agree
Notes: Might want to mention that multiple vantage points also protects against ASes that happen to be on the route between a CA and a victim.

## Slide 45: Multiple Vantage Points
Key factor influencing Let’s Encrypts staging deployment
Full deployment coming soon
3 Remote Vantage Points in AS 16509
Data Center in AS 13649
1
2
3
Notes: Add emphasis on key phrases in color. BGPsec: our work serves as motivation for BGPsec.
Can add here that you are engaging with Symantec and LetsEncrypt + potentially an open source community effort etc.

## Slide 46: Resilience Improvement of Multiple Vantage Points
Resilience computed using Let’s Encrypt data center and optimally located additional vantage points
Notes: Mention CAA records in the presentation

## Slide 47: Resilience Improvement of Multiple Vantage Points
Median resilience improves from .60 to .95
Median
Resilience computed using Let’s Encrypt data center and optimally located additional vantage points
Notes: Mention CAA records in the presentation

## Slide 48: Other Defenses
CAs:
  BGP Monitoring
  CA Prefix Length
  CA Resilience
Domains:
  CAA DNS Records
  DNSSEC
Notes: Explain DNS as Domain Name Service. Please see paper for more details.

## Slide 49: Overview
Domain Control Validation
BGP Attacks
Quantifying Vulnerability
Countermeasures
Takeaways

## Slide 50: Takeaways

## Slide 51: Takeaways
Next BGP phishing attack the malicious certificate might be trusted!
Notes: Move to after demo

## Slide 52: Takeaways
CAs bootstrap trust on the internet through digital certificates
The majority of domains and CAs are vulnerable
CAs must implement countermeasures soon
Secure routing (i.e., BGPsec, RPKI, SCION) is still important even with end-to-end encryption
More information at https://secure-certificates.princeton.edu/
Thanks to support from

## Slide 53: Takeaways
CAs bootstrap trust on the internet through digital certificates
The majority of domains and CAs are vulnerable
CAs must implement countermeasures soon
Secure routing (i.e., BGPsec, RPKI, SCION) is still important even with end-to-end encryption
More information at https://secure-certificates.princeton.edu/
Thanks to support from
Questions?